Technical Committee

LAN Emulation Servers Management Specification 1.0

af-lane-0057.000

March 1996

LAN Emulation Servers Management Specification 1.0

af-lane-0057.000

March 1996

(C) 1996 The ATM Forum. All Rights Reserved. No part of this publication may be reproduced in any form or by any means.

The information in this publication is believed to be accurate as of its publication date.  Such information is subject to change without notice and the ATM Forum is not responsible for any errors.  The ATM Forum does not assume any responsibility to update or correct any information in this publication. Notwithstanding anything to the contrary, neither The ATM Forum nor the publisher make any representation or warranty, expressed or implied, concerning the completeness, accuracy, or applicability of any information contained in this publication.  No liability of any kind shall be assumed by The ATM Forum or the publisher as a result of reliance upon any information contained in this publication.

The receipt or any use of this document or its contents does not in any way create by implication otherwise:

¥	Any express or implied license or right to or under any ATM Forum member company's patent, copyright, trademark or trade secret rights which are or may be associated with the ideas, techniques, concepts or expressions contained herein; nor

¥	Any warranty or representation that any ATM Forum member companies will announce any product(s) and/or service(s) related thereto, or if such announcements are made, that such announced product(s) and/or service(s) embody any or all of the ideas, technologies, or concepts contained herein; nor

¥	Any form of relationship between any ATM Forum member companies and the recipient or user of this document.

Implementation or use of specific ATM standards or recommendations and ATM Forum specifications will be voluntary, and no company shall agree or be obliged to implement them by virtue of participation in The ATM Forum.

The ATM Forum is a non-profit international organization accelerating industry cooperation on ATM technology.  The ATM Forum does not, expressly or otherwise, endorse or promote any specific products or services.

NOTE:  The user's attention is called to the possibility that implementation of the ATM interoperability specification contained herein may require use of an invention covered by patent rights held by ATM Forum Member companies or others.  By publication of this ATM interoperability specification, no position is taken by  The ATM Forum with respect to validity of any patent claims or of any patent rights related thereto or the ability to obtain the license to use such rights.  ATM Forum Member companies agree to grant licenses under the relevant patents they own on reasonable and nondiscriminatory terms and conditions to applicants desiring to obtain such a license.  For additional information contact:

The ATM Forum

Worldwide Headquarters

2570 West El Camino Real

Suite 304

Mountain View, CA 94040

Tel:    +1-415-949-6700

Fax:    +1-415-949-6705

Acknowledgement

The contributions adopted by the ATM Forum and the assistance by the editing group of the LAN Emulation Sub-working Group, who contributed text and reviewed the contributions were essential to this specification.

In particular, the editor would like to recognise members who made significant contributions to this effort:

Chris Young

Ian Griffiths

Prakash Desai

The assistance by these members and all who participated in the LAN Emulation Sub-working Group, especially chairman Keith McCloghrie is appreciated.

Faye Ly, Editor

1. Introduction

1.1 Abbreviations

1.2 References

2. Management Functions

2.1 Configuration Management

2.2 Performance Management

2.3 Fault Management

2.4 Security Management

2.5 Accounting Management

3. Management Framework

3.1 The SNMP Network Management Framework

3.2 Requirements for LAN Emulation Servers

3.2.1 Requirements for SNMP

3.3 MIB Conventions

4. MIB-II and other MIB support

4.1 MIB II support

4.2 AToMMIB Support

5. Emulated LAN MIB Description

5.1 Management model

5.2 MIB Groups

5.2.1 ELAN Administration Group

5.2.2 ELAN Configuration Group

5.2.3 LECS Configuration Group

5.2.4 LECS Statistics Group

This table lists all counters associated with the LECS this agent maintains.

5.2.5 LECS Fault Management Group

6. LAN Emulation Server MIB Description

6.1 Management model

6.2 MIB Organisation

6.3 MIB Groups

6.3.1 LES Configuration Group

6.3.2 LES Statistics Group

6.3.3 LES-LEC Statistics Group

6.3.4 LES Fault Management Group

7. Broadcast and Unknown Server MIB description

7.1 Management model

7.2 MIB Organisation

7.3 MIB Groups

7.3.1 BUS Configuration Group

7.3.2 BUS Statistics Group

7.4.2 BUS Fault Management Group

8. LAN Emulation Servers MIB Definitions

1.	Introduction

ATM LAN Emulation emulates services of existing LANs across an ATM network.  It provides a MAC layer service, specifically Ethernet/IEEE 802.3 and IEEE 802.5, over an ATM network.  LAN emulation is described in the ATM Forum document “LAN Emulation Over ATM Specification - Version 1.0” [1].  This document describes how to manage some of the components in the LAN Emulation.

The LAN Emulation specification 1.0 defines four components: LEC (LAN Emulation Client), LES (LAN Emulation Server), BUS (Broadcast and Unknown Server) and LECS (LAN Emulation Configuration Server).  LES, BUS and LECS provide various services to enable communication between LECs, and are referred to in this document collectively as ‘LAN Emulation servers’.

This document defines the management information for LES, BUS and LECS.  The management information of the LEC is defined in [6]. This specification include three MIB modules.  The ELAN MIB provides ELAN configuration and LECS management information.  The LECS management group is mandatory if and only if the LECS is implemented.  The LAN Emulation LESServer MIB covers LES management information, and BUS MIB provides BUS management information.

1.1	Abbreviations

The following acronyms are used throughout this document.

AAL	ATM Adaptation Layer

ATM	Asynchronous Transfer Mode

BUS	Broadcast and Unknown Server

ELAN	Emulated Local Area Network

LAN	Local Area Network

LANE	LAN Emulation

LE	LAN Emulation

LE_ARP	LAN Emulation Address Resolution Protocol

LEC	LAN Emulation Client

LECS	LAN Emulation Configuration Server

LES	LAN Emulation Server

LNNI	LAN Emulation Network-Network Interface

LUNI	LAN Emulation User-Network Interface

MAC	Media Access Control

RD	Route Descriptor

RFC	Request For Comment (Document Series)

UNI	User-Network Interface

VCC	Virtual Channel Connection

VCI 	Virtual Channel Identifier

VPI 	Virtual Path Identifier

1.2	References

[1] The ATM Forum, LAN Emulation Over ATM Specification, Version 1.0.

[2] RFC 1213, McCloghrie and Rose, Management Information Base for Network Management of TCP/IP-based internets: MIB-II.

[3] RFC 1573, McCloghrie and KastenHoltz, Evolution of the Interfaces Group of MIB-II.

[4] RRC 1695, Ahmed and Tesink, Definitions of Managed Objects for ATM Management.

[5] Internet Drafts, Ly, Noto, Smith, Tesink, Definitions of Supplemental Managed Objects for ATM Management. (draft-ietf-atommib-atm2-01.txt)

[6] The ATM Forum. LAN Emulation Client Management: Version 1.0 Specification.

[7] RFC 1442, Case, McCloghrie, Rose and Waldbusser, Structure of Management Information for version 2 of the Simple Network Management Protocol (SNMPv2).

[8] RFC 1445, Galvin and McCloghrie, Administrative Model for version 2 of the Simple Network Management Protocol (SNMPv2).

[9] RFC 1448, Case, McCloghrie, Rose and Waldbusser, Protocol Operations for version 2 of the Simpel Network Management Protocol (SNMPv2).

[10] RFC 1443, Case, McCloghrie, Rose and Waldbusser, Textual Conventions for version 2 of the Simple Network Management Protocol (SNMPv2).

2.	Management Functions

Network management can be divided into the areas of configuration, performance, fault, security, and accounting management.

2.1	Configuration Management

The MIBs enable network managers to:

create and destroy Emulated LANs (ELANs)

assign clients to and delete them from an ELAN

control the parameters of the LECS, LES and BUS

monitor ELAN topology, e.g. which LECs are joined to a LES

identifying the VCCs being used by the LES or BUS

No information is provided about VCCs beyond describing which are being used.  Management of VCC configuration is specified in [4] and [5]. Management issues relating to the LANE server-to-server (LNNI) protocol are outside the scope of this specification because at time of writing the Forum work on this topic is not complete. It is however a design goal to make the MIB modules easy to extend to accommodate the future LNNI support, and it is anticipated that this will be done in a future revision of these MIBs once the LNNI protocols have been published by the ATM Forum.

2.2	Performance Management

Network managers can obtain statistics for ELAN server components.  These are collected for every server and also for each server-client pairing.  While LES- and BUS-related statistics are located in the LES MIB and BUS MIB respectively, LECS statistics (along with all other LECS management) are to be found in the optional LECS part of the ELAN MIB.

2.3	Fault Management

The MIBs contain Facilities for detection of problems in an ELAN that are caused by the failures detected by service components.  Information is provided as follows:

operational status is available for each service component (indicates server is ‘up’ or ‘down’)

error logs are maintained for each service component (see section 5 for details)

2.4	Security Management

Security management is outside the scope of this version of the LAN Emulation Server Management specification.

2.5	Accounting Management

Accounting management is outside the scope of this version of the LAN Emulation Server Management specification.

3.	Management Framework

The network management framework for LAN Emulation Servers is defined using SNMP MIBs.  SNMP is an Internet-standard network management framework of which there are currently more than one versions.  The MIB modules specified in this document are both compliant to the SNMPv2, and semantically identical to the peer SNMPv1 definitions.  This specification does not mandate the use of SNMPv2.  RFC 1452 describes how SNMPv1 and SNMPv2 coexist, and The Simple Times reports that automatic translations can be obtained by mailing SNMPv2 MIBs to mib-v2tov1@dbc.mtview.ca.us.

3.1	The SNMP Network Management Framework

The SNMP Network Management Framework are defined in the RFCs  Since the SNMP is still evolving, this document only lists a few RFCs that are related..  They are:

RFC 1442 [7] which defines the SMI, the mechanisms used for describing and naming objects for the purpose of management

STD 17, RFC 1213 [2] defines MIB-II, the core set of managed objects for the Internet suite of protocols

RFC 1445 [8] which defines the administrative and other architectural aspects of the framework

RFC 1448 [9] which defines the protocol used for network access to managed objects

RFC 1443 [10] which defines the textual conventions used by network management information definitions

The Framework permits new objects to be defined for the purpose of experimentation and evaluation.

3.2	Requirements for LAN Emulation Servers

The LAN Emulation Server and Broadcast and Unknown Server should be network manageable .  eEither via the SNMP network management protocol or via some other network management protocol.  The management of the LAN Emulation Configuration Server is required only for the system that implements it.

3.2.1	Requirements for SNMP

SNMP agents that support LAN Emulation Configuration Servers, LAN Emulation Servers and Broadcast and Unknown Servers MUST implement:

Three MIB modules defined in this specification: ELAN MIB, LES MIB and BUS MIB

3.3	MIB Conventions

The following convention is used in the MIB definitions in this specification:  When a table is defined to allow row creation and deletion or to be read-creatable, the RowStatus object is required in the ‘create’ or ‘destroy’ operation.  This operation is performed on the row indicated by the instance given in the SNMP request.

RowStatus is a textual convention defined in RFC 1443 [10].  It is defined with 6 enumeration:

active

notInService

notReady

createAndGo

createAndWait

destroy

This specification uses RowStatus in every read-creatable table.

4.	MIB-II and other MIB support

All SNMP agents supporting LAN Emulation Servers may implement MIB II, and are also encouraged to implement RFC 1695.  This chapter explains how ELAN MIB, LES MIB and BUS MIB are related to each of these MIB modules.

4.1	MIB II support

LAN Emulation Servers present no interfaces as defined in MIB II.  They are however related to one or more ATM interfaces in many ways though:

LECS can be listening to one or more ATM interfaces with a well-known ATM address as defined in the LANE Specification.

LES can be receiving/sending control or ATM Le-ARP traffic via one or more ATM interfaces.

BUS can be receiving/forwarding traffic on one or more ATM interfaces.

The ATM interface is specified throughout the MIB modules where Virtual Circuits in use by servers are defined.  It is also specified in every server configuration table where the server’s ATM addresses are defined.  The latter is provided to enable network managers to determine which ATM switch the servers derived their ATM addresses from.

4.2	AToMMIB Support

LAN Emulation Servers use Virtual Circuits (Switched or Permanent) to communicate with the Clients.  Full information on the VCCs is found in the AToMMIB.  LAN Emulation Servers MIB provide the indexing for these VCCs so network managers can obtain the attributes of a server VCC from the AToMMIB.

PVCs (Permanent Virtual Circuits) are created by the network manager  in the AToMMIB.  LAN Server MIBs provide writable objects so the network manager can use the PVCs created in the AToMMIB. (i.e. the lesVccTable and busVccTable)..

5.	Emulated LAN MIB Description

5.1	Management model

This specification defines three MIB modules: ELAN MIB, LES MIB and BUS MIB.  The ELAN MIB provides network manager with the means to change the configuration of  ELANs.  The LES and BUS MIBs allow reading back of the current status of the ELANs.  This chapter describes ELAN MIB.

It is important to understand that the ELAN MIB only manages a repository of static information.  To create an ELAN which a client can join will actually require three stages using these MIBs:

create a new ELAN in the ELAN MIB

create a LES for that ELAN using the LES MIB

create a BUS for that ELAN using the BUS MIB

These operations must be performed in these separate MIBs because there is no guarantee that any of the components in question will be collocated.  Indeed while a LES and BUS may be likely to be managed by a single agent, it is highly likely that the user of information in the ELAN MIB (e.g. an LECS) will not be collocated with the LES or BUS.  The LANE specification currently provides no standard method for centralised creation of LE Servers, hence the three operations required to create an ELAN.

The ELAN MIB simply deals with information that will be required to enable a client to join an ELAN.  This information can be divided into two types:  information required to decide which ELAN a client should join and information which a client will need to join the ELAN.

The assignment of clients to ELANs is controlled using ‘policies’.  A policy is a rule based on information available on a client (such as ATM address, ELAN type etc.) linking that client to an ELAN.  These are described in detail later in this chapter.

Typically the information in this MIB would be used by an LECS, the former in deciding which ELAN, if any, a client should be assigned to on the basis of its CONFIG_REQUEST, and the latter in deciding what to put in a CONFIG_RESPONSE.  It is possible for an ELAN to exist without an LECS however, with a client obtaining this information by some other means.  While such means are outside the LANE specification and therefore outside the scope of this document, it was the intention not to preclude such implementations.  This is why the LECS portion of the ELAN MIB is a separate group, allowing the ELAN MIB to exist without requiring an LECS.

Systems which implements the LECS must  implement the LECS group , to allow the LECS to be monitored and controlled.  TLV information also resides in this part of the MIB since this is specific to the LECS configuration mechanism.

While the topology of ELANs can be controlled using the ELAN MIB, by determining which ELANs and LESs clients will use, this MIB does not reflect the current topology.  To determine the current topology of an ELAN (which clients are attached to which LESs and BUSs) the LES MIB [2] and BUS MIB [3] (and the LEC MIB [1] if detailed information on the client is required) must be used.

The design goal is to decouple the configured and actual ELAN topology to achieve maximum flexibility in LEC assignment and also future LNNI (LAN Emulation Server to Server Protocol) support.

5.2	MIB Groups

This section briefly describes each group and object in the ELAN MIB.  For more detail consult the MIB definition and the LANE Emulation specification [1.

5.2.1	ELAN Administration Group

This group provides a registry for the LEC assignment policy types.  There are six LEC assignment policies defined in this group:

byAtmAddr - assign a LEC to an ELAN by it’s ATM address

byMacAddr - assign a LEC to an ELAN by it’s MAC address

byRouteDescriptor - assign a LEC to an ELAN by it’s Route Descriptor

byLanType - assign a LEC to an ELAN by it’s LAN type, i.e. ieee802.3 or ieee802.5

byPktSize - assign a LEC to an ELAN by it’s DataFrameSize

byElanName - assign a LEC to an ELAN by its ELAN name

This table represents the set of assignment policy types which may be supported by the standard implementations of MIBs.  These are based on the information available in a typical CONFIG REQUEST.

Vendors wishing to create new policies should not extend this table, but instead should define similar tables or objects in their own MIBs.  Policy types are defined as OIDs (AutonomousType) to allow vendors to implement their own policies without needing centralised administration of policy types.  This table may be extended in the future revisions of the ELAN MIB.

5.2.2	ELAN Configuration Group

This group provides configuration information for Emulated LANs.  An ELAN is constructed or destroyed in this group for configuration purposes only;  an ELAN can be created and many LECs can be assigned to this ELAN (by policies), but this MIB would not reflect whether or not LECs have actually joined the ELAN.  The network manager has to poll the individual LECs or the LES/BUS to determine the actual ELAN topology.

For example, consider an ELAN ‘red’ in the ELAN Configuration table, where the LEC with the ATM address ‘xxx...redx’ is assigned to the ‘red’ ELAN in the LEC assignment by ATM address table.  In other words, the LEC ‘xxx...redx’ is configured to ELAN ‘red’ in the ELAN MIB.  The LES with the ATM address ‘yyy...redy’ is one of the servers which serves the ELAN ‘red’ as defined in the ELAN MIB’s LES table.

In order to determine whether the LEC ‘xxx...redx’ has actually joined the ELAN ‘red’, or joined the LES ‘yyy...redy’, the network manager must either read the LEC-to-LES information in the LES MIB from the agent of LES ‘yyy...redy’ or talk to the agent of the LEC ‘xxx...redx’ to obtain the LES information from the LEC MIB.  In either case, the network manager can match the information from the LES ‘yyy...redy’ or LEC ‘xxx...redx’ to the LEC assignment table by ATM address or the LES table.

In the case where assignment policies are more broad, (e.g. a policy could assign all clients with LanType ‘iee802.5’ to the ELAN ‘Token-Ring’, or address masks might be used so that all clients with a certain ATM address prefix are directed to a particular ELAN) there will be no complete list of clients in the ELAN MIB.  In this case a network manager would have to use the LES MIB to find a real list of clients.

In conclusion, the ELAN group provides statically configured information and the LES and LEC MIBs provide the dynamic status information for the Emulated LAN.

5.2.2.1	ELAN Configuration Table

elanConfTable lists all Emulated LANs on which this agent maintains information;  the elanConfIndex object, an arbitrary integer used as an index in this table, is used elsewhere in the ELAN MIB to identify a particular ELAN.  Emulated LANs should be created or destroyed from this table in conjunction with operations to create or destroy the related service components as described in section 5.1.  This table can be used by the entity which assigns a LAN Emulation clients to ELANs.  This might be a LAN Emulation Configuration Server (LECS), or in an environment where there is no LECS, the information might be used directly by a system to configure LAN Emulation Clients (LECs).

A network manager can construct the ELAN configuration table as well as the LEC assignment table locally.  And then configures the LEC according to the configuration through the LEC MIB defined in [6].

The table contains the ELAN’s name, LAN type, maximum frame size, and also has a TLV selector to enable it to choose a set of TLV-defined properties (set to zero if the LECS group is not supported).

5.2.2.2	ELAN LES table

This table lists all LES associated with ELANs managed by the agent.  Only the ATM address of the LES is held, and because the LANE specification permits multiple LES addresses per ELAN, there may be more than one LES per ELAN.  All LEC assignment tables are indexed by both the ELAN (elanConfIndex) and LES index (elanLesIndex) to allow the selection of a specific LES address for any client within an ELAN.

5.2.2.3	ELAN Policy Table

Throughout this section, all terms are used and they are: ‘accept’ meaning the policy accepts the client (the client has the matching information of the correct type), ‘rejected’ meaning the policy rejects the client (the client didn’t have the information or the information doesn’t match), and ‘failed’ meaning the client was not assigned to any ELAN as the results of the execution of all the policies.

This table describes policies currently in use for assigning LECs to particular ELANs and LESs.  These policies will be carried out by whatever entity is using this information, typically an LECS but not necessarily.

When a LECS is supported, the LECS assigns a client to an ELAN based on the information given in the CONFIG request.  Information in the CONFIG request is checked against the various policy tables in the ELAN MIB.

There can be multiple policies used in determining the LEC assignment at one time.  These policies are  executed in order of their priorities, with the lowest number getting the highest priority.  (A policy with priority of 1 would be executed first.)  Conflicts between policies may occur but the LECS behavior is implementation dependent.

If there exist multiple policies of the same priority, they are executed at the same time, and all policies must succeed.

Policies are grouped with the elanPolicySelectorIndex.  This allows disjoint policy sets to be created which allows individual LECSs (or other users of this data) to use different policies.

Users of the information in the policy and assignment tables should use the following procedure when attempting to assign clients:

Find the first policy with the highest priority level with the appropriate PolicySelectorIndex.

Check to see if the client matches any assignments for this policy type.  For the standard policies this will involve looking up in an assignment table (e.g. for elanPolicyType of byAtmAddr, the elanLecAtmAddrTable must be consulted).  If the client passes, there will be one or more ELAN/LES index pairs.  If the client fails to find any appropriate ELAN/LES pair with this policy, it has failed, and must restart from the next priority down.  If there are no policies with a lower priority than the current one, then the client is not assigned to any ELAN and has been rejected.

If there are more policies with the same priority level as the one which just passed, these must also be evaluated as described above.

If a client has passed all the policies with a particular priority level, there will have been at least one ELAN/LES pair generated per priority.  If no pair is common to every policy (i.e. the client passed every policy, but the policies failed to agree on any ELAN/LES pair) then the client has failed for this priority level, and behaviour is as if the client had failed against any one of the policies at this priority.  If a single ELAN/LES pair can be identified as common to the results of all the policies, then this is taken as the final result.  If there are multiple matches and the client could be assigned validly to more than one ELAN/LES, any may be chosen, the particular outcome being implementation defined.

An example configuration might consist of  four ELANs: TRed, TBlue, ERed and EBlue.  Clients with an ATM address prefix of rrrrrrrrrrrrrrr would be assigned to the Red ELANs, TRed if they are Token-ring clients and ERed if they are Ethernet clients.  Otherwise they get assigned to TBlue or EBlue again according to LAN type.  This would require three ElanPolicyEntries, at two priority levels.  There would be two entries at priority level one:  a policy of type byAtmAddr and a policy of type byLanType.  There would be one entry at priority level two:  byLanType.  The assignment by ATM address table would contain two entries, both with an ATM address beginning with rrrrrrrrrrrrrrr and an address mask with only the relevant prefix bits set, one pointing to TRed and an appropriate LES index, the other pointing to ERed with an appropriate LES index.  As for the byLanType, the object elanConfLanType in the elanConfTable is used.  If the client’s requesting LAN type is Ethernet, then the first elanConfEntry that has the elanConfLanType set to aflane8023(2) and it also matches the ATM prefix is the ELAN this client is assigned to.

If there is no data available on the client for a policy, then that policy would fail.  The client is rejected by that policy.

The agent should refuse to create any policy it does not support.

5.2.2.4	LEC assignment table by ATM address

This table is indexed by the ELAN index which points to the ELAN this LEC belongs to, the particular LES within that ELAN it will be sent to, and the ATM address plus mask of the LEC.  The ATM mask allows the network manager to specify portions of an ATM address.  A client would be matched by an assignment entry if bits in its address corresponding to non-zero bits in the mask match the address in the table.

5.2.2.5	LEC assignment table by MAC address

This table is indexed by the ELAN index, LES index within the ELAN, and the MAC address (with mask) of the LEC.  The MAC address is compared with the client’s when executing byMacAddress policies.

5.2.2.6	LEC assignment table by Route Descriptor

This table is indexed by the ELAN index, the LES within the ELAN, and the Route Descriptor of the LEC, which consists of a segment id and a bridge number.  The route descriptor is compared with the client’s when executing byRouteDescriptor policies.

5.2.3	LECS Configuration Group

This enables network managers to configure and monitor LECSs.  It also provides configuration information on TLV (type, length and value ) entries to be used in CONFIG responses..

5.2.3.1	LECS Configuration table

This table contains the configuration and status information for all LECS managed by this agent.  This table is used to create, delete or configure a LECS.  Critical objects such as the lecsAtmIfIndex, lecsAtmAddrSpec, and lecsAtmAddrMask cannot be modified unless the lecsAdminStatus is set to down(2).  That is, the network manager has to bring the LECS down to in order to change a LECS’s ATM address or ATM interface value.  These changes can be brought into effect by setting the lecsAdminStatus to up(1).

The object lecsAtmIfIndex provides the number of the ATM interface on which the LECS is listening for CONFIGURE requests.  This value must match an existing value in the ifTable.  This object is set to zero when the ATM interface is not specified or there is more than one ATM interface used by the LECS.

A network manager may instruct the LECS to attempt to register and listen on a particular address.  This is achieved through use of the lecsAtmAddrSpec and lecsAtmAddrMask objects.  The default values for these objects will cause a LECS to use the with a well-known ATM address (reference to LANE 1.0 specification section 5.2.1.2 ).  Clearly if more than one LECS is created on any interface (or on multiple interfaces which would share the domain of the well known address) at least one of them should use some other address.

To enable different LECSs to enact different sets of policies, a policy selector index is set for each LECS.

5.2.3.2	TLV table

This table is used to configure TLVs (Type, Length, and Value) for each ELAN.  The table is indexed by a selector index, the TLV tag and an index. The selector allows multiple TLVs to be grouped together, so different ELANs can use different sets of TLVs. The index allows multiple TLVs with the same tag but different values

Network manager can create TLVs and assign them to an ELAN by specifying corresponding selector indices in both the TLV table and the elanConfTable.

5.2.3.3	VCC table

This table contains the LE CONFIG VCCs from all LECs to the LECS.  This table can be used by the network manager as the central place for tracing VCCs.

5.2.4	LECS Statistics Group

In addition to the LECS fault management group, the LECS statistics group also provides per LECS error counters.

5.3.45.1	LECS statistics table

TThis table lists all counters associated with the LECS this agent maintains.

5.2.5	LECS Fault Management Group

This group provides fault information for LECSs.  The network manager can enable or disable the error logging capability of a LECS.  The enabled LECS will log the error events until the maximum number error log entry is reached.

The logged events are saved in the LECS Error Log table.

5.2.5.4.1	LECS Error Log Control Table

This table is used to control error logging capability on a LECS.  The network manager can enable/disable error logging of a particular LECS managed by the agent.  It can also reset the error log of a LECS.  The LECS must clear all the error log entries upon such a request.

The object lecsErrCtlMaxEntries describes the maximum number of errors a LECS can log.  If this object is one, the LECS can only save the last error event.  It is a read only object.  The object lecsErrCtlLastEntry gives a pointer to the last error log saved by a LECS in the lecsErrLogTable. It can be used by the network manager to read the most recent entry.

5.2.54.2	LECS Error Log Table

This table contains all the error logs maintained by the LECSs managed by the agent.  Each entry describes when the error occurred, the nature of the error and the ATM address of the client whose CONFIG request resulted in the error.

The lecsErrLogIndex ranges from 2 to 32 minus 1 down to 1.  It is assigned consecutively in the descending order.  The network manager can easily retrieve the most recent N entries by using the get-next on the value of this object.  The entries after 1 are discarded.  For example, if the lecsErrCtlMaxEntries is 5, and the LECS has received 2 to 32 minus 1 minus 100 entries so far.  The values of the lecsErrLogIndex for this LECS in the lecsErrLogTable are 100, 99, 98, 97 and 96 with the entry 96 being the most recent error occurred.

6.	LAN Emulation Server MIB Description

This MIB provides LES management information.  The implementation of this MIB is mandatory for agents managing LESs.

6.1	Management model

The LES management model is designed to be compliant with the LAN Emulation 1.0 specification.  It was also intended to facilitate the accommodation of future LAN Emulation Server to server protocol management extensions.

This MIB should may be used to determine the distribution of the LECs among LESs, and to create, configure and monitor LESs.

6.2	MIB Organisation

The MIB is divided into four groups:  the LES Configuration group which provides configuration and topology information;  the LES Statistics Group which provides various counters for each LES;  the LES-LEC Statistics group which provides per LES/LEC pair counters;  the LES Fault management group which logs LES error information.

6.3	MIB Groups

6.3.1	LES Configuration Group

6.3.1.1	LES Configuration table

This table lists all LAN Emulation Servers managed by this agent.

The object lesAtmAddrSpec specifies an ATM  address that, with the ATM address mask, determines a  portion of the ATM address that the LES on the designated ATM interface will use to derive the actual ATM address from the network or ILMI.  The derived ATM address is specified in the object lesAtmAddrActual, which is used to receive ATM ARP requests.

The object lesElanName gives the name of the Emulated LAN this LES is providing service for.  This object may be used to identify the ELAN the LES is in.

The object lesLanType describes the type of the ATM Emulated LAN this LES is providing service to. If the LEC has specified a LAN type in its JOIN request that does not match with the value of this object, the LES will reject the request.  OAt present only 802.3 and 802.5 LAN types are supported.

6.3.1.2	LES VCC Table

This table lists all the Control Distribute VCCs used by the LES to distribute control traffic to the participating LECs.  The Control Distribute VCC can either be point-to-point or point-to-multipoint calls.  This table is read only if SVCs are used and writable if PVCs are used.

Each entry indicates the ATM interface number, VPI value and VCI value, which comprise the index to the atmVclTable in the AToMMIB.

6.3.1.3	LES ARP table by MAC address

This table provides access to an ATM LAN Emulation Server’s MAC-to-ATM address table..  It contains entries for unicast addresses and , the broadcast address and multicast addresses.

An entry for the broadcast MAC address will have the ATM address of a BUS.  When the entry is for a unicast or multicast MAC address the corresponding ATM address will be for a LEC.

6.3.1.4	LES ARP table by Route Descriptor

This table provides access to an ATM LAN Emulation Server’s RouteDescriptor-to-ATM ARP cache.  The entries in this table are set-up by the agent or network manager depending on the entry type.

The Route Descriptors are presented as Segment Id (ring number) and Bridge number.

6.3.1.5	LES-LEC topology table

This table lists all LAN Emulation clients serviced by LESs specified in the lesConfTable.  This table can be used to retrieve the topology of an ELAN, i.e. the LES to LECs mapping information.

An entry in this table is created by the agent when a LEC registers successfully with the LES. The lesLecCtlDirectVpi and lesLecCtlDirectVci objects can be modified by the network manager if PVC is used.

6.3.2	LES Statistics Group

This table contains all counters the LESs maintain.  This table augments the lesConfTable.  It provides performance and fault counters on a per LES basis.

The table lists all error types listed in the Table 13 in “ATM Forum LAN Emulation Over ATM Specification, V1.0”.

6.3.3	LES-LEC Statistics Group

This table contains all LE-ARP request related counters and error counts on a per LEC-LES pair basis.

6.3.4	LES Fault Management Group

This group provides fault management information for managing a LES.  The network manager can enable/disable the error logging capability of a LES.  The enabled LES will log the error event until the maximum number error log entry is reached.

The logged events are saved in the LES Error Log table.

6.3.4.1	LES Error Log Control Table

This table is used to control the error logging capability of a LES.  The network manager may  enable or disable error logging on a particular LES managed by the agent.  It can also reset the error log of a LES.

The object lesErrCtlMaxEntries describes the maximum number of errors a LES can log.  If this object is one, the LES will only save the last error event.  The object lesErrCtlLastEntry gives a pointer to the last error log saved by  a LES in the lesErrLogTable.

6.3.4.2	LEC Error Log Table

This table contains all the error logs maintained by the LESs managed by the same agent.  Each entry describes the error occurred, the nature of the error and the ATM address of  the client whose JOIN REQUEST  request that resulted in the error.

The lesErrLogIndex ranges from 2 to 32 minus 1 to 1.  It is assigned consecutively in the descending order.  The network manager can easily retrieve the most recent N entries by using the get-next on the value of this object.  The entries after 1 are discarded.  For example, if the lesErrCtlMaxEntries is 5, and the LES has received 100 entries so far.  The values of the lesErrLogIndex for this LES in the lesErrLogTable are 100, 99, 98, 97 and 96 with the entry 100 being the most recent error occurred.

7.	Broadcast and Unknown Server MIB description

7.1	Management model

This MIB enables network managers to create, destroy, configure and determine the current status of BUSs and topology of the portions of ELANs being served by BUSs.

7.2	MIB Organisation

The MIB is devided into two groups: BUS Configuration group which provides BUS topology information.  And BUS Fault Management group which provides BUS statistics and BUS-LEC statistics.

7.3	MIB Groups

7.3.1	BUS Configuration Group

This group includes the object busNextId, BUS Configuration table, BUS VCC table and BUS-LEC topology table.

The object busNextId provides the network manager the next available index used to create a BUS.

7.3.1.1	BUS Configuration Table

This table lists all LAN Emulation Broadcast and Unknown Servers (BUS) this agent manages.  The BUS handles data sent by an LE Client to the broadcast MAC address, all multicast traffic, and initial unicast frames which are sent by a LEC before the appropriate data direct target ATM address has been resolved.  There can be multiple BUSs per ELAN, but a BUS can service only one ELAN.

7.3.1.2	BUS VCC Table

This table lists all the Multicast Forward VCCs used by the BUS to forward multicast traffic to the participating LECs. Multicast Forward VCCs can either be point-to-point or point-to-multipoint.  This table is read only if SVCs are used and writable if PVCs are used.

7.3.1.3	BUS-LEC Topology Table

This table lists the actual LECs being serviced by the BUS.  It can be used to determine the mapping between BUSs and LECs.

This table provides information for Multicast send VCCs between BUS and LE clients.  Objects busLecMcastSendAtmIfIndex, busLecMcastSendVpi and busLecMcstSendVci can only be modified if PVC is used.

7.3.2	BUS Statistics Group

7.3.2.1	BUS Statistics Table

This table contains all counters maintained by BUSs.  This table augments the busConfTable.

7.3.2.2	BUS-LEC Statistics Table

This table contains all LEC counters the BUS maintains.

7.4.2	BUS Fault Management Group

This group provides fault management information for managing a BUS.  The network manager can enable/disable the error logging capability of a BUS.  The enabled BUS will log the error event until the maximum number error log entry is reached.

The logged events are saved in the BUS Error Log table.

7.4.2.1	BUS Error Log Control Table

This table is used to control the error logging capability of a BUS.  The network manager may  enable or disable error logging on a particular BUS managed by the agent.  It can also reset the error log of a BUS.

The object busErrCtlMaxEntries describes the maximum number of errors a BUS can log.  If this object is one, the BUS will only save the last error event.  The object busErrCtlLastEntry gives a pointer to the last error log saved by  a BUS in the busErrLogTable.

7.4.2.2	LEC Error Log Table

This table contains all the error logs maintained by the BUSs managed by the same agent.  Each entry describes the error occurred, the nature of the error and the ATM address of  the client whose frame cause the error.

The busErrLogIndex ranges from 2 to 32 minus 1 to 1.  It is assigned consecutively in the descending order.  The network manager can easily retrieve the most recent N entries by using the get-next on the value of this object.  The entries after 1 are discarded.  For example, if the busErrCtlMaxEntries is 5, and the BUS has received 100 entries so far.  The values of the busErrLogIndex for this BUS in the busErrLogTable are 100, 99, 98, 97 and 96 with the entry 100 being the most recent error occurred.

7.4	Limitations

8.	LAN Emulation Servers MIB Definitions

8. LAN Emulation Servers MIB Definitions

--

--      MIB for managing configuration data for ATM Emulated LANs

--

LAN-EMULATION-ELAN-ELAN-MIB DEFINITIONS ::= BEGIN

IMPORTS

MODULE-IDENTITY, OBJECT-TYPE,

Counter32, Integer32                   FROM SNMPv2-SMI

TEXTUAL-CONVENTION, DisplayString,

RowStatus, MacAddress,

AutonomousType, TimeStamp              FROM SNMPv2-TC

MODULE-COMPLIANCE, OBJECT-GROUP        FROM SNMPv2-CONF

LecDataFrameSize, LecDataFrameFormat,

AtmLaneAddress, atmfLanEmulation,

VpiInteger, VciInteger                 FROM LAN-EMULATION-CLIENT-MIB;

elanMIB MODULE-IDENTITY

LAST-UPDATED "95090712009602121200Z"

ORGANIZATION "ATM Forum LAN Emulation Sub-Working Group"

CONTACT-INFO

"

The ATM Forum

303 Vintage Park Drive

Foster City, CA  94404

United States of America

2570 West El Camino Real,

Ste 304,

Mountain View, CA 94040-1313

Tel: 415-578-6860949-6711

E-mail: info@atmforum.com"

DESCRIPTION

"This is the MIB module for managing ATM

Emulated LANs as well as LAN Emulation

Configuration Server (LECS).  It provides

mechanism for constructing and destroying

ELANs, for distributing members of an

ELAN and for figuring out the topology

of an ELAN.  It also provides management

information for LECS."

::= { atmfLanEmulationatmfLanEmulation 22 }

--

--    Textual Conventions

--

IfIndexOrZero  ::= TEXTUAL-CONVENTION

STATUS     current

DESCRIPTION

"An integer defined as to equivalent

to ifIndex in the ifTable defined

in RFC 1213 and the value zero."

SYNTAX     INTEGER (0..65535)

ElanLocalIndex ::= TEXTUAL-CONVENTION

STATUS     current

DESCRIPTION

"A value which uniquely identifies a

conceptual row in the elanConfTable.

This number is only used locally by the agent to

distinguish between ELANs."

SYNTAX     Integer32

AtmLaneMask ::= TEXTUAL-CONVENTION

STATUS	     current

DESCRIPTION

"A twenty-octet binary string, containing a standard

ATM Forum address mask."

SYNTAX	     OCTET STRING (SIZE(20))

TlvSelectorIndexType ::= TEXTUAL-CONVENTION

STATUS     current

DESCRIPTION

"An arbitrary integer used in identifying

a set of TLV encoding.  This number

is locally managed by the agent."

SYNTAX     Integer32

PolicySelectorIndexType ::= TEXTUAL-CONVENTION

STATUS     current

DESCRIPTION

"An arbitrary integer used in identifying

a set of LEC assignment policies.

This number is locally managed by the

agent."

SYNTAX     Integer32

LecsErrLogIndexType ::= TEXTUAL-CONVENTION

STATUS     current

DESCRIPTION

"An arbitrary integer used in identifying

an error log associated with a LECS."

SYNTAX     Integer32(1..2147483647)

-- This MIB module consists of the following groups:

--

--  (1) ELAN Administration Group

--      (a) ELAN Admin Policy Table

--

--  (2) ELAN Configuration Group

--      (a) Elan Conf table

--      (b) LES table

--      (c) ELAN policy table

--      (d) LEC assignment table by ATM address

--      (e) LEC assignment table by MAC address

--      (f) LEC assignment table by Route Descriptor

--

--  (3) LECS Group

--     (3.1) LECS Configuration Group

--      (a) LECS configuration table

--      (b) LECS to ELAN mapping table

--      (c) TLV (Type, Length and Value) table

--     (3.2) LECS Fault Management Group

--      (c) LECS log control table

--      (d) LECS log table

--     (3.3) LECS Statistics Group

--      (c) LECS Statistics table

--

--

elanAdminGroup OBJECT IDENTIFIER ::= { elanMIB 1 }

elanConfGroup  OBJECT IDENTIFIER ::= { elanMIB 2 }

elanLecsGroup  OBJECT IDENTIFIER ::= { elanMIB 3 }

elanLecsConfGroup OBJECT IDENTIFIER

::= { elanLecsGroup 1 }

elanLecsFaultGroup OBJECT IDENTIFIER

::= { elanLecsGroup 2 }

elanLecsStatGroup OBJECT IDENTIFIER

::= { elanLecsGroup 3 }

--

--  (1) ELAN Administration Group

--      (a) ELAN Admin Policy Registry

--          Registration for LEC assignment policy

--          types The following are defined for posssible

--          values of the elanPolicytype object

--

elanAdminPolicyVal  OBJECT IDENTIFIER ::= { elanAdminGroup 1 }

-- assign LEC to an ELAN by it's ATM address & Mask

byAtmAddr OBJECT IDENTIFIER ::= { elanAdminPolicyVal 1 }

-- assign LEC to an ELAN by it's MAC address

byMacAddr OBJECT IDENTIFIER ::= { elanAdminPolicyVal 2 }

-- assign LEC to an ELAN by it's Route Descriptor

byRouteDescriptor OBJECT IDENTIFIER ::= { elanAdminPolicyVal 3 }

-- assign LEC to an ELAN by it's LAN type

byLanType  OBJECT IDENTIFIER ::= { elanAdminPolicyVal 4 }

-- assign LEC to an ELAN by it's Packet size

byPktSize  OBJECT IDENTIFIER ::= { elanAdminPolicyVal 5 }

-- assign LEC to an ELAN by it’s ELAN name

byElanName OBJECT IDENTIFIER ::= { elanAdminPolicyVal 6 }

-- other user defined values should go here start from 6

--

--  (2) ELAN Configuration Group

--

--      (a) ELAN Conf table

--

elanConfNextId  OBJECT-TYPE

SYNTAX    ElanLocalIndex

MAX-ACCESS read-only

STATUS    current

DESCRIPTION

"The next available ELAN index provided

by the agent.  The value of this object

can be used as the index to the

elanConfTable during creation."

::= { elanConfGroup 1 }

elanConfTable   OBJECT-TYPE

SYNTAX      SEQUENCE OF ElanConfEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

"This table contains all Emulated LANs

(ELANs) this agent manages.  An ELAN

is defined by the ELAN name, a set of

TLVs, and other parameters.  After an

ELAN is created, members of the ELAN

such as the LAN Emulation Server (LES)

or Client (LEC) can be added to this

ELAN entry in their repective tables.

There are four memebers to an ELAN and

they are LECS, LES, BUS (Broadcast and

Unknown Server ) and LEC.  The support

of LECS is optional.  The addition and

deletion of LECS is done in the

elanLecsConfGroup defined in this MIB.

The addition and deletion of the LEC

are done in the LEC Assignment tables

defined in this ELAN Configuration group.

The addition and deletion of the LES

are also defined in this group.  The

addition and deletion of the BUS are

done in the LES MIB due to the fact that

LEC learns the BUS address only from

the LES it corresponds to."

::= { elanConfGroup 2 }

elanConfEntry    OBJECT-TYPE

SYNTAX       ElanConfEntry

MAX-ACCESS   not-accessible

STATUS       current

DESCRIPTION

"Each entry in this table represents an

Emulated LAN.  Objects elanConfIndex

and elanConfRowStatus are required

during row creation and deletion. "

INDEX { elanConfIndex }

::= { elanConfTable 1 }

ElanConfEntry ::=

SEQUENCE {

elanConfIndex

ElanLocalIndex,

elanConfName

DisplayString,

elanConfTlvIndex

TlvSelectorIndexType,

elanConfLanType

LecDataFrameFormat,

elanConfMaxFrameSize

LecDataFrameSize,

elanConfRowStatus

RowStatus

}

elanConfIndex     OBJECT-TYPE

SYNTAX        ElanLocalIndex

MAX-ACCESS    not-accessible

STATUS        current

DESCRIPTION

"A value which uniquely identifies a

conceptual row in the elanConfTable.

If the conceptual row identified by this value

of elanConfIndex is recreated following an agent

restart, the same value of elanConfIndex must be

used to identify the recreated row."

::= { elanConfEntry 1 }

elanConfName      OBJECT-TYPE

SYNTAX         DisplayString(SIZE(0..32))

MAX-ACCESS     read-create

STATUS         current

DESCRIPTION

"The name of this Emulated LAN entry.

When this object length is zero then the

ELAN name is not specified.  The clients

assigned to this ELAN will also have

a zero length string as the ELAN name.

The value of this object is used in the

LE CONFIGURE response by the LECS if supported.

Note that ELAN name may be used as cross

reference to the LES MIB and BUS MIB

though not required.  Multiple ELANs

with no ELAN name specified will cause

conflicts in reference to LES and BUS MIBs."

REFERENCE

"LAN Emulation Over ATM Specification -

version 1.0. C5."

DEFVAL { "" }

::= { elanConfEntry 2 }

elanConfTlvIndex   OBJECT-TYPE

SYNTAX          TlvSelectorIndexType

MAX-ACCESS      read-create

STATUS          current

DESCRIPTION

"The value of this object identifies

one or more rows in the lecsTlvTable which

applies to this ELAN.  This object is

set to zero if 1) LECS is not supported.

or 2) there is no TLV associated with

this entry.  If the LEC assignment policy

type is by TLVs, then the LECS matches

the TLVs in the CONFIGURE request with

TLVs assigned to each ELAN, and assign

the requestor to the matching ELAN.

If the LECS receives a CONFIGURE request

with no TLV, the LECS may try to match

it to the entry in this table with a

zero value elanConfTlvIndex.  In the case

there is more than one entry in this table

with zero value elanConfTlvIndex, the

behavior of the LECS is not specified."

::= { elanConfEntry 3 }

elanConfLanType     OBJECT-TYPE

SYNTAX          LecDataFrameFormat

MAX-ACCESS      read-create

STATUS          current

DESCRIPTION

"The LAN type of this ELAN entry. This

object is required to be either 802.3 or

802.5.  If the LEC assignment policy is

by LAN type.  That is, if the LECS is

assigning the LEC to ELAN according to

its LAN type, this object is used to

indicate the LAN type of the ELAN."

REFERENCE

"LAN Emulation Over ATM Specification -

version 1.0. S2."

DEFVAL { unspecified }

::= { elanConfEntry 4 }

elanConfMaxFrameSize   OBJECT-TYPE

SYNTAX             LecDataFrameSize

MAX-ACCESS         read-create

STATUS             current

DESCRIPTION

"The maximum data frame size of this

ELAN entry.  The maximum AAL-5 SDU size

of a data frame that this ELAN can support.

The value of this object is returned to the

LEC in the LE CONFIGURE response."

REFERENCE

"LAN Emulation Over ATM Specification -

version 1.0. S3."

DEFVAL { unspecified }

::= { elanConfEntry 5 }

elanConfRowStatus       OBJECT-TYPE

SYNTAX              RowStatus

MAX-ACCESS          read-create

STATUS              current

DESCRIPTION

"This object is used to create or

delete entries in the elanConfTable."

REFERENCE "RFC 1443, [10] Textual Conventions

for version 2 of the Simple Network Management

Protocol (SNMPv2)."

::= { elanConfEntry 6 }

--

--      (b) LES table

--

elanLesTable      OBJECT-TYPE

SYNTAX      SEQUENCE OF ElanLesEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

"This table contains all LESs for each

ELAN specified in the elanConfTable.

Each ELAN can have more than

one LES providing LAN Emulation

services.  Each LES can service only

one ELAN.  The table is indexed by the

elanConfIndex which points to the ELAN

this LES is providing service to, and

elanLesIndex which unquely identifies

a LES.  This table is used for configuration

of an ELAN only, that is, creating a

LES in this table does not instantiate

a LES in the network.  It is done in

the LES MIB."

::= { elanConfGroup 3 }

elanLesEntry    OBJECT-TYPE

SYNTAX      ElanLesEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

"Each entry in this table represents

a LES/Emulated LAN pair.  Object

elanLesAtmAddress besides elanLesRowStatus

is also required during row creation."

INDEX { elanConfIndex, elanLesIndex }

::= { elanLesTable 1 }

ElanLesEntry ::=

SEQUENCE {

elanLesIndex

Integer32,

elanLesAtmAddress

AtmLaneAddress,

elanLesRowStatus

RowStatus

}

elanLesIndex       OBJECT-TYPE

SYNTAX         Integer32

MAX-ACCESS     not-accessible

STATUS         current

DESCRIPTION

"An arbitrary number which uniquely

identifies the LES this entry pertains

to."

::= { elanLesEntry 1 }

elanLesAtmAddress  OBJECT-TYPE

SYNTAX         AtmLaneAddress

MAX-ACCESS     read-create

STATUS         current

DESCRIPTION

"The ATM address of the LES entry.

If LECS is supported, the value of

this object is the LES ATM address

LECS returns to the LEC in the

CONFIGURE response.  If LECS

is not supported, the value of this

object pertains to the LES ATM address

network manager provides to the

LEC.  The LEC assigned to this ELAN

uses this ATM address as the called

party address in the JOIN request.

The calling party address used by

LES in the JOIN response is not

specified by this MIB."

DEFVAL { "" }

::= { elanLesEntry 2 }

elanLesRowStatus   OBJECT-TYPE

SYNTAX         RowStatus

MAX-ACCESS     read-create

STATUS         current

DESCRIPTION

"This object is used to create or

delete entries in the elanLesfTable."

REFERENCE "RFC 1443, [10] Textual Conventions

for version 2 of the Simple Network Management

Protocol (SNMPv2)."

::= { elanLesEntry 3 }

--

--      (c) ELAN policy table

--

elanPolicyTable   OBJECT-TYPE

SYNTAX      SEQUENCE OF ElanPolicyEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

"This table contains all policies this

agent supports for assigning a LEC to

an ELAN.

A set of policies with the same or

different priorities can be selected

by the entity which provides ELAN

configuration service such

as the LECS.  The policy with the

highest priority or with the smallest

elanPolicyPriority , is evaluated

first.  The policies with the same

elanPolicyPriority are evaluated

at the same time with the AND operation.

When LECS receives a configure

request, it checks it's policies selected

from this table to determine which

ELAN and LES the LEC will join.

This table is indexed by a selector

index and a policy index.  The policy

index unquely identifies a policy and

the selector index allows multiple

policies be selected by one LECS or

an entity that is providing ELAN

configuration service."

::= { elanConfGroup 4 }

elanPolicyEntry    OBJECT-TYPE

SYNTAX         ElanPolicyEntry

MAX-ACCESS     not-accessible

STATUS         current

DESCRIPTION

"Each entry in this table represents a

policy supported by the entity which

provides ELAN configuration

services.  Each policy can be used to

evaluate the CONFIGURE request from

the LEC in determining which ELAN it

belongs to. "

INDEX { elanPolicySelectorIndex, elanPolicyIndex }

::= { elanPolicyTable 1 }

ElanPolicyEntry ::=

SEQUENCE {

elanPolicySelectorIndex

PolicySelectorIndexType,

elanPolicyIndex

Integer32,

elanPolicyPriority

Integer32,

elanPolicyType

AutonomousType,

elanPolicyRowStatus

RowStatus

}

elanPolicySelectorIndex      OBJECT-TYPE

SYNTAX        PolicySelectorIndexType

MAX-ACCESS    not-accessible

STATUS        current

DESCRIPTION

"The value of this object indicates

a group of policies that can be selected

by the ELAN configuration service

provider such as the LECS."

::= { elanPolicyEntry 1 }

elanPolicyIndex     OBJECT-TYPE

SYNTAX   Integer32 (1..65000)

MAX-ACCESS      not-accessible

STATUS          current

DESCRIPTION

"The value of this object uniquely

identifies a single policy entry in

this table. "

::= { elanPolicyEntry 2 }

elanPolicyPriority  OBJECT-TYPE

SYNTAX          Integer32 (1..65000)

MAX-ACCESS      read-create

STATUS          current

DESCRIPTION

"The priority of this policy entry.

Policies are evaluated by the

entity which provides ELAN configuration

service (LECS) by their

priorities.  Policies with the

same priority values should be

evludated at the same time with

an AND operation.  That is, if

one of the policy with the same

priority is not met,

the evluation should fail.

The value 1 has the highest priority. "                                                             ::= { elanPolicyEntry 3 }

elanPolicyType     OBJECT-TYPE

SYNTAX         AutonomousType

MAX-ACCESS      read-create

STATUS          current

DESCRIPTION

"The type of this policy.

The value of this object is

an object identifier points

to a leaf in the elanAdminGroup

The value of this object has

to exist in the tree before

being modified or created.

A vender can use a vender

specific policy added to the

elanAdminPolicyVal or a

separate vender tree.  must

reference a definition of a type

of policy.  Some of such definition

exist within the elanAdminPolicyVal

subtree.  Others may be defined

within enterprise specific subtrees.

The

agent is not required to

support every types specified

in the elanAdminGroup under defined

within the

elanAdminPolicyVal subtree.."

::= { elanPolicyEntry 4 }

elanPolicyRowStatus OBJECT-TYPE

SYNTAX          RowStatus

MAX-ACCESS      read-create

STATUS          current

DESCRIPTION

"This object is used to create or

delete entries in the elanPolicyTable."

REFERENCE "RFC 1443, [10] Textual Conventions

for version 2 of the Simple Network Management

Protocol (SNMPv2)."

::= { elanPolicyEntry 5 }

--

--      (d) LEC assignment table by ATM address

--

elanLecAtmAddrTable  OBJECT-TYPE

SYNTAX      SEQUENCE OF ElanLecAtmAddrEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

"This table is used to assign a LEC

to an ELAN by ATM address.

When the by ATM address policy is

used, this table is used to specify

the LEC's ATM address or portion of an ATM

address.  The ATM address is used by

the LECS or other entity which serves

the LANE configuration function to

determine the ELAN membership.

This table is indexed

by the elanConfIndex which points

to the ELAN this LEC belongs, the

elanLesIndex which points to the

LES this LEC should join, the

LEC's ATM address and an ATM address

mask.  Portions of ATM address

can be used in dertermining ELAN

membership by using both the ATM

address and the mask."

::= { elanConfGroup 5 }

elanLecAtmAddrEntry   OBJECT-TYPE

SYNTAX         ElanLecAtmAddrEntry

MAX-ACCESS     not-accessible

STATUS         current

DESCRIPTION

"Each entry represents a LEC to ELAN

binding."

INDEX { elanConfIndex, elanLesIndex,

elanLecAtmAddress , elanLecAtmMask }

::= { elanLecAtmAddrTable 1 }

ElanLecAtmAddrEntry ::=

SEQUENCE {

elanLecAtmAddress

AtmLaneAddress,

elanLecAtmMask

AtmLaneAddress,

elanLecAtmRowStatus

RowStatus

}

elanLecAtmAddress     OBJECT-TYPE

SYNTAX            AtmLaneAddress

MAX-ACCESS        not-accessible

STATUS            current

DESCRIPTION

"The value of this object is the

ATM address of a LAN Emulation

client.  This object and the

object elanLecAtmMask are used

to form an ATM address or portion

of an ATM address to be used

by the LECS in determining the

ELAN membership when the policy

of this LECS is by ATM address."

::= { elanLecAtmAddrEntry 1 }

elanLecAtmMask        OBJECT-TYPE

SYNTAX            AtmLaneAddress

MAX-ACCESS        not-accessible

STATUS            current

DESCRIPTION

"The ATM address mask associated with

the object elanLecAtmAddress.  The value

of the mask is an ATM address with

the don't care portion set to zero

and the valid ATM address portion set to one."

::= { elanLecAtmAddrEntry 2 }

elanLecAtmRowStatus   OBJECT-TYPE

SYNTAX            RowStatus

MAX-ACCESS        read-create

STATUS            current

DESCRIPTION

"This object is used to create or

destroy entries in this table."

REFERENCE "RFC 1443, [10] Textual Conventions

for version 2 of the Simple Network Management

Protocol (SNMPv2)."

::= { elanLecAtmAddrEntry 4 }

--

--      (e) LEC assignment table by MAC address

--

elanLecMacAddrTable  OBJECT-TYPE

SYNTAX      SEQUENCE OF ElanLecMacAddrEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

"This table is used to assign a LEC

to an ELAN by MAC address.

When the byMacAddress policy is

used, this table is used to specify

the LEC's ELAN membership by ATM

address.  This table is indexed

by the elanConfIndex which points

to the ELAN this LEC belongs, the

elanLesIndex which points to the

LES this LEC should join, and the

LEC's MAC address."

::= { elanConfGroup 6 }

elanLecMacAddrEntry   OBJECT-TYPE

SYNTAX         ElanLecMacAddrEntry

MAX-ACCESS     not-accessible

STATUS         current

DESCRIPTION

"Each entry represents a LEC to ELAN

binding."

INDEX { elanConfIndex, elanLesIndex,

elanLecMacAddress  }

::= { elanLecMacAddrTable 1 }

ElanLecMacAddrEntry ::=

SEQUENCE {

elanLecMacAddress

MacAddress,

elanLecMacRowStatus

RowStatus

}

elanLecMacAddress     OBJECT-TYPE

SYNTAX            MacAddress

MAX-ACCESS        not-accessible

STATUS            current

DESCRIPTION

"The value of this object is the

MAC address of a LAN Emulation

client.  When a CONFIGURE request

is received with this MAC address,

it will be assigned to the ELAN

which elanConfIndex is pointing

to."

::= { elanLecMacAddrEntry 1 }

elanLecMacRowStatus   OBJECT-TYPE

SYNTAX            RowStatus

MAX-ACCESS        read-create

STATUS            current

DESCRIPTION

"This object is used to create or

destroy entries in this table."

REFERENCE "RFC 1443, [10] Textual Conventions

for version 2 of the Simple Network Management

Protocol (SNMPv2)."

::= { elanLecMacAddrEntry 2 }

--

--      (f) LEC assignment table by Route Descriptor

--

elanLecRdTable  OBJECT-TYPE

SYNTAX      SEQUENCE OF ElanLecRdEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

"This table is used to assign a LEC

to an ELAN by Route Descriptor.

When the by Route Descriptor policy is

used, this table is used to specify

the LEC's ELAN membership by Route

Descriptor.  This table is indexed

by the elanConfIndex which points

to the ELAN this LEC belongs, the

elanLesIndex which points to the

LES this LEC should join, and the

LEC's Route Descriptors."

::= { elanConfGroup 7 }

elanLecRdEntry   OBJECT-TYPE

SYNTAX         ElanLecRdEntry

MAX-ACCESS     not-accessible

STATUS         current

DESCRIPTION

"Each entry represents a LEC to ELAN

binding. "

INDEX { elanConfIndex, elanLesIndex,

elanLecRdSegId, elanLecRdBridgeNum }

::= { elanLecRdTable 1 }

ElanLecRdEntry ::=

SEQUENCE {

elanLecRdSegId

Integer32,

elanLecRdBridgeNum

Integer32,

elanLecRdRowStatus

RowStatus

}

elanLecRdSegId     OBJECT-TYPE

SYNTAX            Integer32 (0..4095)

MAX-ACCESS        not-accessible

STATUS            current

DESCRIPTION

"The LAN ID portion of the IEEE 802.5

route descriptor associated with this

conceptual row."

::= { elanLecRdEntry 1 }

elanLecRdBridgeNum    OBJECT-TYPE

SYNTAX            Integer32 (0..15)

MAX-ACCESS        not-accessible

STATUS            current

DESCRIPTION

"The Bridge Number portion of the

IEEE 802.5 route descriptor associated

with this conceptual row."

::= { elanLecRdEntry 2 }

elanLecRdRowStatus   OBJECT-TYPE

SYNTAX            RowStatus

MAX-ACCESS        read-create

STATUS            current

DESCRIPTION

"This object is used to create or

destroy entries in this table."

REFERENCE "RFC 1443, [10] Textual Conventions

for version 2 of the Simple Network Management

Protocol (SNMPv2)."

::= { elanLecRdEntry 4 }

--

--      (g) LEC assignment table by Packet Size

--

elanLecPktSizeTable  OBJECT-TYPE

SYNTAX      SEQUENCE OF ElanLecPktSizeEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

"This table is used to assign a LEC

to an ELAN by Packet Size. When the by Packet Size policy is used, this table is used to specifythe LEC's ELAN membership by Packet Size.  This table is indexed by the elanConfIndex which points to the ELAN this LEC belongs, the elanLesIndex which points to the

LES this LEC should join, and the

LEC's Packet Size."

::= { elanConfGroup 8 }

elanLecPktSizeEntry   OBJECT-TYPE

SYNTAX         ElanLecPktSizeEntry

MAX-ACCESS     not-accessible

STATUS         current

DESCRIPTION

"Each entry represents a LEC to ELAN

binding. "

INDEX { elanConfIndex, elanLesIndex,

elanLecFrameSize }

::= { elanLecPktSizeTable 1 }

ElanLecPktSizeEntry ::=

SEQUENCE {

elanLecFrameSize

LecDataFrameSize,

elanLecPktSizeRowStatus

RowStatus

}

elanLecFrameSize     OBJECT-TYPE

SYNTAX            LecDataFrameSize

MAX-ACCESS        not-accessible

STATUS            current

DESCRIPTION

"The maximum AAL-5 SDU size this LEC can support. "

::= { elanLecPktSizeEntry 1 }

elanLecPktSizeRowStatus   OBJECT-TYPE

SYNTAX            RowStatus

MAX-ACCESS        read-create

STATUS            current

DESCRIPTION

"This object is used to create or

destroy entries in this table."

REFERENCE "RFC 1443, [10] Textual Conventions

for version 2 of the Simple Network Management

Protocol (SNMPv2)."

::= { elanLecPktSizeEntry 2 }

--

--      (e) LEC assignment table by ELAN name

--

elanLecNameTable  OBJECT-TYPE

SYNTAX      SEQUENCE OF ElanLecNameEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

"This table is used to assign a LEC

to an ELAN by ELAN name. When the by ELAN name policy is used, this table is used to specifythe LEC's ELAN membership by ELAN name.  This table is indexed by the elanConfIndex which points to the ELAN this LEC belongs, the elanLesIndex which points to the

LES this LEC should join, and the

LEC's ELAN name."

::= { elanConfGroup 9 }

elanLecNameEntry   OBJECT-TYPE

SYNTAX         ElanLecNameEntry

MAX-ACCESS     not-accessible

STATUS         current

DESCRIPTION

"Each entry represents a LEC to ELAN

binding. "

INDEX { elanConfIndex, elanLesIndex,

elanLecElanName }

::= { elanLecNameTable 1 }

ElanLecNameEntry ::=

SEQUENCE {

elanLecElanName

DisplayString,

elanLecNameRowStatus

RowStatus

}

elanLecElanName     OBJECT-TYPE

SYNTAX            DisplayString(SIZE(0..32))

MAX-ACCESS        not-accessible

STATUS            current

DESCRIPTION

"The name of the ELAN this LEC belongs. "

::= { elanLecNameEntry 1 }

elanLecNameRowStatus   OBJECT-TYPE

SYNTAX            RowStatus

MAX-ACCESS        read-create

STATUS            current

DESCRIPTION

"This object is used to create or

destroy entries in this table."

REFERENCE "RFC 1443, [10] Textual Conventions

for version 2 of the Simple Network Management

Protocol (SNMPv2)."

::= { elanLecNameEntry 2 }

--

--  (2) LECS Group - Optional

--     (2.1) LECS Configuration Group

--           (a) LECS Configuration table

--           (b) LECS to ELAN mapping table

--           (c) LECS TLV table

--           (d) LECS VCC table

--     (2.3) LECS Statistics Group

--           (a) LECS Statistics table

--     (2.2) LECS Fault Management Group

--           (a) LECS Fault Control table

--           (b) LECS Error Log table

lecsConfNextId  OBJECT-TYPE

SYNTAX    ElanLocalIndex

MAX-ACCESS read-only

STATUS    current

DESCRIPTION

"The next available LECS index.  The

value of this object can be used as

the index to the lecsTable during

creation."

::= { elanLecsConfGroup 1 }

lecsConfTable OBJECT-TYPE

SYNTAX     SEQUENCE OF LecsConfEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"This table contains the configuration

information of all LECS this agent

manages.  This table can also be

used to create, delete or configure

a LECS."

::= { elanLecsConfGroup 2 }

lecsConfEntry OBJECT-TYPE

SYNTAX     LecsConfEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"Each entry represents a LECS this

agent maintains.

Objects lecsAtmIfIndex, lecsAtmAddrSpec,

and lecsAtmAddrMask cannot be modified

unless the lecsAdminStatus is set to

down(2).  And the change does not take

effect until the lecsAdminStatus is set

to up(1)."

INDEX { lecsConfIndex }

::= { lecsConfTable 1 }

LecsConfEntry ::= SEQUENCE {

lecsConfIndex           Integer32,

lecsAtmIfIndex          IfIndexOrZero,

lecsAtmAddrSpec         AtmLaneAddress,

lecsAtmAddrMask         AtmLaneMask,

lecsAtmAddrActual       AtmLaneAddress,

lecsPolicySelIndex      PolicySelectorIndexType,

lecsLastInitialized     TimeStamp,

lecsOperStatus          INTEGER,

lecsAdminStatus         INTEGER,

lecsRowStatus           RowStatus

}

lecsConfIndex OBJECT-TYPE

SYNTAX     Integer32

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"An arbitrary integer which represents

a LECS this agent manages.

If the conceptual row identified by this value

of lecsConfIndex is recreated following an agent

restart, the same value of elanConfIndex must be

used to identify the recreated row."

::= { lecsConfEntry 1 }

lecsAtmIfIndex OBJECT-TYPE

SYNTAX     IfIndexOrZero

MAX-ACCESS read-create

STATUS     current

DESCRIPTION

"An ATM interface which the LECS receives

CONFIGURE requests

from.  This value must match an existing

value  in the   ifTable.  This object

is set to zero when the ATM interface

is not specified or there is more than

one ATM interface used by the LECS."

DEFVAL { '0'H }

::= { lecsConfEntry 2 }

lecsAtmAddrSpec OBJECT-TYPE

SYNTAX     AtmLaneAddress

MAX-ACCESS read-create

STATUS     current

DESCRIPTION

"An ATM  address specified by  the

network or local management that,

with the ATM address mask, determines

a  portion of  the  ATM address  that

the  LECS on the designated ATM interface

will use  to derive the actual ATM

address from the network or ILMI.  The derived

ATM address is specified in the object

lecsAtmAddrActual, which is used to

receive CONFIGURE requests.

The value of this object, if not

specified, is defaulted to the

well-known LECS ATM address specified

in the LAN Emulation Spec. 1.0."

DEFVAL { '4700790000000000000000000000A03E00000100'H }

::= { lecsConfEntry 3 }

lecsAtmAddrMask OBJECT-TYPE

SYNTAX     AtmLaneMask

MAX-ACCESS read-create

STATUS     current

DESCRIPTION

"The ATM address mask associated with

the object lecsAtmAddrSpec.  The value

of the mask is an ATM address with

the don't care portion set to zero

and the valid ATM address portion set to one."

DEFVAL { 'FFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFF'H }

::= { lecsConfEntry 4 }

lecsAtmAddrActual OBJECT-TYPE

SYNTAX     AtmLaneAddress

MAX-ACCESS read-only

STATUS     current

DESCRIPTION

" The resulting ATM address that the

LECS is accepting CONFIGURE

requests on the interface indicated

by the object lecsAtmIfIndex.

This  address is   the  result of  the

specified   ATM address,  its   mask   and

interaction through the ILMI  with  the

switch. Note  that   this object is only

valid  when the corresponding lecsOperStatus

is 'up'."

::= { lecsConfEntry 5 }

lecsPolicySelIndex      OBJECT-TYPE

SYNTAX     PolicySelectorIndexType

MAX-ACCESS read-only

STATUS     current

DESCRIPTION

"The set of policies used

by this LECS in dertermining

requesters ELAN membership.

The policies are defined in

the elanPolicyTable.  The value

of this object must exist in the

elanPolicyTable."

::= { lecsConfEntry 6 }

lecsLastInitialized OBJECT-TYPE

SYNTAX     TimeStamp

MAX-ACCESS read-only

STATUS     current

DESCRIPTION

"The value of the sysUpTime since

LECS has last entered the state

indicated by the object lecsOperStatus."

::= { lecsConfEntry 7 }

lecsOperStatus OBJECT-TYPE

SYNTAX     INTEGER {

other(1), -- unspecified

up(2),    -- LECS is accepting

-- CONFIGURE request

down(3)   -- LECS is not accepting

-- CONFIGURE request

}

MAX-ACCESS read-only

STATUS     current

DESCRIPTION

" This  object reflects the actual

state of  the LECS which  may differ

from that   of the  lecsAdminStatus

object.   This     can occur    when

the  interface ifOperStatus     is

'down'   but the   corresponding

lecsAdminStatus is 'up'."

::= { lecsConfEntry 8 }

lecsAdminStatus OBJECT-TYPE

SYNTAX     INTEGER {

up(1),         -- LECS is accepting

-- CONFIGURE request

down(2) }      -- LECS is not accepting

-- CONFIGURE request

MAX-ACCESS read-create

STATUS     current

DESCRIPTION

"The desired  state of the  LECS on

this interface as prescribed by the

operator.   The actions of the agent

will,  if  at all possible,  eventually

result in the desired  state being

reflected in the lecsOperStatus."

DEFVAL  { up }

::= { lecsConfEntry 9 }

lecsRowStatus OBJECT-TYPE

SYNTAX     RowStatus

MAX-ACCESS read-create

STATUS     current

DESCRIPTION

"This object is used to create or

delete entries in this table."

REFERENCE "RFC 1443, [10] Textual Conventions

for version 2 of the Simple Network Management

Protocol (SNMPv2)."

::= { lecsConfEntry 10 }

--

-- LECS to ELAN mapping table

--

lecsElanTable OBJECT-TYPE

SYNTAX     SEQUENCE OF LecsElanEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"This table contains the mapping between

ELANs and LECS.  One LECS can manage more than

one ELAN and one ELAN can only be managed by

a LECS.

When a LECS is deleted from the lecsConfTable,

all entries associated with this entry will

also be deleted."

::= { elanLecsConfGroup 3 }

lecsElanEntry OBJECT-TYPE

SYNTAX     LecsElanEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"Each entry represents an ELAN to LECS

mapping."

INDEX { elanConfIndex, lecsConfIndex }

::= { lecsElanTable 1 }

LecsElanEntry ::= SEQUENCE {

lecsElanRowStatus  RowStatus

}

lecsElanRowStatus  OBJECT-TYPE

SYNTAX         RowStatus

MAX-ACCESS     read-create

STATUS         current

DESCRIPTION

"This object is used to create or

delete an entry from this table."

REFERENCE "RFC 1443, [10] Textual Conventions

for version 2 of the Simple Network Management

Protocol (SNMPv2)."

::= { lecsElanEntry 1 }

--

--      (c) TLV (Type, Length and Value) table

--

lecsTlvTable      OBJECT-TYPE

SYNTAX      SEQUENCE OF LecsTlvEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

"This table contains all TLVs this

agent supports.  This currently configured

sets of TLVs in this LECS. These sets can

includes

not only the standard TLVs specified

in the LAN Emulation Spec. 1.0 [1] but

also the additional parameters

exchanged between the LECS and LEC.

This table is indexed by a selector

index, which allows more than one

TLV to be selected by an ELAN; and

the TLV tag, which specified the type

of the TLV; and a TLV index which

is used to distinguish between different

entries with the same TLV tag.

How does the LECS treat the TLVs

that are not specified in this table

in the CONFIGURE requests are not

defined in this MIB."

::= { elanLecsConfGroup 4 }

lecsTlvEntry       OBJECT-TYPE

SYNTAX         LecsTlvEntry

MAX-ACCESS     not-accessible

STATUS         current

DESCRIPTION

"Each entry represents a set of TLV

encodings for an ELAN represented

by the elanConfIndex.  Objects lecsTlvVal

and lecsTlvRowStatus are required during

row creation."

INDEX { lecsTlvSelectorIndex,

lecsTlvTag, lecsTlvIndex }

::= { lecsTlvTable 1 }

LecsTlvEntry ::=

SEQUENCE {

lecsTlvSelectorIndex

TlvSelectorIndexType,

lecsTlvTag

OCTET STRING,

lecsTlvIndex

Integer32,

lecsTlvVal

OCTET STRING,

lecsTlvRowStatus

RowStatus

}

lecsTlvSelectorIndex      OBJECT-TYPE

SYNTAX        TlvSelectorIndexType

MAX-ACCESS    not-accessible

STATUS        current

DESCRIPTION

"The value of this object indicates

a group of TLVs that can be selected."

::= { lecsTlvEntry 1 }

lecsTlvTag        OBJECT-TYPE

SYNTAX        OCTET STRING (SIZE(4))

MAX-ACCESS    not-accessible

STATUS        current

DESCRIPTION

"The value of this object represents the

type of the contents of the lecsTlvVal

field in the entry.  The OUI field

in this object occupies the first

( or most significant )3 octets.

The OUI value 00-A0-3E is used for

the standard values defined by the ATM

Forum specification."

::= { lecsTlvEntry 2 }

lecsTlvIndex      OBJECT-TYPE

SYNTAX        Integer32 ( 1..2147483647 )

MAX-ACCESS    not-accessible

STATUS        current

DESCRIPTION

"The index of this TLV encoding entry.

The value of this object can be used

to distinguish between different entries

with the same lecsTlvTag value."

::= { lecsTlvEntry 3 }

lecsTlvVal        OBJECT-TYPE

SYNTAX        OCTET STRING (SIZE(0..1024))

MAX-ACCESS    read-create

STATUS        current

DESCRIPTION

"The value of this TLV entry.  Note that

the length is implied by the length of

the OCTET STRING."

::= { lecsTlvEntry 4 }

lecsTlvRowStatus  OBJECT-TYPE

SYNTAX        RowStatus

MAX-ACCESS    read-create

STATUS        current

DESCRIPTION

"This object is used to create or

destroy entries in this table. "

REFERENCE "RFC 1443, [10] Textual Conventions

for version 2 of the Simple Network Management

Protocol (SNMPv2)."

::= { lecsTlvEntry 5 }

--

--      (d) LECS Config VCC table

--

lecsVccTable      OBJECT-TYPE

SYNTAX      SEQUENCE OF LecsVccEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

"This table contains all the CONFIG VCCs of the

LECS.  The CONFIG VCC is used by the LEC to send/

receive ATM LE CONFIGURE request/response to/from

the LECS.  This table is writable if PVC is used

and read only if SVC is used. "

::= { elanLecsConfGroup 5 }

lecsVccEntry       OBJECT-TYPE

SYNTAX         LecsVccEntry

MAX-ACCESS     not-accessible

STATUS         current

DESCRIPTION

"Each entry represents a CONFIG VCC

between a pair of LEC and LECS."

INDEX { lecsConfIndex, lecsVccIfIndex,

lecsVccVpi, lecsVccVci }

::= { lecsVccTable 1 }

LecsVccEntry ::=

SEQUENCE {

lecsVccIfIndex

IfIndexOrZero,

lecsVccVpi

VpiInteger,

lecsVccVci

VciInteger,

lecsVccRowStatus

RowStatus

}

lecsVccIfIndex      OBJECT-TYPE

SYNTAX        IfIndexOrZero

MAX-ACCESS    not-accessible

STATUS        current

DESCRIPTION

"The ATM interface which the CONFIG VCC is established.

This value must be an existing value in the

ifTable.  The value of this object is set to zero

when the ATM interface is an internal connection. "

::= { lecsVccEntry 1 }

lecsVccVpi        OBJECT-TYPE

SYNTAX        VpiInteger

MAX-ACCESS    not-accessible

STATUS        current

DESCRIPTION

"The VPI value of the CONFIG VCC.  The object

lecsVccIfIndex, lecsVccVci and this object

uniquely identifies a VCC within an ATM system."

::= { lecsVccEntry 2 }

lecsVccVci      OBJECT-TYPE

SYNTAX        VciInteger

MAX-ACCESS    not-accessible

STATUS        current

DESCRIPTION

"The VCI value of the CONFIG VCC. The object

lecsVccIfIndex, lecsVccVpi and this object

uniquely identifies a VCC within an ATM system "

::= { lecsVccEntry 3 }

lecsVccRowStatus  OBJECT-TYPE

SYNTAX        RowStatus

MAX-ACCESS    read-create

STATUS        current

DESCRIPTION

"This object is used to create or

destroy entries in this table. "

REFERENCE "RFC 1443, [10] Textual Conventions

for version 2 of the Simple Network Management

Protocol (SNMPv2)."

::= { lecsVccEntry 4 }

--

--  (2.2) LECS Statistics Group

--     (a) LECS Statstistics table

--

lecsStatsTable OBJECT-TYPE

SYNTAX     SEQUENCE OF LecsStatsEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

" A (conceptual) table of statistics

associated with all

LECS instances on the device."

::= { elanLecsStatGroup 1 }

lecsStatsEntry OBJECT-TYPE

SYNTAX     LecsStatsEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

" A (conceptual) row in the

lecsStatsTable which corresponds

to the statistics kept by a particular

instance of a LECS."

AUGMENTS { lecsConfEntry }

::= { lecsStatsTable 1 }

LecsStatsEntry ::= SEQUENCE {

lecsStatSuccessful

Counter32,

lecsStatInBadFrames

Counter32,

lecsStatInvalidParam

Counter32,

lecsStatInsufRes

Counter32,

lecsStatAccDenied

Counter32,

lecsStatInvalidReq

Counter32,

lecsStatInvalidDest

Counter32,

lecsStatInvalidAddr

Counter32,

lecsStatNoConf

Counter32,

lecsStatConfError

Counter32,

lecsStatInsufInfo

Counter32

}

lecsStatSuccessful  OBJECT-TYPE

SYNTAX          Counter32

MAX-ACCESS      read-only

STATUS          current

DESCRIPTION

"The number of CONFIGURE requests

successfully granted since the agent

was last initialized."

::= { lecsStatsEntry 1 }

lecsStatInBadFrames  OBJECT-TYPE

SYNTAX          Counter32

MAX-ACCESS      read-only

STATUS          current

DESCRIPTION

"The number of mal formed CONFIGURE

requests dropped by the LECS."

::= { lecsStatsEntry 2 }

lecsStatInvalidParam   OBJECT-TYPE

SYNTAX         Counter32

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"The number of CONFIGURE requests

rejected due to the invalid request

parameters error."

REFERENCE

"LAN Emulation Over ATM Spec. v1.0. Table 13"

::= { lecsStatsEntry 3 }

lecsStatInsufRes    OBJECT-TYPE

SYNTAX         Counter32

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"The number of CONFIGURE requests rejected due

to the insufficent resources to grant request

error."

REFERENCE

"LAN Emulation Over ATM Spec. v1.0. Table 13"

::= { lecsStatsEntry 4 }

lecsStatAccDenied   OBJECT-TYPE

SYNTAX         Counter32

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"The number of CONFIGURE requests rejected due

to the access denied error."

REFERENCE

"LAN Emulation Over ATM Spec. v1.0. Table 13"

::= { lecsStatsEntry 5 }

lecsStatInvalidReq  OBJECT-TYPE

SYNTAX         Counter32

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"The number of CONFIGURE requests rejected due

to the invalid requester-id error."

REFERENCE

"LAN Emulation Over ATM Spec. v1.0. Table 13"

::= { lecsStatsEntry 6 }

lecsStatInvalidDest OBJECT-TYPE

SYNTAX         Counter32

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"The number of CONFIGURE requests rejected due

to the invalid destination error."

REFERENCE

"LAN Emulation Over ATM Spec. v1.0. Table 13"

::= { lecsStatsEntry 7 }

lecsStatInvalidAddr OBJECT-TYPE

SYNTAX         Counter32

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"The number of CONFIGURE requests rejected due

to the invalid ATM address error."

REFERENCE

"LAN Emulation Over ATM Spec. v1.0. Table 13"

::= { lecsStatsEntry 8 }

lecsStatNoConf   OBJECT-TYPE

SYNTAX         Counter32

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"The number of CONFIGURE requests rejected due

to the LE Client is not recognized error."

REFERENCE

"LAN Emulation Over ATM Spec. v1.0. Table 13"

::= { lecsStatsEntry 9 }

lecsStatConfError   OBJECT-TYPE

SYNTAX         Counter32

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"The number of CONFIGURE requests rejected due

to the LE_CONFIGURE error."

REFERENCE

"LAN Emulation Over ATM Spec. v1.0. Table 13"

::= { lecsStatsEntry 10 }

lecsStatInsufInfo   OBJECT-TYPE

SYNTAX         Counter32

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"The number of CONFIGURE requests rejected due

to the insufficient information error."

REFERENCE

"LAN Emulation Over ATM Spec. v1.0. Table 13"

::= { lecsStatsEntry 11 }

--

--  (2.3) LECS Fault Management Group - optional

--      (a) LECS Error log control table

--      (b) LECS error log table

--

lecsErrCtlTable OBJECT-TYPE

SYNTAX     SEQUENCE OF LecsErrCtlEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"This table contains error log control

information of all LECS instances.

This table is an extention to the

lecsConfTable.  It is used to enable

or disable error logs for a particular

LECS entry."

::= { elanLecsFaultGroup 1 }

lecsErrCtlEntry OBJECT-TYPE

SYNTAX     LecsErrCtlEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"Each entry represents a LECS entry

in the lecsConfTable."

AUGMENTS { lecsConfEntry }

::= { lecsErrCtlTable 1 }

LecsErrCtlEntry ::=

SEQUENCE {

lecsErrCtlAdminStatus

INTEGER,

lecsErrCtlOperStatus

INTEGER,

lecsErrCtlClearLog

INTEGER,

lecsErrCtlMaxEntries

INTEGER,

lecsErrCtlLastEntry

LecsErrLogIndexType

}

lecsErrCtlAdminStatus     OBJECT-TYPE

SYNTAX        INTEGER {

enable(1),        -- enable error log

disable(2)        -- disable error log

}

MAX-ACCESS    read-create

STATUS        current

DESCRIPTION

"This object is used to enable/disable error

logging for the LECS."

::= { lecsErrCtlEntry 1 }

lecsErrCtlOperStatus            OBJECT-TYPE

SYNTAX        INTEGER {

other(1),        -- not specified

active(2),        -- error logging

outOfRes(3),        -- Out of buffer error

failed(4),        -- failed to start

-- error log for reasons

-- other than out of

-- resources

disabled(5)     -- the error logging capability

-- is disabled

}

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"This object is used to indicate

the result of a set operation to the

object lecsErrCtlAdminStatus.

If the error log was successfully

started, it is in active(2) mode.

Otherwise, it is set to either

outOfRes(3) or failed(4) for

the respective reasons."

::= { lecsErrCtlEntry 2 }

lecsErrCtlClearLog            OBJECT-TYPE

SYNTAX        INTEGER {

noOp(1),        -- read only value

clear(2)        -- clear the error log associated

-- with this LECS entry

}

MAX-ACCESS        read-create

STATUS                current

DESCRIPTION

"This object is used to clear the error log

entries associated with this LECS."

::= { lecsErrCtlEntry 3 }

lecsErrCtlMaxEntries        OBJECT-TYPE

SYNTAX        INTEGER ( 1..65535 )

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"The maximum entries of the error

log a LECS can support."

::= { lecsErrCtlEntry 4 }

lecsErrCtlLastEntry        OBJECT-TYPE

SYNTAX        LecsErrLogIndexType

MAX-ACCESS    read-create

STATUS        current

DESCRIPTION

"The index to the last entry in the error

log table associated with this LECS."

::= { lecsErrCtlEntry 5 }

--

--

--   LECS error log table

--

lecsErrLogTable OBJECT-TYPE

SYNTAX     SEQUENCE OF LecsErrLogEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"This table contains error logs

of the LECS instances enabled

in the lecsErrCtlTable.  This table

is indexed by the LECS instance

index and an arbitrary integer

uniquely identifies an error

log."

::= { elanLecsFaultGroup 2 }

lecsErrLogEntry OBJECT-TYPE

SYNTAX     LecsErrLogEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"Each entry represents a LEC that

was rejected due to a violation

against the policies or an error."

INDEX { lecsConfIndex, lecsErrLogIndex }

::= { lecsErrLogTable 1 }

LecsErrLogEntry ::=

SEQUENCE {

lecsErrLogIndex

LecsErrLogIndexType,

lecsErrLogAtmAddr

AtmLaneAddress,

lecsErrLogErrCode

INTEGER,

lecsErrLogTime

TimeStamp

}

lecsErrLogIndex     OBJECT-TYPE

SYNTAX          LecsErrLogIndexType

MAX-ACCESS      not-accessible

STATUS          current

DESCRIPTION

"An arbitrary integer which uniquely

identifies an error log entry. The first

entry after reset or clearing the error

log is an assigned value (2^32-1).  Succeding

entries are assigned with descending values

consecutively.  Entries after 1 are discarded.This

number ranges from 1 to the value of

the object lecsErrCtlMaxEntries times

number of LECS error log capability

enabled.  The enabling/disabling of

the error log capability is done in

the lecsErrCtlTable."

::= { lecsErrLogEntry 1 }

lecsErrLogAtmAddr OBJECT-TYPE

SYNTAX        AtmLaneAddress

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"The ATM address of the requester

which sends the CONFIGURE request

and causes the error to occur.

The corresponding error code is

specified in the object lecsErrLogErrCode."

::= { lecsErrLogEntry 2 }

lecsErrLogErrCode OBJECT-TYPE

SYNTAX        INTEGER (0..22)

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"The Error code which indicates the

cause of the error triggered by the

CONFIGURE request sent by the

requester indicated by the value of

the object lecsErrLogAtmAddr."

::= { lecsErrLogEntry 3 }

lecsErrLogTime    OBJECT-TYPE

SYNTAX        TimeStamp

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"The sysUpTime when this entry was logged by

the LECS."

::= { lecsErrLogEntry 4 }

-- Conformance Information

elanMIBConformance      OBJECT IDENTIFIER ::= { elanMIB 4 }

elanMIBGroups           OBJECT IDENTIFIER ::=

{ elanMIBConformance 1 }

elanMIBCompliances      OBJECT IDENTIFIER ::=

{ elanMIBConformance 2 }

-- Compliance Statements

elanMIBCompliance        MODULE-COMPLIANCE

STATUS           current

DESCRIPTION      "The compliance statement for SNMP

entities which support ATM Emulated LANs LAN Emulation

ELAN MIB."

MODULE -- this module

MANDATORY-GROUPS  { elanCConfGroup }

GROUP   elanLecAssignByAtmGroup

DESCRIPTION

"This group is mandatory only for thoes

agent that implements the LEC assignment

policy 'by ATM address'."

GROUP   elanLecAssignByMacGroup

DESCRIPTION

"This group is mandatory only for thoes

agent that implements the LEC assignment

policy 'by MAC address'."

GROUP   elanLecAssignByRdGroup

DESCRIPTION

"This group is mandatory only for thoes

agent that implements the LEC assignment

policy 'by Route Descriptor'."

GROUP   lecsCStatGroup

DESCRIPTION

"This group is mandatory only for those

agent that supports LECS."

GROUP   lecsCGroup

DESCRIPTION

"This group is mandatory only for those

agent that supports LECS."

GROUP   lecsCFaultGroup

DESCRIPTION

"This group is mandatory only to those agents

that support LECS and Fault Management."

::= { elanMIBCompliances 1 }

-- Units of Conformance

elanCConfGroup    OBJECT-GROUP

OBJECTS {

elanConfNextId,

elanConfName,

elanConfTlvIndex,

elanConfLanType,

elanConfMaxFrameSize,

elanConfRowStatus,

elanLecPktSizeRowStatus,

elanLecNameRowStatus,

elanLesAtmAddress,

elanLesRowStatus,

elanPolicyPriority,

elanPolicyType,

elanPolicyRowStatus

}

STATUS     current

DESCRIPTION

"A collection of objects providing configuration

information about an Emulated LAN."

::= { elanMIBGroups 1 }

elanLecAssignByAtmGroup  OBJECT-GROUP

OBJECTS {

elanLecAtmRowStatus

}

STATUS    current

DESCRIPTION

"A collection of objects providing ATM addresses

of LECs."

::= { elanMIBGroups 2 }

elanLecAssignByMacGroup OBJECT-GROUP

OBJECTS {

elanLecMacRowStatus

}

STATUS    current

DESCRIPTION

"A collection of objects providing MAC addresses

of LECs."

::= { elanMIBGroups 3 }

elanLecAssignByRdGroup OBJECT-GROUP

OBJECTS {

elanLecRdRowStatus

}

STATUS    current

DESCRIPTION

"A collection of objects providing Route Descriptors

of LECs."

::= { elanMIBGroups 4 }

lecsCStatGroup    OBJECT-GROUP

OBJECTS {

lecsStatSuccessful,

lecsStatInBadFrames,

lecsStatInvalidParam,

lecsStatInsufRes,

lecsStatAccDenied,

lecsStatInvalidReq,

lecsStatInvalidDest,

lecsStatInvalidAddr,

lecsStatNoConf,

lecsStatConfError,

lecsStatInsufInfo

}

STATUS     current

DESCRIPTION

"A collection of objects providing information

about LECS statistics."

::= { elanMIBGroups 5 }

lecsCGroup    OBJECT-GROUP

OBJECTS {

lecsConfNextId,

lecsAtmIfIndex,

lecsAtmAddrSpec,

lecsAtmAddrMask,

lecsAtmAddrActual,

lecsElanRowStatus,

lecsPolicySelIndex,

lecsTlvVal,

lecsTlvRowStatus,

lecsVccRowStatus,

lecsLastInitialized,

lecsOperStatus,

lecsAdminStatus,

lecsRowStatus }

STATUS     current

DESCRIPTION

"A group of objects used for LECS

management only."

::= { elanMIBGroups 6 }

lecsCFaultGroup  OBJECT-GROUP

OBJECTS {

lecsErrCtlAdminStatus,

lecsErrCtlOperStatus,

lecsErrCtlClearLog,

lecsErrCtlMaxEntries,

lecsErrCtlLastEntry,

lecsErrLogTime,

lecsErrLogAtmAddr,

lecsErrLogErrCode

}

STATUS     current

DESCRIPTION

"A group of objects used for LECS

fault management only."

::= { elanMIBGroups 7 }

END

LAN-EMULATION-LES-MIB DEFINITIONS ::= BEGIN

IMPORTS

MODULE-IDENTITY, OBJECT-TYPE,

Counter32, Integer32

FROM SNMPv2-SMI

TEXTUAL-CONVENTION, DisplayString,

RowStatus, MacAddress,

TruthValue, TimeStamp

FROM SNMPv2-TC

MODULE-COMPLIANCE, OBJECT-GROUP

FROM SNMPv2-CONF

LeArpTableEntryType,

AtmLaneAddress,

VpiInteger,

VciInteger,

atmfLanEmulationatmfLanEmulation

FROM LAN-EMULATION-CLIENT-MIB

IfIndexOrZero, AtmLaneMask

FROM LAN-EMULATION-ELAN-MIB;

lesMIB MODULE-IDENTITY

LAST-UPDATED "96021212009509071200Z"

ORGANIZATION "ATM Forum LAN Emulation Sub-Working Group"

CONTACT-INFO

"

The ATM Forum

303 Vintage Park Drive

Foster City, CA  94404

United States of America

2570 West EL camino Real,

Ste 304, Mountain View,

CA 94040-1313, USA

Tel: 415-578-6860

E-mail: info@atmforum.com"

DESCRIPTION

"This is the MIB module for managing ATM

LAN Emulation Servers."

::= { atmfLanEmulation 3atmfLanEmulation 3 }

--

--    Textual Conventions

--

LecId ::= TEXTUAL-CONVENTION

STATUS     current

DESCRIPTION

"C14 LE Client Identifier."

SYNTAX      INTEGER( 0..65279 )

BusConfIndex ::= TEXTUAL-CONVENTION

STATUS     current

DESCRIPTION

"A value which uniquely identifies a BUS.

This number is only used locally by the agent to

distinguish between BUSs."

SYNTAX      Integer32

LesLocalIndex ::= TEXTUAL-CONVENTION

STATUS     current

DESCRIPTION

"A value which uniquely identifies a

conceptual row in the lesConfTable.

This number is only used locally by the agent to

distinguish between LESs."

SYNTAX     Integer32

LesLecDataFrameFormat ::= TEXTUAL-CONVENTION

STATUS     current

DESCRIPTION

"A 'LAN Type' value.

SC2  LAN Type.  The type of LAN that the LE Client is,

or wishes to become, a member of.  This MUST be one

of Ethernet/IEEE 802.3 or IEEE 802.5 Server is servicing."

REFERENCE

"ATM Forum LAN Emulation Over ATM Specification, V1.0,

Section 5.1.2.1"

SYNTAX      INTEGER {

aflane8023(2),

aflane8025(3)

}

LesLecDataFrameSize ::= TEXTUAL-CONVENTION

STATUS     current

DESCRIPTION

"A 'Maximum Data Frame Size' value.

C3                   S3  Maximum Data Frame Size.  The maximum AAL-5 SDU size.

of a data frame that the LE Client wishes to send on

the Multicast Send VCC or to receive on the

Multicast Send VCC or Multicast Forward VCC.  This

parameter also specifies the maximum AAL-5 SDU on

all of a LE Client's Data Direct VCCs.  This MUST be

either 1516, 4544, 9234, or 18190 octets."

REFERENCE

"ATM Forum LAN Emulation Over ATM Specification, V1.0,

Section 5.1.2.1"

SYNTAX      INTEGER {

max1516(2),

max4544(3),

max9234(4),

max18190(5)

}

LesErrLogIndexType ::= TEXTUAL-CONVENTION

STATUS     current

DESCRIPTION

"An arbitrary integer used in identifying

an erro log associated with a LES."

SYNTAX     Integer32(1..2147483647)

-- This MIB module consists of the following groups:

--

--  (1) LES Conf Group

--      (a) LES table

--      (b) LES VCC table

--      (c) BUS table

--      (d) ATM ARP table

--      (e) ATM Route Descriptor ARP table

--      (f) LES-LEC table

--

--  (2) LES Monitoring Group

--      (a) LES Statistics Table

--

--  (3) LES-LEC Monitoring Group

--      (a) LES-LEC statistics table

--  (4) LES Fault Management Group

--      (a) LES Error Log Control Table

--      (b) LES Error Log Table

--

lesConfGroup  OBJECT IDENTIFIER ::= { lesMIB 1 }

lesStatGroup  OBJECT IDENTIFIER ::= { lesMIB 2 }

lesLecStatGroup OBJECT IDENTIFIER ::= { lesMIB 3 }

lesFaultGroup OBJECT IDENTIFIER ::= { lesMIB 4 }

lesConfNextId  OBJECT-TYPE

SYNTAX    LesLocalIndex

MAX-ACCESS read-only

STATUS    current

DESCRIPTION

"The next available LES index.  The

value of this object can be used as

the index by the network manager to

create an entry in the lesConfTable."

::= { lesConfGroup 1 }

--

--  LES table

--

lesConfTable    OBJECT-TYPE

SYNTAX      SEQUENCE OF LesConfEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

"This table contains all LAN Emulation

Servers this agent manages.  The LES

is one of the components in the Emulated

LAN which implements the control coordination function.

It is the address resolution server for a given ELAN.

The LES provides a facility for registering and resolving

MAC addresses and/or route descriptors to ATM

addresses.  There can be multiple LES per ELAN

but a LES can serve only one ELAN."

::= { lesConfGroup 2 }

lesConfEntry     OBJECT-TYPE

SYNTAX       LesConfEntry

MAX-ACCESS   not-accessible

STATUS       current

DESCRIPTION

"Each entry in this table represents a

LES.  The parameters in each entry apply

to one emulated LAN served by one LES.

Objects lesLanType and lesMaxFrameSize

are also required besides lesRowStatus

during row creation."

INDEX { lesConfIndex }

::= { lesConfTable 1 }

LesConfEntry ::=

SEQUENCE {

lesConfIndex

LesLocalIndex,

lesAtmAddrSpec

AtmLaneAddress,

lesAtmAddrMask

AtmLaneMask,

lesAtmAddrActual

AtmLaneAddress,

lesElanName

DisplayString,

lesLanType

LesLecDataFrameFormat,

lesLastChange

TimeStamp,

lesMaxFrameSize

LesLecDataFrameSize,

lesControlTimeOut

INTEGER,

lesOperStatus

INTEGER,

lesAdminStatus

INTEGER,

lesRowStatus

RowStatus

}

lesConfIndex      OBJECT-TYPE

SYNTAX        LesLocalIndex

MAX-ACCESS    not-accessible

STATUS        current

DESCRIPTION

"A value which uniquely identifies a

conceptual row in the lesConfTable.

If the conceptual row identified by this value

of lesConfIndex is recreated following an agent

restart, the same value of lesConfIndex must be

used to identify the recreated row."

::= { lesConfEntry 1 }

lesAtmAddrSpec    OBJECT-TYPE

SYNTAX         AtmLaneAddress

MAX-ACCESS     read-create

STATUS         current

DESCRIPTION

"An ATM  address specified by  the

network or local management that,

with the ATM address mask, determines

a  portion of  the  ATM address  that

the  LES on the designated ATM interface

will use  to derive the actual ATM

address from the network or ILMI.  The derived

ATM address is specified in the object

lesAtmAddrActual, which is used to

receive ATM ARP requests."

REFERENCE

"LAN Emulation Over ATM Specification -

version 1.0. S1."

::= { lesConfEntry 2 }

lesAtmAddrMask OBJECT-TYPE

SYNTAX     AtmLaneMask

MAX-ACCESS read-create

STATUS     current

DESCRIPTION

"The ATM address mask associated with

the object lesAtmAddrSpec.  The value

of the mask is an ATM address with

the don't care portion set to zero

and the valid ATM address portion set to one."

REFERENCE

"LAN Emulation Over ATM Specification -

version 1.0. S1."

DEFVAL { 'FFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFF'H }

::= { lesConfEntry 3 }

lesAtmAddrActual OBJECT-TYPE

SYNTAX     AtmLaneAddress

MAX-ACCESS read-only

STATUS     current

DESCRIPTION

" The resultant ATM address  in use by  the LES.  This

object is a product of the specified ATM address, mask

and  interaction  with  the network.  This object is

created by the agent."

REFERENCE

"LAN Emulation Over ATM Specification -

version 1.0. S1."

::= { lesConfEntry 4 }

lesElanName    OBJECT-TYPE

SYNTAX          DisplayString (SIZE (0..32))

MAX-ACCESS      read-create

STATUS          current

DESCRIPTION

"The name of the Emulated LAN this LES

is providing service for.  This object

may be used to identify the ELAN the LES

is in."

REFERENCE

"LAN Emulation Over ATM Specification -

version 1.0. C5."

DEFVAL { "" }

::= { lesConfEntry 5 }

lesLanType         OBJECT-TYPE

SYNTAX          LesLecDataFrameFormat

MAX-ACCESS      read-create

STATUS          current

DESCRIPTION

"The type of the ATM Emulated LAN this

LES is providing service to. If the

LEC has spcified a LAN type in its

JOIN request that does not match with

the value of this object, the LES

may reject the request.  At present only 802.3 and

802.5 LAN types are supported."

REFERENCE

"LAN Emulation Over ATM Specification -

version 1.0. S2."

::= { lesConfEntry 6 }

lesLastChange OBJECT-TYPE

SYNTAX     TimeStamp

MAX-ACCESS read-only

STATUS     current

DESCRIPTION

"The  value of   sysUpTime  when  this LES

has entered the state indicated by the

object lesOperStatus."

::= { lesConfEntry 7 }

lesMaxFrameSize    OBJECT-TYPE

SYNTAX          LesLecDataFrameSize

MAX-ACCESS      read-create

STATUS          current

DESCRIPTION

"The maximum AAL-5 SDU size of a data

frame that the LE service can guarantee

not to drop because it is too large.

This value is also returned to client when

a LEC spcified value in the JOIN request does

not match with this value."

REFERENCE

"LAN Emulation Over ATM Specification -

version 1.0. S3."

::= { lesConfEntry 8 }

lesControlTimeOut  OBJECT-TYPE

SYNTAX          INTEGER (10..300)

UNITS           "seconds"

MAX-ACCESS      read-create

STATUS          current

DESCRIPTION

"Time out period used for timing out most

request/response control frame interactions.

This is the time a Client has to issue a join

request to a LES after a control direct VCC is

established with a LES.

This object is measured in seconds."

REFERENCE

"LAN Emulation Over ATM Specification -

version 1.0. S4."

DEFVAL     { 120 }

::= { lesConfEntry 9 }

lesOperStatus   OBJECT-TYPE

SYNTAX      INTEGER {

other(1),       -- unknown state

up(2),          -- LES is up and running

down(3)         -- LES is up down or not available

}

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"The operational state of this LES entry.

When in 'up' state the LES will respond

to LEC requests.  Any other state the

LES is notavailable for service and may

release all the existing VCCs and refuse

service to all clients."

::= { lesConfEntry 11 }

lesAdminStatus OBJECT-TYPE

SYNTAX     INTEGER {

up(2),          -- LES is up and running

down(3)         -- LES is up down or not available

}

MAX-ACCESS read-create

STATUS     current

DESCRIPTION

"  The  desired  state   of  the  designated   LES  as

prescribed by the operator. The  actions of the  agent

will, if at  all  possible, eventually  result  in the

desired state being  reflected in  the lesOperStatus."

DEFVAL { up }

::= { lesConfEntry 12 }

lesRowStatus OBJECT-TYPE

SYNTAX     RowStatus

MAX-ACCESS read-create

STATUS     current

DESCRIPTION

"This object is used to create or

delete entries in the elanConfTable."

REFERENCE "RFC 1443, [10] Textual Conventions

for version 2 of the Simple Network Management

Protocol (SNMPv2)."

::= { lesConfEntry 13 }

--

--  LES VCC table

--

lesVccTable     OBJECT-TYPE

SYNTAX      SEQUENCE OF LesVccEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

"This table contains all the Control Distribute

VCCs used by the LES to distribute control traffic

to the participating LECs.  The Control Distribute

VCC can either be point-to-point or point-to-

multipoint calls.  This table is read only if

SVCs are used and writable if PVCs are used."

::= { lesConfGroup 3 }

lesVccEntry      OBJECT-TYPE

SYNTAX       LesVccEntry

MAX-ACCESS   not-accessible

STATUS       current

DESCRIPTION

"Each entry in this table represents a

LES entry and it's associated Control Distribute VCC. "

INDEX { lesConfIndex, lesVccAtmIfIndex,

lesVccCtlDistVpi, lesVccCtlDistVci }

::= { lesVccTable 1 }

LesVccEntry ::=

SEQUENCE {

lesVccAtmIfIndex

IfIndexOrZero,

lesVccCtlDistVpi

VpiInteger,

lesVccCtlDistVci

VciInteger,

lesVccRowStatus

RowStatus

}

lesVccAtmIfIndex  OBJECT-TYPE

SYNTAX     IfIndexOrZero

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"The ATM interface which the Control

Distribute VCC is running on.

This value must match an existing

value  in the   ifTable.

The value of this object is set

to zero when the ATM interface is

an internal connection."

::= { lesVccEntry 1 }

lesVccCtlDistVpi  OBJECT-TYPE

SYNTAX     VpiInteger

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"The VPI value of the Control

Distribute VCC.  The object

lesVccAtmIfIndex, lesVccCtlDistVci

and the value of this object uniquely

identfies a VCC within a ATM host."

::= { lesVccEntry 2 }

lesVccCtlDistVci  OBJECT-TYPE

SYNTAX     VciInteger

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"The VCI value of the Control

Distribute VCC.  The object

lesVccAtmIfIndex, lesVccCtlDistVci

and the value of this object uniquely

identfies a VCC within a ATM host."

::= { lesVccEntry 3 }

lesVccRowStatus   OBJECT-TYPE

SYNTAX     RowStatus

MAX-ACCESS read-create

STATUS     current

DESCRIPTION

"This object is used to create or

delete entries in the elanConfTable."

REFERENCE "RFC 1443, [10] Textual Conventions

for version 2 of the Simple Network Management

Protocol (SNMPv2)."

::= { lesVccEntry 4 }

--

--  BUS table

--

lesBusTable     OBJECT-TYPE

SYNTAX      SEQUENCE OF LesBusEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

"This table contains the BUSs paired

with the LESs found in the lesConfTable.

The BUS (Broadcast and Unknown Server)

handles data sent by a LE client to

the broadcast MAC address, all multicast

traffic, and initial unicast frames

which are sent by a LAN Emulation Client

before the data direct target ATM address

has been resolved."

::= { lesConfGroup 4 }

lesBusEntry      OBJECT-TYPE

SYNTAX       LesBusEntry

MAX-ACCESS   not-accessible

STATUS       current

DESCRIPTION

"Each entry in this table represents aLES/BUS pair. Object lesBusAddress is required duringrow creation. This table is indexed by lesConfIndex and lesBusConfIndexto show the pairing relationship betweenthe LES and BUS."

INDEX { lesConfIndex, lesBusConfIndex }

::= { lesBusTable 1 }

LesBusEntry ::=

SEQUENCE {

lesBusConfIndex

BusConfIndex,

lesBusAddress

AtmLaneAddress

}

lesBusConfIndex      OBJECT-TYPE

SYNTAX           BusConfIndex

MAX-ACCESS       not-accessible

STATUS           current

DESCRIPTION

"A value which uniquely identifies a

BUS ATM address.

If the BUS ATM address identified by this value

of lesBusConfIndex is recreated following an agent

restart, the same value of lesBusConfIndex must be

used to identify the recreated BUS ATM address."

::= { lesBusEntry 1 }

lesBusAddress     OBJECT-TYPE

SYNTAX        AtmLaneAddress

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"The ATM address of the BUS. This BUS is associated

with LES specified by the lesConfIndex. A BUS may

have several ATM addresses, this object provides

the ATM address the LES returns in response to the

LE-ARP request by the LEC."

REFERENCE

"LAN Emulation Over ATM Specification -

version 1.0. S6."

::= { lesBusEntry 2 }

--

--  ATM LE-ARP table (by MAC address)

--

--  This table provides LE-ARP cache table for MAC-to-ATM addresses.

--  The entries are created by the agent and Network manager

--  depending on the entry type.

--        The entries can be any one of the following types:

--

--     viaRegister - This entry was registered by the LEC.

--

--     staticVolatile - This entry was created by Network manager.

--                This static entry is not aged but WILL NOT survive

--                restart of the client.   Agent may allow this entry

--                to be created but may require LES to be in operational

--                state.

--

--

--     staticNonVolatile - This entry was created by Network manager.

--          This static entry is not aged but will survive

--          restart of the client.   Agent may allow this entry

--                to be created but may require LES to be in

--                operational state.

--

--

--

--

--

lesLeArpMacTable  OBJECT-TYPE

SYNTAX      SEQUENCE OF LesLeArpMacEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

"This table provides access to an ATM LAN Emulation

Server's MAC-to-ATM ARP cache table.  It contains entries

for unicast addresseds, the broadcast address and

the multicast addresses.

When the entry is for broadcast MAC address the

corresponding ATM address is of a BUS.

When the entry is for unicast or multicast MAC

address the corresponding ATM address represents

a LEC."

::= { lesConfGroup 5 }

lesLeArpMacEntry   OBJECT-TYPE

SYNTAX       LesLeArpMacEntry

MAX-ACCESS   not-accessible

STATUS       current

DESCRIPTION

"An ATM LAN Emulation ARP table cache entry containing

information about the binding of one MAC address

to one ATM address."

INDEX { lesConfIndex, lesLeArpMacAddr }

::= { lesLeArpMacTable 1 }

LesLeArpMacEntry ::=

SEQUENCE {

lesLeArpMacAddr

MacAddress,

lesLeArpLecId

LecId,

lesLeArpAtmAddr

AtmLaneAddress,

lesLeArpEntryType

LeArpTableEntryType,

lesLeArpRowStatus

RowStatus

}

lesLeArpMacAddr     OBJECT-TYPE

SYNTAX        MacAddress

MAX-ACCESS    not-accessible

STATUS        current

DESCRIPTION

"The MAC address for which this cache table entry provides

a translation.  Since ATM LAN Emulation uses an LE ARP

protocol to locate the Broadcast and Unknown Server,

the value of this object could be the broadcast MAC

address.

MAC addresses should be unique within any given ATM

Emulated LAN.  However, there's no requirement that

they be unique across disjoint emulated LANs."

::= { lesLeArpMacEntry 1 }

lesLeArpLecId     OBJECT-TYPE

SYNTAX        LecId

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"The LE Client Identifier (LECID) of this

entry.  Each LE Client requires a LECID

assigned by the LE Server during the

Join phase.

If this entry is for a BUS then this object

value will be zero."

::= { lesLeArpMacEntry 2 }

lesLeArpAtmAddr     OBJECT-TYPE

SYNTAX         AtmLaneAddress

MAX-ACCESS     read-create

STATUS         current

DESCRIPTION

"The ATM address of the Broadcast & Unknown Server

or LAN Emulation Client whose MAC address is stored

in 'lesLeArpMacAddr'.

This volume may be registered by a LAN Emulation

Client or specified by network management."

::= { lesLeArpMacEntry 3 }

lesLeArpEntryType    OBJECT-TYPE

SYNTAX          LeArpTableEntryType

MAX-ACCESS      read-create

STATUS          current

DESCRIPTION

"This object is used to indicate how

this LE-ARP entry was created.

The possible values for this object are:

viaRegister(1),  -  agent

staticVolatile(2), - network manager

staticNonVolatile(3) - network manager

This object is filled in by agent or network

manager depending on the type."

REFERENCE

"LAN Emulation Client MIB definition."

DEFVAL { staticVolatile }

::= { lesLeArpMacEntry 4 }

lesLeArpRowStatus    OBJECT-TYPE

SYNTAX          RowStatus

MAX-ACCESS      read-create

STATUS          current

DESCRIPTION

"This object is used to create or

delete entries in the elanConfTable."

REFERENCE "RFC 1443, [10] Textual Conventions

for version 2 of the Simple Network Management

Protocol (SNMPv2)."

::= { lesLeArpMacEntry 5 }

--

--  ATM LE-ARP table by Route Descriptors

--

--  This table provides ARP cache for Route Descriptor-to-ATM addresses.

--  The entries are created by the agent and Network manager

--  depending on the entry type.

--  The entries can be any one of the following types:

--

--     viaRegister - This entry was registered by the LEC.

--

--     staticVolatile - This entry was created by Network manager.

--          This static entry is not aged but WILL NOT survive

--          restart of the client.   Agent may allow this entry

--          to be created but may require LES to be in operational

--          state.

--

--

--     staticNonVolatile - This entry was created by Network manager.

--          This static entry is not aged but will survive

--          restart of the client.   Agent may allow this entry

--          to be created but may require LES to be in

--          operational state.

lesLeArpRdTable  OBJECT-TYPE

SYNTAX      SEQUENCE OF LesLeArpRdEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

"This table provides access to an ATM LAN Emulation

Server's RouteDescriptor-to-ATM ARP cache.

The entries in this table are set-up by the agent

or network manager depending on the entry type.

The Route Descriptors are presented as Segment Id

(ring number) and Bridge number."

::= { lesConfGroup 6 }

lesLeArpRdEntry   OBJECT-TYPE

SYNTAX       LesLeArpRdEntry

MAX-ACCESS   not-accessible

STATUS       current

DESCRIPTION

"An ATM LAN Emulation ARP cache entry containing

information about the binding of one Route

Descriptor to one ATM address."

INDEX { lesConfIndex, lesLeArpRdSegId,

lesLeArpRdBridgeNum }

::= { lesLeArpRdTable 1 }

LesLeArpRdEntry ::=

SEQUENCE {

lesLeArpRdSegId

INTEGER,

lesLeArpRdBridgeNum

INTEGER,

lesLeArpRdLecId

LecId,

lesLeArpRdAtmAddr

AtmLaneAddress,

lesLeArpRdEntryType

LeArpTableEntryType,

lesLeArpRdRowStatus

RowStatus

}

lesLeArpRdSegId     OBJECT-TYPE

SYNTAX        INTEGER (0..4095)

MAX-ACCESS    not-accessible

STATUS     current

DESCRIPTION

"The LAN ID (ring number) portion of the

IEEE 802.5 route descriptor associated

with this LES."

::= { lesLeArpRdEntry 1 }

lesLeArpRdBridgeNum    OBJECT-TYPE

SYNTAX            INTEGER (0..15)

MAX-ACCESS        not-accessible

STATUS            current

DESCRIPTION

"The Bridge Number portion of the

IEEE 802.5 route descriptor associated

with this LES."

::= { lesLeArpRdEntry 2 }

lesLeArpRdLecId   OBJECT-TYPE

SYNTAX        LecId

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"The LE Client Identifier (LECID) of this

entry.  Each LE Client requires a LECID

assigned by the LE Server during the

Join phase.

If this entry is for a BUS then this object

value will be zero."

::= { lesLeArpRdEntry 3 }

lesLeArpRdAtmAddr     OBJECT-TYPE

SYNTAX         AtmLaneAddress

MAX-ACCESS     read-create

STATUS         current

DESCRIPTION

"The ATM address associated with the

Route Descriptor."

::= { lesLeArpRdEntry 4 }

lesLeArpRdEntryType    OBJECT-TYPE

SYNTAX          LeArpTableEntryType

MAX-ACCESS      read-create

STATUS          current

DESCRIPTION

"This object is used to indicate how

this LE-ARP entry was learned:

viaRegister(1),  -  agent

staticVolatile(2), - network manager

staticNonVolatile(3) - network manager

This object is filled in by agent or network

manager depending on the type."

DEFVAL { staticVolatile }

::= { lesLeArpRdEntry 5 }

lesLeArpRdRowStatus    OBJECT-TYPE

SYNTAX          RowStatus

MAX-ACCESS      read-create

STATUS          current

DESCRIPTION

"This object is used to create or

delete entries in the elanConfTable."

REFERENCE "RFC 1443, [10] Textual Conventions

for version 2 of the Simple Network Management

Protocol (SNMPv2)."

::= { lesLeArpRdEntry 6 }

--

--  LES-LEC table

--

lesLecTableLastChange OBJECT-TYPE

SYNTAX      TimeStamp

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"The value of sysUptime when an entry was created/deleted."

::= { lesConfGroup 7 }

lesLecTable     OBJECT-TYPE

SYNTAX      SEQUENCE OF LesLecEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

"This table contains all LAN Emulation

clients serviced by LESs specified in

the lesConfTable.  This table can be

used to retrieve the topology of an

ELAN, in particular, the LES to LECs

mapping information.

An entry in this table is filled in

by the agent when a LEC registers successfully

with the LES.  Objects lesLecCtlDirectVpi

and lesLecCtlDirectVci can be modified  by the

network manager after creation if PVC is used."

::= { lesConfGroup 87 }

lesLecEntry      OBJECT-TYPE

SYNTAX       LesLecEntry

MAX-ACCESS   not-accessible

STATUS       current

DESCRIPTION

"Each entry represents a LANE client to LES

binding."

INDEX { lesConfIndex, lesLecIndex }

::= { lesLecTable 1 }

LesLecEntry ::=

SEQUENCE {

lesLecIndex

INTEGER,

lesLecAtmAddr

AtmLaneAddress,

lesLecProxy

TruthValue,

lesLecId

LecId,

lesLecAtmIfIndex

IfIndexOrZero,

lesLecCtlDirectVpi

VpiInteger,

lesLecCtlDirectVci

VciInteger,

lesLecLastChange

TimeStamp,

lesLecState

INTEGER,

lesLecRowStatus

RowStatus

}

lesLecIndex       OBJECT-TYPE

SYNTAX         INTEGER (1..65535)

MAX-ACCESS     not-accessible

STATUS         current

DESCRIPTION

"An arbitrary integer which uniquely identifies

a LEC in this table."

::= { lesLecEntry 1 }

lesLecAtmAddr     OBJECT-TYPE

SYNTAX         AtmLaneAddress

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"The ATM address of the LANE client.  This

is the primary ATM address of the LEC used

in joining phase."

REFERENCE

"ATM Forum LAN Emulation Over ATM Specification, V1.0,

Section 5.4.3"

::= { lesLecEntry 2 }

lesLecProxy       OBJECT-TYPE

SYNTAX         TruthValue

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"Whether this client is acting as a

proxy.  Proxy clients are allowed

to represent unregistered MAC addresses,

and receive copies of LE_ARP_REQUEST

packets for such addresses."

REFERENCE

"ATM Forum LAN Emulation Over ATM Specification, V1.0,

Section 5.1.1"

DEFVAL { false }

::= { lesLecEntry 3 }

lesLecId          OBJECT-TYPE

SYNTAX        LecId

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"The LE Client Identifier (LECID) of this

entry.  Each LE Client requires a LECID

assigned by the LE Server during the

Join phase.  The LECID is placed

in control requests by the LE Client and MAY be

used for echo suppression on multicast data frames

sent by that LE Client."

DEFVAL { 0 }

::= { lesLecEntry 4 }

lesLecAtmIfIndex      OBJECT-TYPE

SYNTAX       IfIndexOrZero

MAX-ACCESS   read-create

STATUS       current

DESCRIPTION

"The ifIndex of ATM port where this LEC entry

has established the control direct VCC to

the LES.  The value of this object

maps to an existing ifIndex value in the

ifTable of MIB-II.

When an internal connection is used, this object is

set to zero."

::= { lesLecEntry 5 }

lesLecCtlDirectVpi OBJECT-TYPE

SYNTAX     VpiInteger

MAX-ACCESS read-create

STATUS     current

DESCRIPTION

" The VPI of the bi-directional control

direct connection between the LEC and LES."

::= { lesLecEntry 6 }

lesLecCtlDirectVci OBJECT-TYPE

SYNTAX     VciInteger

MAX-ACCESS read-create

STATUS     current

DESCRIPTION

" The VCI of the bi-directional control

direct connection between the LEC and LES."

::= { lesLecEntry 7 }

lesLecLastChange  OBJECT-TYPE

SYNTAX         TimeStamp

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"The value of sysUpTime of this entry when the LEC enters

the state indicated by the object lesLecState."

::= { lesLecEntry 8 }

lesLecState       OBJECT-TYPE

SYNTAX         INTEGER {

other(1),          -- LEC state is unknown

noLesConnect(2),   -- LEC is not connected to the LES

lesConnect(3),     -- LEC has established a

-- VCC connection to the LES

joining(4),        -- LEC JOIN request has been

-- received by the LES

addLec(5),         -- LES is setting up Control Distribute

-- VCC to this LEC

joinedLes(6)       -- LEC has joined to the LES

-- successfully

}

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"This object is used to indicate the

status this LEC entry is in from the

LES's perspective.  The state of this

object is updated by the agent as

it discovers various phases of this LEC."

::= { lesLecEntry 9 }

lesLecRowStatus OBJECT-TYPE

SYNTAX     RowStatus

MAX-ACCESS read-create

STATUS     current

DESCRIPTION

" This object provides a way for the network manager

to selectively remove a LE Client from the designated

LES.  Or in a system where PVCs are used, this table

is used to configure Control Direct VCCs between LES

and LEC."

REFERENCE "RFC 1443, [10] Textual Conventions

for version 2 of the Simple Network Management

Protocol (SNMPv2)."

::= { lesLecEntry 10 }

--

--  LES statistics table

--

lesStatTable    OBJECT-TYPE

SYNTAX      SEQUENCE OF LesStatEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

"This table contains all counters the

LES maintain.  This table is an extention

to the lesConfTable.  It provides performance

and fault counters on a per LES basis."

::= { lesStatGroup 1 }

lesStatEntry     OBJECT-TYPE

SYNTAX       LesStatEntry

MAX-ACCESS   not-accessible

STATUS       current

DESCRIPTION

"Each entry in this table contains a

LES and its counters."

AUGMENTS { lesConfEntry }

::= { lesStatTable 1 }

LesStatEntry ::=

SEQUENCE {

lesStatJoinOk

Counter32,

lesStatVerNotSup

Counter32,

lesStatInvalidReqParam

Counter32,

lesStatDupLanDest

Counter32,

lesStatDupAtmAddr

Counter32,

lesStatInsRes

Counter32,

lesStatAccDenied

Counter32,

lesStatInvalidReqId

Counter32,

lesStatInvalidLanDest

Counter32,

lesStatInvalidAtmAddr

Counter32,

lesStatInBadPkts

Counter32,

lesStatOutRegFails

Counter32,

lesStatLeArpIn

Counter32,

lesStatLeArpFwd

Counter32

}

lesStatJoinOk     OBJECT-TYPE

SYNTAX        Counter32

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"Number of successful Join responses

send out by the LAN Emulation Server."

::= { lesStatEntry 1 }

lesStatVerNotSup  OBJECT-TYPE

SYNTAX        Counter32

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"Number of version not supported errors.

All the errors for Join, Register, and

Unregistered are included in this

counter."

REFERENCE

"ATM Forum LAN Emulation Over ATM Specification, V1.0,

Table 13."

::= { lesStatEntry 2 }

lesStatInvalidReqParam     OBJECT-TYPE

SYNTAX        Counter32

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"Number of invalid request parameters errors.

All the errors for Join, Register, and

Unregistered are included in this

counter."

REFERENCE

"ATM Forum LAN Emulation Over ATM Specification, V1.0,

Table 13."

::= { lesStatEntry 3 }

lesStatDupLanDest OBJECT-TYPE

SYNTAX        Counter32

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"Number of duplicate LAN destination errors.

All the errors for Join and Register

are included in this counter."

::= { lesStatEntry 4 }

lesStatDupAtmAddr OBJECT-TYPE

SYNTAX        Counter32

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"Number of duplicate ATM address errors.

All the errors for Join and Register

are included in this counter."

REFERENCE

"ATM Forum LAN Emulation Over ATM Specification, V1.0,

Table 13."

::= { lesStatEntry 5 }

lesStatInsRes     OBJECT-TYPE

SYNTAX        Counter32

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"Number of insufficient resources to grant

errors.

All the errors for Join and Register

are included in this counter."

REFERENCE

"ATM Forum LAN Emulation Over ATM Specification, V1.0,

Table 13."

::= { lesStatEntry 6 }

lesStatAccDenied  OBJECT-TYPE

SYNTAX        Counter32

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"Number of access denied for security

reasons errors.

All the errors for Join and Register

are included in this counter."

REFERENCE

"ATM Forum LAN Emulation Over ATM Specification, V1.0,

Table 13."

::= { lesStatEntry 7 }

lesStatInvalidReqId OBJECT-TYPE

SYNTAX        Counter32

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"Number of invalid LEC ID errors.

All the errors for Join, Register,

and Unregister are included in this counter."

REFERENCE

"ATM Forum LAN Emulation Over ATM Specification, V1.0,

Table 13."

::= { lesStatEntry 8 }

lesStatInvalidLanDest OBJECT-TYPE

SYNTAX        Counter32

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"Number of invalid LAN destination errors.

All the errors for Join and Register

are included in this counter."

REFERENCE

"ATM Forum LAN Emulation Over ATM Specification, V1.0,

Table 13."

::= { lesStatEntry 9 }

lesStatInvalidAtmAddr OBJECT-TYPE

SYNTAX        Counter32

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"Number of invalid ATM address errors.

All the errors for Join and Register

are included in this counter."

REFERENCE

"ATM Forum LAN Emulation Over ATM Specification, V1.0,

Table 13."

::= { lesStatEntry 10 }

lesStatInBadPkts OBJECT-TYPE

SYNTAX        Counter32

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"Number of mal formed ATM ARP requests

received by the LES."

::= { lesStatEntry 11 }

lesStatOutRegFails OBJECT-TYPE

SYNTAX        Counter32

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"Number of registration failures sent

out by this LES."

::= { lesStatEntry 12 }

lesStatLeArpIn OBJECT-TYPE

SYNTAX     Counter32

MAX-ACCESS read-only

STATUS     current

DESCRIPTION

"The total number of LE_ARP_REQUEST frames the LES has

accepted since its last initialization."

::= { lesStatEntry 13 }

lesStatLeArpFwd OBJECT-TYPE

SYNTAX     Counter32

MAX-ACCESS read-only

STATUS     current

DESCRIPTION

"The number of LE_ARP_REQUESTs that the LES forwarded

onto the clients (either via the control distribute or

individually over each control direct) rather than

answering directly.  This may be due to implementation

decision (forward all requests) or because the resolution

to the request did not reside in the LES's LE ARP cache."

::= { lesStatEntry 14 }

--

--  LES-LEC Statistics Table

--

lesLecStatTable    OBJECT-TYPE

SYNTAX      SEQUENCE OF LesLecStatEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

"This table contains all LE-ARP request

related counters and error counts on

a per LEC-LES pair basis."

::= { lesLecStatGroup 1 }

lesLecStatEntry     OBJECT-TYPE

SYNTAX       LesLecStatEntry

MAX-ACCESS   not-accessible

STATUS       current

DESCRIPTION

"Each entry in this table represents a

LEC and its ARP counters.  This table

is an extention to the lesLecTable."

AUGMENTS { lesLecEntry }

::= { lesLecStatTable 1 }

LesLecStatEntry ::=

SEQUENCE {

lesLecRecvs

Counter32,

lesLecSends

Counter32,

lesLecInRegReq

Counter32,

lesLecInUnReg

Counter32,

lesLecInLeArpUcast

Counter32,

lesLecInLeArpBcast

Counter32,

lesLecInLeArpResp

Counter32,

lesLecInNArp

Counter32

}

lesLecRecvs     OBJECT-TYPE

SYNTAX      Counter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"Number of requests received from this

LEC.  This includes all control

frames as well as LE-ARP requests."

::= { lesLecStatEntry 1 }

lesLecSends     OBJECT-TYPE

SYNTAX      Counter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"Number of requests or responses

sent to the LEC entry from this

LES.  This number includes NARP

requests, Topology Change requests

and LE-ARP responses."

::= { lesLecStatEntry 3 }

lesLecInRegReq     OBJECT-TYPE

SYNTAX      Counter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"Number of Register requests received

from this LEC.  "

::= { lesLecStatEntry 4 }

lesLecInUnReg     OBJECT-TYPE

SYNTAX      Counter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"Number of UnRegister requests received

from this LEC.  "

::= { lesLecStatEntry 5 }

lesLecInLeArpUcast     OBJECT-TYPE

SYNTAX      Counter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"Number of LE-ARP requests for UNICAST

address received from this LEC. "

::= { lesLecStatEntry 6 }

lesLecInLeArpBcast    OBJECT-TYPE

SYNTAX      Counter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"Number of LE-ARP requests for MULTICAST

and Broadcast address received from this LEC. "

::= { lesLecStatEntry 7 }

lesLecInLeArpResp     OBJECT-TYPE

SYNTAX      Counter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"Number of LE-ARP responses

received from this LEC. "

::= { lesLecStatEntry 8 }

lesLecInNAArp     OBJECT-TYPE

SYNTAX      Counter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"Number of N-ARP requestsresponses

received from this LEC. "

::= { lesLecStatEntry 10 }

--

-- LES Fault Mangement Group

--   (a) LES Error Control Table

--   (b) LES Error Log Table

--

lesErrCtlTable OBJECT-TYPE

SYNTAX     SEQUENCE OF LesErrCtlEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"This table contains error log control

information of all LES instances.

This table is an extention to the

lesConfTable.  It is used to enable

or disable error logs for a particular

LES entry."

::= { lesFaultGroup 1 }

lesErrCtlEntry OBJECT-TYPE

SYNTAX     LesErrCtlEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"Each entry represents a LES entry

in the lesConfTable."

AUGMENTS { lesConfEntry }

::= { lesErrCtlTable 1 }

LesErrCtlEntry ::=

SEQUENCE {

lesErrCtlAdminStatus

INTEGER,

lesErrCtlOperStatus

INTEGER,

lesErrCtlClearLog

INTEGER,

lesErrCtlMaxEntries

INTEGER,

lesErrCtlLastEntry

LesErrLogIndexType

}

lesErrCtlAdminStatus     OBJECT-TYPE

SYNTAX        INTEGER {

enable(1),        -- enable error log

disable(2)        -- disable error log

}

MAX-ACCESS    read-write

STATUS        current

DESCRIPTION

"This object is used to enable/disable error

logging for the LES."

::= { lesErrCtlEntry 1 }

lesErrCtlOperStatus            OBJECT-TYPE

SYNTAX        INTEGER {

other(1),        -- not specified

active(2),        -- error logging

outOfRes(3),        -- Out of buffer error

failed(4),        -- failed to start

-- error log for reasons

-- other than out of

-- resources

disabled(5)     -- error logging is disabled

}

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"This object is used to indicate

the result of a set operation to the

object lesErrCtlAdminStatus.

If the error log was successfully

started, it is in active(2) mode.

Otherwise, it is set to either

outOfRes(3) or failed(4) for

the respective reasons."

::= { lesErrCtlEntry 2 }

lesErrCtlClearLog            OBJECT-TYPE

SYNTAX        INTEGER {

noOp(1),        -- read only value

clear(2)        -- clear the error log associated

-- with this LES entry

}

MAX-ACCESS        read-write

STATUS                current

DESCRIPTION

"This object is used to clear the error log

entries associated with this LES."

::= { lesErrCtlEntry 3 }

lesErrCtlMaxEntries        OBJECT-TYPE

SYNTAX        INTEGER ( 1..65535 )

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"The maximum entries of the error

log a LES can support."

::= { lesErrCtlEntry 4 }

lesErrCtlLastEntry        OBJECT-TYPE

SYNTAX        LesErrLogIndexType

MAX-ACCESS    read-write

STATUS        current

DESCRIPTION

"The index to the last entry in the error

log table for this LES."

::= { lesErrCtlEntry 5 }

--

--

--   LES error log table

--

lesErrLogTable OBJECT-TYPE

SYNTAX     SEQUENCE OF LesErrLogEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"This table contains error logs

of the LES instances enabled

in the lesErrCtlTable.  This table

is indexed by the LES instance

index and an arbitrary integer

uniquely identifies an error

log."

::= { lesFaultGroup 2 }

lesErrLogEntry OBJECT-TYPE

SYNTAX     LesErrLogEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"Each entry represents a JOIN or REGISTER that

was rejected due to an error."

INDEX { lesConfIndex, lesErrLogIndex }

::= { lesErrLogTable 1 }

LesErrLogEntry ::=

SEQUENCE {

lesErrLogIndex

LesErrLogIndexType,

lesErrLogAtmAddr

AtmLaneAddress,

lesErrLogErrCode

INTEGER,

lesErrLogTime

TimeStamp

}

lesErrLogIndex     OBJECT-TYPE

SYNTAX          LesErrLogIndexType

MAX-ACCESS      not-accessible

STATUS          current

DESCRIPTION

"An arbitrary integer which uniquely

identifies an error log entry. The first

entry after reset or clearing the error

log is an assigned value (2^32-1).  Succeding

entries are assigned with descending values

consecutively.  Entries after 1 are discarded.This

number ranges from 1 to the value of

the object lesErrCtlMaxEntries times

number of LES with the error log capability

enabled.  The enabling/disabling of

the error log capability is done in

the lesErrCtlTable."

::= { lesErrLogEntry 1 }

lesErrLogAtmAddr OBJECT-TYPE

SYNTAX        AtmLaneAddress

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"The ATM address of the requester

which sends the JOIN or REGISTER request

and causes the error to occur.

The corresponding error code is

specified in the object lesErrLogErrCode."

::= { lesErrLogEntry 2 }

lesErrLogErrCode OBJECT-TYPE

SYNTAX        INTEGER (0..22)

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"The Error code which indicates the

cause of the error triggered by the

JOIN or REGISTER request sent by the

requester indicated by the value of

the object lesErrLogAtmAddr."

::= { lesErrLogEntry 3 }

lesErrLogTime    OBJECT-TYPE

SYNTAX        TimeStamp

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"The sysUpTime when this entry was logged by

the LES."

::= { lesErrLogEntry 4 }

-- Conformance Information

lesMIBConformance      OBJECT IDENTIFIER ::= { lesMIB 5 }

lesMIBGroups           OBJECT IDENTIFIER ::=

{ lesMIBConformance 1 }

lesMIBCompliances      OBJECT IDENTIFIER ::=

{ lesMIBConformance 2 }

-- Compliance Statements

lesMIBCompliance        MODULE-COMPLIANCE

STATUS           current

DESCRIPTION      "The compliance statement for SNMP

entities which support the ATM LAN Emulation

Services LES MIB."

MODULE -- this module

MANDATORY-GROUPS  { lesCConfGroup,

lesCStatGroup,

lesLecCStatGroup,

lesFaultCGroup }

OBJECT lesVccRowStatus

MIN-ACCESS read-only

DESCRIPTION

" Implementations that do not support LES over

PVCs are not required to allow write/create access

to the lesVccRowStatus object."

OBJECT lesLecAtmIfIndex

MIN-ACCESS read-only

DESCRIPTION

" Implementations that do not support LECs over

PVCs are not required to allow write/create access

to the lesLecAtmIfIndex object."

OBJECT lesLecCtlDirectVpi

MIN-ACCESS read-only

DESCRIPTION

" Implementations that do not support LECs over

PVCs are not required to allow write/create access

to the lesLecCtlDirectVpi object."

OBJECT lesLecCtlDirectVci

MIN-ACCESS read-only

DESCRIPTION

" Implementations that do not support LECs over

PVCs are not required to allow write/create access

to the lesLecCtlDirectVci object."

OBJECT lesLecRowStatus

WRITE-SYNTAX INTEGER { destroy(6) }

DESCRIPTION

" Implementations that do not support LECs over

PVCs need only support the destroy enumeration

of the RowStatus textual convention."

GROUP   lesRdGroup

DESCRIPTION

"This group is mandatory only for those

LESs that support elan802.5."

::= { lesMIBCompliances 1 }

-- Units of Conformance

lesCConfGroup    OBJECT-GROUP

OBJECTS { lesConfNextId,

lesAtmAddrSpec,

lesAtmAddrMask,

lesAtmAddrActual,

lesElanName,

lesLanType,

lesLastChange,

lesControlTimeOut,

lesMaxFrameSize,

lesVccRowStatus,

lesOperStatus,

lesAdminStatus,

lesRowStatus,

lesBusAddress,

lesLeArpLecId,

lesLeArpAtmAddr,

lesLeArpEntryType,

lesLeArpRowStatus,

lesLecTableLastChange,

lesLecAtmIfIndex,

lesLecProxy,

lesLecAtmAddr,

lesLecId,

lesLecCtlDirectVpi,

lesLecCtlDirectVci,

lesLecLastChange,

lesLecRowStatus,

lesLecState

}

STATUS     current

DESCRIPTION

"A collection of objects providing configuration

information about the LAN Emulation Services."

::= { lesMIBGroups 1 }

lesRdGroup    OBJECT-GROUP

OBJECTS {

lesLeArpRdLecId,

lesLeArpRdAtmAddr,

lesLeArpRdEntryType,

lesLeArpRdRowStatus }

STATUS     current

DESCRIPTION

"A group of objects used for 802.5

ATM LAN Emulation management only."

::= { lesMIBGroups 2 }

lesCStatGroup    OBJECT-GROUP

OBJECTS {

lesStatJoinOk,

lesStatInBadPkts,

lesStatOutRegFails,

lesStatVerNotSup,

lesStatInvalidReqParam,

lesStatDupLanDest,

lesStatDupAtmAddr,

lesStatInsRes,

lesStatAccDenied,

lesStatInvalidReqId,

lesStatInvalidLanDest,

lesStatInvalidAtmAddr,

lesStatLeArpIn,

lesStatLeArpFwd

}

STATUS   current

DESCRIPTION

"A collection of objects providing

monitoring information about the

LES."

::= { lesMIBGroups 3 }

lesLecCStatGroup  OBJECT-GROUP

OBJECTS {

lesLecRecvs,

lesLecSends,

lesLecInRegReq,

lesLecInUnReg,

lesLecInLeArpUcast,

lesLecInLeArpBcast,

lesLecInLeArpResp,

lesLecInNArp

}

STATUS    current

DESCRIPTION

"A collection of objects providing

monitoring information about the

LEC to/from LES traffic."

::= { lesMIBGroups 4 }

lesFaultCGroup  OBJECT-GROUP

OBJECTS {

lesErrCtlAdminStatus,

lesErrCtlOperStatus,

lesErrCtlClearLog,

lesErrCtlMaxEntries,

lesErrCtlLastEntry,

lesErrLogAtmAddr,

lesErrLogErrCode,

lesErrLogTime

}

STATUS   current

DESCRIPTION

"A collection of objects providing

fault management for the LES."

::= { lesMIBGroups 5 }

END

LAN-EMULATION-BUS-MIB DEFINITIONS ::= BEGIN

IMPORTS

MODULE-IDENTITY, OBJECT-TYPE,

Counter32, Integer32         FROM SNMPv2-SMI

MODULE-COMPLIANCE, OBJECT-GROUP FROM SNMPv2-CONF

TEXTUAL-CONVENTION, RowStatus, DisplayString,

TimeStamp        FROM SNMPv2-TC

AtmLaneAddress,

VpiInteger,

VciInteger,

atmfLanEmulation

FROM LAN-EMULATION-CLIENT-MIB

IfIndexOrZero, AtmLaneMask

FROM LAN-EMULATION-ELAN-MIB;

busMIB MODULE-IDENTITY

LAST-UPDATED "96021212009507051200Z"

ORGANIZATION "ATM Forum LAN Emulation Sub-Working Group"

CONTACT-INFO

"

The ATM Forum

303 Vintage Park Drive

Foster City, CA  94404

United States of America

Tel: 415-578-6860

2570 West El Camino Real, Ste 304,

Mountain View, CA 94040-1313

E-mail: info@atmforum.com"

DESCRIPTION

" The MIB module for the management of LANE broadcast and

known servers. This MIB should be used in conjunction

with the ELAN and LES MIBs."

::= { atmfLanEmulation 4atmfLanEmulation 4 }

--

--    Textual Conventions

--

BusLocalIndex ::= TEXTUAL-CONVENTION

STATUS     current

DESCRIPTION

"An unique number identifying an

BUS.  This number is only

used locally by the agent to

distinguish between BUS."

SYNTAX     Integer32

BusErrLogIndexType ::= TEXTUAL-CONVENTION

STATUS     current

DESCRIPTION

"An arbitrary integer used in identifying

an erro log associated with a BUS."

SYNTAX     Integer32(1..2147483647)

-- This MIB module consists of the following groups:

--

--  (1) BUS Conf Group

--      (a) BUS table

--      (b) BUS-VCC table

--      (c) BUS-LEC table

--

--  (2) Stat Group

--      (d) BUS Stat table

--      (e) BUS-LEC Statistics table

--

--  (3) Fault Management Group

--      (a) error control table

--      (b) error log table

busConfGroup  OBJECT IDENTIFIER ::= { busMIB 1 }

busStatGroup  OBJECT IDENTIFIER ::= { busMIB 2 }

busFaultGroup OBJECT IDENTIFIER ::= { busMIB 3 }

--

--  (1) BUS Conf Group

--  (a) BUS table

--

busConfNextId  OBJECT-TYPE

SYNTAX     BusLocalIndex

MAX-ACCESS read-only

STATUS     current

DESCRIPTION

"The next available BUS index.  The

value of this object can be used as

the index by the network manager to

create an entry in the busConfTable."

::= { busConfGroup 1 }

busConfTable   OBJECT-TYPE

SYNTAX     SEQUENCE OF BusConfEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"This table contains all LAN Emulation

Broadcast and Unknown Servers (BUS) this

agent manages.  The BUS handles data sent

by an LE Client to the broadcast MAC

address, all multicast traffic, and initial unicast

frames which are sent by a LEC before the data

direct target ATM address has been resolved.

There can be multiple BUSs per ELAN, but a

BUS can service only one ELAN."

::= { busConfGroup 2 }

busConfEntry  OBJECT-TYPE

SYNTAX     BusConfEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"Each entry in this table represents a

BUS.  The parameters in each entry apply

to one emulated LAN served by one BUS.

Object busRowStatus is required during

row creation and deletion.  Object busElanName

is used to indicate the ELAN this BUS

is servicing and is used to cross reference

tables defined in the LAN Emulation Server MIB.

Note that objects busAtmAddrSpec and busAtmAddrMask

are used to configure the ATM address of a BUS.

The BUS typically derives it's ATM address

from the switch or the network and the actual

ATM address used is indicated in the object

busAtmAddrActual."

INDEX      { busConfIndex }

::= { busConfTable 1 }

BusConfEntry ::= SEQUENCE {

busConfIndex                 BusLocalIndex,

busConfAtmAddrSpec           AtmLaneAddress,

busConfAtmAddrMask           AtmLaneMask,

busConfAtmAddrActual           AtmLaneAddress,

busConfElanName              DisplayString,

busConfLastChange            TimeStamp,

busConfMaxFrameAge           INTEGER,

busConfOperStatus            INTEGER,

busConfAdminStatus           INTEGER,

busConfRowStatus             RowStatus

}

busConfIndex OBJECT-TYPE

SYNTAX     BusLocalIndex

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"A value which uniquely identifies a

conceptual row in the busConfTable.

If the conceptual row identified by this value

of busConfIndex is recreated following an agent

restart, the same value of busConfIndex must be

used to identify the recreated row."

::= { busConfEntry 1 }

busConfAtmAddrSpec OBJECT-TYPE

SYNTAX     AtmLaneAddress

MAX-ACCESS read-create

STATUS     current

DESCRIPTION

"An ATM  address specified by  the

network or local management that,

with the ATM address mask, determines

a  portion of  the  ATM address  that

the  BUS on the designated ATM interface

will use  to derive the actual ATM

address from the network or ILMI.  The derived

ATM address is specified in the object

busAtmAddrActual, which is used to

receive multicast or broadcast traffic."

::= { busConfEntry 2 }

busConfAtmAddrMask OBJECT-TYPE

SYNTAX     AtmLaneMask

MAX-ACCESS read-create

STATUS     current

DESCRIPTION

"The ATM address mask associated with

the object busAtmAddrSpec.  The value

of the mask is an ATM address with

the don't care portion set to zero

and the valid ATM address portion set to one."

DEFVAL { 'FFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFF'H }

::= { busConfEntry 3 }

busConfAtmAddrActual OBJECT-TYPE

SYNTAX     AtmLaneAddress

MAX-ACCESS read-only

STATUS     current

DESCRIPTION

" The resultant ATM address  in use by  the BUSLES.  This

object is a product of the specified ATM address, mask

and  interaction  with  the network.  This object is

created by the agent."

::= { busConfEntry 4 }

busConfElanName OBJECT-TYPE

SYNTAX     DisplayString (SIZE (0..32))

MAX-ACCESS read-create

STATUS     current

DESCRIPTION

"The name of the ELAN this BUS is providing service to."

::= { busConfEntry 5 }

busConfLastChange OBJECT-TYPE

SYNTAX     TimeStamp

MAX-ACCESS read-only

STATUS     current

DESCRIPTION

"The  value of the sysUpTime  when  this BUS

has entered the state indicated by the

object busConfOperStatus."

::= { busConfEntry 6 }

busConfMaxFrameAge  OBJECT-TYPE

SYNTAX       INTEGER (1..4)

MAX-ACCESS   read-create

STATUS       current

DESCRIPTION

"Time out period for a frame that has been

received but not been transmitted by BUS

to all relevant Multicast Send VCCs or

Multicast Forward VCCs."

REFERENCE

"LAN Emulation Over ATM Specification -

version 1.0. S5."

DEFVAL { 1 }

::= { busConfEntry 7 }

busConfOperStatus OBJECT-TYPE

SYNTAX     INTEGER {

other(1),       -- unknown state

up(2),          -- BUS is up and running

down(3)         -- BUS is down or not available

}

MAX-ACCESS read-only

STATUS     current

DESCRIPTION

"The operational state of this BUS entry.

When in 'up' state the BUS will forward

LEC traffic.  Any other state the

BUS is not available for service and may

release all the existing VCCs and refuse

service to all clients."

::= { busConfEntry 8 }

busConfAdminStatus OBJECT-TYPE

SYNTAX     INTEGER {

up(2),          -- BUS is up and running

down(3)         -- BUS is down or not available

}

MAX-ACCESS read-create

STATUS     current

DESCRIPTION

"  The  desired  state   of  the  designated   BUS  as

prescribed by the operator. The  actions of the  agent

will, if at  all  possible, eventually  result  in the

desired state being  reflected in  the busOperStatus."

DEFVAL     { up }

::= { busConfEntry 9 }

busConfRowStatus OBJECT-TYPE

SYNTAX     RowStatus

MAX-ACCESS read-create

STATUS     current

DESCRIPTION

"This object is used to create or

delete entries in the buselanConfTable."

REFERENCE "RFC 1443, [10] Textual Conventions

for version 2 of the Simple Network Management

Protocol (SNMPv2)."

::= { busConfEntry 10 }

--

--  (b) BUS VCC table

--

busVccTable     OBJECT-TYPE

SYNTAX      SEQUENCE OF BusVccEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

"This table contains all the Multicast Forward

VCCs used by the BUS to forward multicast traffic

to the participating LECs.  The Multicast Forward

VCC can either be point-to-point or point-to-

multipoint calls.  This table is read only if

SVCs are used and writable if PVCs are used."

::= { busConfGroup 3 }

busVccEntry      OBJECT-TYPE

SYNTAX       BusVccEntry

MAX-ACCESS   not-accessible

STATUS       current

DESCRIPTION

"Each entry in this table represents a

BUS with it's Multicast Forward VCC of the BUS."

INDEX { busConfIndex, busVccAtmIfIndex,

busVccMtFwdVpi, busVccMtFwdVci }

::= { busVccTable 1 }

BusVccEntry ::=

SEQUENCE {

busVccAtmIfIndex

IfIndexOrZero,

busVccMtFwdVpi

VpiInteger,

busVccMtFwdVci

VciInteger,

busVccRowStatus

RowStatus

}

busVccAtmIfIndex  OBJECT-TYPE

SYNTAX     IfIndexOrZero

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"The ATM interface which the Multicast

Forward VCC is running on.

This value must match an existing

value  in the   ifTable.

The value of this object is set

to zero when the ATM interface is

undefined."

::= { busVccEntry 1 }

busVccMtFwdVpi    OBJECT-TYPE

SYNTAX     VpiInteger

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"The VPI value of the Multicast

Forward VCC.  The object

busVccAtmIfIndex, busVccMtFwdVci

and the value of this object uniquely

identfies a VCC within a ATM host."

::= { busVccEntry 2 }

busVccMtFwdVci    OBJECT-TYPE

SYNTAX     VciInteger

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"The VCI value of the Multicast

Forward VCC.  The object

busVccAtmIfIndex, busVccMtFwdVpi

and the value of this object uniquely

identfies a VCC within a ATM host."

::= { busVccEntry 3 }

busVccRowStatus   OBJECT-TYPE

SYNTAX     RowStatus

MAX-ACCESS read-create

STATUS     current

DESCRIPTION

"This object is used to create or

delete entries in the buselanConfTable."

REFERENCE "RFC 1443, [10] Textual Conventions

for version 2 of the Simple Network Management

Protocol (SNMPv2)."

::= { busVccEntry 4 }

--

--  (b) BUS - LEC table

--

busLecTableLastChange OBJECT-TYPE

SYNTAX     TimeStamp

MAX-ACCESS read-only

STATUS     current

DESCRIPTION

"The value of sysUpTime when an entry of the

busLecTable was created/deleted."

::= { busConfGroup 4 }

busLecTable    OBJECT-TYPE

SYNTAX     SEQUENCE OF BusLecEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

" This table contains the BUS and the

actual LECs being serviced by the BUS.

It can be used as the actual mapping

between BUS and LEC.

This table provides information

for Multicast send VCCs

between BUS and clients.  Objects

busLecMcastSendAtmIfIndex, busLecMcastSendVpi,

and busLecMcstSendVci can only be modified

if PVC is used."

::= { busConfGroup 54 }

busLecEntry OBJECT-TYPE

SYNTAX       BusLecEntry

MAX-ACCESS   not-accessible

STATUS       current

DESCRIPTION

"Each entry represents a BUS to LEC

mapping."

INDEX { busConfIndex , busLecAtmAddr }

::= { busLecTable 1 }

BusLecEntry::=

SEQUENCE {

busLecAtmAddr

AtmLaneAddress,

busLecMcastSendAtmIfIndex

IfIndexOrZero,

busLecMcastSendVpi

VpiInteger,

busLecMcastSendVci

VciInteger,

busLecRowStatus

RowStatus

}

busLecAtmAddr     OBJECT-TYPE

SYNTAX        AtmLaneAddress

MAX-ACCESS    not-accessible

STATUS        current

DESCRIPTION

"The ATM address of the LEC.  This

is the primary ATM address of the LEC."

::= { busLecEntry 1 }

busLecMcastSendAtmIfIndex  OBJECT-TYPE

SYNTAX     IfIndexOrZero

MAX-ACCESS read-create

STATUS     current

DESCRIPTION

"The  ATM  interface  index this BUS uses for

Multicast Send traffic.  The value of this

object has to exist in the ifTable in MIB II

unless an internal connection is used.  When

an internal connection is used, this object

is set to zero."

::= { busLecEntry 2 }

busLecMcastSendVpi        OBJECT-TYPE

SYNTAX     VpiInteger

MAX-ACCESS read-create

STATUS     current

DESCRIPTION

" The   virtual  path  identifier used to receive

multicast traffic by this BUS."

::= { busLecEntry 4 }

busLecMcastSendVci        OBJECT-TYPE

SYNTAX     VciInteger

MAX-ACCESS read-create

STATUS     current

DESCRIPTION

" The   virtual  channel  identifier used to receive

multicast traffic by this BUS."

::= { busLecEntry 5 }

busLecRowStatus OBJECT-TYPE

SYNTAX     RowStatus

MAX-ACCESS read-create

STATUS     current

DESCRIPTION

" This object provides a way for the network manager

to selectively remove a LE Client from the designated

BUS.  Or in a system where PVCs are used, this table

is used to create Multicast Send VCCs between BUS

and LEC."

::= { busLecEntry 6 }

--

--  (2) BUS Stat Group

--

--  (a) BUS Statistic table

--

busStatTable    OBJECT-TYPE

SYNTAX      SEQUENCE OF BusStatEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

"This table contains all counters the

BUS maintain.  This table is an extention

to the busConfTable."

::= { busStatGroup 1 }

busStatEntry OBJECT-TYPE

SYNTAX     BusStatEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"Each entry in this table contains a

BUS and its counters."

AUGMENTS { busConfEntry }

::= { busStatTable 1 }

BusStatEntry ::= SEQUENCE {

busStatInDiscards		Counter32,

busStatInOctets                  Counter32,

busStatInUcastFrms               Counter32,

busStatInMcastFrms              Counter32,

busStatFrmTimeOuts              Counter32,

busStatMcastSendRefused                Counter32,

busStatMcastFwdFailure                Counter32

}

busStatInDiscards OBJECT-TYPE

SYNTAX     Counter32

MAX-ACCESS read-only

STATUS     current

DESCRIPTION

"  The number of frames discarded due to resource

error."

::= { busStatEntry 1 }

busStatInOctets OBJECT-TYPE

SYNTAX     Counter32

MAX-ACCESS read-only

STATUS     current

DESCRIPTION

"  The number of  octets that  this  BUS has received

since its initialization."

::= { busStatEntry 2 }

busStatInUcastFrms OBJECT-TYPE

SYNTAX     Counter32

MAX-ACCESS read-only

STATUS     current

DESCRIPTION

" The number  of  frames that  the BUS  has  received

which were  unicast data frames  andincluding all control

frames (i.e. they were flooded from the client)."

::= { busStatEntry 3 }

busStatInMcastFrms OBJECT-TYPE

SYNTAX     Counter32

MAX-ACCESS read-only

STATUS     current

DESCRIPTION

"  The number of  frames  that  the BUS has  received

which were multicast frames."

::= { busStatEntry 4 }

busStatFrmTimeOuts OBJECT-TYPE

SYNTAX     Counter32

MAX-ACCESS read-only

STATUS     current

DESCRIPTION

" The number of frames dropped by

the BUS due to time out."

::= { busStatEntry 5 }

busStatMcastSendRefused OBJECT-TYPE

SYNTAX     Counter32

MAX-ACCESS read-only

STATUS     current

DESCRIPTION

"  The number of  multicast send VCC request

the BUS has  refused for any reason from

clientsconnection setup attempts to the BUS which were refused."

::= { busStatEntry 6 }

busStatMcastFwdFailure OBJECT-TYPE

SYNTAX     Counter32

MAX-ACCESS read-only

STATUS     current

DESCRIPTION

"  The number of  multicast forward VCC requests

has refused by the LEC for any reasons from this BUSconnection setup attempts from the BUS which were unsuccessful

for any reason."

::= { busStatEntry 7 }

--

--  (b) BUS - LEC statistics table

--

busLecStatTable    OBJECT-TYPE

SYNTAX      SEQUENCE OF BusLecStatEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

"This table contains all LEC counters

the BUS maintains.  This table can also

be used to retrieve all LECs a BUS

is providing service to."

::= { busStatGroup 2 }

busLecStatEntry     OBJECT-TYPE

SYNTAX       BusLecStatEntry

MAX-ACCESS   not-accessible

STATUS       current

DESCRIPTION

"Each entry in this table represents a

LEC and its counters."

AUGMENTS { busLecEntry }

::= { busLecStatTable 1 }

BusLecStatEntry ::=

SEQUENCE {

busLecRecvs         Counter32,

busLecForwards         Counter32,

busLecDiscards         Counter32

}

busLecRecvs     OBJECT-TYPE

SYNTAX      Counter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"Number of Multicast, Broadcast and

Unknown Forward requests received by

the BUS from this LEC."

::= { busLecStatEntry 1 }

busLecForwards  OBJECT-TYPE

SYNTAX      Counter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"Number of Multicast, Broadcast and

Unkown Forward requests forwarded by

the BUS from this LEC.  The value

of this object indicate how many requests

have been forwarded by the BUS."

::= { busLecStatEntry 2 }

busLecDiscards  OBJECT-TYPE

SYNTAX      Counter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"Number of Multicast, Broadcast and

Unkown Forward requests discarded by

the BUS from this LEC.  The value

of this object indicate how many requests

have been discarded by the BUS."

::= { busLecStatEntry 3 }

--

-- BUS Fault Mangement Group

--   (a) BUS Error Control Table

--   (b) BUS Error Log Table

--

busErrCtlTable OBJECT-TYPE

SYNTAX     SEQUENCE OF BusErrCtlEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"This table contains error log control

information of all BUS instances.

This table is an extention to the

busConfTable.  It is used to enable

or disable error logs for a particular

BUS entry."

::= { busFaultGroup 1 }

busErrCtlEntry OBJECT-TYPE

SYNTAX     BusErrCtlEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"Each entry represents a BUS entry

in the busConfTable."

AUGMENTS { busConfEntry }

::= { busErrCtlTable 1 }

BusErrCtlEntry ::=

SEQUENCE {

busErrCtlAdminStatus

INTEGER,

busErrCtlOperStatus

INTEGER,

busErrCtlClearLog

INTEGER,

busErrCtlMaxEntries

INTEGER,

busErrCtlLastEntry

BusErrLogIndexType

}

busErrCtlAdminStatus     OBJECT-TYPE

SYNTAX        INTEGER {

enable(1),        -- enable error log

disable(2)        -- disable error log

}

MAX-ACCESS    read-write

STATUS        current

DESCRIPTION

"This object is used to enable/disable error

logging for the BUS."

::= { busErrCtlEntry 1 }

busErrCtlOperStatus            OBJECT-TYPE

SYNTAX        INTEGER {

other(1),        -- not specified

active(2),        -- error logging

outOfRes(3),        -- Out of buffer error

failed(4),        -- failed to start

-- error log for reasons

-- other than out of

-- resources

disabled(5)     -- error loggin was disabled

}

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"This object is used to indicate

the result of a set operation to the

object busErrCtlAdminStatus.

If the error log was successfully

started, it is in active(2) mode.

Otherwise, it is set to either

outOfRes(3) or failed(4) for

the respective reasons."

::= { busErrCtlEntry 2 }

busErrCtlClearLog            OBJECT-TYPE

SYNTAX        INTEGER {

noOp(1),        -- read only value

clear(2)        -- clear the error log associated

-- with this BUS entry

}

MAX-ACCESS        read-write

STATUS                current

DESCRIPTION

"This object is used to clear the error log

entries associated with this BUS."

::= { busErrCtlEntry 3 }

busErrCtlMaxEntries        OBJECT-TYPE

SYNTAX        INTEGER ( 1..65535 )

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"The maximum entries of the error

log a BUS can support."

::= { busErrCtlEntry 4 }

busErrCtlLastEntry        OBJECT-TYPE

SYNTAX        BusErrLogIndexType

MAX-ACCESS    read-write

STATUS        current

DESCRIPTION

"The index to the last entry in the error

log table for this BUS."

::= { busErrCtlEntry 5 }

--

--

--   BUS error log table

--

busErrLogTable OBJECT-TYPE

SYNTAX     SEQUENCE OF BusErrLogEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"This table contains error logs

of the BUS instances enabled

in the busErrCtlTable.  This table

is indexed by the BUS instance

index and an arbitrary integer

uniquely identifies an error

log."

::= { busFaultGroup 2 }

busErrLogEntry OBJECT-TYPE

SYNTAX     BusErrLogEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"Each entry represents a JOIN or REGISTER that

was rejected due to an erroran error detected by the BUS."

INDEX { busConfIndex, busErrLogIndex }

::= { busErrLogTable 1 }

BusErrLogEntry ::=

SEQUENCE {

busErrLogIndex

BusErrLogIndexType,

busErrLogAtmAddr

AtmLaneAddress,

busErrLogErrCode

INTEGER,

busErrLogTime

TimeStamp

}

busErrLogIndex     OBJECT-TYPE

SYNTAX          BusErrLogIndexType

MAX-ACCESS      not-accessible

STATUS          current

DESCRIPTION

"An arbitrary integer which uniquely

identifies an error log entry. The first

entry after reset or clearing the error

log is an assigned value (2^32-1).  Succeding

entries are assigned with descending values

consecutively.  Entries after 1 are discarded.This

number ranges from 1 to the value of

the object busErrCtlMaxEntries times

number of BUS with the error log capability

enabled.  The enabling/disabling of

the error log capability is done in

the busErrCtlTable."

::= { busErrLogEntry 1 }

busErrLogAtmAddr OBJECT-TYPE

SYNTAX        AtmLaneAddress

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"The primary ATM address of the requester

which sends the JOIN or REGISTER request

and causes the error to occur LE Client on whose Multicast

Send VCC the error occured.

The corresponding error code is

specified in the object busErrLogErrCode."

::= { busErrLogEntry 2 }

busErrLogErrCode OBJECT-TYPE

SYNTAX        INTEGER {

outOfRes(1),     -- Out of resources error

badCtlFrame(2),  -- Malformed control frame

badDataFrame(3), -- Malformed data frame, i.e.

wrongSize(4),    -- the frame received by the

-- BUS is either too big or too small

other(45)         -- any other errors

}

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"The Error code which indicates the

cause of the error triggered by the

JOIN or REGISTER request sent by the

requester indicated by the value of

the object busErrLogAtmAddr."

::= { busErrLogEntry 3 }

busErrLogTime    OBJECT-TYPE

SYNTAX        TimeStamp

MAX-ACCESS    read-only

STATUS        current

DESCRIPTION

"The sysUpTime when this entry was logged by

the BUS."

::= { busErrLogEntry 4 }

busMIBConformance OBJECT IDENTIFIER ::= { busMIB 4 }

busMIBGroups OBJECT IDENTIFIER ::= { busMIBConformance 1 }

busMIBCompliances OBJECT IDENTIFIER ::= { busMIBConformance 2 }

busMIBCompliance MODULE-COMPLIANCE

STATUS current

DESCRIPTION

" The compliance statement for SNMP entities that support

the ATM LAN Emulation BUS MIB."

MODULE -- this module

MANDATORY-GROUPS    { busCConfGroup, busCStatGroup, busCFaultGroup }

OBJECT busConfAtmAddrSpec

MIN-ACCESS read-only

DESCRIPTION

" Those implementations that do not support seperately

configured broadcast/unknown and LE servers are note required to

provide write access to the busConfAtmAddrSpec object."

OBJECT busConfAtmAddrMask

MIN-ACCESS read-only

DESCRIPTION

" Those implementations that do not support seperately

configured broadcast/unknown and LE servers are note required to

provide write access to the busConfAtmAddrMask object."

OBJECT busConfElanName

MIN-ACCESS read-only

DESCRIPTION

" Those implementations that do not support seperately

configured broadcast/unknown and LE servers are note required to

provide write access to the busConfElanName object."

OBJECT busConfAdminStatus

MIN-ACCESS read-only

DESCRIPTION

" Those implementations that do not support seperately

configured broadcast/unknown and LE servers are note required to

provide write access to the busConfAdminStatus object."

OBJECT busConfRowStatus

MIN-ACCESS read-only

DESCRIPTION

" Those implementations that do not support seperately

configured broadcast/unknown and LE servers are note required to

provide write access to the busConfRowStatus object."

OBJECT busVccRowStatus

MIN-ACCESS read-only

DESCRIPTION

" Implementations that do not support broadcast/unknown

servers over PVCs are not required to allow write/create

access to the busVccRowStatus object."

OBJECT busLecMcastSendAtmIfIndex

MIN-ACCESS read-only

DESCRIPTION

" Implementations that do not support LECs over PVCs

are note required to allow write/create access to the

busLecMcastSendAtmIfIndex object."

OBJECT busLecMcastSendVpi

MIN-ACCESS read-only

DESCRIPTION

" Implementations that do not support LECs over

PVCs are note required to allow write/create access to

the busLecMcastSendVpi object."

OBJECT busLecMcastSendVci

MIN-ACCESS read-only

DESCRIPTION

" Implementations that do not support LECs over

PVCs are note required to allow write/create access to

the busLecMcastSendVci object."

OBJECT busLecRowStatus

WRITE-SYNTAX INTEGER { destroy(6) }

DESCRIPTION

" Implementations that do not support LECs over

PVCs need only support the destroy enumeration of the

RowStatus textual convention."

GROUP busLecCGroup

DESCRIPTION

"This group is optional."

::= { busMIBCompliances 1 }

-- Units of Conformance

busCConfGroup OBJECT-GROUP

OBJECTS   { busConfNextId,

busConfAtmAddrSpec,

busConfAtmAddrMask,

busConfAtmAddrActual,

busConfElanName,

busConfLastChange,

busConfMaxFrameAge,

busConfOperStatus,

busConfAdminStatus,

busConfRowStatus,

busVccRowStatus,

busLecTableLastChange,

busLecMcastSendAtmIfIndex,

busLecMcastSendVpi,

busLecMcastSendVci,

busLecRowStatus

}

STATUS    current

DESCRIPTION

" A collection of objects for the

managing of BUS operation."

::= { busMIBGroups 1 }

busCStatGroup OBJECT-GROUP

OBJECTS   {

busStatInOctets,

busStatInDiscards,

busStatInUcastFrms,

busStatInMcastFrms,

busStatFrmTimeOuts,

busStatMcastSendRefused,

busStatMcastFwdFailure

}

STATUS    current

DESCRIPTION

" A collection of objects providing information

about BUS statistics."

::= { busMIBGroups 2 }

busCFaultGroup OBJECT-GROUP

OBJECTS   {

busErrLogAtmAddr,

busErrLogErrCode,

busErrLogTime,

busErrCtlAdminStatus,

busErrCtlOperStatus,

busErrCtlClearLog,

busErrCtlMaxEntries,

busErrCtlLastEntry

}

STATUS    current

DESCRIPTION

" A collection of objects providing information

about BUS statistics."

::= { busMIBGroups 3 }

busLecCGroup OBJECT-GROUP

OBJECTS   {

busLecRecvs,

busLecForwards,

busLecDiscards

}

STATUS    current

DESCRIPTION

" A collection of objects providing information

about LEC-BUS statistics."

::= { busMIBGroups 4 }

END