Technical Committee

Auto-configuration of PVCs

AF-NM-0122.000

May, 1999

© 1999 by The ATM Forum.  This specification/document may be reproduced and distributed in whole, but (except as provided in the next sentence) not in part, for internal and informational use only and not for commercial distribution.  Notwithstanding the foregoing sentence, any protocol implementation conformance statements (PICS) or implementation conformance statements (ICS) contained in this specification/document may be separately reproduced and distributed provided that it is reproduced and distributed in whole, but not in part, for uses other than commercial distribution.  All other rights reserved.  Except as expressly stated in this notice, no part of this specification/document may be reproduced or transmitted in any form or by any means, or stored in any information storage and retrieval system, without the prior written permission of The ATM Forum.

The information in this publication is believed to be accurate as of its publication date.  Such information is subject to change without notice and The ATM Forum is not responsible for any errors.  The ATM Forum does not assume any responsibility to update or correct any information in this publication.  Notwithstanding anything to the contrary, neither The ATM Forum nor the publisher make any representation or warranty, expressed or implied, concerning the completeness, accuracy, or applicability of any information contained in this publication.  No liability of any kind shall be assumed by The ATM Forum or the publisher as a result of reliance upon any information contained in this publication.

The receipt or any use of this document or its contents does not in any way create by implication or otherwise:

•	Any express or implied license or right to or under any ATM Forum member company's patent, copyright, trademark or trade secret rights which are or may be associated with the ideas, techniques, concepts or expressions contained herein; nor

•	Any warranty or representation that any ATM Forum member companies will announce any product(s) and/or service(s) related thereto, or if such announcements are made, that such  announced product(s) and/or service(s) embody any or all of the ideas, technologies, or  concepts contained herein; nor

•	Any form of relationship between any ATM Forum member companies and the recipient or user of this document.

Implementation or use of specific ATM standards or recommendations and ATM Forum specifications will be voluntary, and no company shall agree or be obliged to implement them by virtue of participation in The ATM Forum.

The ATM Forum is a non-profit international organization accelerating industry cooperation on ATM technology.  The ATM Forum does not, expressly or otherwise, endorse or promote any specific products or services.

NOTE:  The user's attention is called to the possibility that implementation of the ATM interoperability specification contained herein may require use of an invention covered by patent rights held by ATM Forum Member companies or others.  By publication of this ATM interoperability specification, no position is taken by The ATM Forum with respect to validity of any patent claims or of any patent rights related thereto or the ability to obtain the license to use such rights.  ATM Forum Member companies agree to grant licenses under the relevant patents they own on reasonable and nondiscriminatory terms and conditions to applicants desiring to obtain such a license.  For additional information contact:

The ATM Forum

Worldwide Headquarters

2570 West El Camino Real, Suite 304

Mountain View, CA 94040-1313

Tel:	   +1-650-949-6700

Fax:	+1-650-949-6705

Editors:	Kathleen Jarosinski

Andrew J. Mayer, Ph.D.

Table of Contents

1.	Introduction	1

2.	Overview	1

3.	Auto-Configuration Requirements	2

3.1	Service Type (R)	2

3.2	Connection Information (R)	2

3.3	AAL Encapsulation (O)	2

3.4	Traffic Management Class and Parameters (R)	2

3.5	UNI Parameters (R)	3

4.	ILMI MIB Support for Auto-Configuration Requirements	4

4.1	Service Type	4

4.2	Connection Information	4

4.3	AAL Encapsulation	4

4.4	Traffic Management Class and Parameters	5

4.5	UNI Parameters	5

5.	Extensions to the ILMI SNMP MIB	6

# Introduction

This document defines the requirements and extensions to the SNMP MIB required for using ILMI to auto-configure ATM permanent virtual circuits (PVCs) in remote CPE. The ILMI operates between the network (e.g., Digital Subscriber Loop Access Mux (DSLAM)) and the ATM Network Termination at the customer premises (e.g., ADSL modem, a.k.a. ATU-R). Auto-configuration will allow the network to use the ILMI to send ATM PVC information and characteristics to the ATM Network Termination. This information includes the PVC VPI/VCI, AAL, traffic type and parameters. Also, in the event there are multiple PVCs terminated at ATM Network Termination with different QoS, ILMI will provide enough distinguishing information, so that the appropriate ATM PVC is automatically selected.

# Overview

Currently, when a service requiring remote configuration (e.g., ADSL) is sold to a customer, the carrier must dispatch a service technician to the customer’s house to configure the CPE (e.g., ATU-R), or depend on the customer to do it himself. This creates a potential frustrating situation for the customer who is now required to understand ATM. It also creates a security risk situation for theft of service, should a user with enough familiarity with the network provide valid connection identifiers which are not assigned to him.

The current ILMI 4.0 specification provides network address registration for ATM SVCs. This feature enables an ATM end station to provide its address to the network. The extensions to the existing SNMP MIB defined in this document will allow the ILMI to be used to carry information regarding the configuration ATM specific aspects of the remote CPE.   Figure 1 provides an example of auto-configuration using ILMI for ADSL.

Figure 1: Example of Auto-configuration for ADSL using ILMI

# Auto-Configuration Requirements

## Service Type (R)

A service type shall be defined for the Auto-Configuration table, which is present on the network side of the ATM UNI. This table, implemented by the IME on the network side of the ATM UNI, contains all of the services that are available to the user side IME indexed by the service. This information contains the service specific attributes associated with the different ATM PVCs such as the name of the service provided by the PVC, the service category (CBR, rt-VBR, nrt-VBR, UBR, ABR, GFR) as defined by TM 4.0, and the conformance definition (CBR.1, VBR.1, VBR.2, VBR.3, UBR.1, UBR.2, ABR, GFR.1, GFR.2) as defined by TM 4.0.

## Connection Information (R)

Each PVC must be identified by a unique VPI/VCI.

The connection shall be associated with service type information.

Optionally, the connection may be named.

## AAL Encapsulation (O)

The ATM Adaptation Layer (AAL) Type and Parameters may be specified for the endpoint of the VCC. Valid values of the AAL Type are none, AAL1, AAL2, AAL3/4, and AAL5. If the value of this field is none, then the AAL parameters are not specified.

## Traffic Management Class and Parameters (R)

The traffic management class and its associated parameters shall be specified as follows:

- Constant Bit Rate (CBR)

- Peak Cell Rate (PCR)

- Cell Delay Variation Tolerance (CDVT)

- Variable Bit Rate – (VBR)

- Peak Cell Rate (PCR)

- Maximum Burst Size (MBS)

- Sustained Cell Rate (SCR)

- Cell Delay Variation Tolerance (CDVT)

- Available Bit Rate (ABR)

- Peak Cell Rate (PCR)

- Cell Delay Variation Tolerance (CDVT)

- Minimum Cell Rate (MCR)

- Initial Cell Rate (ICR)

- Number of data cells per forward RM-cell (Nrm)

- Maximum time between forward RM-cells (Trm)

- Cutoff Decrease Factor (CDF)

- Rate Increment Factor (RIF)

- Rate Decrease Factor (RDF)

- ACR Decrease Time Factor (ADTF)

- RM-cells before Cutoff (CRM)

- Unspecified Bit Rate (UBR)

- Peak Cell Rate (PCR)

- Cell Delay Variation Tolerance (CDVT)

- Guaranteed Frame Rate (GFR)

- Peak Cell Rate (PCR)

- Minimum Cell Rate (MCR)

- Maximum Burst Size (MBS)

- Maximum Frame Size (MFS)

- Cell Delay Variation Tolerance (CDVT)

## UNI Parameters (R)

There shall be an indication of whether or not SVC service is supported at the UNI.

# ILMI MIB Support for Auto-Configuration Requirements

## Service Type

Support for Service Type information is provided by the atmfAtmServiceTypeTable, a new extension to the ILMI MIB.  There is one entry in the atmfAtmServiceTypeTable per Service Type.

Service Type information includes:

- Service Provider Name

- Service Type Name

- Service Type Sub-name (if any)

- Client Layer Protocol Name (if any)  (e.g., PPP, MPEG-2, etc.)

- TM 4.0 Service Category (CBR, rt-VBR, nrt-VBR, UBR, ABR, GFR)

- TM 4.0 Conformance Definition (CBR.1, VBR.1, VBR.2, VBR.3, UBR.1, UBR.2, ABR, GFR.1, GFR.2)

## Connection Information

Support for Connection is provided by the atmfAtmServiceConnInfoTable, a new extension to the ILMI MIB.  There is one entry in the atmfAtmServiceConnInfoTable per customer service connection.

Service Connection Information includes:

- ATM Port

- VP or VC connection indicator

- Connection VPI

- Connection VCI

- Association to Service Type

- Optional connection name

Specific information about each PVC may be found in the ILMI 4.0 atmfVpcTable for VP connections or the ILMI 4.0 atmfVccTable for VC connections.

Information about signaling support on the interface may be found in the ILMI 4.0 atmfATMLayerTable

## AAL Encapsulation

Support for the AAL Encapsulation Type is provided by additions in the atmfAtmServiceConnInfoTable, a new extension to the ILMI MIB.

To support AAL Encapsulation the following is included in the atmfAtmServiceConnInfoTable:

- AAL Type

- AAL Profile Assocation

Specific AAL parameters are provided by the atmfAAL1ProfileTable, atmfAAL34ProfileTable, and atmfAAL5ProfileTable.

AAL 1 Profile information inlcudes:

- AAL1 Subtype (are NULL, Voice-band based on 64 KBPS, Circuit Emulation (synchronous), Circuit Emulation (asynchronous), High- quality Audio, and Video)

- CBR Rate

- Clock Recovery Type (Synchronous, Asynchronous-SRTS, or Asynchronous-Adaptive Clock Recovery)

- Forward Error Correction Type (no FEC, FEC for Loss Sensitive Signal Transport, or FEC for Delay Sensitive Signal Transport)

- Structure Data Transfer (A value of TRUE means SDT has been selected.  This attribute value can be set to TRUE only when the Forward Error Correction Type attribute is no FEC)

- Partially Filled Cells (identifies the number of leading octets in use)

- Cell Loss Integration Period (represents the time in milliseconds for the cell loss integration period)

AAL 3/4 Profile information inlcudes:

- Max CPCS SDU Size Forward

- Max CPCS SDU Size Backward

- MID Range Low

- MID Range High

- AAL Mode (message mode or stream mode, assured or unassured)

- SSCS Type (NULL, Data SSCS based on SSCOP (assured operation), Data SSCS based on SSCOP (non-assured operation), or Frame Relay SSCS)

AAL 5 Profile information inlcudes:

- Max CPCS SDU Size Forward

- Max CPCS SDU Size Backward

- AAL Mode (message mode or stream mode, assured or unassured)

- SSCS Type (NULL, Data SSCS based on SSCOP (assured operation), Data SSCS based on SSCOP (non-assured operation), or Frame Relay SSCS)

## Traffic Management Class and Parameters

In addition to the traffic management class information described in the atmfServiceTypeTable, the ILMI 4.0 MIB provides per connection traffic management class and parameter information in the atmfVpcTable and the atmfVccTable.  Additional traffic parameters for ABR service are provided in the atmfVpcAbrTable and atmfVccAbrTable found in ILMI 4.0.  These tables provide sufficient coverage of the required traffic parameters.  Beyond what has already been described, no new extension to ILMI is necessary for Traffic Management Class and Parameter information.

## UNI Parameters

If SVC service is supported at the UNI, then the value of ILMI 4.0 atmfAtmLayerTable's atmfAtmLayerUniVersion shall indicate the UNI Signalling Version, otherwise it shall be set to unsupported.  The ILMI 4.0 atmfAtmLayerTable's atmfAtmLayerMaxSvpcVpi and atmfAtmLayerMaxSvccVpi values shall equal zero if SVC service is not supported at the UNI.

# Extensions to the ILMI SNMP MIB

ATM-FORUM-AUTO-CONFIG DEFINITIONS ::= BEGIN

------------------------------------------------------------------

-- ATM Forum ILMI Extension for Auto Configuration

--

-- This definition contains the following tables

--        ATM Service Type Table

--        ATM Service Connection Information Table

--        AAL1 Profile Table

--        AAL3/4 Profile Table

--        AAL 5 Profile Table

------------------------------------------------------------------

IMPORTS

DisplayString                        FROM SNMPv2-TC

atmForum, atmForumUni                FROM ATM-FORUM-TC-MIB;

atmfAutoConfigGroup   OBJECT IDENTIFIER ::= { atmForumUni 12 }

------------------------------------------------------------------

-- ATM Forum ILMI Extension for Auto Configuration

-- ATM Service Type

------------------------------------------------------------------

atmfAtmServiceTypeTable OBJECT-TYPE

SYNTAX    SEQUENCE OF    AtmfAtmServiceTypeEntry

MAX-ACCESS     not-accessible

STATUS    current

DESCRIPTION

"The ATM Forum ILMI Auto Configuration Extension ATM

Service Type Information. "

::= { atmfAutoConfigGroup 1 }

atmfAtmServiceTypeEntry OBJECT-TYPE

SYNTAX    AtmfAtmServiceTypeEntry

MAX-ACCESS     not-accessible

STATUS    current

DESCRIPTION

"An entry in the service type table describes the reference

information about a service that may be associated with

individual ATM connections for the purpose of auto-

configuration.  This information describe the name and sub-

name of the service, the client layer protocol using the ATM

service, the TM 4.0 service category, and the TM 4.0

conformance definition."

INDEX          { atmfAtmServiceTypeIndex }

::= { atmfAtmServiceTypeTable 1 }

AtmfAtmServiceTypeEntry ::= SEQUENCE {

atmfAtmServiceTypeIndex            INTEGER,

atmfAtmServiceProviderName         DisplayString,

atmfAtmServiceName                 DisplayString,

atmfAtmServiceSubName              DisplayString,

atmfAtmServiceClient               DisplayString,

atmfAtmServiceTMCategory           INTEGER,

atmfAtmServiceTMConformanceDef     INTEGER

}

atmfAtmServiceTypeIndex OBJECT-TYPE

SYNTAX    INTEGER (1..2147483647)

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"A number between which identifies the entry in the Service

Type Table. "

::= { atmfAtmServiceTypeEntry 1 }

atmfAtmServiceProviderName OBJECT-TYPE

SYNTAX    DisplayString

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"This string identifies the name of the service provider for

the service described in this profile. The value of this

attribute should not set to NULL."

::= { atmfAtmServiceTypeEntry 2 }

atmfAtmServiceName OBJECT-TYPE

SYNTAX    DisplayString

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"This string identifies the name of the service described in

this profile.  The value of this attribute should not be set

to NULL.  "

::= { atmfAtmServiceTypeEntry 3 }

atmfAtmServiceSubName OBJECT-TYPE

SYNTAX    DisplayString

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"This string identifies the sub-name of the service described

in this profile.  A Service may have zero or more sub-names,

each with its own service type profile. "

::= { atmfAtmServiceTypeEntry 4 }

atmfAtmServiceClient OBJECT-TYPE

SYNTAX    DisplayString

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"This string identifies the client protocol of the service

described in this profile.  A Service (sub-service) may have

zero or more described client, each with its own service type

profile. "

::= { atmfAtmServiceTypeEntry 5 }

atmfAtmServiceTMCategory OBJECT-TYPE

SYNTAX    INTEGER {

other  (1),

cbr    (2),

rtVbr  (3),

nrtVbr (4),

abr    (5),

ubr    (6),

gfr    (7)

}

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"The TM 4.0 Service category used for this service type.

Indicates CBR, rt-VBR, nrt-VBR, ABR, UBR, (or GFR) "

::= { atmfAtmServiceTypeEntry 6 }

atmfAtmServiceTMConformanceDef OBJECT-TYPE

SYNTAX    INTEGER {

none (0),

other(1),

cbr1 (2),

vbr1 (3),

vbr2 (4),

vbr3 (5),

ubr1 (6),

ubr2 (7),

abr  (8),

gfr1  (9),

gfr2 (10)

}

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"The TM 4.1 conformance definition used for this service type.

Indicates CBR.1, VBR.1, VBR.2, VBR.3, UBR.1, UBR.2, ABR,

GFR.1, or GFR.2. "

::= { atmfAtmServiceTypeEntry 7 }

------------------------------------------------------------------

-- ATM Forum ILMI Extension for Auto Configuration

-- ATM Service Connection Information

------------------------------------------------------------------

atmfAtmServiceConnInfoTable OBJECT-TYPE

SYNTAX    SEQUENCE OF    AtmfAtmServiceConnInfoEntry

MAX-ACCESS     not-accessible

STATUS    current

DESCRIPTION

"The ATM Forum ILMI Auto Configuration Extension ATM

Service Connection Information. "

::= { atmfAutoConfigGroup 2 }

atmfAtmServiceConnInfoEntry OBJECT-TYPE

SYNTAX    AtmfAtmServiceConnInfoEntry

MAX-ACCESS     not-accessible

STATUS    current

DESCRIPTION

"An entry in the service connection information table

describes the ATM connection that provides a service across

an ATM interface.  The connection is identified by port and

VPI/VCI value.  Information about the connection includes the

connection type (VP or VC, SVC or PVC), and the association of

the connection with a service type.  Specific connection

information, such as traffic descriptors, should be accessed

in the atmfVpc and atmfVcc tables defined in ILMI. "

INDEX          { atmfAtmServicePortIndex, atmfAtmServiceVpi,

atmfAtmServiceVci }

::= { atmfAtmServiceConnInfoTable 1 }

AtmfAtmServiceConnInfoEntry ::= SEQUENCE {

atmfAtmServicePortIndex            INTEGER,

atmfAtmServiceVpi                  INTEGER,

atmfAtmServiceVci                  INTEGER,

atmfAtmServiceSignalId             INTEGER,

atmfAtmServiceConnServiceIndex     INTEGER,

atmfAtmServiceConnName             DisplayString,

atmfAtmServiceConnAALType          INTEGER,

atmfAtmServiceConnAALIndex         INTEGER

}

atmfAtmServicePortIndex OBJECT-TYPE

SYNTAX    INTEGER (0..2147483647)

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"The value of 0 (zero)has the special meaning of identifying

the ATM Interface over which this ILMI message was received. "

::= { atmfAtmServiceConnInfoEntry 1 }

atmfAtmServiceVpi OBJECT-TYPE

SYNTAX    INTEGER (0..255)

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"The VPI value of the ATM service connection at the local ATM

interface. "

::= { atmfAtmServiceConnInfoEntry 2 }

atmfAtmServiceVci OBJECT-TYPE

SYNTAX    INTEGER (0..65535)

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"The VCI value of the ATM service connection at the local ATM

interface. If the atmfAtmServiceSignalId indicates that the

connection is a VP connection, the value of this attribute

shall be set to 0 (zero) and any meaning of this attribute

ignored."

::= { atmfAtmServiceConnInfoEntry 3 }

atmfAtmServiceSignalID OBJECT-TYPE

SYNTAX    INTEGER {

vcCI(0),

vpCI(1)

}

MAX-ACCESS     read-only

STATUS    current

DESCRIPTION

"This attribute represents the characteristic

information of the layer network domain. It may be set to

either VC characteristic information (vcCI) or VP

characteristic information (vpCI)."

::= { atmfAtmServiceConnInfoEntry 4 }

atmfAtmServiceConnServiceIndex OBJECT-TYPE

SYNTAX    INTEGER

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"The value of this object identifies the row in the

atmfAtmServiceTypeTable. This entry represents the

association between an ATM service connection and an ATM

service type profile that describes it. "

::= { atmfAtmServiceConnInfoEntry 5 }

atmfAtmServiceConnName OBJECT-TYPE

SYNTAX    DisplayString

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"This string identifies the name of the service connection.

The value of this attribute may be set to NULL.  "

::= { atmfAtmServiceConnInfoEntry 6 }

atmfAtmServiceConnAALType OBJECT-TYPE

SYNTAX    INTEGER {

none  (0),

aal1  (1),

aal34 (2),

aal5  (3),

other (4),

unknown (5),

aal2  (6)

}

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"Describes the AAL Type of the ATM service connection.  A

value of none indicates that no AAL is used.  The AAL types

include AAL1, AAL 3/4, and AAL 5.  The value other may be a

user-defined AAL type.  The unknown type indicates that the

AAL type cannot be determined. "

::= { atmfAtmServiceConnInfoEntry 7 }

atmfAtmServiceConnAALIndex OBJECT-TYPE

SYNTAX    INTEGER

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"The value of this object identifies the row in the

atmfAAL1ProfileTable for AAL 1 connection, the

atmfAAL34ProfileTable for AAL3/4 connection, and the

atmfAAL5ProfileTable for AAL 5 connections. This entry

represents the association between an ATM service connection

and an ATM Adaptation Layer profile that describes it. "

::= { atmfAtmServiceConnInfoEntry 8 }

------------------------------------------------------------------

-- ATM Forum ILMI Extension for Auto Configuration

-- ATM AAL1 Profile

------------------------------------------------------------------

atmfAAL1ProfileTable OBJECT-TYPE

SYNTAX    SEQUENCE OF    AtmfAAL1ProfileEntry

MAX-ACCESS     not-accessible

STATUS    current

DESCRIPTION

"The ATM Forum ILMI Auto Configuration Extension AAL1

Profile Information. "

::= { atmfAutoConfigGroup 3 }

atmfAAL1ProfileEntry OBJECT-TYPE

SYNTAX    AtmfAAL1ProfileEntry

MAX-ACCESS     not-accessible

STATUS    current

DESCRIPTION

"An entry in the AAL1 Profile table provides data that

describes the AAL1 processing function. "

INDEX          { atmfAAL1ProfileIndex }

::= { atmfAAL1ProfileTable 1 }

AtmfAAL1ProfileEntry ::= SEQUENCE {

atmfAAL1ProfileIndex               INTEGER,

atmfAAL1Subtype                    INTEGER,

atmfAAL1CBRRate                    INTEGER,

atmfAAL1ClkRecoveryType            INTEGER,

atmfAAL1FEC                        INTEGER,

atmfAAL1SDT                        INTEGER,

atmfAAL1PartiallyFilledCells       INTEGER,

atmfAAL1CellLossIntegrPeriod       INTEGER

}

atmfAAL1ProfileIndex OBJECT-TYPE

SYNTAX    INTEGER (1..2147483647)

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"A number between which identifies the entry in the AAL1

Profile Table. "

::= { atmfAAL1ProfileEntry 1 }

atmfAAL1Subtype OBJECT-TYPE

SYNTAX    INTEGER {

null (0),

voiceBand (1),

circuitEmulationSynchronous (2),

circuitEmulationAsynchronous (3),

highQualityAuto (4),

video (5)

}

MAX-ACCESS     read-only

STATUS    current

DESCRIPTION

"This attribute describes AAL type 1 subtype used by the CBR

service application (e.g.  64 KBPS voice band signal

transport, circuit transport). "

::= { atmfAAL1ProfileEntry 2 }

atmfAAL1CBRRate OBJECT-TYPE

SYNTAX    INTEGER

MAX-ACCESS     read-only

STATUS    current

DESCRIPTION

"This attribute describes the rate of the CBR service

supported by the AAL."

::= { atmfAAL1ProfileEntry 3 }

atmfAAL1ClkRecoveryType OBJECT-TYPE

SYNTAX    INTEGER {

synchronous (0),

srts(1),

adaptive (2)

}

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"This attribute indicates whether the clock recovery type is

synchronous, asynchronous-SRTS(Synchronous Residual Time Stamp),

or asynchronous-Adaptive Clock Recovery. "

::= { atmfAAL1ProfileEntry 4 }

atmfAAL1FEC OBJECT-TYPE

SYNTAX    INTEGER {

noFEC (0),

lossSensitiveSignalFEC (1),

delaySensitiveSignalFEC (2)

}

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"This attribute indicates the FEC method: no FEC, FEC for

Loss Sensitive Signal Transport, or FEC for Delay Sensitive

Signal Transport. "

::= { atmfAAL1ProfileEntry 5 }

atmfAAL1SDT OBJECT-TYPE

SYNTAX    INTEGER {

false (0),

true(1)

}

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"This attribute indicates whether Structured Data Transfer

(SDT) has been configured at the AAL.  A value of TRUE means

SDT has been selected.  This attribute value can be set to

TRUE only when the Forward Error Correction Type attribute

equals noFEC. "

::= { atmfAAL1ProfileEntry 6 }

atmfAAL1PartiallyFilledCells OBJECT-TYPE

SYNTAX    INTEGER

MAX-ACCESS     read-only

STATUS    current

DESCRIPTION

"This attribute identifies the number of leading octets in

use."

::= { atmfAAL1ProfileEntry 7 }

atmfAAL1CellLossIntegrPeriod OBJECT-TYPE

SYNTAX    INTEGER

MAX-ACCESS     read-only

STATUS    current

DESCRIPTION

"This attribute represents the time in milliseconds for the

cell loss integration period.  If cells are lost for this

period of time, the Interworking VCC Termination Point entity

will generate a cell starvation alarm."

::= { atmfAAL1ProfileEntry 8 }

------------------------------------------------------------------

-- ATM Forum ILMI Extension for Auto Configuration

-- ATM AAL3/4 Profile

------------------------------------------------------------------

atmfAAL34ProfileTable OBJECT-TYPE

SYNTAX    SEQUENCE OF    AtmfAAL34ProfileEntry

MAX-ACCESS     not-accessible

STATUS    current

DESCRIPTION

"The ATM Forum ILMI Auto Configuration Extension AAL3/4

Profile Information. "

::= { atmfAutoConfigGroup 4 }

atmfAAL34ProfileEntry OBJECT-TYPE

SYNTAX    AtmfAAL34ProfileEntry

MAX-ACCESS     not-accessible

STATUS    current

DESCRIPTION

"An entry in the AAL34 Profile table provides data that

describes the AAL3/4 processing function. "

INDEX          { atmfAAL34ProfileIndex }

::= { atmfAAL34ProfileTable 1 }

AtmfAAL34ProfileEntry ::= SEQUENCE {

atmfAAL34ProfileIndex                INTEGER,

atmfAAL34MaxCpcsSduSizeForward       INTEGER,

atmfAAL34MaxCpcsSduSizeBackward      INTEGER,

atmfAAL34MIDRangeLow                 INTEGER,

atmfAAL34MIDRangeHigh                INTEGER,

atmfAAL34AALMode                     INTEGER,

atmfAAL34SscsType                    INTEGER

}

atmfAAL34ProfileIndex OBJECT-TYPE

SYNTAX    INTEGER (1..2147483647)

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"A number between which identifies the entry in the AAL3/4

Profile Table. "

::= { atmfAAL34ProfileEntry 1 }

atmfAAL34MaxCpcsSduSizeForward OBJECT-TYPE

SYNTAX    INTEGER (1..65535)

MAX-ACCESS     read-only

STATUS    current

DESCRIPTION

"This attribute represents the maximum CPCS_PDU size that will

be transmitted over the connection in both the incoming

(forward) direction of transmission. "

::= { atmfAAL34ProfileEntry 2 }

atmfAAL34MaxCpcsSduSizeBackward OBJECT-TYPE

SYNTAX    INTEGER (1..65535)

MAX-ACCESS     read-only

STATUS    current

DESCRIPTION

"This attribute represents the maximum CPCS_PDU size that will

be transmitted over the connection in both the outgoing

(backward) direction of transmission. "

::= { atmfAAL34ProfileEntry 3 }

atmfAAL34MIDRangeLow OBJECT-TYPE

SYNTAX    INTEGER (1..66536)

MAX-ACCESS     read-only

STATUS    current

DESCRIPTION

"This attribute represents the low value of MID supported at

the AAL for the supporting VCC."

::= { atmfAAL34ProfileEntry 4 }

atmfAAL34MIDRangeHigh OBJECT-TYPE

SYNTAX    INTEGER (1..66536)

MAX-ACCESS     read-only

STATUS    current

DESCRIPTION

"This attribute represents the high value of MID supported at

the AAL for the supporting VCC."

::= { atmfAAL34ProfileEntry 5 }

atmfAAL34AALMode OBJECT-TYPE

SYNTAX    INTEGER {

messageAssured (0),

messageUnassured (1),

streamingAssured (2),

streamingUnassured (3)

}

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"This attribute indicates whether the AAL for the supporting

VCC is operating in message mode or streaming mode, assured or

unassured. "

::= { atmfAAL34ProfileEntry 6 }

atmfAAL34SscsType OBJECT-TYPE

SYNTAX    INTEGER {

null (0),

dataAssured (1),

dataNonAssured (2),

frameRelay (3)

}

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"This attribute identifies the SSCS type for the AAL.  Valid

values are NULL, Data SSCS based on SSCOP (assured operation),

Data SSCS based on SSCOP (non-assured operation), or Frame

Relay SSCS "

::= { atmfAAL34ProfileEntry 7 }

------------------------------------------------------------------

-- ATM Forum ILMI Extension for Auto Configuration

-- ATM AAL5 Profile

------------------------------------------------------------------

atmfAAL5ProfileTable OBJECT-TYPE

SYNTAX    SEQUENCE OF    AtmfAAL5ProfileEntry

MAX-ACCESS     not-accessible

STATUS    current

DESCRIPTION

"The ATM Forum ILMI Auto Configuration Extension AAL5

Profile Information. "

::= { atmfAutoConfigGroup 5 }

atmfAAL5ProfileEntry OBJECT-TYPE

SYNTAX    AtmfAAL5ProfileEntry

MAX-ACCESS     not-accessible

STATUS    current

DESCRIPTION

"An entry in the AAL5 Profile table provides data that

describes the AAL5 processing function. "

INDEX          { atmfAAL5ProfileIndex }

::= { atmfAAL5ProfileTable 1 }

AtmfAAL5ProfileEntry ::= SEQUENCE {

atmfAAL5ProfileIndex                INTEGER,

atmfAAL5MaxCpcsSduSizeForward       INTEGER,

atmfAAL5MaxCpcsSduSizeBackward      INTEGER,

atmfAAL5AALMode                     INTEGER,

atmfAAL5SscsType                    INTEGER

}

atmfAAL5ProfileIndex OBJECT-TYPE

SYNTAX    INTEGER (1..2147483647)

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"A number between which identifies the entry in the AAL5

Profile Table. "

::= { atmfAAL5ProfileEntry 1 }

atmfAAL5MaxCpcsSduSizeForward OBJECT-TYPE

SYNTAX    INTEGER (1..65535)

MAX-ACCESS     read-only

STATUS    current

DESCRIPTION

"This attribute represents the maximum CPCS_PDU size that will

be transmitted over the connection in both the incoming

(forward) direction of transmission. "

::= { atmfAAL5ProfileEntry 2 }

atmfAAL5MaxCpcsSduSizeBackward OBJECT-TYPE

SYNTAX    INTEGER (1..65535)

MAX-ACCESS     read-only

STATUS    current

DESCRIPTION

"This attribute represents the maximum CPCS_PDU size that will

be transmitted over the connection in both the outgoing

(backward) direction of transmission. "

::= { atmfAAL5ProfileEntry 3 }

atmfAAL5AALMode OBJECT-TYPE

SYNTAX    INTEGER {

messageAssured (0),

messageUnassured (1),

streamingAssured (2),

streamingUnassured (3)

}

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"This attribute indicates whether the AAL for the supporting

VCC is operating in message mode or streaming mode, assured or

unassured. "

::= { atmfAAL5ProfileEntry 4 }

atmfAAL5SscsType OBJECT-TYPE

SYNTAX    INTEGER {

null (0),

dataAssured (1),

dataNonAssured (2),

frameRelay (3)

}

MAX-ACCESS     read-only

STATUS         current

DESCRIPTION

"This attribute identifies the SSCS type for the AAL.  Valid

values are NULL, Data SSCS based on SSCOP (assured operation),

Data SSCS based on SSCOP (non-assured operation), or Frame

Relay SSCS "

::= { atmfAAL5ProfileEntry 5 }

END