Technical Committee

Remote Monitoring MIB Extensions
for ATM Networks

AF-NM-TEST-0080.000

May, 1997

© 1997 The ATM Forum. All Rights Reserved. No part of this publication may be reproduced in any form or by any means.

The information in this publication is believed to be accurate as of its publication date.  Such information is subject to change without notice and The ATM Forum is not responsible for any errors.  The ATM Forum does not assume any responsibility to update or correct any information in this publication.  Notwithstanding anything to the contrary, neither The ATM Forum nor the publisher make any representation or warranty, expressed or implied, concerning the completeness, accuracy, or applicability of any information contained in this publication.  No liability of any kind shall be assumed by The ATM Forum or the publisher as a result of reliance upon any information contained in this publication.

The receipt or any use of this document or its contents does not in any way create by implication or otherwise:

¥	Any express or implied license or right to or under any ATM Forum member company's patent,

copyright, trademark or trade secret rights which are or may be associated with the ideas, techniques,

concepts or expressions contained herein; nor

¥	Any warranty or representation that any ATM Forum member companies will announce any product(s) 	and/or service(s) related thereto, or if such announcements are made, that such announced product(s) 	and/or service(s) embody any or all of the ideas, technologies, or concepts contained herein; nor

¥	Any form of relationship between any ATM Forum member companies and the recipient or user of this

document.

Implementation or use of specific ATM standards or recommendations and ATM Forum specifications will be voluntary, and no company shall agree or be obliged to implement them by virtue of participation in The ATM Forum.

The ATM Forum is a non-profit international organization accelerating industry cooperation on ATM technology.  The ATM Forum does not, expressly or otherwise, endorse or promote any specific products or services.

NOTE:  The user's attention is called to the possibility that implementation of the ATM interoperability specification contained herein may require use of an invention covered by patent rights held by ATM Forum Member companies or others.  By publication of this ATM interoperability specification, no position is taken by The ATM Forum with respect to validity of any patent claims or of any patent rights related thereto or the ability to obtain the license to use such rights.  ATM Forum Member companies agree to grant licenses under the relevant patents they own on reasonable and nondiscriminatory terms and conditions to applicants desiring to obtain such a license.  For additional information contact:

The ATM Forum

Worldwide Headquarters

2570 West El Camino Real, Suite 304

Mountain View, CA 94040-1313

Tel:	+1-415-949-6700

Fax:	+1-415-949-6705

Introduction

ATM Monitoring Application Framework Requirements

Alignment with RMON

Extending RMON for ATM

RMON Resource Sharing Model

Relationship to Existing MIBs

RMON

TR-RMON

RMON-2 MIB

RMON-2 Protocol Identifiers

ATOM MIB

ATOM Supplemental MIB

ATM-RMON MIB Functional Requirements

Physical Ports and Logical Ports

Address-Based vs. Non-Address-Based Traffic

Cell-Level Filter and Capture

Collection Perspective

Cell Collection Requirements

Frame Collection Requirements

ATM-RMON Design

Switch Port Aggregation

Data Reduction

Pre-collection Data Reduction

Post-collection Data Reduction

Collection Source Identifier

Definitions

MIB Objects

References

Introduction

This contribution addresses the traffic monitoring and analysis functionality required for ATM networks. It includes a MIB proposal and design rationale, which are based on the IETF Remote Monitoring (RMON) MIBs.

This specification addresses issues related to applying 'RMON technology' to ATM Networks:

functional applicability of existing RMON groups

new functionality for ATM networks

collection source design issues

flexible resource allocation

data reduction mechanisms

RMON-based applications can provide system administrators with valuable data about network utilization and behavior. RMON agents offer applications developers resource-intensive functions such as high-level statistics gathering and low-level filtering/capture of MAC frames.

RMON is traditionally deployed as one or more NMS applications managing multiple RMON probes, each of which is monitoring one or more network segments. RMON for ATM networks will require a different deployment model, as well as many other new MIB features.

ATM Monitoring Application Framework Requirements

Network administrators need access to traffic utilization statistics in order to effectively manage their networks. The RMON MIB already provides a rich set of statistical information and management functions for Ethernet and Token Ring networks, and it is desirable to extend this set of functionality to ATM networks.

Adapting RMON to ATM networks requires standards work in three areas:

Monitoring Application Framework -- a set of requirements and rationale focusing the application and MIB design.

Monitoring MIB -- a set of monitoring functions suitable for distributed deployment on various platforms, including switch-embedded and external probe implementations.

RMON-2 Protocol Identifiers for ATM -- a set of protocol encapsulation macros must be added to the RMON-2 Protocol Identifiers Specification to support upper-layer packet decoding for specific ATM encapsulations (e.g., LANE). All frame-based analysis of ATM network traffic can be supported directly by RMON-2, without additional MIB objects.

Figure 1: RMON MIB Framework

2.1.	Alignment with RMON

The RMON MIBs embody a set of design choices and rationale, which has been standardized and refined over the last six years, such as:

RMON promiscuously monitors address-based traffic on an individual (physical) subnetwork.

RMON provides high-level functionality, focusing on correlating network bandwidth/resource utilization to the individual entities using a network, and the conversations between those network entities.

RMON is intended for remote deployment -- different physical location from the system administrators, and/or attached to different subnetwork(s) than the network management station(s).

RMON is intended to concurrently support multiple NMS applications, and provide for resource sharing between such applications.

RMON provides resource-intensive bit-filtering and capture of selected frames for exception handling applications, usually deployed sparingly because of high cost.

RMON is partially auto-configured, and partially manually configured -- resource-intensive functions such as TopN reporting and filter/capture must be started explicitly, by control-row creation.

2.2.	Extending RMON for ATM

The current RMON MIBs analyze frame-based traffic. With some very minor additions to the RMON-2 MIB, frames carried in AAL-5 cell-flows can be counted using the RMON-2 MIB [9].

In addition to frame analysis, an RMON MIB which provides cell-based (per-host and per-conversation) traffic information is desirable.

From an application development perspective, a monitoring MIB is required which has the following attributes:

maintains RMON structure and architecture to leverage existing application development and user experience.

provides flexible configuration mechanisms, suited to the connection-oriented nature of ATM.

provides basic statistics for each monitored cell-stream, for each identified ATM host, and conversation between two ATM hosts, identified by the probe.

provide aggregated and compacted statistical data to the NMS, reducing NMS load and data transfer times.

hide low-level details, such as specific VPI/VCI information, which does not pertain to any manageable resource by an NMS. This level of detail does not provide enough useful management information to justify the expense of storing and indexing a huge amount of data on the agent, and then transferring that data to the NMS.  (Other MIBs exist which collect per-connection accounting statistics.)

provide mechanisms to an NMS to allocate probe resources in the more effective ways.

allows for cost-efficient implementation for both switch-embedded and stand-alone probe designs.

allows for cost-effective monitoring of high speed links, through configuration optimization and statistical sampling of frame-based traffic.

2.3	RMON Resource Sharing Model

There are some design features that are used throughout all the RMON MIBs.  The most important is the RMON resource-sharing model. RMON agents are expected to create certain 'common' data-collection resources (ownerString starts with the string 'monitor'). Only system administrators should be allowed to delete or modify these 'monitor-owned' resources.

NMS applications can create short-lived control entries (ownerString set to unique NMS-ID) if the monitor-owned collections are not appropriate for a given task. Some features, such as TopN reporting, event- reporting, history collection (other than 30 sec/30 min intervals), and filter/capture, require some NMS configuration in most implementations.

The resource owner (NMS) is expected to pick a unique value for the owner string and supply this value in the first setRequest PDU creating the control row. An NMS must check the rowStatus object (i.e., errorStatus of PDU setting status to createAnd* before using the resource, to make sure another NMS was not allocated the resource instead.  Before terminating, the NMS application must delete any control entries that it created. There is no control-row garbage collection defined in RMON, so an NMS application must check for its own old, unused control entries before creating new ones, upon startup.

An NMS application may optionally use another applications' resources in a read-only manner, if applicable. Usually, this is only done when a resource request is refused. The system administrator is responsible for deleting RMON resources (monitor or NMS-owned) to make room for new applications.

The latest RMON documents also provide a time-stamp in every data table row, to help an NMS detect the deletion and re-creation of that row. This MIB also provides 'lastCreateTime' time-stamps in all the data

tables, as well as the control tables which do not have associated data tables.

This MIB also contains a new resource management feature called the 'ResourcePriority'. Each control entry contains a configurable resource priority identifier ('low', 'normal', or 'high'), which the probe may inspect during garbage-collection of host or matrix entries, in order to avoid inadvertent deletion of important data.

Note that the ResourcePriority only provides additional information to the probe for use during that probe's proprietary garbage collection algorithm (if any).  It does not mandate any specific garbage collection or memory management design or implementation. At this time, least recently used (LRU) garbage collection is the recommended approach for probe host and matrix data table memory management.

2.4	Relationship to Existing MIBs

There are several RFCs and Internet drafts which define RMON technology, which may relate to this MIB:

2.4.1.	RMON

The Remote Network Monitoring MIB (RMON or RMON-1) [7] provides several management functions that may be directly or indirectly applicable to ATM Networks:

Detailed link layer statistics for ethernet segments (etherStats group); ATM-RMON maintains a 'stats' group, simply to provide a grand total for the associated host and matrix tables.

Remote polling of detailed link layer statistics for ethernet segments (history, etherHistory groups); ATM-RMON utilizes the generic history collection application, found in the RMON-2 MIB [9] (see the section on RMON-2 for details).

Basic statistics--per host and per conversation--for all valid MAC addresses discovered on each monitored segment (host and matrix groups); ATM-RMON contains host and matrix functionality based on the versions found in RMON-2, which contain some updates to the RMON-1 versions.

TopN Report statistics (topN talkers or errors)--per-host--for each valid MAC address discovered on each monitored segment (hostTopN group) bit-level frame filtering and frame-slice capture (filter, channel, capture groups); ATM-RMON does not implement a hostTopN function, but rather a matrixTopN instead, since hostTopN can be derived from matrixTopN data.

Simple threshold monitoring, event-logging, and event-notification for any MIB instance; ATM-RMON utilizes the alarms and events groups from RMON-1 [7] without modification.  These groups from RMON-1 [7] should be implemented on ATM-RMON probes if a simple thresholding mechanism is desired.

2.4.2.	TR-RMON

The Token Ring Extensions for RMON MIB (RFC1513) (TR-RMON) [8] provides the same kind of detailed link layer statistics and remote polling as found in RMON-1 (tokenRingMLStats/History, tokenRingPStats/History). The TR-RMON MIB is highly integrated with RMON-1, which is possible because both link layers use the same address format. An RMON MIB for ATM cannot be structured and positioned like the TR-MIB, because none of the shared tables can be directly applied to ATM. Since RMON-1 will be augmented and updated by RMON-2, any ATM-RMON standardization effort should align with the RMON-2 MIB [9], but maintain the same 'extensions MIB' structure as found in the TR-RMON MIB.

2.4.3.	RMON-2 MIB

The emerging 'RMON-2' standard (RMON-2) [9] provides many additions and improvements to RMON-1:

Complete protocol distribution per segment (or 'collection source').

Collection of network to MAC address bindings seen in packets on all segments.

Collection of source MAC address to physical interface bindings on all segments.

Probe configuration, such as startup parameters and trap destination management.

Collection of per network-layer host basic statistics (network layer and above).

Collection of per-conversation basic statistics (network layer and above).

TopN Report statistics per conversation (network layer and above).

Improvements such as relative-offset frame filtering, user-defined remote-polling, faster table retrieval, better NMS control of probe resources, and better accuracy reporting.

Although the protocol analysis features are not directly applicable, there are many design improvements in RMON-2 that can be integrated into ATM-RMON:

TopN report improvements such as auto-restart, report count, reverse-rates, and 'last-create-time' to detect discontinuities.

Control entry inserts and deletes counters (this replaces the RMON-1 'table-size' object).

ProtocolDirectory collection-control design (i.e., central configuration defines what data is collected in each functional group).

The usrHistory group (user-defined history collection) should be implemented on ATM-RMON probes if a history collection mechanism is desired for atmStats entries.

2.4.4.	RMON-2 Protocol Identifiers

The RMON Protocol Identifiers Specification (RMONPROT) [10] defines encoding rules for protocolDirID, protocolDirParameters, and protocolDirType MIB objects It is required only if RMON-2 packet analysis is applied to frames monitored (on connections which use frames). Statistical analysis of frames is not directly applicable to this MIB, and is not discussed in this document.

2.4.5.	ATOM MIB

The Atom MIB is the fundamental MIB for managing ATM networks (RFC 1695) [11], but it is not directly referenced by this MIB, except for use of the 'IfIndex' textual convention. It is possible other textual conventions will be imported as well.

2.4.6.	ATOM Supplemental MIB

The Atom Supplemental MIB [12] defines additional management capabilities for ATM networks. The 'AtmAddr' textual convention is used from this MIB, as well as the AtmVclAddrTable.

Since ATM-RMON only monitors address-based traffic, endpoint addresses have to be configured for a PVC before it can be counted by a probe.

An agent implementation may choose to support statistics collection on PVC circuits if the AtmVclAddrTable is implemented as well.  An NMS must properly configure the endpoint addresses on each PVC to be monitored, before activating any related ATM-RMON collections.

3.	ATM-RMON MIB Functional Requirements

Applying RMON to ATM networks will require some new design changes and new functionality. Special problems such as  high speeds, "cells vs. frames" issues, and the connection-oriented nature of ATM need special MIB solutions in order to implement RMON for ATM networks.

3.1.	Physical Ports and Logical Ports

Support for VP-tunneling via ATM Logical Ports [12] should be provided without special-case MIB objects. An NMS should be able to specify 'monitored-connections' (in part) by the ifIndex values associated with the ATM interfaces to be monitored. Any ifIndex value associated with an ifType value of 'atm(37)' (Interfaces MIB RFC 1573 [13]) or 'atmLogicalPort(80)' [12] can be specified for monitoring purposes.

Note that a given ATM port is allowed to be included in at most one collection group, so as not to require a probe to count each monitored cell-stream more than once per function (e.g., stats, host, matrix).

3.2.	Address-Based vs. Non-Address-Based Traffic

Although ATM networks are capable of carrying many types of traffic (e.g., voice, video, data), only a subset of this traffic is monitored by ATM-RMON probes. RMON technology traditionally provides functions to monitor address-based traffic (i.e., transmissions for which the source and destination entities can be identified by examination).

Therefore, an ATM-RMON probe only monitors connections established between two endpoint addresses. Although the 'AtmAddr' textual convention [12] allows several address type variants, only the 20 octet NSAP format is used in this MIB.

An NMS can monitor the 'ifInOctets' and 'ifOutOctets' objects for a particular ATM port (ifType = 'atm(37)' or 'atmLogicalPort(80)') to determine the total cell traffic through that port. The ATM-RMON MIB can be configured to provide the total address-based cell-traffic for a given port, which can be subtracted from the if*Octets counters to produce the non-address-based traffic totals.

Note that the term "source address" is used throughout the MIB to indicate the ATM address of the particular end of an ATM connection from which the cells are sent, and the term "destination address" indicates the ATM address of the particular end of an ATM connection at which the cells are received. This is irrespective of whether such an address was the Calling Party or Called Party on the particular connection.

3.3.	Cell-Level Filter and Capture

Since most applications requiring filter/capture functionality in the probe are for frame-based traffic (handled by RMON-1 and RMON-2), no cell-specific filter/capture MIB objects are included at this time. This functionality may be added in a future release of this MIB.

Note that cell-specific filter/capture would not be restricted to address-based traffic, and may possibly be specified several ways (e.g., ifIndex/VPI/VCI or endpoint address).

3.4.	Collection Perspective

There are four different 'collection perspectives' that are possible:

(A)  stand-alone probe attached to a single port of a switch. ATM traffic is copied somehow to the RMON probe.

(B)  embedded probe within a switch., with no access to the switch fabric. ATM traffic is copied somehow to the RMON probe.

(C)  embedded probe within a switch, with access to the switch fabric. ATM traffic is monitored directly, possibly  implemented in hardware.  Probes of this type are likely to monitor traffic at cell header level only. A lower level of conformance, or some other mechanism (e.g., additional software), will most likely be needed for this type of probe.

(D)  stand-alone probe, tapping an NNI link between two switches.  ATM traffic is monitored directly (subject to probe capabilities), without switch intervention. All cells in both directions are monitored somehow by the RMON probe, without disturbing traffic on the link.

Figure2: Probe Location

Unless RMON instrumentation is embedded into the switch fabric (C), or placed between two switches (D), then circuit steering is required (A and B) for RMON instrumentation software to access ATM traffic. For such probes, each full-duplex circuit is (presumably) mapped into two redirected half-duplex ATM connection:

inbound(ifIndex/VPI/VCI)

outbound(ifIndex/VPI/VCI)

A 'probe-tap' (D) does not pre-filter data by selecting particular ATM connections for monitoring. Instead, it receives all VCs on an NNI link, without switch participation.

3.5	Cell Collection Requirements

This MIB provides the following new functionality:

ATM layer instrumentation

collection source aggregation

data reduction configuration and status

basic cell statistics  (i.e., statsTable)

basic cell statistics per host  (i.e., hostTable)

basic cell counts per conversation  (i.e., matrixTable)

sorted reports, based on basic cell counts per conversation (i.e., matrixTopNTable)

At this time, only some very basic statistics are defined in the proposed MIB:

cells-sent count (32/32 pair and 64-bit counter)

cells-received count (32/32 pair and 64-bit counter)

number of successful call setups (32 bit counter)

number of attempted call setups (32 bit counter)

total connection time (32 bit counter, units of seconds)

Other statistics (e.g., error counters) may be added in the future.

Figure 3: ATM-RMON Counters

Circuit Steering requirements are not addressed in this document.  RMON collection requirements will be considered independently of circuit steering techniques. Although references to 'copied' ATM connections are made in this document, actual circuit-steering implementation may be different. Therefore, this MIB is (presently) only directly applicable to collection models which do not require circuit-steering (i.e., models 'C' and 'D' in figure2).

3.6.	Frame Collection Requirements

An optional feature set for ATM-RMON is the analysis of frames on AAL-5 ATM connections. This can be accomplished with some minor additions to the RMON-2 MIB [9].  New values for dataSource objects can be defined which reference ATM collection sources.  The data can be formatted into RMON-2 host, matrix, matrixTopN, and filter/capture groups without requiring any RMON-2 MIB changes. (Encapsulation definitions have to be added to the Protocol Identifiers Specification [10].)

Details on frame analysis integration with RMON-1 and RMON-2 MIBs are not discussed in this document, and will be deferred to a future release.

4.	ATM-RMON Design

The RMON Working Group within the Internet Engineering Task Force (IETF) will be updating and augmenting the RMON MIB soon, and several of these changes can be incorporated into an ATM-RMON MIB. The main advantages of borrowing from the RMON MIB [7]:

allow system administrators to reuse operational experience with RMON concepts and RMON data presentation (e.g., basic stats/host/matrix for a given media or protocol).

allow portions of standard MIBs to be applied directly to ATM-RMON without modification.

allow RMON NMS and probe vendors to possibly take advantage of their RMON-1 implementation experience.

allow flexible configuration with low complexity.

ATM-RMON will require new configuration mechanisms to deal with varying application needs and probe capabilities. RMON-1 [7] defines a 'dataSource' object of type OBJECT IDENTIFIER, which allows new or proprietary mechanisms beyond the 'ifIndex' object. RMON-2 provides for extension of allowable dataSource values.

4.1.	Switch Port Aggregation

Since ATM-RMON implementation is (in part) intended for ATM switches, special consideration for switches is desirable.

All switched-based-RMON technology shares a similar problem regarding the per-port nature of RMON. AN NMS must configure and collect statistics independently for each monitored port. Usually, an NMS will 'collapse' most of the per-port statistics into an aggregate version for the switch.

ATM-RMON provides a flexible mechanism to specify a particular 'data- source', including the ability to aggregate traffic from different ports into a single collection.  See the portSelectGroup set of MIB objects for more details on port aggregation.

Figure 4: PortSelectGroup example

4.2.	Data Reduction

Traditionally, RMON host and matrix tables can be very large, and take a great deal of resources to manage by the NMS and maintain by the agent. The high speeds and complex collection requirements of ATM-RMON make it very desirable to reduce both the agent and NMS load for processing cell-traffic data.

Generally, agent resources can be saved with pre-collection data reduction, and NMS resources can be saved with post-collection data reduction. Both types are integrated into ATM-RMON.

4.2.1.	Pre-collection Data Reduction

The most effective way to save probe resources is to limit what data is processed in any manner by the probe, such as the use of statistical sampling. Note that statistical sampling only applies to frame capture and analysis.  Frame capture mechanisms for ATM are not defined in this document, and there is no provision for the sampling of cells in the ATM-RMON MIB.

The portSelectGroup mechanism described in the ATM-RMON MIB provides configurable grouping of cell traffic for ATM-RMON counting purposes. This feature can be configured to reduce the amount of data that must be maintained for each collection, and reduce overall redundant data collection within the probe.

Agents are not required to allow a particular port to be included in more than one port select group at a time.

4.2.2.	Post-collection Data Reduction

Even with pre-collection data reduction it is possible that ATM-RMON data tables will grow quite large, so it is also desirable to minimize the number of SNMP transactions required to retrieve or refresh these data tables.

The mechanisms included in this MIB are:

collection aggregation -- ability to control the granularity of the entries in the host and matrix tables. Entries can be selected by full-address or partial-address (e.g., the ESI bytes can be cleared to zero for indexing and counting purposes).  This reduces the number of entries actually maintained by the probe.

TopN Report aggregation -- probe can continuously monitor the top talkers over a given interval, and automatically generate a report at the end of each interval.

4.3.	Collection Source Identifier

This MIB does not use the traditional RMON 'dataSource and arbitrary integer index' model for identifying collection sources.  Instead, a set of global tables are used to define 'circuit selection groups' (called 'portSelectGroups').

Traditional RMON collections (e.g., stats, host, matrix, matrixTopN) can be done using a portSelectGroup as the 'dataSource'. However, instead of an OBJECT IDENTIFIER dataSource identifier, a common integer index (identifying the portSelectGroup) is used in each control and data table.  This allows an NMS to identify the source of a collection by examining the index of any columnar object. It also prevents duplicate collections from occurring on the probe.

Note the collection criteria setup cannot be modified on the fly for a particular portSelectGroup, while any collections based on that portSelectGroup are in progress. In order to reduce agent complexity and maintain data integrity, specific collections must be halted, reconfigured, and then restarted (with an empty data-set) if runtime changes are required. However, individual atmStatsControl, atmHostControl, atmMatrixControl, and atmMatrixTopNControl entries may be created, modified, or destroyed while the associated portSelGrpEntry is active.

5.	Definitions

The following MIB proposal is based, in part, on the RMON-2 MIB [9].

The MIB contains four groups:

portSelect -- port selection; data tables are indexed by a common object (portSelGrpIndex), which replaces the columnar 'dataSource' pointer and arbitrary integer index used in all other RMON MIBs.

atmStats -- basic statistics; allows individual host traffic contribution percentage to be easily calculated.

atmHost -- ATM per-host statistics.

atmMatrix -- ATM per-circuit statistics and ATM per-circuit matrixTopN reporting.

Figure 5: ATM-RMON MIB Structure

The portSelectGroup is used to define the ports to be monitored for a particular set of functions (a subset of all ATM-RMON, RMON-1, and RMON-2 groups).

For processing of frames collected (in an implementation-specific manner) from the portSelectGroup, the appropriate RMON-1 or RMON-2 dataSource instance is set to the OBJECT IDENTIFIER 'portSelGrpIndex.I'.

For processing of packets collected on behalf of RMON-2 functions, the proper protocol identifiers must be set up before the nlHost, alHost, nlMatrix, alMatrix, and filter2 groups can be utilized.

5.1	MIB Objects

This section includes the ATM-RMON MIB proposal described in the previous section, which was originally published as an Internet Draft [14].

ATM-RMON-MIB DEFINITIONS ::= BEGIN

IMPORTS

MODULE-IDENTITY, OBJECT-TYPE, Counter32, Integer32,

Counter64, Gauge32, experimental, TimeTicks, Unsigned32

FROM SNMPv2-SMI

TEXTUAL-CONVENTION, RowStatus, DisplayString,

TimeStamp

FROM SNMPv2-TC

MODULE-COMPLIANCE, OBJECT-GROUP

FROM SNMPv2-CONF

OwnerString

FROM RMON-MIB

ZeroBasedCounter32, LastCreateTime

FROM RMON2-MIB

AtmAddr

FROM ATM-TC-MIB

ifIndex

FROM IF-MIB;

--  Remote Network Monitoring MIB for ATM Networks

atmRmon MODULE-IDENTITY

LAST-UPDATED Ò9702210000ZÓ

ORGANIZATION ÒATM ForumÓ

CONTACT-INFO

ÒAndy Bierman

Cisco Systems, Inc.

Phone: +1 408 527-3711

Email: abierman@cisco.com

Keith McCloghrie

Cisco Systems, Inc.

Phone: +1 408 526-5260

Email: kzm@cisco.comÓ

DESCRIPTION

ÒThe MIB module for managing remote monitoring device implementations for ATM networks.Ó

::= { experimental xx }

-- ATM-RMON MIB groups

atmRmonMIBObjects        OBJECT IDENTIFIER ::= { atmRmon 1 }

atmRmonNotifications       OBJECT IDENTIFIER ::= { atmRmon 2 }

atmRmonConformance      OBJECT IDENTIFIER ::= { atmRmon 3 }

-- ATM-RMON MIB object groups

portSelect                           OBJECT IDENTIFIER ::= { atmRmonMIBObjects 1 }

atmStats                             OBJECT IDENTIFIER ::= { atmRmonMIBObjects 2 }

atmHost                             OBJECT IDENTIFIER ::= { atmRmonMIBObjects 3 }

atmMatrix                          OBJECT IDENTIFIER ::= { atmRmonMIBObjects 4 }

-- Textual Conventions:

ServiceClass ::= TEXTUAL-CONVENTION

STATUS current

DESCRIPTION

ÒThis TC describes an object that identifies the cell delivery class-of-service classification, associated with a particular statistics collection.  In order to conserve agent resources, the classifications are limited to two values which distinguish delay-guarantee.

Statistics gathered on behalf on collections identified by the ÔcbrAndVbr(1)Õ enumeration represent constant-bit-rate  (CBR), real-time and non-real-time variable bit rate (VBR) traffic.

Statistics gathered on behalf on collections identified by the ÔabrAndUbr(2)Õ enumeration represent available-bit-rate  (ABR) and unspecified-bit-rate (UBR) traffic.Ó

SYNTAX INTEGER  {

cbrAndVbr(1),     -- constant and variable bit rate
abrAndUbr(2)      -- available and unspecified bit rate

}

ResourcePriority ::= TEXTUAL-CONVENTION

STATUS current

DESCRIPTION

ÒThis TC describes an object which indicates the desired resource priority of the entire entry. Lower priorities indicate a lesser requirement to retain resources than higher priority values.

A management station can use the resource priority to provide a probe with additional information for managing memory allocation.  A probe is strongly encouraged, but not required, to honor all priority requests, all of the time.

Objects declared with this TC should be contained within a conceptual control table entry. The indicated resource priority applies to the control entry, all internal data structures maintained on behalf of the control entry, and all external MIB data represented by the control entry.

A probe should honor the priority requests in an implementation-dependent way. The data allocation granularity (i.e., shared data structures) may vary greatly for different implementations, so a particular implementation strategy is not mandated. However, the following guidelines are suggested for those agents which implement garbage-collection based on Ôleast-recently usedÕ  (LRU) or other criteria:

In the event that the probe runs short of resources, and data entries are to be removed from particular tables to reclaim resources, then entries associated with lower ResourcePriority values should be deleted before entries associated with higher ResourcePriority values, regardless of the resource reclamation algorithm in use. In addition, entries associated with a higher AddressCollectScope value should be deleted before entries with a lower AddressCollectScope value.

Note that the priority ordering of entries with the same ResourcePriority and addressCollectScope values is unspecified.Ó

SYNTAX INTEGER  {

lowPriority(1),

normalPriority(2),

highPriority(3)

}

AddressCollectScope ::= TEXTUAL-CONVENTION

STATUS current

DESCRIPTION

ÒThis TC describes an object which indicates the granularity of the addresses represented in associated ATM-RMON collections.

Addresses gathered on behalf of collections identified by the Ôprefix(1)Õ enumeration will be cleared to zero in bytes 13 through 20, for indexing and counting purposes.

Addresses gathered on behalf of collections identified by the ÔprefixAndEsi(2)Õ enumeration will be cleared to zero in byte 20, for indexing and counting purposes.

Addresses gathered on behalf of collections identified by the ÔentireAddr(3)Õ enumeration will be unmodified, for indexing and counting purposes.Ó

SYNTAX INTEGER {

prefix(1),

prefixAndEsi(2),

entireAddr(3)

}

ConnectTime ::= TEXTUAL-CONVENTION

STATUS current

DESCRIPTION

ÒThis TC describes an object which indicates the sum of the elapsed times of all connections associated with a particular collection. This is a cumulative total and includes all connections which currently exist and all connections which have been released.

Elapsed connection time begins when the call attempt is detected, and ends when the call is released. It is an implementation-specific matter whether call attempts which do not result in successful connections are represented in this total.

Call duration is maintained in units of seconds, and may be rounded to the nearest second when counted.Ó

SYNTAX Gauge32

--

-- Port Selection (portSelect Group)

--

-- Defines the ports to be included in a particular stats, host or matrix collection.

--

--    portSelGrpTable

--    portSelTable

portSelGrpTable OBJECT-TYPE

SYNTAX      SEQUENCE OF PortSelGrpEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒControls the setup of port and ATM connection selection criteria used on behalf of any collection associated with entries in this table (e.g., atmHostTable).

This table allows portSelTable entries with the same value of the portSelCollectGroup object to be grouped together to form port select groups.

Note that an agent implementation may restrict the actual number of portSelGrp entries, due to resource limitations.Ó

::= { portSelect 1 }

portSelGrpEntry OBJECT-TYPE

SYNTAX      PortSelGrpEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒA conceptual row in the portSelGrpTable.

An example of the indexing of this entry is portSelGrpCreateTime.7 .Ó

INDEX { portSelGrpIndex }

::= { portSelGrpTable 1 }

PortSelGrpEntry ::= SEQUENCE {

portSelGrpIndex                   Integer32,

portSelGrpDescr                   DisplayString,

portSelGrpCreateTime         LastCreateTime,

portSelGrpOwner                 OwnerString,

portSelGrpStatus                  RowStatus

}

portSelGrpIndex OBJECT-TYPE

SYNTAX      Integer32 (1..65535)

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒAn arbitrary and unique index for this portSelGrpEntry.  If portSelGrpTable entries are recreated by the agent after a restart, then the portSelGrpIndex value must be retained across a restart as well.Ó

::= { portSelGrpEntry 1 }

portSelGrpDescr  OBJECT-TYPE

SYNTAX      DisplayString (SIZE(0..64))

MAX-ACCESS  read-create

STATUS      current

DESCRIPTION

ÒAn administratively-assigned descriptive label for this portSelGrp entry.Ó

::= { portSelGrpEntry 2 }

portSelGrpCreateTime OBJECT-TYPE

SYNTAX      LastCreateTime

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe value of sysUpTime when this portSelGrp entry was activated.  This can be used by the management station to ensure that the table has not been deleted and recreated between polls.Ó

::= { portSelGrpEntry 3 }

portSelGrpOwner OBJECT-TYPE

SYNTAX      OwnerString

MAX-ACCESS  read-create

STATUS      current

DESCRIPTION

ÒThe entity that configured this entry and is therefore using the resources assigned to it.Ó

::= { portSelGrpEntry 4 }

portSelGrpStatus OBJECT-TYPE

SYNTAX      RowStatus

MAX-ACCESS  read-create

STATUS      current

DESCRIPTION

ÒThe status of this row.

An entry may not exist in the active state unless all objects in the entry have an appropriate value.  No objects are required to be written prior to the row being set to active(1).  However, all portSelTable entries which are to be included in collections on behalf of this portSelectGroup, must be completely configured and activated before this object is set to active(1), since the associated instances of portSelStatus cannot be modified once this object has been set to active(1).

If this object is not equal to active(1), all associated data collections shall be deleted (e.g., any associated collections in the atmStats, atmHostTable or atmMatrixSDTable).  Note that associated portSelTable and any configured collection control entries (e.g., atmHostControlTable) are not deleted when this entry leaves the active state.Ó

::= { portSelGrpEntry 5 }

--

-- portSelTable: used to specify the collection configuration

-- for a single ATM port

--

portSelTable OBJECT-TYPE

SYNTAX      SEQUENCE OF PortSelEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒControls the setup of selection criteria for a single ATM port, used on behalf of any collections identified with the associated portSelectGroup (identified by its portSelGrpIndex value).

This table identifies the collection characteristics for the ATM port indicated by the ifIndex value in the index. Note that an agent implementation may restrict the actual number of portSelTable entries, due to resource limitations.Ó

::= { portSelect 2 }

portSelEntry OBJECT-TYPE

SYNTAX      PortSelEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒA conceptual row in the portSelTable.

Entries may only be created on behalf of ATM interfaces. That is, the ifType value associated with each ifIndex value must be equal to atm(37) or atmLogicalPort(80).

An example of the indexing of this entry is portSelCreateTime.7 .Ó

INDEX { ifIndex }

::= { portSelTable 1 }

PortSelEntry ::= SEQUENCE {

portSelCollectGroup            Integer32,

portSelCreateTime              LastCreateTime,

portSelOwner                      OwnerString,

portSelStatus                       RowStatus

}

portSelCollectGroup OBJECT-TYPE

SYNTAX      Integer32 (1..65535)

MAX-ACCESS  read-create

STATUS      current

DESCRIPTION

ÒThis object identifies the associated instance of portSelGrpIndex, which indicates the portSelectGroup to which this port is assigned.

This object may not be modified if the associated instance of portSelStatus is equal to active(1).Ó

::= { portSelEntry 1 }

portSelCreateTime OBJECT-TYPE

SYNTAX      LastCreateTime

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe value of sysUpTime when this entry was activated.  This can be used by the management station to ensure that the table has not been deleted and recreated between polls.Ó

::= { portSelEntry 2 }

portSelOwner OBJECT-TYPE

SYNTAX      OwnerString

MAX-ACCESS  read-create

STATUS      current

DESCRIPTION

ÒThe entity that configured this entry and is therefore using the resources assigned to it.Ó

::= { portSelEntry 3 }

portSelStatus OBJECT-TYPE

SYNTAX      RowStatus

MAX-ACCESS  read-create

STATUS      current

DESCRIPTION

ÒThe status of this row.

An entry may not exist in the active state unless all objects in the entry have an appropriate value. Specifically, an appropriate value for the portSelCollectGroup object must be set before this object may be set to active(1). An agent may wish to allow portSelTable entries to exist which reference non-existent portSelGrpTable entries, in order to reduce row creation order dependencies.

All portSelTable entries which are to be included in a particular collection (as indicated by the portSelCollectGroup object), should be completely configured and activated before the associated portSelGrpStatus object is set to active(1).  Configuration of a portSelectGroup cannot be modified once collections on its behalf have been started.

This object may not be modified if the associated portSelGroupStatus is in the active(1) state, indicated by a portSelGrpIndex value identical to the value of the portSelCollectGroup object in this entry.Ó

::= { portSelEntry 4 }

--

-- ATM Stats Group

--

-- Counts the total amount of traffic

-- counted on behalf of one or more portSelectGroups

atmStatsControlTable OBJECT-TYPE

SYNTAX      SEQUENCE OF AtmStatsControlEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒA list of ATM basic statistic collection table control entries.  These entries will enable the collection of statistical totals for an entire portSelectGroup.Ó

::= { atmStats 1 }

atmStatsControlEntry OBJECT-TYPE

SYNTAX      AtmStatsControlEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒA conceptual row in the atmStatsControlTable.  Entries in this table are identified and indexed by the portSelGrpIndex object.  At most one atmStats collection is done per portSelectGroup.

An example of the indexing of this entry is atmStatsDropEvents.1 .Ó

INDEX { portSelGrpIndex }

::= { atmStatsControlTable 1 }

AtmStatsControlEntry ::= SEQUENCE {

atmStatsControlDropEvents           Counter32,

atmStatsControlOwner                   OwnerString,

atmStatsControlStatus                    RowStatus

}

atmStatsControlDropEvents OBJECT-TYPE

SYNTAX     Counter32

MAX-ACCESS read-only

STATUS     current

DESCRIPTION

ÒThe total number of events in which cells which should have been counted in the associated atmStatsEntry, but were dropped by the probe due to lack of resources.  Note that this number is not necessarily the number of cells or calls dropped; it is just the number of times this condition has been detected.Ó

::= { atmStatsControlEntry 1 }

atmStatsControlOwner OBJECT-TYPE

SYNTAX      OwnerString

MAX-ACCESS  read-create

STATUS      current

DESCRIPTION

ÒThe entity that configured this entry and is therefore using the resources assigned to it.Ó

::= { atmStatsControlEntry 2 }

atmStatsControlStatus OBJECT-TYPE

SYNTAX      RowStatus

MAX-ACCESS  read-create

STATUS      current

DESCRIPTION

ÒThe status of this atmStatsControlEntry.

This control entry may be created and destroyed independently of the associated portSelGrpEntry, however its associated atmStatsTable can exist only when the portSelGrpEntry controlling this collection is active.

If this object is not equal to active(1), all associated entries in the atmStatsTable shall be deleted.Ó

::= { atmStatsControlEntry 3 }

-- atmStatsTable

-- call and traffic basic statistics collected on behalf of specific

-- portSelectGroups

atmStatsTable OBJECT-TYPE

SYNTAX      SEQUENCE OF AtmStatsEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒA collection of statistical totals for all ATM addresses that have been discovered on behalf of the portSelectGroup associated with this entry.Ó

::= { atmStats 2 }

atmStatsEntry OBJECT-TYPE

SYNTAX      AtmStatsEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒA conceptual row in the atmStatsTable.

The portSelGrpIndex value in the index identifies the portSelectGroup on whose behalf this entry was created.

An example of the indexing of this entry is atmStatsCells.8.1Ó

INDEX { portSelGrpIndex, atmStatsSClass }

::= { atmStatsTable 1 }

AtmStatsEntry ::= SEQUENCE {

atmStatsSClass                      ServiceClass,

atmStatsCreateTime              LastCreateTime,

atmStatsCells                         Counter32,

atmStatsCellsRollovers         Counter32,

atmStatsHCCells                   Counter64,

atmStatsNumCallAttempts    Counter32,

atmStatsNumCalls                 Counter32,

atmStatsConnTime                ConnectTime

}

atmStatsSClass OBJECT-TYPE

SYNTAX      ServiceClass

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒThe quality of service classification for this entry.  See the ServiceClass textual convention for details and specific class-of-service values.Ó

::= { atmStatsEntry 1 }

atmStatsCreateTime OBJECT-TYPE

SYNTAX     LastCreateTime

MAX-ACCESS read-only

STATUS     current

DESCRIPTION

ÒThe value of sysUpTime when this entry was created.  This can be used by the management station to ensure that the entry has not been deleted and recreated between polls.Ó

::= { atmStatsEntry 2 }

atmStatsCells OBJECT-TYPE

SYNTAX      Counter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe total number of error-free cells detected on all ATM connections on behalf of this portSelectGroup collection.  Note that a particular cell may only cause this counter to increment once, even if multiple criteria is met for inclusion in this portSelectGroup.Ó

::= { atmStatsEntry 3 }

atmStatsCellsRollovers OBJECT-TYPE

SYNTAX      Counter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe number of times that the associated instance of the atmStatsCells object has incremented from the value 2^^32-1 to zero.Ó

::= { atmStatsEntry 4 }

atmStatsHCCells OBJECT-TYPE

SYNTAX      Counter64

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe high capacity version of the atmStatsCells object.Ó

::= { atmStatsEntry 5 }

atmStatsNumCallAttempts OBJECT-TYPE

SYNTAX      Counter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe number of call attempts detected on all signalled ATM connections on behalf of this portSelectGroup collection.  A probe should increment this counter each time a connection setup attempt (identified with this portSelectGroup) is detected. For point-to-multipoint connections, this counter is incremented once per counted connection, regardless of the number of leafs identified in the connection.Ó

::= { atmStatsEntry 6 }

atmStatsNumCalls OBJECT-TYPE

SYNTAX      Counter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe number of successfully established calls detected on all signalled ATM connections on behalf of this portSelectGroup collection.  Note that this value includes successfully established calls that are currently in progress.  A probe should increment this counter each time a valid connection (identified with this portSelectGroup) is successfully established. For point-to-multipoint ATM connections, this counter is incremented once per counted connection, regardless of the number of leafs identified in the connection. Note that when a point-to-point connection setup enters on one port and leaves on another port in the same port select group, it is counted only once.Ó

::= { atmStatsEntry 7 }

atmStatsConnTime OBJECT-TYPE

SYNTAX      ConnectTime

UNITS       ÒsecondsÓ

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe elapsed time of all calls identified by the associated instance of the atmStatsNumCallAttempts object.  Note that point-to-multipoint calls are counted only once, regardless of the number of leafs participating in the call.Ó

::= { atmStatsEntry 8 }

--

-- ATM Host Group

--

-- Counts the amount of traffic sent on behalf of each ATM address

-- discovered by the probe, according to associated portSelectGroup

-- criteria

atmHostControlTable OBJECT-TYPE

SYNTAX      SEQUENCE OF AtmHostControlEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒA list of ATM host table control entries.

These entries will enable the collection of ATM host information in the atmHostTable.

Entries in the atmHostTable will be created on behalf of each entry in this table. A probe is required to support at most one atmHost collection per instance of an associated portSelectGroup, therefore the table is indexed by the portSelGrpIndex.Ó

::= { atmHost 1 }

atmHostControlEntry OBJECT-TYPE

SYNTAX      AtmHostControlEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒA conceptual row in the atmHostControlTable.  Entries in this table are identified and indexed by the portSelGrpIndex object.  At most one atmHost collection is done per portSelectGroup.

An example of the indexing of this entry is atmHostControlInserts.1Ó

INDEX { portSelGrpIndex }

::= { atmHostControlTable 1 }

AtmHostControlEntry ::= SEQUENCE {

atmHostControlInserts                          Counter32,

atmHostControlDeletes                         Counter32,

atmHostControlMaxDesiredEntries      Integer32,

atmHostControlPriority                         ResourcePriority,

atmHostControlAddrCollectScope       AddressCollectScope,

atmHostControlDropEvents                  Counter32,

atmHostControlOwner                          OwnerString,

atmHostControlStatus                           RowStatus

}

atmHostControlInserts OBJECT-TYPE

SYNTAX     Counter32

MAX-ACCESS read-only

STATUS     current

DESCRIPTION

ÒThe number of times an atmHost entry has been inserted into the atmHost table.  If an entry is inserted, then deleted, and then inserted, this counter will be incremented by 2.

To allow for efficient implementation strategies, agents may delay updating this object for short periods of time.  For example, an implementation strategy may allow internal data structures to differ from those visible via SNMP for short periods of time.  This counter may reflect the internal data structures for those short periods of time.

Note that the table size can be determined by subtracting atmHostControlDeletes from atmHostControlInserts.Ó

::= { atmHostControlEntry 1 }

atmHostControlDeletes OBJECT-TYPE

SYNTAX     Counter32

MAX-ACCESS read-only

STATUS     current

DESCRIPTION

ÒThe number of times an atmHost entry has been deleted from the atmHost table (for any reason).  If an entry is deleted, then inserted, and then deleted, this counter will be incremented by 2.

To allow for efficient implementation strategies, agents may delay updating this object for short periods of time.  For example, an implementation strategy may allow internal data structures to differ from those visible via SNMP for short periods of time.  This counter may reflect the internal data structures for those short periods of time.

Note that the table size can be determined by subtracting atmHostControlDeletes from atmHostControlInserts.Ó

::= { atmHostControlEntry 2 }

atmHostControlMaxDesiredEntries OBJECT-TYPE

SYNTAX      Integer32

MAX-ACCESS  read-create

STATUS      current

DESCRIPTION

ÒThe maximum number of entries that are desired in the atmHostTable on behalf of this control entry. The probe will not create more than this number of associated entries in the table, but may choose to create fewer entries in this table for any reason including the lack of resources.

If this value is set to -1, the probe may create any number of entries in this table.

If the associated instance of atmHostControlStatus object is equal to active(1), this object may not be modified.Ó

DEFVAL { -1 }

::= { atmHostControlEntry 3 }

atmHostControlPriority OBJECT-TYPE

SYNTAX        ResourcePriority

MAX-ACCESS     read-create

STATUS        current

DESCRIPTION

ÒThe priority this collection should be given to retain resources, in the event the probe must reclaim some resources in order to add new entries to an existing atmHost collection or add new collections of other types.

If the associated instance of atmHostControlStatus object is equal to active(1), this object may not be modified.Ó

DEFVAL { normalPriority }

::= { atmHostControlEntry 4 }

atmHostControlAddrCollectScope OBJECT-TYPE

SYNTAX      AddressCollectScope

MAX-ACCESS  read-create

STATUS      current

DESCRIPTION

ÒThis object controls the granularity of address collection in atmHostTable entries created on behalf of this control entry, according to the rules specified by the AddressCollectScope textual convention.

If the associated instance of atmHostControlStatus object is equal to active(1), this object may not be modified.Ó

DEFVAL { prefixAndEsi }

::= { atmHostControlEntry 5 }

atmHostControlDropEvents OBJECT-TYPE

SYNTAX      Counter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe total number of events in which cells which should have been counted in the associated atmHostEntry, but were dropped by the probe due to lack of resources.  Note that this number is not necessarily the number of cells or calls dropped; it is just the number of times this condition has been detected.Ó

::= { atmHostControlEntry 6 }

atmHostControlOwner OBJECT-TYPE

SYNTAX      OwnerString

MAX-ACCESS  read-create

STATUS      current

DESCRIPTION

ÒThe entity that configured this entry and is therefore using the resources assigned to it.Ó

::= { atmHostControlEntry 7 }

atmHostControlStatus OBJECT-TYPE

SYNTAX      RowStatus

MAX-ACCESS  read-create

STATUS      current

DESCRIPTION

ÒThe status of this atmHostControlEntry.

An entry may not exist in the active state unless all objects in the entry have an appropriate value. Specifically, appropriate values for the associated instances of atmHostControlMaxDesiredEntries, atmHostControlPriority, and atmHostControlAddrCollectScope must be set before this object may be set to active(1).

This control entry may be created and destroyed independently of the associated portSelGrpEntry, however its associated atmHostTable can exist only when the portSelGrpEntry controlling this collection is active.

If this object is not equal to active(1), all associated entries in the atmHostTable shall be deleted.Ó

::= { atmHostControlEntry 8 }

--

-- ATM Host Table

--

atmHostTable OBJECT-TYPE

SYNTAX      SEQUENCE OF AtmHostEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒA collection of statistics for a particular ATM host address that has been discovered on behalf of the portSelectGroup associated with this entry.

The probe will add to this table all addresses seen as the source or destination address in all calls, on all ports configured in the portSelGrpEntry controlling this collection.Ó

::= { atmHost 2 }

atmHostEntry OBJECT-TYPE

SYNTAX      AtmHostEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒA conceptual row in the atmHostTable.

The portSelGrpIndex value in the index identifies the portSelectGroup on whose behalf this entry was created.

An example of the indexing of this entry is atmHostInCells.4.20.<NSAP>.2Ó

INDEX { portSelGrpIndex, atmHostAddress, atmHostSClass }

::= { atmHostTable 1 }

AtmHostEntry ::= SEQUENCE {

atmHostAddress                        AtmAddr,

atmHostSClass                           ServiceClass,

atmHostCreateTime                   LastCreateTime,

atmHostInCells                          ZeroBasedCounter32,

atmHostInCellsRollovers           ZeroBasedCounter32,

atmHostInHCCells                     Counter64,

atmHostOutCells                        ZeroBasedCounter32,

atmHostOutCellsRollovers         ZeroBasedCounter32,

atmHostOutHCCells                   Counter64,

atmHostInNumCallAttempts      ZeroBasedCounter32,

atmHostInNumCalls                   ZeroBasedCounter32,

atmHostOutNumCallAttempts   ZeroBasedCounter32,

atmHostOutNumCalls                ZeroBasedCounter32,

atmHostInConnTime                  ConnectTime,

atmHostOutConnTime               ConnectTime

}

atmHostAddress OBJECT-TYPE

SYNTAX      AtmAddr

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒThe ATM address for this atmHostEntry.

This is represented as an octet string with specific semantics and length as identified by the AtmAddr textual convention. Note that only 20 octet ÔAtmAddrÕ addresses are collected in this table.Ó

::= { atmHostEntry 1 }

atmHostSClass OBJECT-TYPE

SYNTAX      ServiceClass

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒThe quality of service classification for this entry.  See the ServiceClass textual convention for details and specific class-of-service values.Ó

::= { atmHostEntry 2 }

atmHostCreateTime OBJECT-TYPE

SYNTAX      LastCreateTime

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe value of sysUpTime when this entry was activated.  This can be used by the management station to ensure that the entry has not been deleted and recreated between polls.Ó

::= { atmHostEntry 3 }

atmHostInCells OBJECT-TYPE

SYNTAX      ZeroBasedCounter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe number of error-free cells detected on ATM connections associated with this portSelectGroup, in which this ATM address was identified as the receiver address, or one of the leaf addresses on a point-to-multipoint ATM connection.  This counter includes OAM cells transmitted on behalf of this source address.Ó

::= { atmHostEntry 4 }

atmHostInCellsRollovers OBJECT-TYPE

SYNTAX      ZeroBasedCounter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe number of times that the associated instance of the atmHostInCells object has incremented from the value 2^^32-1 to zero.Ó

::= { atmHostEntry 5 }

atmHostInHCCells OBJECT-TYPE

SYNTAX      Counter64

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe high capacity version of the atmHostInCells object.Ó

::= { atmHostEntry 6 }

atmHostOutCells OBJECT-TYPE

SYNTAX      ZeroBasedCounter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe number of error-free cells detected on ATM connections associated with this portSelectGroup, in which this ATM address was identified as the sender address. This counter includes OAM cells transmitted on behalf of this  destination address.Ó

::= { atmHostEntry 7 }

atmHostOutCellsRollovers OBJECT-TYPE

SYNTAX      ZeroBasedCounter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe number of times that the associated instance of the atmHostOutCells object has incremented from the value 2^^32-1 to zero.Ó

::= { atmHostEntry 8 }

atmHostOutHCCells OBJECT-TYPE

SYNTAX      Counter64

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe high capacity version of the atmHostOutCells object.Ó

::= { atmHostEntry 9 }

atmHostInNumCallAttempts OBJECT-TYPE

SYNTAX      ZeroBasedCounter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe number of calls detected on ATM connections associated with this entry, in which the associated endpoint address was identified as the Called Party in an signalled ATM connection establishment attempt.

Note that this value includes calls that are currently in progress.  A probe should increment this counter each time a connection attempt is detected in which this ATM host is identified as the Called Party, or one of the leaf addresses for point-to-multipoint ATM connections.Ó

::= { atmHostEntry 10 }

atmHostInNumCalls OBJECT-TYPE

SYNTAX      ZeroBasedCounter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe number of successfully established calls detected on ATM connections associated with this entry, in which the associated endpoint address was identified as the Called Party address.

Note that this value includes calls that are currently in progress.  A probe should increment this counter each time a connection is successfully established in which this ATM host is identified as the Called Party address, or one of the leaf addresses for point-to-multipoint ATM connections.Ó

::= { atmHostEntry 11 }

atmHostOutNumCallAttempts OBJECT-TYPE

SYNTAX      ZeroBasedCounter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe number of calls detected on ATM connections associated with this entry, in which the associated endpoint address was identified as the Calling Party in an signalled ATM connection establishment attempt.

Note that this value includes calls that are currently in progress.  A probe should increment this counter each time a connection attempt is detected in which this ATM host is identified as the Calling Party.

Note that for point-to-multipoint ATM connections, this counter is incremented only once per call, regardless of the number of leafs established at setup time or the number of leaf-initiated-join attempts since the call was established.Ó

::= { atmHostEntry 12 }

atmHostOutNumCalls OBJECT-TYPE

SYNTAX      ZeroBasedCounter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe number of successfully established calls detected on ATM connections associated with this entry, in which the associated endpoint address was identified as the Calling Party address.

Note that this value includes calls that are currently in progress.  A probe should increment this counter each time a connection is successfully established in which this ATM host is identified as the Calling Party address.Ó

::= { atmHostEntry 13 }

atmHostInConnTime OBJECT-TYPE

SYNTAX      ConnectTime

UNITS       ÒsecondsÓ

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe elapsed time of all calls identified by the associated instance of atmHostInNumCallAttempts.Ó

::= { atmHostEntry 14 }

atmHostOutConnTime OBJECT-TYPE

SYNTAX      ConnectTime

UNITS       ÒsecondsÓ

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe elapsed time of all calls identified by the associated instance of atmHostOutNumCallAttempts.Ó

::= { atmHostEntry 15 }

--

-- ATM Matrix Group

--

-- Counts the amount of traffic sent on behalf of each source

-- and destination ATM address discovered by the probe,

-- according to associated portSelectGroup criteria

atmMatrixControlTable OBJECT-TYPE

SYNTAX      SEQUENCE OF AtmMatrixControlEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒA list of ATM matrix table control entries.

These entries will enable the collection of ATM matrix information in the atmMatrixSDTable and atmMatrixDSTable.

A probe is required to support at most one atmMatrix collection per instance of an associated portSelectGroup, therefore the table is indexed by the portSelGrpIndex.Ó

::= { atmMatrix 1 }

atmMatrixControlEntry OBJECT-TYPE

SYNTAX      AtmMatrixControlEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒA conceptual row in the atmMatrixControlTable.

An example of the indexing of this entry is atmMatrixControlInserts.1Ó

INDEX { portSelGrpIndex }

::= { atmMatrixControlTable 1 }

AtmMatrixControlEntry    ::= SEQUENCE {

atmMatrixControlInserts                            Counter32,

atmMatrixControlDeletes                           Counter32,

atmMatrixControlMaxDesiredEntries        Integer32,

atmMatrixControlPriority                           ResourcePriority,

atmMatrixControlAddrCollectScope         AddressCollectScope,

atmMatrixControlDropEvents                   Counter32,

atmMatrixControlOwner                           OwnerString,

atmMatrixControlStatus                            RowStatus

}

atmMatrixControlInserts OBJECT-TYPE

SYNTAX      Counter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe number of times an atmMatrix entry has been inserted into the atmMatrix table.  If an entry is inserted, then deleted, and then inserted, this counter will be incremented by 2.  The addition of a conversation into both the atmMatrixSDTable and atmMatrixDSTable shall be counted as two insertions (even though every addition into one table must be accompanied by an insertion into the other).

To allow for efficient implementation strategies, agents may delay updating this object for short periods of time.  For example, an implementation strategy may allow internal data structures to differ from those visible via SNMP for short periods of time.  This counter may reflect the internal data structures for those short periods of time.Ó

::= { atmMatrixControlEntry 1 }

atmMatrixControlDeletes OBJECT-TYPE

SYNTAX      Counter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe number of times an atmMatrix entry has been deleted from the atmMatrix table (for any reason).  If an entry is deleted, then inserted, and then deleted, this counter will be incremented by 2.  The deletion of a conversation from both the atmMatrixSDTable and atmMatrixDSTable shall be counted as two deletions (even though every deletion from one table must be accompanied by a deletion from the other).

To allow for efficient implementation strategies, agents may delay updating this object for short periods of time.  For example, an implementation strategy may allow internal data structures to differ from those visible via SNMP for short periods of time.  This counter may reflect the internal data structures for those short periods of time.

Note that the table size can be determined by subtracting atmMatrixControlDeletes from atmMatrixControlInserts, and dividing the result by two.Ó

::= { atmMatrixControlEntry 2 }

atmMatrixControlMaxDesiredEntries OBJECT-TYPE

SYNTAX      Integer32

MAX-ACCESS  read-create

STATUS      current

DESCRIPTION

ÒThe maximum number of entries that are desired in the atmMatrixTable on behalf of this control entry. The probe will not create more than this number of associated entries in the table, but may choose to create fewer entries in this table for any reason including the lack of resources.

If this value is set to -1, the probe may create any number of entries in this table.

If the associated instance of atmMatrixControlStatus object is equal to active(1), this object may not be modified.Ó

DEFVAL { -1 }

::= { atmMatrixControlEntry 3 }

atmMatrixControlPriority OBJECT-TYPE

SYNTAX      ResourcePriority

MAX-ACCESS  read-create

STATUS      current

DESCRIPTION

ÒThe priority this collection should be given to retain resources, in the event the probe must reclaim some resources in order to add new entries to an existing atmMatrix collection or add new collections of other types.

If the associated instance of atmMatrixControlStatus object is equal to active(1), this object may not be modified.Ó

DEFVAL { normalPriority }

::= { atmMatrixControlEntry 4 }

atmMatrixControlAddrCollectScope OBJECT-TYPE

SYNTAX AddressCollectScope

MAX-ACCESS  read-create

STATUS      current

DESCRIPTION

ÒThis object controls the granularity of address collection in atmMatrixSDTable and atmMatrixDSTable entries created on behalf of this control entry, according to the rules specified by the AddressCollectScope textual convention.

If the associated instance of atmMatrixControlStatus object is equal to active(1), this object may not be modified.Ó

DEFVAL { prefixAndEsi }

::= { atmMatrixControlEntry 5 }

atmMatrixControlDropEvents OBJECT-TYPE

SYNTAX      Counter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe total number of events in which cells which should have been counted in the associated atmMatrixSDEntry and atmMatrixDSEntry, but were dropped by the probe due to lack of resources.  Note that this number is not necessarily the number of cells or calls dropped; it is just the number of times this condition has been detected.Ó

::= { atmMatrixControlEntry 6 }

atmMatrixControlOwner OBJECT-TYPE

SYNTAX      OwnerString

MAX-ACCESS  read-create

STATUS      current

DESCRIPTION

ÒThe entity that configured this entry and is therefore

using the resources assigned to it.Ó

::= { atmMatrixControlEntry 7 }

atmMatrixControlStatus OBJECT-TYPE

SYNTAX      RowStatus

MAX-ACCESS  read-create

STATUS      current

DESCRIPTION

ÒThe status of this atmMatrixControlEntry.

An entry may not exist in the active state unless all objects in the entry have an appropriate value.  Specifically, the associated instances of atmMatrixControlMaxDesiredEntries, atmMatrixControlPriority, and atmMatrixControlAddrCollectScope objects must be set to appropriate values before this object may be set to active(1).

This control entry may be created and destroyed independently of the associated portSelGrpEntry, however its associated atmMatrixSDTable and atmMatrixDSTable can exist only when the portSelGrpEntry controlling this collection is active.

If this object is not equal to active(1), all associated entries in the atmMatrixSDTable and atmMatrixDSTable shall be deleted.Ó

::= { atmMatrixControlEntry 8 }

-- atmMatrixSDTable

-- call and traffic data collected on behalf of specific

-- portSelectGroups; sorted by source address first

atmMatrixSDTable OBJECT-TYPE

SYNTAX      SEQUENCE OF AtmMatrixSDEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒA collection of statistics for conversations between particular ATM endpoint addresses that have been discovered on behalf of the portSelectGroup associated with this entry.

The probe will add a new entry to this table for all conversations (connections) between distinct source and destination address pairs, detected in all calls, on all ports configured in the portSelGrpEntry controlling this collection.  Further, this table will only contain entries that have a corresponding entry in the atmMatrixDSTable with the same source address and destination address.Ó

::= { atmMatrix 2 }

atmMatrixSDEntry OBJECT-TYPE

SYNTAX      AtmMatrixSDEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒA conceptual row in the atmMatrixSDTable.

The portSelGrpIndex value in the index identifies the portSelectGroup on whose behalf this entry was created.

An example of the indexing of this entry is atmMatrixSDCells.1.20.<NSAP>.20.<NSAP>.2Ó

INDEX { portSelGrpIndex, atmMatrixSDSrcAddress,

atmMatrixSDDstAddress, atmMatrixSDSClass }

::= { atmMatrixSDTable 1 }

AtmMatrixSDEntry    ::= SEQUENCE {

atmMatrixSDSrcAddress              AtmAddr,

atmMatrixSDDstAddress              AtmAddr,

atmMatrixSDSClass                      ServiceClass,

atmMatrixSDCreateTime              LastCreateTime,

atmMatrixSDCells                         ZeroBasedCounter32,

atmMatrixSDCellsRollovers         ZeroBasedCounter32,

atmMatrixSDHCCells                   Counter64,

atmMatrixSDNumCallAttempts   ZeroBasedCounter32,

atmMatrixSDNumCalls                ZeroBasedCounter32,

atmMatrixSDConnTime               ConnectTime

}

atmMatrixSDSrcAddress OBJECT-TYPE

SYNTAX      AtmAddr

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒThe transmitting endpoint ATM address for this atmMatrixSDEntry.

This is represented as an octet string with specific semantics and length as identified by the AtmAddr textual convention. Note that only 20 octet ÔAtmAddrÕ addresses are collected in this table.Ó

::= { atmMatrixSDEntry 1 }

atmMatrixSDDstAddress OBJECT-TYPE

SYNTAX      AtmAddr

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒThe destination endpoint ATM address for this atmMatrixSDEntry.

This is represented as an octet string with specific semantics and length as identified by the AtmAddr textual convention. Note that only 20 octet ÔAtmAddrÕ addresses are collected in this table.Ó

::= { atmMatrixSDEntry 2 }

atmMatrixSDSClass OBJECT-TYPE

SYNTAX      ServiceClass

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒThe quality of service classification for this entry.  See the ServiceClass textual convention for details and specific class-of-service values.Ó

::= { atmMatrixSDEntry 3 }

atmMatrixSDCreateTime OBJECT-TYPE

SYNTAX      LastCreateTime

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe value of sysUpTime when this entry was activated.  This can be used by the management station to ensure that the entry has not been deleted and recreated between polls.Ó

::= { atmMatrixSDEntry 4 }

atmMatrixSDCells OBJECT-TYPE

SYNTAX      ZeroBasedCounter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe number of error-free cells detected on connections in which these ATM addresses were identified as the transmitting and receiving endpoint addresses.

Note that for point-to-multipoint connections, an entry is created for each root-to-leaf address-pair that exists, and each cell sent from the root on a point-to-multipoint ATM connection is counted once in each distinct matrix entry.  This counter includes OAM cells transmitted on behalf of this  source/destination address-pair.Ó

::= { atmMatrixSDEntry 5 }

atmMatrixSDCellsRollovers OBJECT-TYPE

SYNTAX      ZeroBasedCounter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe number of times that the associated instance of the atmMatrixSDCells object has incremented from the value 2^^32-1 to zero.Ó

::= { atmMatrixSDEntry 6 }

atmMatrixSDHCCells OBJECT-TYPE

SYNTAX      Counter64

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe high capacity version of the atmMatrixSDCells object.Ó

::= { atmMatrixSDEntry 7 }

atmMatrixSDNumCallAttempts OBJECT-TYPE

SYNTAX      ZeroBasedCounter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe number of SVC call setup attempts detected on ATM connections within the specified portSelectGroup, in which the indicated atmMatrixSDSrcAddress endpoint address was identified as the Calling Party and the indicated atmMatrixSDDstAddress was identified as the Called Party.

Note that this value includes calls that are currently in progress.  A probe should increment this counter each time a connection attempt is detected in which these ATM addresses are identified as the calling and called parties.Ó

::= { atmMatrixSDEntry 8 }

atmMatrixSDNumCalls OBJECT-TYPE

SYNTAX      ZeroBasedCounter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe number of successful SVC call setups detected on ATM connections within the specified portSelectGroup, in which the indicated atmMatrixSDSrcAddress endpoint address was identified as the Calling Party and the indicated atmMatrixSDDstAddress was identified as the Called Party.

Note that this value includes calls that are currently in progress.  A probe should increment this counter each time a valid connection is established in which these ATM addresses are identified as the calling and called parties.Ó

::= { atmMatrixSDEntry 9 }

atmMatrixSDConnTime OBJECT-TYPE

SYNTAX      ConnectTime

UNITS       ÒsecondsÓ

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe elapsed time of all calls identified by the associated instance of atmMatrixSDNumCallAttempts.Ó

::= { atmMatrixSDEntry 10 }

-- atmMatrixDSTable

-- call and traffic data collected on behalf of specific

-- portSelectGroups; sorted by destination address first

atmMatrixDSTable OBJECT-TYPE

SYNTAX      SEQUENCE OF AtmMatrixDSEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒA collection of statistics for conversations between particular ATM endpoint addresses that have been discovered on behalf of the portSelectGroup associated with this entry.

The probe will add a new entry to this table for all conversations (connections) between distinct source and destination address pairs, detected in all cells identified by the associated portSelGrpEntry criteria.  Further, this table will only contain entries that have a corresponding entry in the atmMatrixSDTable with the same source address and destination address.Ó

::= { atmMatrix 3 }

atmMatrixDSEntry OBJECT-TYPE

SYNTAX      AtmMatrixDSEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒA conceptual row in the atmMatrixDSTable.

The portSelGrpIndex value in the index identifies the portSelectGroup on whose behalf this entry was created.

An example of the indexing of this entry is atmMatrixDSCells.1.20.<NSAP>.20.<NSAP>.2Ó

INDEX { portSelGrpIndex, atmMatrixDSDstAddress,

atmMatrixDSSrcAddress, atmMatrixDSSClass }

::= { atmMatrixDSTable 1 }

AtmMatrixDSEntry    ::= SEQUENCE {

atmMatrixDSSrcAddress                    AtmAddr,

atmMatrixDSDstAddress                    AtmAddr,

atmMatrixDSSClass                            ServiceClass,

atmMatrixDSCreateTime                    LastCreateTime,

atmMatrixDSCells                              ZeroBasedCounter32,

atmMatrixDSCellsRollovers               ZeroBasedCounter32,

atmMatrixDSHCCells                         Counter64,

atmMatrixDSNumCallAttempts          ZeroBasedCounter32,

atmMatrixDSNumCalls                       ZeroBasedCounter32,

atmMatrixDSConnTime                      ConnectTime

}

atmMatrixDSSrcAddress OBJECT-TYPE

SYNTAX      AtmAddr

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒThe transmitting endpoint ATM address for this atmMatrixDSEntry.

This is represented as an octet string with specific semantics and length as identified by the AtmAddr textual convention.  Note that only 20 octet ÔAtmAddrÕ addresses are collected in this table.Ó

::= { atmMatrixDSEntry 1 }

atmMatrixDSDstAddress OBJECT-TYPE

SYNTAX      AtmAddr

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒThe destination endpoint ATM address for this atmMatrixDSEntry.

This is represented as an octet string with specific semantics and length as identified by the AtmAddr textual convention.  Note that only 20 octet ÔAtmAddrÕ addresses are collected in this table.Ó

::= { atmMatrixDSEntry 2 }

atmMatrixDSSClass OBJECT-TYPE

SYNTAX      ServiceClass

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒThe quality of service classification for this entry.  See the ServiceClass textual convention for details and specific class-of-service values.Ó

::= { atmMatrixDSEntry 3 }

atmMatrixDSCreateTime OBJECT-TYPE

SYNTAX      LastCreateTime

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe value of sysUpTime when this entry was activated.  This can be used by the management station to ensure that the entry has not been deleted and recreated between polls.Ó

::= { atmMatrixDSEntry 4 }

atmMatrixDSCells OBJECT-TYPE

SYNTAX      ZeroBasedCounter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe number of error-free cells detected on ATM connections in which these ATM addresses were identified as the transmitting and receiving endpoint addresses.

Note that for point-to-multipoint connections, an entry is created for each root-to-leaf address-pair that exists, and each cell sent from the root on a point-to-multipoint ATM connection is counted once in each distinct matrix entry. This counter includes OAM cells transmitted on behalf of this source/destination address-pair.Ó

::= { atmMatrixDSEntry 5 }

atmMatrixDSCellsRollovers OBJECT-TYPE

SYNTAX      ZeroBasedCounter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe number of times that the associated instance of the atmMatrixDSCells object has incremented from the value 2^^32-1 to zero.Ó

::= { atmMatrixDSEntry 6 }

atmMatrixDSHCCells OBJECT-TYPE

SYNTAX      Counter64

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe high capacity version of the atmMatrixDSCells object.Ó

::= { atmMatrixDSEntry 7 }

atmMatrixDSNumCallAttempts OBJECT-TYPE

SYNTAX      ZeroBasedCounter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe number of SVC call setup attempts detected on ATM connections within the specified portSelectGroup, in which the indicated atmMatrixDSSrcAddress endpoint address was identified as the Calling Party and the indicated atmMatrixDSDstAddress was identified as the Called Party.

Note that this value includes calls that are currently in progress.  A probe should increment this counter each time a connection attempt is detected in which these ATM addresses are identified as the calling and called parties.Ó

::= { atmMatrixDSEntry 8 }

atmMatrixDSNumCalls OBJECT-TYPE

SYNTAX      ZeroBasedCounter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe number of successful SVC call setups detected on ATM connections within the specified portSelectGroup, in which the indicated atmMatrixDSSrcAddress endpoint address was identified as the Calling Party and the indicated atmMatrixDSDstAddress was identified as the Called Party.

Note that this value includes calls that are currently in progress.  A probe should increment this counter each time a valid connection is established in which these ATM addresses are identified as the calling and called parties.Ó

::= { atmMatrixDSEntry 9 }

atmMatrixDSConnTime OBJECT-TYPE

SYNTAX      ConnectTime

UNITS       ÒsecondsÓ

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe elapsed time of all calls identified by the associated instance of atmMatrixDSNumCallAttempts.Ó

::= { atmMatrixDSEntry 10 }

--

-- ATM MatrixTopN Tables

--

-- Finds and reports the top traffic contributors,

-- according to associated portSelectGroup criteria

atmMatrixTopNControlTable OBJECT-TYPE

SYNTAX      SEQUENCE OF AtmMatrixTopNControlEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒA set of parameters that control the creation of a report of the top N matrix entries according to a selected metric.Ó

::= { atmMatrix 4 }

atmMatrixTopNControlEntry OBJECT-TYPE

SYNTAX      AtmMatrixTopNControlEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒA conceptual row in the atmMatrixTopNControlTable.

An example of the indexing of this table is atmMatrixTopNControlDuration.3.1Ó

INDEX { portSelGrpIndex, atmMatrixTopNControlIndex }

::= { atmMatrixTopNControlTable 1 }

AtmMatrixTopNControlEntry    ::= SEQUENCE {

atmMatrixTopNControlIndex                          Integer32,

atmMatrixTopNControlRateBase                    INTEGER,

atmMatrixTopNControlSClass                        ServiceClass,

atmMatrixTopNControlTimeRemaining         Integer32,

atmMatrixTopNControlGeneratedReports      Counter32,

atmMatrixTopNControlDuration                     Integer32,

atmMatrixTopNControlRequestedSize            Integer32,

atmMatrixTopNControlGrantedSize                Integer32,

atmMatrixTopNControlStartTime                   TimeStamp,

atmMatrixTopNControlOwner                        OwnerString,

atmMatrixTopNControlStatus                         RowStatus

}

atmMatrixTopNControlIndex OBJECT-TYPE

SYNTAX      Integer32 (1..65535)

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒAn index that is used to uniquely identify an entry in the atmMatrixTopNControlTable.  Each such entry defines one top N report prepared on behalf of one atmMatrix entry, which must exist before this entry may be created.Ó

::= { atmMatrixTopNControlEntry 1 }

atmMatrixTopNControlRateBase OBJECT-TYPE

SYNTAX INTEGER {

atmMatrixTopNCells(1),

atmMatrixTopNNumCallAttempts(2),

atmMatrixTopNNumCalls(3),

atmMatrixTopNConnTime(4)

}

MAX-ACCESS          read-create

STATUS  current

DESCRIPTION

ÒThe variable for each atmMatrix entry that the atmMatrixTopNEntries are sorted by.

This object may not be modified if the associated atmMatrixTopNControlStatus object is equal to active(1).Ó

::= { atmMatrixTopNControlEntry 2 }

atmMatrixTopNControlSClass OBJECT-TYPE

SYNTAX  ServiceClass

MAX-ACCESS          read-create

STATUS  current

DESCRIPTION

ÒThe service class for which this topN control entry is collecting information in associated atmMatrixTopN reports.

This object may not be modified if the associated atmMatrixTopNControlStatus object is equal to active(1).Ó

::= { atmMatrixTopNControlEntry 3 }

atmMatrixTopNControlTimeRemaining OBJECT-TYPE

SYNTAX      Integer32

MAX-ACCESS  read-create

STATUS      current

DESCRIPTION

ÒThe number of seconds left in the report currently being collected.  When this object is modified by the management station, a new collection is started, possibly aborting a currently running report.  The new value is used as the requested duration of this report, and is immediately loaded into the associated atmMatrixTopNControlDuration object.

When the report finishes, the probe will automatically start another collection with the same initial value of atmMatrixTopNControlTimeRemaining.  Thus the management station may simply read the resulting reports repeatedly, checking the start time and duration each time to ensure that a report was not missed or that the report parameters were not changed.

While the value of this object is non-zero, it decrements by one per second until it reaches zero.  At the time that this object decrements to zero, the report is made accessible in the atmMatrixTopNTable, overwriting any report that may be there.

When this object is modified by the management station, any associated entries in the atmMatrixTopNTable shall be deleted.Ó

DEFVAL { 1800 }

::= { atmMatrixTopNControlEntry 4 }

atmMatrixTopNControlGeneratedReports OBJECT-TYPE

SYNTAX      Counter32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe number of reports that have been generated by this

entry.Ó

::= { atmMatrixTopNControlEntry 5 }

atmMatrixTopNControlDuration OBJECT-TYPE

SYNTAX      Integer32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe number of seconds that this report has collected during the last sampling interval.

When the associated atmMatrixTopNControlTimeRemaining object is set, this object shall be set by the probe to the same value and shall not be modified until the next time the atmMatrixTopNControlTimeRemaining is set.

This value shall be zero if no reports have been requested for this atmMatrixTopNControlEntry.Ó

::= { atmMatrixTopNControlEntry 6 }

atmMatrixTopNControlRequestedSize OBJECT-TYPE

SYNTAX      Integer32

MAX-ACCESS  read-create

STATUS      current

DESCRIPTION

ÒThe maximum number of host entries requested for this report.

When this object is created or modified, the probe should set atmMatrixTopNControlGrantedSize as closely to this object as is possible for the particular probe implementation and available resources.Ó

DEFVAL { 150 }

::= { atmMatrixTopNControlEntry 7 }

atmMatrixTopNControlGrantedSize OBJECT-TYPE

SYNTAX      Integer32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe maximum number of host entries in this report.

When the associated atmMatrixTopNControlRequestedSize object is created or modified, the probe should set this object as closely to the requested value as is possible for the particular implementation and available resources. The probe must not lower this value except as a result of a set to the associated atmMatrixTopNControlRequestedSize object.

For example, if the value of atmMatrixTopNControlRateBase is equal to atmMatrixTopNCells(1), when the next topN report is generated, host entries with the highest value of atmMatrixSDCells shall be placed in this table in decreasing order of this rate until there is no more room or until there are no more matrix entries. Each atmMatrixSDCells value is copied to the associated atmMatrixTopNRate object.

It is an implementation-specific matter how entries with the same value are sorted.  It is also an implementation- specific matter as to whether or not zero-valued entries are available.Ó

::= { atmMatrixTopNControlEntry 8 }

atmMatrixTopNControlStartTime OBJECT-TYPE

SYNTAX      TimeStamp

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe value of sysUpTime when this top N report was last started.  In other words, this is the time that the associated atmMatrixTopNControlTimeRemaining object was modified to start the requested report or the time the report was last automatically (re)started.

This object may be used by the management station to determine if a report was missed or not.Ó

::= { atmMatrixTopNControlEntry 9 }

atmMatrixTopNControlOwner OBJECT-TYPE

SYNTAX      OwnerString

MAX-ACCESS  read-create

STATUS      current

DESCRIPTION

ÒThe entity that configured this entry and is therefore using the resources assigned to it.Ó

::= { atmMatrixTopNControlEntry 10 }

atmMatrixTopNControlStatus OBJECT-TYPE

SYNTAX      RowStatus

MAX-ACCESS  read-create

STATUS      current

DESCRIPTION

ÒThe status of this atmMatrixTopNControlEntry.

An entry may not exist in the active state unless all objects in the entry have an appropriate value.

If this object is not equal to active(1), all associated entries in the atmMatrixTopNTable shall be deleted by the agent.Ó

::= { atmMatrixTopNControlEntry 11 }

--

-- atmMatrixTopNTable

--

atmMatrixTopNTable OBJECT-TYPE

SYNTAX      SEQUENCE OF AtmMatrixTopNEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒA set of statistics for those matrix entries that have counted the highest number of cells, calls, or connection time.Ó

::= { atmMatrix 5 }

atmMatrixTopNEntry OBJECT-TYPE

SYNTAX      AtmMatrixTopNEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒA conceptual row in the atmMatrixTopNTable.

The atmMatrixTopNControlIndex value in the index identifies the atmMatrixTopNControlEntry on whose behalf this entry was created.

An example of the indexing of this table is atmMatrixTopNSrcAddress.1.3.10Ó

INDEX { portSelGrpIndex, atmMatrixTopNControlIndex,

atmMatrixTopNIndex }

::= { atmMatrixTopNTable 1 }

AtmMatrixTopNEntry    ::= SEQUENCE {

atmMatrixTopNIndex                       Integer32,

atmMatrixTopNSrcAddress             AtmAddr,

atmMatrixTopNDstAddress             AtmAddr,

atmMatrixTopNRate                         Integer32,

atmMatrixTopNReverseRate            Integer32

}

atmMatrixTopNIndex OBJECT-TYPE

SYNTAX      Integer32 (1..65535)

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

ÒAn index that uniquely identifies an entry in the atmMatrixTopNTable among those in the same report.  This index is between 1 and N, where N is the number of entries in this report.

Each conversation in the selected atmMatrixSDTable, for the report interval, is ranked in descending order of the metric identified by the atmMatrixTopNRate object.

For example, if the value of atmMatrixTopNControlRateBase is equal to atmMatrixTopNCells(1), increasing values of atmMatrixTopNIndex shall be assigned to entries with decreasing delta values of atmMatrixSDCells (for the report interval), until index N is assigned or there are no more atmMatrixSDEntries.Ó

::= { atmMatrixTopNEntry 1 }

atmMatrixTopNSrcAddress OBJECT-TYPE

SYNTAX      AtmAddr

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe ATM endpoint address identified as the source of the traffic measured in this report.  Note that only 20 octet ÔAtmAddrÕ addresses are collected in this table.Ó

::= { atmMatrixTopNEntry 2 }

atmMatrixTopNDstAddress OBJECT-TYPE

SYNTAX      AtmAddr

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe ATM endpoint address identified as the destination of the traffic measured in this report.  Note that only 20 octet ÔAtmAddrÕ addresses are collected in this table.Ó

::= { atmMatrixTopNEntry 3 }

atmMatrixTopNRate OBJECT-TYPE

SYNTAX      Integer32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe value of the ranked metric for this conversation, for this report.

If the associated value of atmMatrixTopNRateBase is equal to atmMatrixTopNCells(1), then this object is assigned the delta value of the atmMatrixSDCells object during this report interval.

If the associated value of atmMatrixTopNRateBase is equal to atmMatrixTopNNumCallAttempts(2), then this object is assigned the delta value of the atmMatrixSDNumCallAttempts object during this report interval.

If the associated value of atmMatrixTopNRateBase is equal to atmMatrixTopNNumCalls(3), then this object is assigned the delta value of the atmMatrixSDNumCalls object during this report interval.

If the associated value of atmMatrixTopNRateBase is equal to atmMatrixTopNConnTime(4), then this object is assigned the delta value of the atmMatrixSDConnTime object during this report interval.Ó

::= { atmMatrixTopNEntry 4 }

atmMatrixTopNReverseRate OBJECT-TYPE

SYNTAX      Integer32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

ÒThe value of the associated metric for this conversation, and for this report, but for the reverse direction.

For example, if the associated value of atmMatrixTopNRateBase is equal to atmMatrixTopNCells(1), then this object contains the atmMatrixSDCells delta cell rate for the reverse direction traffic (i.e., destination to source traffic).Ó

::= { atmMatrixTopNEntry 5 }

-- Conformance Macros

atmRmonMIBCompliances   OBJECT IDENTIFIER ::= { atmRmonConformance 1 }

atmRmonMIBGroups        OBJECT IDENTIFIER ::= { atmRmonConformance 2 }

atmRmonMIBCompliance MODULE-COMPLIANCE

STATUS  current

DESCRIPTION

ÒDescribes the requirements for conformance to the ATM-RMON MIB.Ó

MODULE  -- this module

MANDATORY-GROUPS {

portSelectGroup,

atmStatsGroup,

atmHostGroup,

atmMatrixGroup

}

::= { atmRmonMIBCompliances 1 }

portSelectGroup OBJECT-GROUP

OBJECTS {

portSelGrpDescr,

portSelGrpCreateTime,

portSelGrpOwner,

portSelGrpStatus,

portSelCollectGroup,

portSelCreateTime,

portSelOwner,

portSelStatus

}

STATUS      current

DESCRIPTION

ÒSelects the ATM connections that should be monitored as part of a specific collection-group.Ó

::= { atmRmonMIBGroups 1 }

atmStatsGroup OBJECT-GROUP

OBJECTS {

atmStatsControlDropEvents,

atmStatsControlOwner,

atmStatsControlStatus,

atmStatsCreateTime,

atmStatsCells,

atmStatsCellsRollovers,

atmStatsNumCallAttempts,

atmStatsNumCalls,

atmStatsConnTime

}

STATUS current

DESCRIPTION

ÒCounts the basic statistics for collections on behalf of particular portSelectGroup collections.Ó

::= { atmRmonMIBGroups 2 }

atmStatsHCGroup OBJECT-GROUP

OBJECTS {

atmStatsHCCells

}

STATUS current

DESCRIPTION

ÒCounts the high capacity basic statistics for collections on behalf of particular portSelectGroup collections. The atmStatsGroup must be implemented if the atmStatsHCGroup is implemented.  This group is mandatory for implementations which support high capacity counters.Ó

::= { atmRmonMIBGroups 3 }

atmHostGroup OBJECT-GROUP

OBJECTS {

atmHostControlInserts,

atmHostControlDeletes,

atmHostControlMaxDesiredEntries,

atmHostControlPriority,

atmHostControlAddrCollectScope,

atmHostControlDropEvents,

atmHostControlOwner,

atmHostControlStatus,

atmHostCreateTime,

atmHostInCells,

atmHostInCellsRollovers,

atmHostOutCells,

atmHostOutCellsRollovers,

atmHostInNumCallAttempts,

atmHostInNumCalls,

atmHostOutNumCallAttempts,

atmHostOutNumCalls,

atmHostInConnTime,

atmHostOutConnTime

}

STATUS  current

DESCRIPTION

ÒCounts the amount of traffic sent from and to each ATM address discovered by the probe, on behalf of particular portSelectGroup collections.Ó

::= { atmRmonMIBGroups 4 }

atmHostHCGroup OBJECT-GROUP

OBJECTS {

atmHostInHCCells,

atmHostOutHCCells

}

STATUS  current

DESCRIPTION

ÒCounts the amount of traffic sent from and to each ATM address discovered by the probe, on behalf of particular portSelectGroup collections, using high-capacity counters.

The atmHostGroup must be implemented if the atmHostHCGroup is implemented.  This group is mandatory for implementations which support high capacity counters.Ó

::= { atmRmonMIBGroups 5 }

atmMatrixGroup OBJECT-GROUP

OBJECTS {

atmMatrixControlInserts,

atmMatrixControlDeletes,

atmMatrixControlMaxDesiredEntries,

atmMatrixControlPriority,

atmMatrixControlAddrCollectScope,

atmMatrixControlDropEvents,

atmMatrixControlOwner,

atmMatrixControlStatus,

atmMatrixSDCreateTime,

atmMatrixSDCells,

atmMatrixSDCellsRollovers,

atmMatrixSDNumCallAttempts,

atmMatrixSDNumCalls,

atmMatrixSDConnTime,

atmMatrixDSCreateTime,

atmMatrixDSCells,

atmMatrixDSCellsRollovers,

atmMatrixDSNumCallAttempts,

atmMatrixDSNumCalls,

atmMatrixDSConnTime,

atmMatrixTopNControlRateBase,

atmMatrixTopNControlSClass,

atmMatrixTopNControlTimeRemaining,

atmMatrixTopNControlGeneratedReports,

atmMatrixTopNControlDuration,

atmMatrixTopNControlRequestedSize,

atmMatrixTopNControlGrantedSize,

atmMatrixTopNControlStartTime,

atmMatrixTopNControlOwner,

atmMatrixTopNControlStatus,

atmMatrixTopNSrcAddress,

atmMatrixTopNDstAddress,

atmMatrixTopNRate,

atmMatrixTopNReverseRate

}

STATUS  current

DESCRIPTION

ÒCounts the amount of traffic sent between each pair of ATM addresses discovered by the probe, on behalf of particular portSelectGroup collections.Ó

::= { atmRmonMIBGroups 6 }

atmMatrixHCGroup OBJECT-GROUP

OBJECTS {

atmMatrixSDHCCells,

atmMatrixDSHCCells

}

STATUS  current

DESCRIPTION

ÒCounts the amount of traffic sent between each pair of ATM addresses discovered by the probe, on behalf of particular portSelectGroup collections, using high capacity counters. The atmMatrixGroup must be implemented if the atmMatrixHCGroup is implemented.  This group is mandatory for implementations which support high capacity counters.Ó

::= { atmRmonMIBGroups 7 }

END

6.	References

[1]  SNMPv2 Working Group, Case, J., McCloghrie, K., Rose, M., and S. Waldbusser, "Structure of Management Information for version 2 of the Simple Network Management Protocol (SNMPv2)", RFC 1902,  January 1996.

[2]  McCloghrie, K., and M. Rose, Editors, "Management Information Base for Network Management of TCP/IP-based internets: MIB-II", STD 17, RFC 1213, Hughes LAN Systems, Performance Systems International, March 1991.

[3]  SNMPv2 Working Group, Case, J., McCloghrie, K., Rose, M., and S. Waldbusser, "Textual Conventions for version 2 of the Simple Network Management Protocol (SNMPv2)", RFC 1903, January 1996.

[4]  SNMPv2 Working Group, Case, J., McCloghrie, K., Rose, M., and S. Waldbusser, "Protocol Operations for version 2 of the Simple Network Management Protocol (SNMPv2)", RFC 1905, January 1996.

[5]  SNMPv2 Working Group, Case, J., McCloghrie, K., Rose, M., and S. Waldbusser, "Conformance Statements for version 2 of the Simple Network Management Protocol (SNMPv2)", RFC 1904, January 1996.

[6]  Case, J., M. Fedor, M. Schoffstall, J. Davin, "Simple Network Management Protocol", RFC 1157, SNMP Research, Performance Systems International, MIT Laboratory for Computer Science, May 1990.

[7]  S. Waldbusser, "Remote Network Monitoring MIB", RFC 1757, Carnegie Mellon University, February 1995.

[8]  S. Waldbusser, "Token Ring Extensions to the Remote Network Monitoring MIB", RFC 1513, Carnegie Mellon University, September 1993.

[9]  S. Waldbusser, "Remote Network Monitoring Management Information Base Version 2 using SMIv2”,  RFC 2021, International Network Services, January 1997.

[10]  Bierman, A., Iddon, R., "Remote Network Monitoring MIB Protocol Identifiers",  RFC 2074, Cisco Systems, 3Com/AXON Networks, January 1997.

[11]  Ahmed, M., and K. Tesink, Editors, "Definitions of Managed Objects for ATM Management Version 8.0 using SMIv2", RFC 1695, Bell Communications Research, August 1994.

[12]  Ly, F., Noto, M., Smith, A., Tesink, K., "Definitions of Supplemental Managed Objects for ATM Management", draft-ietf-atommib-atm2-08.txt, 3Com, Bell Communications Research, Extreme Networks,  December 1996.

[13] K. McCloghrie and F. Kastenholz, "Evolution of the Interfaces Group of MIB-II", RFC 1573, Network Information Center, SRI International, January, 1994.

[14] A. Bierman and K. McCloghrie, "Remote Network Monitoring MIB Extensions for ATM Networks", draft-bierman-rmon-atmrmon-01.txt, Cisco Systems, May, 1996.