TD <>

ETSI TS 101 368 V7.0.0 (1999-08)

Technical Specification

Digital cellular telecommunications system (Phase 2+);

Example protocol stacks for interconnecting

Cell Broadcast Centre (CBC) and

Base Station Controller (BSC)

(GSM 03.49 version 7.0.0 Release 1998)

Reference

RTS/SMG-040349Q7 (co003i03.PDF)

Keywords

Digital cellular telecommunications system, Global System for Mobile communications (GSM)

ETSI

Postal address

F-06921 Sophia Antipolis Cedex - FRANCE

Office address

650 Route des Lucioles - Sophia Antipolis

Valbonne - FRANCE

Tel.: +33 4 92 94 42 00   Fax: +33 4 93 65 47 16

Siret N° 348 623 562 00017 - NAF 742 C

Association à but non lucratif enregistrée à la

Sous-Préfecture de Grasse (06) N° 7803/88

Internet

secretariat@etsi.fr

Individual copies of this ETSI deliverable
can be downloaded from

http://www.etsi.org

If you find errors in the present document, send your comment to: editor@etsi.fr

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© European Telecommunications Standards Institute 1999.

All rights reserved.

Contents

Intellectual Property Rights	4

Foreword	4

Introduction	4

1	Scope	5

1.1	References	5

1.2	Abbreviations	6

2	A protocol stack which utilises an application-network layer convergence function for interconnecting CBC and BSC	6

2.1	CBSE Definition	7

2.2	ASN1 Specification	8

2.3	Application Rules for Avoidance of Collision of CBSE Operations	14

2.4	Non Support of 128 bytes of NS-user-data in Network Connection and Network Connection Release phases	15

3	An OSI Protocol Stack For Interconnecting CBC and BSC	16

3.1	Service elements on the application layer	16

3.2	Detailed specification of the CBRSE services	17

3.3	Application rules	29

3.3.1	Application rule set 1 Semi-permanent symmetric connection	29

3.3.2	Application rule set 2 Transient asymmetric connection	30

4	An SS7 Protocol Stack For Interconnecting CBC And BSC	30

Annex A (informative):	Document change history	31

History	32

# Intellectual Property Rights

IPRs essential or potentially essential to the present document may have been declared to ETSI. The information pertaining to these essential IPRs, if any, is publicly available for ETSI members and non-members, and can be found in SR 000 314: "Intellectual Property Rights (IPRs); Essential, or potentially Essential, IPRs notified to ETSI in respect of ETSI standards", which is available free of charge from the ETSI Secretariat. Latest updates are available on the ETSI Web server (http://www.etsi.org/ipr).

Pursuant to the ETSI IPR Policy, no investigation, including IPR searches, has been carried out by ETSI. No guarantee can be given as to the existence of other IPRs not referenced in SR 000 314 (or the updates on the ETSI Web server) which are, or may be, or may become, essential to the present document.

# Foreword

This Technical Specification (TS) has been produced by the Special Mobile Group (SMG).

The present document specifies three alternative approaches to the specification of protocol stacks of communication protocols for the purpose of fulfilling the service requirements of the primitives specified for the CBC - BSC interface in GSM 03.41 within the digital cellular telecommunications system (Phase 2/Phase 2+).

The contents of the present document are subject to continuing work within SMG and may change following formal SMG approval. Should SMG modify the contents of the present document it will then be republished by ETSI with an identifying change of release date and an increase in version number as follows:

Version 7.x.y

where:

7	indicates GSM Release 1998 of Phase 2+

x	the second digit is incremented for all other types of changes, i.e. technical enhancements, corrections, updates, etc.

y	the third digit is incremented when editorial only changes have been incorporated in the specification.

# Introduction

The present document includes references to features which were introduced into the GSM Technical specifications after Release 96 of GSM Phase 2+. The text that is relevant, if the feature is supported, is marked with designators.

The following table lists all features that were introduced after Release 96 and have impacted this specification:

| Feature | Designator |
| --- | --- |
| In Phase 2+ systems the Restart-Ind, Failure-Ind and Set-DRX-Resp PDUs supply consistent cell-list formats from the BSC. | $(Phase2PBscCellLists)$ |

# 1	Scope

No mandatory protocol between the Cell Broadcast Centre (CBC) and the Base Station Controller (BSC) is specified by GSM; this is a matter of agreement between CBC and PLMN operators.

The present document specifies three alternative approaches to the specification of protocol stacks of communication protocols for the purpose of fulfilling the service requirements of the primitives specified for the CBC - BSC interface in GSM 03.41.

One approach is based upon the use of the complete OSI reference model (see X.200), another approach is based upon the use of only the lower 3 OSI layers, and another approach is based upon the use of CCITT Signalling System No. 7 (see Q.700).

Specifications are based upon individual contributions. Any judgement concerning functionality, completeness and advantages/disadvantages of implementation is intentionally omitted.

## 1.1	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

- References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

- For a specific reference, subsequent revisions do not apply.

- For a non-specific reference, the latest version applies.

- A non-specific reference to an ETS shall also be taken to refer to later versions published as an EN with the same number.

- For this Release 1998 document, references to GSM documents are for Release 1998 versions (version 7.x.y).

[1]	GSM 01.04: "Digital cellular telecommunications system (Phase 2+); Abbreviations and acronyms".

[2]	GSM 03.41: "Digital cellular telecommunications system (Phase 2+); Technical realization of Short Message Service Cell Broadcast (SMSCB)".

[3]	GSM 12.20: "Digital cellular telecommunication system (Phase 2); Network Management (NM) procedures and messages".

[4]	CCITT Recommendation Q.700: "Introduction to CCITT Signalling System No.7".

[5]	CCITT Recommendation Q.931: Integrated services digital network.(ISDN) User-Network interface layer 3 specification for basic control".

[6]	CCITT Recommendation Q.932: "Generic procedures for the control of ISDN supplementary services".

[7]	CCITT Recommendation Q.941: "ISDN user-network interface protocol profile for management".

[8]	CCITT Recommendation Q.1400: "Architecture framework for the development of signalling and organisation, administration and maintenance protocols using OSI concepts".

[9]	CCITT Recommendation X.2 (1988): "International data transmission services and optional user facilities in public data networks and ISDNs".

[10]	CCITT Recommendation X.200: "Reference Model of Open Systems Interconnection for CCITT Applications".

[11]	CCITT Recommendation X.213: "Information technology - Network service definition for Open Systems Interconnection".

[12]	CCITT Recommendation X.215: "Session service definition for open systems interconnection for CCITT applications".

[13]	CCITT Recommendation X.217: "Association control service definition for open systems interconnection for CCITT applications".

[14]	CCITT Recommendation X.219: " Remote operations: model, notation and service definition".

[15]	CCITT Recommendation X.225: "Session protocol specification for Open Systems Interconnection for CCITT Applications".

[16]	CCITT Recommendation X.227: "Information technology - Open Systems Interconnection - protocol specification for the association".

[17]	CCITT Recommendation X.229: "Remote operations Protocol specification".

[18]	GSM 10.01: "Digital cellular telecommunication system (Phase 2+); GSM features and releases"

## 1.2	Abbreviations

Abbreviations used in the present document are listed in GSM 01.04.

# 2	A protocol stack which utilises an application-network layer convergence function for interconnecting CBC and BSC

A convergence function (see Draft CCITT Recommendation Q.941 Report R 22 May 1990) which maps an application entity protocol directly to the Network Layer service defined by X.213 can provide a practical alternative to ACSE, ROSE and OSI layers 6, 5 and 4.

Figure 1

Draft CCITT Recommendation Q.941 proposes to map application layer protocols ACSE and ROSE via a convergence function to network layers defined by CCITT Recommendations Q.931 and Q.932.

The complexity of dealing with the many different network layer protocols is avoided by mapping the application protocols to the Network Layer Service defined by X.213. ACSE and ROSE are specifically defined in terms of the full OSI stack. The use of ACSE and ROSE is avoided by incorporating the functionality provided by ACSE and ROSE into the CBS protocol. The convergence function is embedded in the CBS protocol.

## 2.1	CBSE Definition

The Cell Broadcast Short Message Service Element (CBSE) is defined in terms of the following service:

CBSE-BIND

This operation must be invoked by the party which is responsible for establishing the application association; only after the application association has been established may the remaining CBSE services be used. This operation reports either success (via CBSE-Bind-Confirm) or failure (via CBSE-Bind-Failure).

CBSE-BIND will be mapped to/from N-CONNECT request/indication with CBSE-BIND parameters carried in NS-user-data (if the network layer does not support NS-user-data of 128 octets then CBSE-BIND parameters may be carried by the first N-DATA request/indication following establishment of the network layer connection - see subclause 2.4).

This operation is retained for backward compatibility with Phase 2 systems.

NOTE: 	This PDU should be used in the case of a Phase 2+ entity communicating with a Phase 2 entity.

CBSE-VBIND

This operation must be invoked by the party which is responsible for establishing the application association; only after the application association has been established may the remaining CBSE services be used. This operation reports either success (via CBSE-Bind-Confirm) or failure (via CBSE-Bind-Failure).

CBSE-VBIND will be mapped to/from N-CONNECT request/indication with CBSE-VBIND parameters carried in NS-user-data (if the network layer does not support NS-user-data of 128 octets then CBSE-VBIND parameters may be carried by the first N-DATA request/indication following establishment of the network layer connection - see subclause 2.4).

This operation is used in Phase 2+ systems.

CBSE-BIND-CONFIRM

This operation must be invoked by a party to accept an application association.

CBSE-BIND-CONFIRM will be mapped to/from N-CONNECT confirm/response with CBSE-BIND-CONFIRM parameters carried in NS-user-data (if the network layer does not support NS-user-data of 128 octets then CBSE-BIND-CONFIRM may be carried as the second N-DATA request/indication following establishment of the network layer connection - see Section 2.4).

On receipt of a CBSE-BIND PDU, the recipient must assume that the sender is supporting the Phase 2 version of the interface and must reply with an untagged CBSE-BIND-CONFIRM. If a CBSE-VBIND PDU is received, the recipient must reply with a tagged CBSE-BIND-CONFIRM as a substructure of CBSEapdus.

CBSE-BIND-FAILURE

This operation must be invoked by a party to reject an attempted application association.

CBSE-BIND-FAILURE will be mapped to/from N-DISCONNECT request/indication with CBSE-BIND-FAILURE parameters carried in NS-user-data (if the network layer does not support NS-user-data of 128 octets then CBSE-BIND-FAILURE parameters  shall be carried by the N-DATA request/indication preceding N-DISCONNECT.

GSM phase2 compliance:

If the network layer does not support NS-user-data of 128 octets then CBSE-BIND-FAILURE parameters will not be carried by the network layer - i.e. NS-user-data will be discarded).

CBSE-UNBIND

This operation must be invoked by a party to release the application association.

CBSE-UNBIND will be mapped to/from N-DISCONNECT request/indication with CBSE-UNBIND parameters be carried in NS-user-data (if the network layer does not support NS-user-data of 128 octets then CBSE-UNBIND parameters shall be carried by the N-DATA request/indication preceding N-DISCONNECT - see Section 2.4 ).

GSM phase 2 compliance:

If the network layer does not support NS-user-data of 128 octets then reception of N-DISCONNECT shall be interpreted as a CBSE-UNBIND even if the N-DISCONNECT is not preceded by a N-DATA packet carrying the CBSE-UNBIND parameters.

$start$(Phase2PBscCellLists)$

CBSE-WRITE-REPLACE, CBSE-KILL, CBSE-REPORT,

CBSE-STATUS-CBCH-QUERY, CBSE-STATUS-CBCH-QUERY-RESP, CBSE-STATUS-MESS-QUERY, CBSE-STATUS-MESS-QUERY-RESP, CBSE-REJECT, CBSE-RESTART-IND, CBSE-RESTART-IND-PHASE2P, CBSE-RESET, CSE-FAILURE-IND, CSE-FAILURE-IND-PHASE2P, CBSE-SET-DRX, CBSE-SET-DRX-RESP

Application data units CBSE-WRITE-REPLACE, CBSE-KILL, CBSE-REPORT, CBSE-STATUS-CBCH-QUERY, CBSE-STATUS-CBCH-QUERY-RESP, CBSE-STATUS-MESSAGE-QUERY, CBSE-STATUS-MESS-QUERY-RESP., CBSE- REJECT, CBSE -RESTART-IND, CBSE -RESTART-IND-PHASE2P, CBSE-RESET, CBSE-FAILURE-IND, CBSE-FAILURE-IND-PHASE2P, CBSE-SET-DRX, CBSE-SET-DRX-RESP provide the services specified via primitives Write-Replace, Kill, Report, Status-CBCH, Status-CBCH-Response, Status-Message, Status-Message-Response, Reject, Restart-Indication, Restart-Indication-Phase2P, Reset, Failure-Indication, Failure-Indication-Phase2P, Set-DRX and Set-DRX-Response respectively in GSM 03.41.

$end$(Phase2PBscCellLists)$

These application data units will be mapped to/from N-DATA request/indication.

## 2.2	ASN1 Specification

The Abstract Syntax Notation of the Cell Broadcast Short Message Service Element


CBSE

1st module of 2:

CBS-UsefulDefinitions

CBS-UsefulDefinitions	{

ccitt identified-organization (4) etsi (0) mobile-domain (0)

gsm-messaging (4) gsm-sms3 (12) usefulDefinitions (10) }

DEFINITIONS

IMPLICIT TAGS

::=

BEGIN

ID	::= OBJECT IDENTIFIER

mobile-domain ID	::= {ccitt identified-organization (4) etsi (0) mobile-domain(0)}

--	root for all sms allocations

gsm-messaging ID	::= { mobile-domain gsm-messaging(4) }

--	categories

gsm-sms3 ID		::= { gsm-messaging 12 }

END

2nd module of 2:

Application Protocol

ApplicationProtocol {

ccitt identified-organization (4) etsi (0) mobile-domain(0)

gsm-messaging(4) gsm-sms3 (12) applicationProtocol(11) }

DEFINITIONS

IMPLICIT TAGS

::=

BEGIN

--	CBSE-BIND will be carried as N-CONNECT request/indication

--	CBSE-BIND-Parameters will carried in the User Data field of the N-CONNECT

--	request/indication message.

--  Note that this structure should be used by Phase 2 systems only.

CBSE-BIND-Parameters ::=  SEQUENCE {

initiatorID	[0] Name,

password	[1] Password   OPTIONAL

}

--	Above and in CBSE-BIND-CONFIRM

--	initiatorID/respID: identify the initiating/responding telecommunication subsystem

--	password: may assist in authentication

--	CBSE-VBIND-Parameters will only be used as an element of CBSEapdus in the

--  User Data field of the N-CONNECT request/indication message.

--  Note that this structure should be used by Phase 2+ and higher systems only.

CBSE-VBIND-Parameters ::=  SEQUENCE {

initiatorID	[0] Name,

password	[1] Password   OPTIONAL,

version		[2]	Version

}

--	Above

--	initiatorID/respID: identify the initiating/responding telecommunication subsystem

--	password: may assist in authentication

--	version: identify the interface version supported, defined below

Name ::=    SEQUENCE {

operator			[0] Operator		OPTIONAL,

bilateralAgreem		[1] BilateralAgreem	OPTIONAL,

dataNetworkAddress	[2] Xl2lAddress	OPTIONAL,

iSDNAddress		[3] CBS-Address	OPTIONAL

}

--	operator is a text string containing the name of the CBC/PLMN operator. bilateralagreem is a text

--	string identifying the bilateral agreement between the CBC and the PLMN operators which allows

--	for this association to be established.

--	dataNetworkAddress is the PSPDN X.121 address of the CBC/BSC issuing the BIND or

--	CONFIRM, occurring only if a PSPDN is used.

--	iSDNAddress is the PLMN address of the CBC (same datum in both BIND and CONFIRM).

--	Any pair of subsets of these parameters may be used to identify the CBC and the BSC to one

--	another.

--	upper bound settings

Operator ::= PrintableString (SIZE (0..20))

BilateralAgreem  ::=  PrintableString  (SIZE (0 .. 20))

Xl2lAddress ::= NumericString  (SIZE(0..15))

--	Definition of Cell Broadcast Short Message Service address

CBS-Address	::= [APPLICATION 0]  SEQUENCE {

address-type      INTEGER {  unknown-type(0),

international-number(1),

national-number(2),

network-specific-number(3),

short-number(4) },

numbering-plan  INTEGER   { unknown-numbering(0),

iSDN-numbering(1),

data-network-numbering(3),

telex-numbering(4),

national-numbering(8),

private-numbering(9) },

address-value     CHOICE   {

octet-format

SemiOctetString

-- other formats are for further study

}

}

--	each octet contains two binary coded decimal digits

SemiOctetString ::=  OCTET STRING (SIZE(1..10))

Password	::=   PrintableString  (SIZE(0..20))

--	Version provides one of the indications given in the following table.

--  Any future substantive interface definition changes must be added to this table.

Table 1

| Version indication | Document Version | Compatible with previous version |
| --- | --- | --- |
| release-97 | This mandates adherence to 03.49 version 6.0.0. | No (see Note 1) |
| reserved-1 |  |  |
| reserved-2 |  |  |
| reserved-3 |  |  |
| reserved-4 |  |  |
| reserved-5 |  |  |
| reserved-6 |  |  |

Note 1: PDUs not backwards compatible with Phase 2 include, but may not be limited to, Report, Reject, Status-CBCH-Resp, and Status-Mess-Resp.

Version	::=  INTEGER {

release-97 (0),

reserved-1 (1),

reserved-2 (2),

reserved-3 (3),

reserved-4 (4),

reserved-5 (5),

reserved-6 (6)

}

--	CBSE-BIND-CONFIRM will carried as N-CONNECT response/confirm

--	CBSE-BIND-CONFIRM parameters will be carried in User Data of the N-CONNECT

--	response/confirm message

CBSE-BIND-CONFIRM-Parameters ::=    SEQUENCE {

respId		[0] Name,

password	[1] Password     OPTIONAL

}

--	The following defines the choices and tags for the N-DISCONNECT.request/indication User Data.

Applic-protocol-discs	::= CHOICE {

bindfail [1] CBSE-BIND-FAILURE,

unbindreq [2] CBSE-UNBIND

}

CBSE-BIND-FAILURE	::= Connect-failure-reason

--	connect-failure-reason provides one of the error indications given in the following table.

Table 2

| Error indications | Reason |
| --- | --- |
| not-entitled | The responder is not entitled to accept a request for an association between itself and the initiator. |
| temporary-overload | The responder is not capable of establishing an association due to temporary overload. |
| temporary-failure | The responder is not capable of establishing an association due to a temporary failure. |
| incorrect-ID-or-password | The responder will not accept the request to establish an association between itself and the initiator due to incorrect identity or password. |
| version-unsupported | The version specified is not supported by the recipient. |

--

Connect-failure-reason	::=  INTEGER {

not-entitled (0),

temporary-overload (1),

temporary-failure (2),

incorrect-ID-or-password (3),

version-unsupported (4)

}

CBSE-UNBIND  ::= NULL

--	The following defines the choices and tags for the N-DATA.request/indication User Data

CBSMSEapdus		::=	CHOICE {

cbse-WRITE-REPLACE			[1] Write-Replace,

cbse-KILL					[2] Kill,

cbse-REPORT					[3] Report,

cbse-STATUS-CBCH-QUERY		[4] Status-CBCH,

cbse-STATUS-CBCH-QUERY-RESP	[5] Status-CBCH-Resp,

cbse-STATUS-MESSAGE-QUERY	[6] Status-Message,

cbse-STATUS-MESS-QUERY-RESP	[7] Status-Mess-Resp,

cbse-REJECT					[8]	Reject,

cbse-RESTART-IND			[9] Restart-Ind,

cbse-RESET					[10] Reset,

cbse-FAILURE-IND			[11] Failure-Ind,

cbse-SET-DRX				[12] Set-DRX,

cbse-SET-DRX-RESP			[13] Set-DRX-Resp,

cbse-VBIND					[14] CBSE-VBIND-Parameters,

cbse-BIND-CONFIRM			[15] CBSE-BIND-CONFIRM-Parameters,

cbse-BIND-FAILURE			[16] CBSE-BIND-FAILURE,

cbse-UNBIND					[17] CBSE-UNBIND,

cbse-RESTART-IND-PHASE2P	[18] Restart-Ind-Phase2P, --	$(Phase2PBscCellLists)$

cbse-FAILURE-IND-PHASE2P	[19] Failure-Ind-Phase2P  --	$(Phase2PBscCellLists)$

}

--	PDU parameter definitions from 03.41

Message-Identifier			::= INTEGER (0 .. 65535)

Serial-Number				::= INTEGER (0 .. 65535)

No-of-Pages					::=	INTEGER (1 .. 15)

Cell-List					::= SEQUENCE {

length	INTEGER, -- number of cells in the list

disc	Cell-Id-Disc,

list	SEQUENCE OF Cell-Id

}

Channel						::= INTEGER {

basic-channel (0),

extended-channel (1)

}

Category					::=	INTEGER {

high-priority (0),

normal-priority (1),

background (2)

}

Repetition-Period			::=	INTEGER (1 .. 1024)

No-of-Broadcast-Req			::=	INTEGER (0 ..65535)

No-of-Broadcasts-Compl-List ::=	SEQUENCE OF SEQUENCE {

cell-id						Cell,

no-of-broadcasts-compl		INTEGER,

no-of-broadcasts-compl-info No-of-Broadcasts-Compl-Info-Type OPTIONAL

}

Cell-Id						::=	OCTET STRING (SIZE(4))

--								Note:

--								If Cell-Id-Disc equals ciOnly then only the last 2 octets of

--								Cell-ID are to be considered

--								If Cell-Id-Disc equals lacOnly then only the first 2 octets of

--								Cell-ID are to be considered. The unused octets are filler octets

--								If Cell-Id-Disc equals allCells, Cell-ID only contains filler octets

Schedule-Period				::= INTEGER (0 .. 40)

Reserved-Slots				::= INTEGER (0 .. 40)

Failure-List				::=	SEQUENCE OF SEQUENCE {

cell-id		Cell,

cause		Failure-Reason,

diagnostic	Diagnostic-Info	OPTIONAL

}

Cbch-Loading-List 			::=	SEQUENCE OF SEQUENCE{

cell-id				Cell,

cbch-loading		Cbch-Loading

-- 								indicates the predicted short term load, expressed as a percentage

-- 								(min:0, max: 100)

}

Cbch-Loading				::=	INTEGER(0..100)

Failure-Reason 				::= INTEGER {

parameter-not-recognised (0),

unused-failure-reason-1 (1), -- not used

parameter-value-invalid (2),

valid-CBS-message-not-identified (3),

cell-identity-not-valid (4),

unrecognised-primitive (5),

missing-mandatory-element (6),

bss-capacity-exceeded (7),

cell-memory-exceeded (8),

bss-memory-exceeded (9),

unspecifed-error (10),

incompatible-DRX-parameter (11),

unused-failure-reason-12 (12), -- not used

cell-broadcast-not-supported (13),

cell-broadcast-not-operational (14),

extended-channel-not-supported (15),

message-reference-already-used (16)

}

Diagnostic-Info 			::= OCTET STRING (SIZE (1..20))

Data-Coding-Scheme			::=	INTEGER (0 .. 255)

Page-Inf					::= SEQUENCE {

message-info-useful-octets	Message-Info-Useful-Octets,

message-info-page			Message-Info-Page

}

Message-Info-Useful-Octets	::=	INTEGER (0..82)

Recovery-Indication			::= BOOLEAN

-- 								TRUE indicates data is available

-- 								False indicates data is lost

--	Definitions used by the PDU parameters

Message-Info-Page			::=	OCTET STRING (SIZE(82))

Cell-Id-Disc				::= OCTET STRING (SIZE(1))

-- 								values from the following table

lacAndCi OCTET STRING (SIZE(1)) ::= '1'H -- 2 Octet lac, followed by 2 Octet Cell Id

ciOnly OCTET STRING (SIZE(1))   ::= '2'H -- Cell Id only

lacOnly OCTET STRING (SIZE(1))  ::= '5'H -- 2 Octet lac only, all cells in this LAC (NOT USED BY BSC)

allCells OCTET STRING (SIZE(1)) ::= '6'H -- all cells in this BSS  (NOT USED BY BSC)

Cell						::=	SEQUENCE {

disc		Cell-Id-Disc,

id		Cell-Id

}

No-of-Broadcasts-Compl-Info-Type::=  INTEGER {

unknown (0),

overflow (1)

}

--	Definitions of PDUs

Write-Replace	::= SEQUENCE {

message-Identifier		Message-Identifier,

new-Serial-Number		Serial-Number,

no-of-Pages				No-of-Pages,

data-coding-scheme		Data-Coding-Scheme,

cell-list				Cell-List,

repetition-Period		Repetition-Period,

no-of-broadcast-req		No-of-Broadcast-Req,

cbs-Page-Inf			SEQUENCE OF [15] Page-Inf,

old-Serial-Number		[3] Serial-Number 	OPTIONAL,

category				[2] Category	OPTIONAL,

channel-indicator		[4] Channel		OPTIONAL

}

Kill	::= SEQUENCE {

message-Identifier		Message-Identifier,

old-Serial-Number		Serial-Number,

cell-List				Cell-List,

channel-indicator		[4] Channel		OPTIONAL

}

Report	::= SEQUENCE {

message-Identifier				Message-Identifier,

serial-Number					Serial-Number,

no-of-Broadcasts-Compl-List		[0] No-of-Broadcasts-Compl-List OPTIONAL,

failure-List					[1] Failure-List OPTIONAL,

channel-indicator				[4] Channel		OPTIONAL

}

Status-CBCH		::= SEQUENCE{

cell-List				Cell-List,

channel-indicator		[4] Channel		OPTIONAL

}

Status-CBCH-Resp	::= SEQUENCE{

cbch-loading-List		[0] Cbch-Loading-List OPTIONAL,

failure-List			[1] Failure-List OPTIONAL,

channel-indicator		[4] Channel		OPTIONAL

}

Status-Message	::= SEQUENCE {

message-Identifier	Message-Identifier,

old-Serial-No		Serial-Number,

cell-List			Cell-List,

channel-indicator	[4] Channel		OPTIONAL

}

Status-Mess-Resp	::= SEQUENCE {

message-Identifier				Message-Identifier,

old-serial-number				Serial-Number,

no-of-Broadcasts-Compl-List		[0] No-of-Broadcasts-Compl-List OPTIONAL,

failure-List					[1] Failure-List OPTIONAL,

channel-indicator				[4] Channel		OPTIONAL

}

Reject::= SEQUENCE {

cause				Failure-Reason,

diagnostic			Diagnostic-Info	OPTIONAL,

message-Identifier	[7]	Message-Identifier	OPTIONAL,

serial-Number		[3]	Serial-Number	OPTIONAL

}

--	$start$(Phase2PBscCellLists)$

--	The Restart-Ind PDU is retained for backward compatibility with Phase 2 systems,

--	and may be used in Phase 2+ systems

Restart-Ind	::= SEQUENCE {

cell-list				Cell-List,

recovery-Indication		Recovery-Indication		OPTIONAL

}

--	coding of the recovery-Indication states is Data-available TRUE, Data-lost FALSE

--	The Restart-Ind-Phase2P PDU is used in Phase 2+ systems

Restart-Ind-Phase2P	::= CHOICE {

restart-list1		[0] SEQUENCE {

cell-list				Cell-List,

recovery-Indication		Recovery-Indication	OPTIONAL

},

restart-list2		[1]	SEQUENCE {

cell-list				SEQUENCE OF Cell,

recovery-Indication		Recovery-Indication	OPTIONAL

}

}

--	$end$(Phase2PBscCellLists)$

Reset			::= SEQUENCE {

cell-list		Cell-List

}

Set-DRX	::= SEQUENCE {

cell-list			Cell-List,

schedule-Period		[6]	Schedule-Period	OPTIONAL,

reserved-Slots		[2] Reserved-Slots	OPTIONAL,

channel-indicator	[4] Channel			OPTIONAL

}

--	$start$(Phase2PBscCellLists)$

Set-DRX-Resp	::= SEQUENCE {

cell-list					[0]	SEQUENCE OF Cell	OPTIONAL,

failure-List				[1] Failure-List OPTIONAL,

channel-indicator			[4] Channel		OPTIONAL

}

--	$end$(Phase2PBscCellLists)$

--	$start$(Phase2PBscCellLists)$

--	The Failure-Ind PDU is retained for backward compatibility with Phase 2 systems,

--	and may be used in Phase 2+ systems

Failure-Ind	::= SEQUENCE{

cell-list		Cell-List

}

--	$start$(Phase2PBscCellLists)$

--	The Failure-Ind-Phase2P PDU is used in Phase 2+ systems

Failure-Ind-Phase2P	::= CHOICE {

failure-list1		[0]	SEQUENCE {

cell-list		Cell-List

},

failure-list2		[1]	SEQUENCE OF Cell

}

--	$end$(Phase2PBscCellLists)$

END

## 2.3	Application Rules for Avoidance of Collision of CBSE Operations

For the purpose of establishing the association between CBSEs in CBC and BSC then either the CBC or the BSC shall be designated as the entity responsible for initiating the association by the operation CBSE-BIND.

Following premature release of the association by N-DISCONNECT then either the CBC or the BSC shall be designated as the entity responsible for re-establishing the association.

Following receipt of N-RESET any command sent by the CBC, for which no corresponding response has been received by the CBC, will be re-sent to the BSC.

## 2.4	Non Support of 128 bytes of NS-user-data in Network Connection and Network Connection Release phases

It is generally intended to make the support of 128 bytes of NS user-data mandatory (see Sections 12.2.8 and 13.2.3 of X.213). CCITT Recommendation X.2 regards provision of Fast Select as essential, thereby ensuring support of 128 bytes of NS-user-data in network connection and network connection release phases. For an interim period support of 128 bytes of NS-user-data in network connection and network connection release phases will remain a provider option. The following figures are therefore provided in order to indicate how CBSE-BIND, CBSE-BIND-CONFIRM, CBSE-BIND-FAILURE and CBSE-UNBIND should be mapped to/from an OSI Network Service definition which does not support 128 bytes of NS-user-data in network connection and network connection release phases.

NOTE 1:	CBSMSE-BIND parameters are carried as NS-user-data.

NOTE 2:	CBSMSE-BIND-CONFIRM is carried as NS-user-data.

NOTE 3:	CBSMSE-BIND-FAILURE is carried as NS-user-data

NOTE 4:	CBSMSE-UNBIND parameters are carried as NS-user-data.

Figure 2

# 3	An OSI Protocol Stack For Interconnecting CBC and BSC

This clause specifies a stack of communication protocols in terms of the OSI Reference Model (see X.200) and therefore makes use of all seven layers for the purpose of fulfilling the service requirements of the primitives specified for the CBC - BSC interface in GSM 03.41. The CBS application layer (layer 7) is mapped to the Presentation Layer via ACSE (see X.217 and X.227) and ROSE (see X.219 and X.229). Only the Kernel functional unit of the Presentation Layer is used. Only the Kernel and Duplex functional units are used in the Session Layer (see X.215 and X.225).

## 3.1	Service elements on the application layer

An association (class 3) between CBRSEs is formed via ACSE and ROSE operations (class 2 and 5) are used to implement the service requirements specified for the CBC - BSC interface in GSM 03.41.

This results in an asynchronous asymmetric situation where the application entity in the CBC or BSC can invoke a CBRSE operation at any time.

The new CBRSE service element is first defined in the following subclause, and then specified in ASN.1 notation in subclause 3.2.

CBRSE definition

This service element defines the following services:

CBRSE-BIND	This operation will normally be invoked by the CBC to establish the application association, but in exceptional circumstances (e.g. following loss of data) the BSC may invoke the operation; only thereafter the remaining CBRSE services may be used. This operation reports either success or failure (result or error).

CBR-WRITE-REPLACE, CBR-KILL, CBR-STATUS-CBCH-QUERY, CBR-STATUS-MESSAGE-QUERY, CBR-RESET, CBR-SET-DRX

These operations may be invoked by the application entity in the CBC; They are used to relay commands from the CBC to a given BSC. The operations report either success or failure.

$start$(Phase2PBscCellLists)$

CBR-RESTART-IND, CBR-RESTART-IND-PHASE2P, CBR-FAILURE-IND, CBR-FAILURE-IND-PHASE2P

This operation may be invoked by the application entity in the BSC. The operation reports success or failure.

$end$(Phase2PBscCellLists)$

CBR-UNBIND	This operation must be invoked by the CBC as the last CBRSE operation before releasing the application association. This operation reports success only.

Of the services defined above, CBR-WRITE-REPLACE semantically means the relay of cell broadcast messages across the CBC-BSC-connection in order to add them to the message list in the BSC, whereas CBR-KILL is used to delete messages from the message list. The CBR-STATUS-CBCH-QUERY command inquires after the current loading of a specific cell broadcast channel, while the CBR-STATUS-MESSAGE-QUERY command requests status information concerning a specific message. The CBR-SET-DRX  command sets the DRX related parameters. These five services combine the primitives defined in GSM 03.41, which can be invoked by the CBC.

The CBR-BIND service is used to exchange identifications, passwords, etc., and in order to negotiate the usage of the other services. The CBR-UNBIND service prepares for the release of the application association.

## 3.2	Detailed specification of the CBRSE services

On the following pages, the new CBRSE service element is specified with the ASN.1 notation, together with the entire protocol.

The Abstract Syntax Notation of
the Cell Broadcast Relay Service Element

CBRSE

1st module of 3:

CBS-UsefulDefinitions

CBS-UsefulDefinitions	{

ccitt identified-organization (4) etsi (0) mobile-domain(0)

gsm-messaging(4)  gsm-sms4(13)  usefulDefinitions(0) }

DEFINITIONS

IMPLICIT TAGS

::=

BEGIN

EXPORTS		id-cb-ot-CBC, id-cb-ot-BSC, id-cb-port,

id-cb-ac-so, id-cb-CBRSE, id-cb-as-CBRSE;

ID	::= OBJECT IDENTIFIER

mobile-domain ID	::= { ccitt identified-organization (4) etsi (0) mobile-domain (0)}

--	root for all sms allocations

gsm-messaging	ID ::= { mobile-domain gsm-messaging (4) }

gsm-sms4	ID	::= {gsm-messaging (13)}

--	categories

id-cb-mod	ID ::= { gsm-messaging 1 } -- modules

id-cb-ot		ID ::= { gsm-messaging 2 } -- object type

id-cb-pt		ID ::= { gsm-messaging 3 } -- port types

id-cb-ac		ID ::= { gsm-messaging 4 } -- appl. contexts

id-cb-ase		ID ::= { gsm-messaging 5 } -- ASEs

id-cb-as		ID ::= { gsm-messaging 6 } -- abstract syntaxes

--	modules

usefulDefinitions		ID ::= { gsm-sms4 0 }

relayProtocol		ID ::= { gsm-sms4 1 }

relayAbstractService	ID ::= { gsm-sms4 2 }

--	object types

id-cb-ot-CBC		ID ::= { id-cb-ot 0 }

id-cb-ot-BSC		ID ::= { id-cb-ot 1 }

--	port types

id-cb-port		ID ::= { id-cb-pt 0 }

--	application contexts

id-cb-ac-so		ID ::= { id-cb-ac 0 }

--	application service elements

id-cb-CBRSE		ID ::= { id-cb-ase 0 }

--	abstract syntaxes

id-cb-as-CBRSE		ID ::= { id-cb-as 0 }

END

2nd module of 3

RelayAbstractService

RelayAbstractService	{

ccitt identified-organization (4) etsi (0) mobile-domain(0)

gsm-messaging(4) gsm-sms4(13)  relayAbstractService(2) }

DEFINITIONS

IMPLICIT TAGS

::=

BEGIN

IMPORTS

BIND, UNBIND

FROM Remote-Operations-Notation {

joint-iso-ccitt remote-operations(4) notation(0) }

OBJECT, PORT, ABSTRACT-BIND, ABSTRACT-UNBIND,

ABSTRACT-OPERATION, ABSTRACT-ERROR

FROM AbstractServiceNotation {

joint-iso-ccitt mhs-motis(6) asdc(2) modules(0) notation(1) }

id-cb-ot-CBC, id-cb-ot-BSC, id-cb-port

FROM CBS-UsefulDefinitions{

ccitt identified-organization (4) etsi (0) mobile-domain(0)

gsm-messaging(4) gsm-sms4(13) usefulDefinitions(0) }

--	upper bound settings

ub-operator-name-length INTEGER	::=	20

ub-agreem-name-length INTEGER	::=	20

ub-X121Address-length INTEGER	::=	15

ub-password-length INTEGER		::=	20

--	Objects

--	The CBC and the BSC are modelled as atomic objects, cBC--Object and bSC-Object. Each

--	object has one port for the interconnection. ([S] and [C] indicate supply and consumption of

--	services, respectively).

cBC-Object	OBJECT

PORTS { cBR-port [S] }

::= id-cb-ot-CBC

bSC-Object	OBJECT

PORTS { cBR-port [C] }

::= id-cb-ot-BSC

--	Port

cBR-port	PORT

CONSUMER INVOKES {CBR-Restart-Ind

--	$start$(Phase2PBscCellLists)$

CBR-Restart-Ind-Phase2P

CBR-Failure-Ind

CBR-Failure-Ind-Phase2P

--	$end$(Phase2PBscCellLists)$

}
			SUPPLIER INVOKES  { CBR-Write-Replace

CBR-Kill

CBR-Status-CBCH-Query

CBR-Status-Message-Query

CBR-Reset

CBR-Set-DRX
				 }

::= id-cb-port

--	The CBR-Bind operation

--	Both, BIND and UNBIND operations, are exclusively within the responsibility of the CBC. The

--	BIND operation is therefore always requested by the CBC

--  Note that this structure should be used by Phase 2 systems only.

CBR-Bind ::=

ABSTRACT-BIND

TO { cBR-port }

BIND

ARGUMENT    CBR-Bind-Parameters

RESULT      CBR-Bind-confirm

BIND-ERROR  CBR-Bind-failure

--	The CBR-Unbind operation

--	The UNBIND is a harsh release of the association and all outstanding operations are aborted.

--	UNBIND is always requested by the CBC. The CBC and the BSC should negotiate (during

--	CBR-BIND) the use of services on the association (the operations parameter - list of 	operation

--	types for the association) in such a way that no harmful losses of operations occur.

CBR-Unbind ::=

ABSTRACT-UNBIND

FROM { cBR-port }

UNBIND

ARGUMENT     Time-when-connected

RESULT       Time-when-disconnected

-	Association control parameters

CBR-Bind-Parameters ::=	SEQUENCE {

initiatorID	[0] Name,

password	[1] Password OPTIONAL,

pswNeeded	[2] BOOLEAN,

iniType	[3] Telecom-System-Type,

operations	[4] List-of-Operations,

transient	[5] BOOLEAN

}

--	Above and in SMR-Bind-confirm

--	initiatorID/respID: identify the initiating/responding telecommunication subsystem

--	password: may assist in authentication

--	pswNeeded (BIND only):requests password into SMR-Bind, SMR-Bind-Confirm

--	iniType/respType: identify the system entity

--	operations: lists the SM relay operations requested and supported on the association:

--	operations listed in both the BIND and the CONFIRM may be used (i.e. this is a negotiation

--	between CBC and BSC)

--	transient:forces the association (and the underlying connections), transient: it must be

--	UNBouND as soon as there are no operations to be performed

Name	::= SEQUENCE {

operator		[0] Operator		OPTIONAL,

bilateralAgreem	[1] BilateralAgreem	OPTIONAL,

dataNetworkAddress	[2] X121Address	OPTIONAL,

iSDNAddress		[3] CBS-Address	OPTIONAL

}

--	operator is a text string containing the name of the CBC/PLMN operator. bilateralAgreem is a

--	text string identifying the bilateral agreement between the CBC and the PLMN operators

--	which allows for this association to be established.

--	dataNetworkAddress is the PSPDN X.121 address of the CBC/BSC issuing the BIND or

--	CONFIRM, occurring only if a PSPDN is used.

--	iSDNAddress is the PLMN address of the CBC as seen by the MSs (same datum in both BIND

and CONFIRM).

--	Any pair of subsets of these parameters may be used to identify the CBC and the BSC to one

--	another.

Operator ::=	PrintableString (SIZE(0..ub-operator-name-length))

BilateralAgreem ::=		PrintableString  (SIZE(0..ub-agreem-name-length))

X121Address	::=	NumericString  (SIZE(0..ub-X121Address-length))

--	CBS-Address is specified later in this module.

Password ::=	PrintableString  (SIZE(0..ub-password-length))

--	Version provides one of the indications given in the following table.

--  Any future substantive interface definition changes must be added to Table 1.

--  For definitions see Table 1.

Version	::=  INTEGER {

release-97 (0),

reserved-1 (1),

reserved-2 (2),

reserved-3 (3),

reserved-4 (4),

reserved-5 (5),

reserved-6 (6)

}

Telecom-System-Type	::= INTEGER {

cell-Broadcast-Service-Centre	(0),

public-Land-Mobile-Network	(1)

--	Extensions are possible: additional telecommunication subsystems 			--	might adopt this service element for their interconnection.

}

List-of-Operations	::= BIT STRING {

cBR-From-CBC-Write-Replace	(0),

cBR-From-CBC-Kill	(1),

cBR-From-CBC-Status-CBCH-Query	(2),

cBR-From-CBC-Status-Message-Query (3),

cBR-From-BSC-Restart-Ind (4),

cBR-From-CBC-Reset (5),

cBR-From-BSC-Failure-Ind (6),

cBR-From- CBC-Set-DRX (7),

cBR-From-BSC-VBind-Request (8),

cBR-From-BSC-Bind-Confirm (9),

cBR-From-BSC-Bind-Failure (10),

cBR-From-BSC-UnBind (11),

--	$start$(Phase2PBscCellLists)$

cBR-From-BSC-Restart-Ind-Phase2P (12),

cBR-From-BSC-Failure-Ind-Phase2P (13)

--	$end$(Phase2PBscCellLists)$

--	Extensions are possible: additional operations may be defined

--	within this service element. Existing systems should tolerate

--	unknown values, but negotiate not to perform unknown

--	operations.}

--  Note that this element replaces the CBR-Bind structure for Phase 2+ and beyond.

CBR-VBind-Request ::=

ABSTRACT-VBIND

TO { cBR-port }

BIND

ARGUMENT    CBR-VBind-Parameters

RESULT      CBR-Bind-confirm

BIND-ERROR  CBR-Bind-failure

CBR-Bind-confirm	::= SEQUENCE {

respId	[0] Name,

password	[1] Password OPTIONAL,

respType	[3] Telecom-System-Type,

operations	[4] List-of-Operations,

transient	[5] BOOLEAN,

connectTime	[6] Time-when-connected

}

CBR-Bind-failure  ::= SEQUENCE {

connect-failure-reason

[0] Connect-failure

}

--	connect-failure-reason contains one of the error indications given in the following table.

Table 3

| Error indications | Reason |
| --- | --- |
| not-entitled | The responder is not entitled to accept a request for an association between itself and the initiator. |
| temporary-overload | The responder is not capable of establishing an association due to temporary overload. |
| temporary-failure | The responder is not capable of establishing an association due to a temporary failure (having impact on an entity at SM-RL or at layers above). |
| incorrect-ID-or-password | The responder will not accept the request to establish an association between itself and the initiator due to incorrect identity or password. |
| not-supported | The responder does not recognize the telecommunication subsystem type of the initiator, or cannot support any of the operations suggested on the association. |
| version-unsupported | The version specified is not supported by the recipient. |

--

Connect-failure     ::= INTEGER {

not-entitled (0),

temporary-overload (1),

temporary-failure (2),

incorrect-ID-or-password (3),

not-supported (4),

version-unsupported (5)

}

Time-when-disconnected	::= UTCTime

Time-when-connected		::= UTCTime

--	The CBR-Write-Replace operation

CBR-Write-Replace ::=

ABSTRACT-OPERATION

ARGUMENT	Write-Replace

RESULT	Report

ERRORS	{Parameter-not-recognized,

Parameter-value-invalid,

Valid-CBS-message-not-identified,

Cell-identity-not-valid,

Unrecognized-primitive,

Missing-mandatory-element,

BSS-capacity-exceeded,

Cell-memory-exceeded,

BSS-memory-exceeded,

Cell-broadcast-not-supported,

Cell-broadcast-not-operational,

Extended-channel-not-supported,

Message-reference-already-used,					Unspecified-error

}

--	The CBR-Kill operation

CBR-Kill ::=

ABSTRACT-OPERATION

ARGUMENT	Kill

RESULT	Report

ERRORS	{Parameter-not-recognized,

Parameter-value-invalid,

Cell-identity-not-valid,

Valid-CBS-message-not-identified,

Unrecognized-primitive,

Missing-mandatory-element,

Cell-broadcast-not-supported,

Cell-broadcast-not-operational,

Extended-channel-not-supported,

Unspecified-error

}

--	The CBR-Status-CBCH-Query operation

CBR-Status-CBCH-Query ::=

ABSTRACT-OPERATION

ARGUMENT	Status-CBCH

RESULT	Status-CBCH-Resp

ERRORS	{Parameter-not-recognized,

Parameter-value-invalid,

Cell-identity-not-valid,

Unrecognized-primitive,

Missing-mandatory-element,

Cell-broadcast-not-supported,

Cell-broadcast-not-operational,

Extended-channel-not-supported,

Unspecified-error

}

--	The CBR-Status-Message-Query operation

CBR-Status-Message-Query ::=

ABSTRACT-OPERATION

ARGUMENT	Status-Message

RESULT	Status-Mess-Resp

ERRORS	{Parameter-not-recognized,

Parameter-value-invalid,

Cell-identity-not-valid,

Valid-CBS-message-not-identified,

Unrecognized-primitive,

Missing-mandatory-element,

Cell-broadcast-not-supported,

Cell-broadcast-not-operational,

Extended-channel-not-supported,

Unspecified-error

}

--	The CBR-Restart-Ind operation

CBR-Restart-Ind ::=

ABSTRACT-OPERATION

ARGUMENT	Restart-Ind

RESULT

ERRORS	{Parameter-not-recognised,

Parameter-value-invalid,

Cell-identity-not-valid,

Unrecognized-primitive,

Missing-mandatory-element,

Unspecified-error
					}

--	$start$(Phase2PBscCellLists)$

--	The CBR-Restart-Ind-Phase2P operation

CBR-Restart-Ind-Phase2P ::=

ABSTRACT-OPERATION

ARGUMENT	Restart-Ind-Phase2P

RESULT

ERRORS	{Parameter-not-recognised,

Parameter-value-invalid,

Cell-identity-not-valid,

Unrecognized-primitive,

Missing-mandatory-element,

Unspecified-error
					}

--	$end$(Phase2PBscCellLists)$

--	The CBR-Reset operation

CBR-Reset ::=

ABSTRACT-OPERATION

ARGUMENT	Reset

RESULT

ERRORS	{Parameter-not-recognized,

Parameter-value-invalid,

Cell-identity-not-valid,

Unrecognized-primitive,

Missing-mandatory-element,

Cell-broadcast-not-supported,

Unspecified-error

}

--	The CBR-Failure-Ind operation

CBR-Failure-Ind ::=

ABSTRACT-OPERATION

ARGUMENT	Failure-Ind

RESULT

ERRORS	{Parameter-not-recognized,

Parameter-value-invalid,

Cell-identity-not-valid,

Unrecognized-primitive,

Missing-mandatory-element,

Unspecified-error

}

--	$start$(Phase2PBscCellLists)$

--	The CBR-Failure-Ind-Phase2P operation

CBR-Failure-Ind-Phase2P ::=

ABSTRACT-OPERATION

ARGUMENT	Failure-Ind-Phase2P

RESULT

ERRORS	{Parameter-not-recognized,

Parameter-value-invalid,

Cell-identity-not-valid,

Unrecognized-primitive,

Missing-mandatory-element,

Unspecified-error

}

--	$end$(Phase2PBscCellLists)$

--	The CBR-Set-DRX operation

CBR-Set-DRX ::=

ABSTRACT-OPERATION

ARGUMENT	Set-DRX

RESULT		Set-DRX-Resp

ERRORS		{Parameter-not-recognized,

Parameter-value-invalid,

Valid-CBS-message-not-identified,

Cell-identity-not-valid,

Unrecognized-primitive,

Missing-mandatory-element,

BSS-capacity-exceeded,

Unspecified-error,

Cell-broadcast-not-supported,

Cell-broadcast-not-operational,

Extended-channel-not-supported,

Incompatible-DRX-parameter

}

--	CBR operation ARGUMENT lists

--	PDU parameter definitions from 03.41

Message-Identifier			::= INTEGER (0 .. 65535)

Serial-Number				::= INTEGER (0 .. 65535)

No-of-Pages					::=	INTEGER (1 .. 15)

Cell-List					::= SEQUENCE {

length	INTEGER, -- number of cells in the list

disc	Cell-Id-Disc,

list	SEQUENCE OF Cell-Id

}

Channel						::= INTEGER {

basic-channel (0),

extended-channel (1)

}

Category					::=	INTEGER {

high-priority (0),

normal-priority (1),

background (2)

}

Repetition-Period			::=	INTEGER (1 .. 1024)

No-of-Broadcast-Req			::=	INTEGER (0 ..65535)

No-of-Broadcasts-Compl-List ::=	SEQUENCE OF SEQUENCE {

cell-id						Cell,

no-of-broadcasts-compl		INTEGER,

no-of-broadcasts-compl-info No-of-Broadcasts-Compl-Info-Type OPTIONAL

}

Cell-Id						::=	OCTET STRING (SIZE(4))

--								Note:

--								If Cell-Id-Disc equals ciOnly then only the last 2 octets of

--								Cell-ID are to be considered

--								If Cell-Id-Disc equals lacOnly then only the first 2 octets of

--								Cell-ID are to be considered. The unused octets are filler octets

--								If Cell-Id-Disc equals allCells, Cell-ID only contains filler octets

Schedule-Period				::= INTEGER (0 .. 40)

Reserved-Slots				::= INTEGER (0 .. 40)

Failure-List				::=	SEQUENCE OF SEQUENCE {

cell-id		Cell,

cause		Failure-Reason,

diagnostic	Diagnostic-Info	OPTIONAL

}

Cbch-Loading-List 			::=	SEQUENCE OF SEQUENCE{

cell-id				Cell,

cbch-loading		Cbch-Loading

-- 								indicates the predicted short term load, expressed as a percentage

-- 								(min:0, max: 100)

}

Cbch-Loading				::=	INTEGER(0..100)

Failure-Reason 				::= INTEGER {

parameter-not-recognised (0),

unused-failure-reason-1 (1), -- not used

parameter-value-invalid (2),

valid-CBS-message-not-identified (3),

cell-identity-not-valid (4),

unrecognised-primitive (5),

missing-mandatory-element (6),

bss-capacity-exceeded (7),

cell-memory-exceeded (8),

bss-memory-exceeded (9),

unspecifed-error (10),

incompatible-DRX-parameter (11),

unused-failure-reason-12 (12), -- not used

cell-broadcast-not-supported (13),

cell-broadcast-not-operational (14),

extended-channel-not-supported (15),

message-reference-already-used (16)

}

Diagnostic-Info 			::= OCTET STRING (SIZE (1..20))

Data-Coding-Scheme			::=	INTEGER (0 .. 255)

Page-Inf					::= SEQUENCE {

message-info-useful-octets	Message-Info-Useful-Octets,

message-info-page			Message-Info-Page

}

Message-Info-Useful-Octets	::=	INTEGER (0..82)

Recovery-Indication			::= BOOLEAN

-- 								TRUE indicates data is available

-- 								False indicates data is lost

--	Definitions used by the PDU parameters

Message-Info-Page			::=	OCTET STRING (SIZE(82))

Cell-Id-Disc				::= OCTET-STRING (SIZE(1))

-- 								values from the following table

lacAndCi OCTET STRING (SIZE(1)) ::= '1'H -- 2 Octet lac, followed by 2 Octet Cell Id

ciOnly OCTET STRING (SIZE(1))   ::= '2'H -- Cell Id only

lacOnly OCTET STRING (SIZE(1))  ::= '5'H -- 2 Octet lac only, all cells in this LAC (NOT USED BY BSC)

allCells OCTET STRING (SIZE(1)) ::= '6'H -- all cells in this BSS  (NOT USED BY BSC)

Cell						::=	SEQUENCE {

disc		Cell-Id-Disc,

id		Cell-Id

}

No-of-Broadcasts-Compl-Info-Type::=  INTEGER {

unknown (0),

overflow (1)

}

Write-Replace	::= SEQUENCE {

message-Identifier		Message-Identifier,

new-Serial-Number		Serial-Number,

no-of-Pages				No-of-Pages,

data-coding-scheme		Data-Coding-Scheme,

cell-list				Cell-List,

repetition-Period		Repetition-Period,

no-of-broadcast-req		No-of-Broadcast-Req,

cbs-Page-Inf			SEQUENCE OF [15] Page-Inf,

old-Serial-Number		[3] Serial-Number 	OPTIONAL,

category				[2] Category	OPTIONAL,

channel-indicator		[4] Channel		OPTIONAL

}

Kill	::= SEQUENCE {

message-Identifier		Message-Identifier,

old-Serial-Number		Serial-Number,

cell-List				Cell-List,

channel-indicator		[4] Channel		OPTIONAL

}

Status-CBCH		::= SEQUENCE{

cell-List				Cell-List,

channel-indicator		[4] Channel		OPTIONAL

}

Status-Message	::= SEQUENCE {

message-Identifier	Message-Identifier,

old-Serial-No		Serial-Number,

cell-List			Cell-List,

channel-indicator	[4] Channel		OPTIONAL

}

--	$start$(Phase2PBscCellLists)$

--	The Restart-Ind PDU is retained for backward compatibility with Phase 2 systems,

--	and may be used in Phase 2+ systems

Restart-Ind	::= SEQUENCE {

cell-list				Cell-List,

recovery-Indication		Recovery-Indication		OPTIONAL

}

--	coding of the recovery-Indication states is Data-available TRUE, Data-lost FALSE

--	The Restart-Ind-Phase2P PDU is used in Phase 2+ systems

Restart-Ind-Phase2P	::= CHOICE {

restart-list1		[0] SEQUENCE {

cell-list				Cell-List,

recovery-Indication		Recovery		OPTIONAL

},

restart-list2		[1]	SEQUENCE {

cell-list				SEQUENCE OF Cell,

recovery-Indication		Recovery	OPTIONAL

}

}

--	The Failure-Ind PDU is retained for backward compatibility with Phase 2 systems,

--	and may be used in Phase 2+ systems

Failure-Ind ::= SEQUENCE{

cell-list	Cell-List

}

--	The Failure-Ind-Phase2P PDU is used in Phase 2+ systems

Failure-Ind-Phase2P	::= CHOICE {

failure-list1		[0]	SEQUENCE {

cell-list		Cell-List

},

failure-list2		[1]	SEQUENCE OF Cell

}

--	$end$(Phase2PBscCellLists)$

Reset ::= SEQUENCE{

cell-list	Cell-List

}

Set-DRX	::= SEQUENCE {

cell-list			Cell-List,

schedule-Period		[6]	Schedule-Period	OPTIONAL,

reserved-Slots		[2] Reserved-Slots	OPTIONAL,

channel-indicator	[4] Channel	OPTIONAL

}

Report	::= SEQUENCE {

message-Identifier				Message-Identifier,

serial-Number					Serial-Number,

no-of-Broadcasts-Compl-List		[0] No-of-Broadcasts-Compl-List OPTIONAL,

failure-List					[1] Failure-List OPTIONAL,

channel-indicator				[4] Channel		OPTIONAL

}

Status-CBCH-Resp	::= SEQUENCE{

cbch-loading-List		[0] Cbch-Loading-List OPTIONAL,

failure-List			[1] Failure-List OPTIONAL,

channel-indicator		[4] Channel		OPTIONAL

Status-Mess-Resp	::= SEQUENCE {

message-Identifier				Message-Identifier,

old-serial-number				Serial-Number,

no-of-Broadcasts-Compl-List		[0] No-of-Broadcasts-Compl-List OPTIONAL,

failure-List					[1] Failure-List OPTIONAL,

channel-indicator				[4] Channel		OPTIONAL

}

--	$start$(Phase2PBscCellLists)$

Set-DRX-Resp	::= SEQUENCE {

cell-list					[0]	SEQUENCE OF Cell	OPTIONAL,

failure-List				[1] Failure-List OPTIONAL,

channel-indicator			[4] Channel		OPTIONAL

}

--	$end$(Phase2PBscCellLists)$

--	CBR operation errors listed below

Parameter-not-recognized ::=

ABSTRACT-ERROR

PARAMETER Diagnostic-Info OPTIONAL

Parameter-value-invalid ::=

ABSTRACT-ERROR

PARAMETER Diagnostic-Info OPTIONAL

Valid-CBS-message-not-identified ::=

ABSTRACT-ERROR

PARAMETER Diagnostic-Info OPTIONAL

Cell-Identity-not-valid ::=

ABSTRACT-ERROR

PARAMETER Diagnostic-Info OPTIONAL

Unrecognized-primitive ::=

ABSTRACT-ERROR

PARAMETER Diagnostic-Info OPTIONAL

Missing-mandatory-element ::=

ABSTRACT-ERROR

PARAMETER Diagnostic-Info OPTIONAL

BSS-capacity-exceeded ::=

ABSTRACT-ERROR

PARAMETER Diagnostic-Info OPTIONAL

Cell-memory-exceeded ::=

ABSTRACT-ERROR

PARAMETER Diagnostic-Info OPTIONAL

BSS-memory-exceeded ::=

ABSTRACT-ERROR

PARAMETER Diagnostic-Info OPTIONAL

Unspecified-error ::=

ABSTRACT-ERROR

PARAMETER Diagnostic-Info OPTIONAL

Incompatible-DRX-parameter ::=

ABSTRACT-ERROR

PARAMETER Diagnostic-Info OPTIONAL

Cell-broadcast-not-supported ::=

ABSTRACT-ERROR

PARAMETER Diagnostic-Info OPTIONAL

Cell-broadcast-not-operational ::=

ABSTRACT-ERROR

PARAMETER Diagnostic-Info OPTIONAL

Extended-channel-not-supported ::=

ABSTRACT-ERROR

PARAMETER Diagnostic-Info OPTIONAL

Message-reference-already-used ::=

ABSTRACT-ERROR

PARAMETER Diagnostic-Info OPTIONAL

--	Definition of Cell Broadcast Relay Service address

CBS-Address ::= [APPLICATION 0] SEQUENCE {

address-type	INTEGER  { unknown-type		(0),

international-number		(1),

national-number		(2),

network-specific-number	(3),

short-number			(4) },

numbering-plan	INTEGER { unknown-numbering	(0),

iSDN-numbering		(1),

data-network-numbering	(3),

telex-numbering		(4),

national-numbering		(8),

private-numbering		(9)}

address-value	CHOICE { octet-format

SemiOctetString

--other formats are for further study}

}

SemiOctetString ::= OCTET STRING (SIZE(1..10))

-- each octet contains two binary coded decimal digits

END

3rd module of 3

RelayProtocol

RelayProtocol {

ccitt identified-organization (4) etsi (0) mobile-domain(0)

gsm-messaging (4) gsm-sms4 (13) relayProtocol(1) }

DEFINITIONS

IMPLICIT TAGS

::=

BEGIN

IMPORTS

--	application service elements and application contexts

aCSE, APPLICATION-SERVICE-ELEMENT, APPLICATION-CONTEXT

FROM Remote-Operations-Notation-extension {

joint-iso-ccitt  remote-operations(4) notation-extension(2) }

rOSE

FROM Remote-Operations-APDUs {

joint-iso-ccitt  remote-operations(4) apdus(1) }

--	object identifiers

id-cb-ac-so, id-cb-CBRSE, id-cb-as-CBRSE,

FROM CBS-UsefulDefinitions{

ccitt identified-organization (4) etsi (0) mobile-domain(0)

gsm-messaging(4) gsm-sms4 (13)  usefulDefinitions(0) } ;

aS-ACSE OBJECT IDENTIFIER ::=

{ joint-iso-ccitt association-control (2) abstractSyntax(1) apdus(0) version(1) }

--	abstract service parameters

CBR-Bind, CBR-Unbind, CBR-Write-Replace, CBR-Kill,

CBR-Status-CBCH-Query,

--	$start$(Phase2PBscCellLists)$

CBR-Status-Message-Query, CBR-Reset, CBR-Restart-Ind, CBR-Restart-Ind-Phase2P,

CBR-Failure-Ind, CBR-Failure-Ind-Phase2P, CBR-Set-DRX,

--	$end$(Phase2PBscCellLists)$

Parameter-not-recognized, Parameter-value-invalid,

Valid-CBS-message-not-identified, Cell-identity-not-valid,

Unrecognized-primitive,

Missing-mandatory-element, BSS-capacity-exceeded,

Cell-memory-exceeded, BSS-memory-exceeded, Unspecified-error, Incompatible-DRX-parameter,

Cell-broadcast-not-supported, Cell-broadcast-not-operational, Extended-channel-not-supported

FROM RelayAbstractService{

ccitt identified-organization (4) etsi (0) mobile-domain(0)

gsm-messaging(4) gsm-sms4(13) relayAbstractService(2) } ;

--	Application contexts

--	Only one application contexts is specified: the CBC is exclusively responsible for the BIND and

--	UNBIND operations.

cBC-BINDs-and-UNBINDs

APPLICATION-CONTEXT

APPLICATION-SERVICE-ELEMENTS { aCSE }

BIND    CBR-Bind

UNBIND  CBR-Unbind

REMOTE OPERATIONS { rOSE }

INITIATOR CONSUMER OF { cBRSE }

ABSTRACT SYNTAXES { id-cb-as-CBRSE , aS-ACSE }

::= id-cb-ac-so

--	Application service elements

cBRSE	APPLICATION-SERVICE-ELEMENT

CONSUMER INVOKES {	CBR-Restart-Ind

--	$start$(Phase2PBscCellLists)$

CBR-Restart-Ind-Phase2P

CBR-Failure-Ind

CBR-Failure-Ind-Phase2P

--	$end$(Phase2PBscCellLists)$

CBR-From-BSC-VBind-Request

CBR-From-BSC-Bind-Confirm

CBR-From-BSC-Bind-Failure

CBR-From-BSC-UnBind

}

SUPPLIER INVOKES { CBR-Write-Replace

CBR-Kill

CBR-Status-CBCH-Query

CBR-Status-Message-Query

CBR-Reset

CBR-Set-DRX

CBR-From-BSC-VBind-Request

CBR-From-BSC-Bind-Confirm

CBR-From-BSC-Bind-Failure

CBR-From-BSC-UnBind

}

::= id-cb-SMRSE

--	Remote operations

cbr-write-replace			CBR-Write-Replace

::= 1

-- Note:	localValue - words are omitted, since they are

--	typically not used, and likely to be removed from

--	the OPERATION and ERROR macros in ROSE.

cbr-kill						CBR-Kill

::= 2

cbr-status-CBCH-query			CBR-Status-CBCH-Query

::= 3

cbr-status-message-query		CBR-Status-Message-Query

::= 4

cbr-restart-ind					CBR-Restart-Ind

::= 5

cbr-reset						CBR-Reset

::= 6

cbr-failure-ind					CBR-Failure-Ind

::= 7

cbr-set-DRX						CBR-Set-DRX

::= 8

--	$start$(Phase2PBscCellLists)$

cbr-restart-ind-phase2p	CBR-Restart-Ind-Phase2P

::= 9

cbr-failure-ind-phase2p	CBR-Failure-Ind-Phase2P

::= 10

--	$end$(Phase2PBscCellLists)$

--	Remote errors, the localValues are provisional

parameter-not-recognized		Parameter-not-recognized

::= 0

parameter-value-invalid			Parameter-value-invalid

::= 2

valid-CBS-message-not-identified	Valid-CBS-message-not-identified

::= 3

cell-identity-not-valid			Cell-identity-not-valid

::= 4

unrecognized-primitive			Unrecognized-primitive

::= 5

missing-mandatory-element		Missing-mandatory-element

::= 6

bss-capacity-exceeded			BSS-capacity-exceeded

::= 7

cell-memory-exceeded			Cell-memory-exceeded

::= 8

bss-memory-exceeded			BSS-memory-exceeded

::= 9

unspecified-error				Unspecified-error

::= 10

incompatible-DRX-parameter		Incompatible-DRX-Parameter

::= 11

cell-broadcast-not-supported	Cell-broadcast-not-supported

::= 13

cell-broadcast-not-operational	Cell-broadcast-not-operational

::= 14

extended-channel-not-supported	Extended-channel-not-supported

::= 15

message-reference-already-used  Message-reference-already-used

::= 16

END

## 3.3	Application rules

The following application rules specify the invocation of different operations on the association. Two alternative sets of application rules are given in 3.3.1 (for semi-permanent connections) and in 3.3.2 (for transient connections); additional sets are possible.

### 3.3.1	Application rule set 1 Semi-permanent symmetric connection

This set of application rules is to be used in situations where the connection (on all the protocol layers) between the CBC and the BSC is maintained for ever.

Within the CBR-BIND service, all operations are allowed on the association; semi-permanent connection is accepted (by not forcing the connection transient). This is negotiated within the CBR-BIND service as follows:

name of parameter	value in request and report

operations		{cBR-From-CBC-Write-Replace,

cBR-From-CBC-Kill,

cBR-From-CBC-Status-CBCH-Query,

cBR-From-CBC-Status-Message-Query,

cBR-From-BSC-Restart-Ind,

cBR-From-BSC-Reset,

cBR-From-BSC-Failure-Ind,

cBR-From-CBC-Set-DRX,

cBR-From-BSC-VBind-Request,

cBR-From-BSC-Bind-Confirm,

cBR-From-BSC-Bind-Failure,

cBR-From-BSC-UnBind,

--	$start$(Phase2PBscCellLists)$

cBR-From-BSC-Restart-Ind-Phase2P,

cBR-From-BSC-Failure-Ind-Phase2P

--	$end$(Phase2PBscCellLists)$

}

transient			FALSE

$start$(Phase2PBscCellLists)$

The CBC invokes cBR-From-CBC-Write-Replace, cBR-From-CBC-Kill, cBR-From-CBC-Status-CBCH-Query, cBR-From-CBC-Status-Message-Query, cBR-From-CBC-Reset, cBR-From-CBC-Set-DRX operations as needed. The BSC invokes cBR-From-BSC-Restart-Ind, cBR-From-BSC-Restart-Ind-Phase2P, cBR-From-BSC-Failure-Ind and cBR-From-BSC-Failure-Ind-Phase2P.

$end$(Phase2PBscCellLists)$

The CBR-UNBIND operation is not normally invoked on the association.

### 3.3.2	Application rule set 2 Transient asymmetric connection

This set of application rules is to be used e.g. in situations where a CBC has connections with many BSCs, and there is a switched data network connecting them. A data network connection (and the higher layer connections on top of it) is maintained for the duration of the relay or alert operations only.

Within the CBR-BIND service, only one type of operation is negotiated for use on the association. The operation of that type must be invoked by the CBC or by the BSC in exceptional circumstances (e.g. in order to invoke CBR-RESET). The BSC or CBC accepts the one type of operation and forces the association transient.

The following is an example of a negotiation procedure within the CBR-BIND service, where the CBR-Write-Replace operation is initiated by the CBC.

name of parameter	value

iniType			cell-Broadcast-Service-Centre

respType			public-Land-Mobile-Network

operations		{ cBR-From-CBC-Write-Replace }

transient			TRUE

The association for cBR-From-CBC-Kill, cBR-From-CBC-Status-CBCH-Query or cBR-From-CBC-Status-Message-Query, cBR-From-CBC-Reset, cBR-From-CBC-Set-DRX are negotiated according to the same principle, the CBC always being the initiator of the CBR-BIND.

The association may be used for invoking operations of the negotiated type(s) as long as there are such operations to be invoked (in other words, until all commands have been relayed).

# 4	An SS7 Protocol Stack For Interconnecting CBC And BSC

Concepts described in Q.1400 (see CCITT Study Group XI - Report R219) are used. These concepts enable, with minor modifications, the protocol specified in Section 3 of GSM 03.49 to be supported via an SS7 protocol stack.

Q.1400 specifies the use of OSI concepts via SS7 for the development of signalling and operations and management protocols. The protocol specified in Section 3 of this report can be carried via an SS7 protocol stack consisting of TCAP, SCCP and MTP (see Q.700 series) with minor adaptations:

-	ROSE operation classes 2 and 5 are replaced by TCAP operation classes 1 and 4 respectively.

-	TCAP provides a connectionless service. The services provided by CBRSE-BIND, CBR-UNBIND, CBR-Bind-confirm and CBR-Bind-failure are therefore not required and subclause 3.3 is not applicable.

PLMN networks may provide interworking between either of the protocols specified by clause 2 or 3 and the SS7 protocol stack for the purpose of fulfilling the service requirements of the primitives specified for the CBC - BSC interface in GSM 03.41.

Annex A (informative):
Document change history

| SPEC | SMG# | CR | PHASE | VERS | NEW_VERS | SUBJECT |
| --- | --- | --- | --- | --- | --- | --- |
| 03.49 | s25 | A032 | R97 | 5.7.0 | 6.0.0 | Version Control for the CBC-BSC interface |
| 03.49 | s25 | A033 | R97 | 5.7.0 | 6.0.0 | Write-Replace ASN.1 |
| 03.49 | s26 | A034 | R97 | 6.0.0 | 6.1.0 | CBC-BSC interface compatibility |
| 03.49 | s29 |  | R98 |  | 7.0.0 | Specification version upgrade to Release 1998 version 7.0.0 7.0.0 |

# History

| Document history |
| --- |
| V7.0.0 | August 1999 | Publication |

ISBN 2-7437-3320-9

Dépôt légal : Août 1999