3GPP TR 23.847 V0.1.0 (200605)

Technical Report

3rd Generation Partnership Project;

Technical Specification Group Services and System Aspects;

Study on Enhancements to IMS Service Functionalities

Facilitating Multicast Bearer services;

(Release 7)

The present document has been developed within the 3rd Generation Partnership Project (3GPP TM) and may be further elaborated for the purposes of 3GPP.	 
The present document has not been subject to any approval process by the 3GPP Organizational Partners and shall not be implemented.	 
This Specification is provided for future development work within 3GPP only. The Organizational Partners accept no liability for any use of this Specification.
Specifications and reports for implementation of the 3GPP TM system should be obtained via the 3GPP Organizational Partners' Publications Offices.

Remove GSM logo from the cover page for pure 3rd Generation documents.

Keywords

<keyword[, keyword]>

Select keywords from list provided in specs database.

3GPP

Postal address

3GPP support office address

650 Route des Lucioles - Sophia Antipolis

Valbonne - FRANCE

Tel.: +33 4 92 94 42 00 Fax: +33 4 93 65 47 16

Internet

http://www.3gpp.org

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© 2004, 3GPP Organizational Partners (ARIB, ATIS, CCSA, ETSI, TTA, TTC).

All rights reserved.

Contents

Foreword	5

Introduction	5

1	Scope	5

2	References	6

3	Definitions, symbols and abbreviations	6

3.1	Definitions	6

3.2	Abbreviations	6

4	General	6

4.1	Context of this study	7

4.2	Goals of this study	7

5	Study Areas	7

5.1	Architecture requirements	7

5.1.1	Architecture requirements	7

5.1.2	Architecture	7

5.2       Procedures to combine IMS session signalling with MBMS bearer services	7

5.3        Charging and Policy control enforcement	7

5.4    	   Considerations on Security	7

Annex <A>: <Annex title>	8

A.1	8

Annex <X>: Change history	9

# Foreword

This Technical Report has been produced by the 3rd Generation Partnership Project (3GPP).

The contents of the present document are subject to continuing work within the TSG and may change following formal TSG approval. Should the TSG modify the contents of the present document, it will be re-released by the TSG with an identifying change of release date and an increase in version number as follows:

Version x.y.z

where:

x	the first digit:

1	presented to TSG for information;

2	presented to TSG for approval;

3	or greater indicates TSG approved document under change control.

y	the second digit is incremented for all changes of substance, i.e. technical enhancements, corrections, updates, etc.

z	the third digit is incremented when editorial only changes have been incorporated in the document.

# Introduction

During the definition of MBMS enhancement requirements, IMS regarding support of media delivery over multicast bearers has been identified in TS 22.228 (v7.2.0) as following:

Multicast services allow IMS users and service providers to send multimedia to a group of  IMS users simultaneously in an unidirectional way of communication.  The underlying network may be able to support mechanisms that optimize the delivery of multimedia to the individual members of that group (e.g. MBMS  [7])

Initial understanding of the architectural implications would base on the regional services to grouped IMS users provided at hot spots as a football stadium. From such a requirement point towards the  feasibility analysis and more IMS services should be investigated for the better understanding of the use and applicability of multicast bearers (e.g. MBMS) in the context of IMS.

# 1	Scope

This study intends to analyze the feasibility and applicability of using multicast bearers (e.g. MBMS) in the context of IMS-based applications.

This study item should capture the results of the technical considerations and solutions into the facilitation of IMS services over multicast bearer services with a focus on the possible enhancements to IMS functionalities and relevant charging, security and service provision procedures.

A brief summary of considerations include:

- Signaling procedures of multicast enabled IMS services should be analyzed based on the grouped communication scenarios and possible optimisations to the delivery mechanisms should be investigated

- Identifying the charging and policy control procedures according to the PCC architecture

- Identifying the service provision procedures both in network elements and UEs

- Investigating the possible security requirements to multicast enabled IMS functionalities and bearer service entities

- Real-time QoS requirements e.g. delay , interruption

- UE capability requirements

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

- References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

- For a specific reference, subsequent revisions do not apply.

- For a non-specific reference, the latest version applies.  In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[<seq>]	<doctype> <#>[ ([up to and including]{yyyy[-mm]|V<a[.b[.c]]>}[onwards])]: "<Title>".

[1]	3GPP TS 23.228: " IP Multimedia Subsystem (IMS); Stage 2”

[2]                       3GPP TS 23.246: "Multimedia Broadcast/Multicast Service (MBMS); Architecture and functional description"

[3]	3GPP TS 33.246: "3G Security; Security of Multimedia Broadcast/Multicast Service (MBMS) "

# 3	Definitions, symbols and abbreviations

## 3.1	Definitions

For the purposes of the present document, the [following] terms and definitions [given in ... and the following] apply.

Definition format

<defined term>: <definition>.

example: text used to clarify abstract rules by applying them literally.

## 3.2	Abbreviations

For the purposes of the present document, the following abbreviations apply:

# General

When looking at the current requirements of IMS services, the multicast bearer based applications on the market is obvious and will developing from a minor role to a larger extent. This is especially valid in the lights of  the deployment of the  grouped real-time multimedia services. The profit of IMS service media delivery optimization based on multicast bearer services is not restricted to traditional IMS services as PoC and conference only, but the emergence  of new value-added services.

In general, it can be expected if there is a technical guidance to enable IMS service functionalities to utilize the efficient multicast bearer service that IMS offer hundreds of  combined real-time multimedia applications one never would have thought of before.

The general issues as the additional enhancements and the alignments with relative architectural requirements as charging and policy control, security should be investigated and identified.

## 4.1	Context of this study

This study intends to describes architectural concepts and procedures for  IMS service functionalities utilizing multicast bearer based on MBMS bearer services defined in [2] for R6 and R7.

## 4.2	Goals of this study

The study shall investigate on the improvements of IMS service functionalities to utilize the multicast bearer services in the core network and  more enhancements due to the related PCC, service provisioning  and security requirements, and identify the influenced standards and the appropriate change requests if deemed necessary.

# Study Areas

## 5.1	Architecture requirements

## 5.1.2	Baseline Architecture

The figure below shows the current architecture of IMS and MBMS.

Figure 1: Architecture of IMS applications using MBMS as a bearer.

-	IMS AS
The means of using an IMS AS is identical to its usage in IMS.

-	CSCFs

The CSCFs functionality is the same as defined in [1].

-	MRFC/MRFP

The MRFC/MRFP functionality is the same as defined in [1].

-	HSS

The HSS functionality is the same as defined in [1].

-	UTRAN/GERAN
The UTRAN and the GERAN are the same as defined in [x].

-	BM-SC

The BM-SC functionality is the same as defined in [2].

-	GGSN

The GGSN functionality is same as defined in [x].

- 	SGSN

The SGSN functionality is the same as defined in [x].

-	HLR

The HLR functionality is the same as defined in [x].

-	UE
The UE needs to support MBMS functionality, IMS functionality and IMS applications (e.g. PoC). Additionally, the UE should support UE capability exchange mechanisms.

-	PCRF

The usage of the PCRF for IMS applications using MBMS as a bearer is FFS.

Editor’s note: In order to support IMS applications using MBMS as a bearer, additional functionalities may be needed in the entities above. What new functionalities are needed is FFS.

## 5.2       Procedures to combine IMS session signalling with MBMS bearer services

This chapter describes the procedures for IMS applications using MBMS as a bearer. The IMS AS should be able to find out UE capabilities. Based on this information, the IMS AS decides which bearer will be used for the IMS application, which will be MBMS in this case. After this the MBMS procedures will take place. Figure 2 shows an information flow for the procedures for IMS applications using MBMS as a bearer.

Editors Note:  It is for further study how the IMS AS identifies that the MBMS bearer is supported at the location serving the UE.

Figure 2: Information flow for IMS applications using MBMS as a bearer.

- Initiation of the IMS session.

2. Exchange of UE capabilities. This information should include the UE capabilities and the QoS parameters.

Note: This may be done after or during the IMS session initiation.

3. The IMS AS decides what bearer should be used for the IMS application. The IMS application bases his decision on the information received during the UE capability exchange (UE capabilities and QoS parameters). In this case the IMS AS chooses MBMS as bearer for the IMS application.

4. At the MBMS bearer signalling, the information regarding the bearer decision of the IMS AS is exchanged. In addition also the QoS parameters should be exchanged.

5. Modification of the IMS session.

6. MBMS bearer activation procedures as defined in [2].

7. MBMS session start procedures as defined in [2].

8. The MBMS data transmission takes place certain time after the MBMS session start procedures.

9. IMS signalling for session tear-down.

10. MBMS bearer deactivation procedures as defined in [2].

## 5.3        Charging and Policy control enforcement

## 5.4    	   Considerations on Security

Annex <A>:
<Annex title>

Annexes are labeled A, B, C, etc. and are "informative"(3G TRs are informative documents by nature).

# A.1

Annex <X>:
Change history

| Change history |
| --- |
| Date | TSG # | TSG Doc. | CR | Rev | Subject/Comment | Old | New |
| 2005-03 | SA2#51 | S2-061215 |  |  | Input proposal including approved TR number at SA#31. | 0.0.0 | 0.0.1 |
| 2006-06 | SA2#52 | S2-061867 |  |  | Input proposal of the skeleton TR | 0.0.1 | 0.1.0 |
| 2006-06 | SA2#52 | S2-061989 |  |  | Input proposal of the baseline architecture for IMS applications using MBMS as a bearer | 0.0.1 | 0.1.0 |
| 2006-06 | SA2#52 | S2-062004 |  |  | Input proposal of Information flow for IMS applications using MBMS as a bearer | 0.0.1 | 0.1.0 |