3GPP TS 24.305 V1.0.0 (2006-09)

Technical Specification

3rd Generation Partnership Project;

Technical Specification Group Core Network and Terminals;

Selective Disabling of 3GPP UE Capabilities (SDoUE) Management Object (MO);

(Release 7)

The present document has been developed within the 3rd Generation Partnership Project (3GPP TM) and may be further elaborated for the purposes of 3GPP.	 
The present document has not been subject to any approval process by the 3GPP Organizational Partners and shall not be implemented.	 
This Specification is provided for future development work within 3GPP only. The Organizational Partners accept no liability for any use of this Specification.
Specifications and reports for implementation of the 3GPP TM system should be obtained via the 3GPP Organizational Partners' Publications Offices.

Keywords

GSM, UMTS, Management

3GPP

Postal address

3GPP support office address

650 Route des Lucioles - Sophia Antipolis

Valbonne - FRANCE

Tel.: +33 4 92 94 42 00 Fax: +33 4 93 65 47 16

Internet

http://www.3gpp.org

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© 2004, 3GPP Organizational Partners (ARIB, ATIS, CCSA, ETSI, TTA, TTC).

All rights reserved.

Contents

Foreword	4

1	Scope	5

2	References	5

3	Definitions, symbols and abbreviations	5

3.1	Definitions	5

3.2	Abbreviations	5

4	Selective Disabling of 3GPP UE Capabilities Management Object	6

5	Management Object parameters	7

5.1	General	7

5.2	Node: <X>	7

5.3	/<X>/Name	7

5.4	/<X>/CS_Calls	7

5.5	/<X>/EmergencyCalls	7

5.6	/<X>/SupplementaryServices	8

5.7	/<X>/CS_SMS	8

5.8	/<X>/PS_SMS	8

5.9	/<X>/CS_LCS	8

5.10	/<X>/PS_LCS	9

5.11	/<X>/GPRS_SM_PDP	9

5.12	/<X>/GPRS_SM_MBMS	9

5.13	/<X>/IMS	9

5.14	/<X>/Text	10

5.15	/<X>/Ext	10

Annex A (informative): Management Object DDF	10

Annex B (informative): Change history	16

# Foreword

This Technical Specification has been produced by the 3rd Generation Partnership Project (3GPP).

The contents of the present document are subject to continuing work within the TSG and may change following formal TSG approval. Should the TSG modify the contents of the present document, it will be re-released by the TSG with an identifying change of release date and an increase in version number as follows:

Version x.y.z

where:

x	the first digit:

1	presented to TSG for information;

2	presented to TSG for approval;

3	or greater indicates TSG approved document under change control.

y	the second digit is incremented for all changes of substance, i.e. technical enhancements, corrections, updates, etc.

z	the third digit is incremented when editorial only changes have been incorporated in the document.

# 1	Scope

The present document provides the protocol details and corresponding behaviour for a mobile device Selective Disabling of 3GPP UE Capabilities (SDoUE) Management Object (MO).

The Selective Disabling of 3GPP UE Capabilities (SDoUE) Management Object is compatible with the OMA Device Management (DM) protocol specifications, version 1.2 and upwards, and is defined using the OMA DM Device Description Framework (DDF) as described in the Enabler Release Definition OMA-ERELD-DM-V1_2 [8].

The Selective Disabling of 3GPP UE Capabilities Management Object consists of the relevant parameters that can be managed for Selective Disabling of UE capabilities.

The Selective Disabling of 3GPP UE Capabilities Management Object defines a repository of data into the ME.

The service requirements for the Selective Disabling of 3GPP UE Capabilities are defined in 3GPP TS 22.011 [2].

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

- References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

- For a specific reference, subsequent revisions do not apply.

- For a non-specific reference, the latest version applies.  In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[2]	3GPP TS 22.011: "Service accessibility".

[3]	3GPP TS 24.008: "Mobile radio interface Layer 3 specification; Core network protocols; Stage 3".

[4]	3GPP TS 24.010: "Mobile radio interface layer 3; Supplementary services specification; General aspects".

[5]	3GPP TS 24.011: "Point-to-Point (PP) Short Message Service (SMS) support on mobile radio interface".

[6]	3GPP TS 24.030: "Location Services (LCS); Supplementary service operations; Stage 3".

[7]	3GPP TS 24.229: "IP Multimedia Call Control Protocol based on SIP and SDP; Stage 3".

[8]	OMA-ERELD-DM-V1_2: "Enabler Release Definition for OMA Device Management".

# 3	Definitions, symbols and abbreviations

## 3.1	Definitions

For the purposes of the present document, the terms and definitions given in 3GPP TR 21.905 [1] apply.

## 3.2	Abbreviations

CS	Circuit Switched

DDF	Device Description Framework

DM	Device Management

MO	Management Object

OMA	Open Mobile Alliance

PS	Packet Switched

SDoUE	Selective Disabling of 3GPP UE Capabilities

UE	User Equipment

# 4	Selective Disabling of 3GPP UE Capabilities Management Object

The Selective Disabling of 3GPP UE Capabilities (SDoUE) Management Object (MO) is used to manage settings of the UE for remotely disabling selected UE capabilities.

The Management Object Identifier is: urn:oma:mo:ext-3gpp-sdoue:1.0.

Editor’s note: The Management Object Identifier is the 3GPP proposal using the latest OMA format available.

The management following nodes and leaf objects are possible under the SDoUE node:

Figure 1: The SDoUE Management Object

# 5	Management Object parameters

## 5.1	General

This clause describes the parameters for the SDoUE Management Object (MO).

## 5.2	Node: <X>

This interior node acts as a placeholder for zero or one accounts for a fixed node.

- Occurrence: ZeroOrOne

- Format: node

- Access Types: Get

- Values: N/A

## 5.3	/<X>/Name

The Name leaf is a name for the SDoUE MO settings.

- Occurrence: ZeroOrOne

- Format: chr

- Access Types: Get

- Values: <User displayable name>

## 5.4	/<X>/CS_Calls

The CS_Calls leaf indicates an operator’s preference to enable or disable mobile-originated Call Control (CC)  procedures except for emergency calls.

The CC procedures are specified in 3GPP TS 24.008 [3].

- Occurrence: ZeroOrOne

- Format: bool

- Access Types: Get

- Values: 0, 1

0 – Indicates mobile-originated CS calls enable.

1 – Indicates mobile-originated CS calls disable.

## 5.5	/<X>/EmergencyCalls

The EmergencyCalls leaf indicates an operator’s preference to enable or disable emergency call procedures.

The emergency call procedures are specified in 3GPP TS 24.008 [3].

Editor’s note: The need of selective disabling of emergency call procedures over IMS is FFS waiting for the completion of the specification work on the IMS Emergency service.

- Occurrence: ZeroOrOne

- Format: bool

- Access Types: Get

- Values: 0, 1

0 – Indicates emergency calls enable.

1 – Indicates emergency calls disable.

## 5.6	/<X>/SupplementaryServices

The SupplementaryServices leaf indicates an operator’s preference to enable or disable mobile-originated Supplementary services operations.

The Supplementary service operations are specified in 3GPP TS 24.010 [4].

NOTE : The functionality indicated by the SupplementaryServices leaf does not include the Location Services (LCS) Supplementary service operations.

- Occurrence: ZeroOrOne

- Format: bool

- Access Types: Get

- Values: 0, 1

0 – Indicates mobile-originated Supplementary service operations enable.

1 – Indicates mobile-originated Supplementary service operations disable

## 5.7	/<X>/CS_SMS

The CS_SMS leaf indicates an operator’s preference to enable or disable mobile-originated Short Message Service (SMS) via CS.

The SMS procedures are specified in 3GPP TS 24.011 [5].

Editor’s note: The need of selective disabling of SMS over IP networks is FFS waiting for the completion of the specification work on this feature.

- Occurrence: ZeroOrOne

- Format: bool

- Access Types: Get

- Values: 0, 1

0 – Indicates mobile-originated SMS via CS enable.

1 – Indicates mobile-originated SMS via CS disable.

## 5.8	/<X>/PS_SMS

The PS_SMS leaf indicates an operator’s preference to enable or disable mobile-originated Short Message Service (SMS) via PS.

The SMS procedures are specified in 3GPP TS 24.011 [5].

Editor’s note: The need of selective disabling of SMS over IP networks is FFS waiting for the completion of the specification work on this feature.

- Occurrence: ZeroOrOne

- Format: bool

- Access Types: Get

- Values: 0, 1

0 – Indicates mobile-originated SMS via PS enable.

1 – Indicates mobile-originated SMS via PS disable.

## 5.9	/<X>/CS_LCS

The CS_LCS leaf indicates an operator’s preference to enable or disable mobile-originated Location Services (LCS) operations via CS.

The LCS Supplementary service operations are specified in 3GPP TS 24.030 [6].

- Occurrence: ZeroOrOne

- Format: bool

- Access Types: Get

- Values: 0, 1

0 – Indicates mobile-originated LCS via CS enable.

1 – Indicates mobile-originated LCS via CS disable.

## 5.10	/<X>/PS_LCS

The PS_LCS leaf indicates an operator’s preference to enable or disable mobile-originated Location Services (LCS) operations via PS.

The LCS Supplementary service operations are specified in 3GPP TS 24.030 [6].

- Occurrence: ZeroOrOne

- Format: bool

- Access Types: Get

- Values: 0, 1

0 – Indicates mobile-originated LCS via PS enable.

1 – Indicates mobile-originated LCS via PS disable.

## 5.11	/<X>/GPRS_SM_PDP

The GPRS_SM_PDP leaf indicates an operator’s preference to enable or disable mobile-originated GPRS Session Management (SM) procedures for PDP contexts, i.e. PDP context activation, deactivation and modification.

The GPRS SM procedures for PDP contexts are specified in 3GPP TS 24.008 [3].

- Occurrence: ZeroOrOne

- Format: bool

- Access Types: Get

- Values: 0, 1

0 – Indicates mobile-originated GPRS SM for PDP contexts enable.

1 – Indicates mobile-originated GPRS SM for PDP contexts disable.

## 5.12	/<X>/GPRS_SM_MBMS

The GPRS_SM_MBMS leaf indicates an operator’s preference to enable or disable GPRS Session Management (SM) procedures for MBMS contexts, i.e. MBMS context activation and deactivation.

The GPRS SM procedures for MBMS contexts are specified in 3GPP TS 24.008 [3].

- Occurrence: ZeroOrOne

- Format: bool

- Access Types: Get

- Values: 0, 1

0 – Indicates GPRS SM for MBMS contexts enable.

1 – Indicates GPRS SM for MBMS contexts disable.

## 5.13	/<X>/IMS

The IMS leaf indicates an operator’s preference to enable or disable IMS procedures for sending IMS registration request.

The IMS procedures for sending IMS registration request are specified in 3GPP TS 24.229 [7].

- Occurrence: ZeroOrOne

- Format: bool

- Access Types: Get

- Values: 0, 1

0 – Indicates IMS procedures for sending IMS registration request enable.

1 – Indicates IMS procedures for sending IMS registration request disable.

## 5.14	/<X>/Text

The Text leaf provides a means for including information that will be displayed by the ME. The information contained in the text leaf should be in the ME selected language, via the OMA DM standard procedure. The information should contain information in order to assist in determining the cause of disability of specific services and what to do for example, a text string indicating the disabled service(s) and customer service number(s). An example of possible information to be displayed: "The GPRS service of the handset is currently disabled. For further information, please contact TelServices Help Centre by calling 111 from your handset or +44 7777 111 111 whilst abroad. Alternatively, you may wish to get in touch with us by email at help@telservices.net".

- Occurrence: ZeroOrOne

- Format: chr

- Access Types: Get

- Values: N/A

## 5.15	/<X>/Ext

The Ext is an interior node for where the vendor specific information about the SDoUE MO is being placed (vendor meaning application vendor, device vendor etc.). Usually the vendor extension is identified by vendor specific name under the ext node. The tree structure under the vendor identified is not defined and can therefore include one or more un-standardized sub-trees.

- Occurrence: ZeroOrOne

- Format: node

- Access Types: Get

- Values: N/A

Annex A (informative):
Management Object DDF

This DDF is the standardized minimal set. A vendor can define it’s own DDF for the complete device. This DDF can include more features than this minimal standardized version.

<?xml version="1.0" encoding="UTF-8"?>

<!DOCTYPE MgmtTree PUBLIC "-//OMA//DTD SYNCML-DMDDF 1.2//EN"

http://www.openmobilealliance.org/tech/DTD/dm_ddf-v1_2.dtd>

<MgmtTree>

<VerDTD>1.2</VerDTD>

<Man>--The device manufacturer--</Man>

<Mod>--The device model--</Mod>

<Node>

<NodeName>x</NodeName>

<DFProperties>

<AccessType>

<Get/>

</AccessType>

<Description>SDoUE settings</Description>

<DFFormat>

<node/>

</DFFormat>

<Occurrence>

<ZeroOrOne/>

</Occurrence>

<Scope>

<Permanent/>

</Scope>

<DFTitle>The SDoUE Management Object.</DFTitle>

<DFType>

<DDFName/>

</DFType>

</DFProperties>

<Node>

<NodeName>Name</NodeName>

<DFProperties>

<AccessType>

<Get/>

</AccessType>

<DFFormat>

<chr/>

</DFFormat>

<Occurrence>

<ZeroOrOne/>

</Occurrence>

<Scope>

<Dynamic/>

</Scope>

<DFTitle>User displayable name for the node.</DFTitle>

<DFType>

<MIME>text/plain</MIME>

</DFType>

</DFProperties>

</Node>

<Node>

<NodeName>CS_Calls</NodeName>

<DFProperties>

<AccessType>

<Get/>

</AccessType>

<DFFormat>

<bool>

</DFFormat>

<Occurrence>

<ZeroOrOne/>

</Occurrence>

<Scope>

<Permanent/>

</Scope>

<DFTitle>Indication of whether mobile-originated CS calls are enable.</DFTitle>

<DFType>

<MIME>text/plain</MIME>

</DFType>

</DFProperties>

</Node>

<Node>

<NodeName>EmergencyCalls</NodeName>

<DFProperties>

<AccessType>

<Get/>

</AccessType>

<DFFormat>

<bool>

</DFFormat>

<Occurrence>

<ZeroOrOne/>

</Occurrence>

<Scope>

<Permanent/>

</Scope>

<DFTitle>Indication of whether emergency calls are enable.</DFTitle>

<DFType>

<MIME>text/plain</MIME>

</DFType>

</DFProperties>

</Node>

<Node>

<NodeName>SupplementaryServices</NodeName>

<DFProperties>

<AccessType>

<Get/>

</AccessType>

<DFFormat>

<bool>

</DFFormat>

<Occurrence>

<ZeroOrOne/>

</Occurrence>

<Scope>

<Permanent/>

</Scope>

<DFTitle>Indication of whether mobile-originated Supplementary service operations are enable.</DFTitle>

<DFType>

<MIME>text/plain</MIME>

</DFType>

</DFProperties>

</Node>

<Node>

<NodeName>CS_SMS</NodeName>

<DFProperties>

<AccessType>

<Get/>

</AccessType>

<DFFormat>

<bool>

</DFFormat>

<Occurrence>

<ZeroOrOne/>

</Occurrence>

<Scope>

<Permanent/>

</Scope>

<DFTitle>Indication of whether mobile-originated SMS via CS is enable.</DFTitle>

<DFType>

<MIME>text/plain</MIME>

</DFType>

</DFProperties>

</Node>

<Node>

<NodeName>PS_SMS</NodeName>

<DFProperties>

<AccessType>

<Get/>

</AccessType>

<DFFormat>

<bool>

</DFFormat>

<Occurrence>

<ZeroOrOne/>

</Occurrence>

<Scope>

<Permanent/>

</Scope>

<DFTitle>Indication of whether mobile-originated SMS via PS is enable.</DFTitle>

<DFType>

<MIME>text/plain</MIME>

</DFType>

</DFProperties>

</Node>

<Node>

<NodeName>CS_LCS</NodeName>

<DFProperties>

<AccessType>

<Get/>

</AccessType>

<DFFormat>

<bool>

</DFFormat>

<Occurrence>

<ZeroOrOne/>

</Occurrence>

<Scope>

<Permanent/>

</Scope>

<DFTitle>Indication of whether mobile-originated LCS via CS is enable.</DFTitle>

<DFType>

<MIME>text/plain</MIME>

</DFType>

</DFProperties>

</Node>

<Node>

<NodeName>PS_LCS</NodeName>

<DFProperties>

<AccessType>

<Get/>

</AccessType>

<DFFormat>

<bool>

</DFFormat>

<Occurrence>

<ZeroOrOne/>

</Occurrence>

<Scope>

<Permanent/>

</Scope>

<DFTitle>Indication of whether mobile-originated LCS via PS is enable.</DFTitle>

<DFType>

<MIME>text/plain</MIME>

</DFType>

</DFProperties>

</Node>

<Node>

<NodeName>GPRS_SM_PDP</NodeName>

<DFProperties>

<AccessType>

<Get/>

</AccessType>

<DFFormat>

<bool>

</DFFormat>

<Occurrence>

<ZeroOrOne/>

</Occurrence>

<Scope>

<Permanent/>

</Scope>

<DFTitle>Indication of whether mobile-originated GPRS SM procedures for PDP contexts are enable.</DFTitle>

<DFType>

<MIME>text/plain</MIME>

</DFType>

</DFProperties>

</Node>

<Node>

<NodeName>GPRS_SM_MBMS</NodeName>

<DFProperties>

<AccessType>

<Get/>

</AccessType>

<DFFormat>

<bool>

</DFFormat>

<Occurrence>

<ZeroOrOne/>

</Occurrence>

<Scope>

<Permanent/>

</Scope>

<DFTitle>Indication of whether mobile-originated GPRS SM procedures for MBMS contexts are enable.</DFTitle>

<DFType>

<MIME>text/plain</MIME>

</DFType>

</DFProperties>

</Node>

<Node>

<NodeName>IMS</NodeName>

<DFProperties>

<AccessType>

<Get/>

</AccessType>

<DFFormat>

<bool>

</DFFormat>

<Occurrence>

<ZeroOrOne/>

</Occurrence>

<Scope>

<Permanent/>

</Scope>

<DFTitle>Indication of whether IMS procedures for sending IMS registration request are enable.</DFTitle>

<DFType>

<MIME>text/plain</MIME>

</DFType>

</DFProperties>

</Node>

<Node>

<NodeName>Text</NodeName>

<DFProperties>

<AccessType>

<Get/>

</AccessType>

<DFFormat>

<chr>

</DFFormat>

<Occurrence>

<ZeroOrOne/>

</Occurrence>

<Scope>

<Permanent/>

</Scope>

<DFTitle>Information to be displayed by the handset.</DFTitle>

<DFType>

<MIME>text/plain</MIME>

</DFType>

</DFProperties>

</Node>

<Node>

<NodeName>Ext</NodeName>

<!-- The Extension node starts here. -->

<DFProperties>

<AccessType>

<Get/>

<Replace/>

</AccessType>

<DFFormat>

<node/>

</DFFormat>

<Occurrence>

<ZeroOrOne/>

</Occurrence>

<Scope>

<Dynamic/>

</Scope>

<DFTitle>A collection of all Extension objects.</DFTitle>

<DFType>

<DDFName/>

</DFType>

</DFProperties>

</Node>

</Node>

</MgmtTree>

Annex B (informative):
Change history

It is usual to include an annex (usually the final annex of the document) for specifications under TSG change control which details the change history of the specification using a table as follows:

| Change history |
| --- |
| Date | TSG # | TSG Doc. | CR | Rev | Subject/Comment | Old | New |
| 2006-03 |  |  |  |  | Rapporteur input framework document agreed at CT1#41. | 0.0.0 | 0.1.0 |
| 2006-05 |  |  |  |  | Implementation of CRs agreed at CT1#42: C1-061070 | 0.1.0 | 0.2.0 |
| 2006-09 |  |  |  |  | Implementation of CRs agreed at CT1#43 : C1-061593, C1-061594, C1-061595, C1-061699 Version 1.0.0 created for presentation for information to plenary (TSG CT #33). | 0.2.0 | 1.0.0 |