Presentation of Specification to TSG or WG

Presentation to:	TSG CT Meeting #33

Document for presentation:	TS 24.305, Version 1.0.0

Presented for:	Information

Abstract of document:

This 3GPP Technical Specification (TS) specifies a mobile device Selective Disabling of 3GPP UE capabilities (SDoUE) Management Object (MO).

The SDoUE MO is compatible with the OMA Device Management (DM) protocol specifications version 1.2 and onwards.

CT WG1 agreed at CT1 #43 to send this TS for information, because the SDoUE Work Item (WI) is considered to be stable enough for information (at least 60%).

Note that the CT1 proposed version 1.0.0 of TS 24.305 is attached as file 24.305-100.

Changes since last presentation to <TSG><WG> Meeting #<N>:

Not applicable since this is the first presentation of the TS to TSG CT.

Outstanding Issues:

- Access to the SDoUE MO when in VPLMN. Two different solutions were presented at CT1#43 in order to complete the work on this topic because of requirements stated in TS 22.011. An LS has been sent out to SA1 asking for guidance on the requirements.

- Behaviour of the UE when services are disabled.

Contentious Issues:

None.