3GPP TS 24.341 V0.2.0 (2006-07)

Technical Specification

3rd Generation Partnership Project;

Technical Specification Group Core Network and Terminals;

Support of SMS and MMS over IP networks;

Stage 3

(Release 7)

The present document has been developed within the 3rd Generation Partnership Project (3GPP TM) and may be further elaborated for the purposes of 3GPP.	
The present document has not been subject to any approval process by the 3GPP Organizational Partners and shall not be implemented.	
This Specification is provided for future development work within 3GPP only. The Organizational Partners accept no liability for any use of this Specification.
Specifications and reports for implementation of the 3GPP TM system should be obtained via the 3GPP Organizational Partners' Publications Offices.

Keywords

UMTS, Network, IP, SIP, SMS, MMS

3GPP

Postal address

3GPP support office address

650 Route des Lucioles - Sophia Antipolis

Valbonne - FRANCE

Tel.: +33 4 92 94 42 00 Fax: +33 4 93 65 47 16

Internet

http://www.3gpp.org

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© 2006, 3GPP Organizational Partners (ARIB, ATIS, CCSA, ETSI, TTA, TTC).

All rights reserved.

Contents

Foreword	4

1	Scope	5

2	References	5

3	Definitions and abbreviations	6

3.1	Definitions	6

3.2	Abbreviations	6

4	Overview of SMS over IP functionality	7

4.1	Introduction	7

4.2	SMS over IP	7

4.3	MMS over IP	7

5	SIP related procedures	7

5.1	Introduction	7

5.2	Functional entities	7

5.2.1	User Equipment (UE)	7

5.2.2	Application Server (AS)	7

5.3	Roles	7

5.3.1	SMS-over-IP sender	7

5.3.1.1	General	7

5.3.1.2	Sending an SMS message	8

5.3.1.3	Sending a delivery report	8

5.3.1.4	Sending a notification about UE having memory available	8

5.3.2	SMS-over-IP receiver	9

5.3.2.1	General	9

5.3.2.2	Receiving an SMS message	9

5.3.2.3	Receiving a submit report	9

5.3.3	IP-Short-Message-Gateway (IP-SM-GW)	9

5.3.3.1	General	9

5.3.3.2	Indication of UE availability for receiving SMS messages	10

5.3.3.3	Indication of UE unavailability for receiving SMS messages	10

5.3.3.4	Forwarding SMS over IP – UE sends SIP MESSAGE request	10

5.3.3.5	Forwarding SMS over IP – UE receives SIP MESSAGE request	10

Annex A (informative): Example signalling flows of SMS over IP functionality	11

A.1	Scope of signalling flows	11

A.2	Introduction	11

A.2.1	General	11

A.2.2	Key required to interpret signalling flows	11

A.3	Signalling flows demonstrating how IP-SM-GW indicates to HSS the availability of UE for receiving SMS messages	12

A.4	Signalling flows demonstrating how IP-SM-GW indicates to HSS the unavailability of UE for receiving SMS messages	13

A.5	Signalling flows demonstrating successful UE originated SMS submission over IP procedure	14

A.6	Signalling flows demonstrating successful UE terminated SMS delivery over IP procedure (including delivery report)	18

A.7	Signalling flows demonstrating successful UE terminated MMS delivery using SMS over IP procedure	22

Annex B (informative): Change history	23

# Foreword

This Technical Specification has been produced by the 3rd Generation Partnership Project (3GPP).

The contents of the present document are subject to continuing work within the TSG and may change following formal TSG approval. Should the TSG modify the contents of the present document, it will be re-released by the TSG with an identifying change of release date and an increase in version number as follows:

Version x.y.z

where:

x	the first digit:

1	presented to TSG for information;

2	presented to TSG for approval;

3	or greater indicates TSG approved document under change control.

y	the second digit is incremented for all changes of substance, i.e. technical enhancements, corrections, updates, etc.

z	the third digit is incremented when editorial only changes have been incorporated in the document.

# 1	Scope

The present document provides the protocol details for SMS over IP within the IP Multimedia (IM) Core Network (CN) subsystem based on the Session Initiation Protocol (SIP) and SIP Events as defined in 3GPP TS 24.229 [10].

Where possible the present document specifies the requirements for this protocol by reference to specifications produced by the IETF within the scope of SIP and SIP Events, either directly, or as modified by 3GPP TS 24.229 [10].

The present document is applicable to Application Servers (ASs) and User Equipment (UE) providing SMS over IP functionality.

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

- References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

- For a specific reference, subsequent revisions do not apply.

- For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[2]	3GPP TS 23.002: "Network Architecture".

[3]	3GPP TS 23.040: "Technical realization of the Short Message Service (SMS)".

Editor’s Note: Currently no Release 7 version available.

[4]	3GPP TS 23.140: "Multimedia Messaging Service (MMS); Functional description; Stage 2".

Editor’s Note: Currently no Release 7 version available.

[5]	3GPP TS 23.204: "Support of SMS and MMS over generic 3GPP IP access; Stage 2".

[6]	3GPP TS 23.218: "IP Multimedia (IM) session handling; IM call model; Stage 2".

[7]	3GPP TS 23.228: "IP Multimedia Subsystem (IMS); Stage 2".

[8]	3GPP TS 24.011: "Point-to-Point (PP) Short Message Service (SMS) support on mobile radio interface".

Editor’s Note: Currently no Release 7 version available.

[9]	3GPP TS 24.228 Release 5: "Signalling flows for the IP multimedia call control based on Session Initiation Protocol (SIP) and Session Description Protocol (SDP); Stage 3".

[10]	3GPP TS 24.229: "Internet Protocol (IP) multimedia call control protocol based on Session Initiation Protocol (SIP) and Session Description Protocol (SDP); Stage 3".

[11]	3GPP TS 29.328: "IP Multimedia (IM) Subsystem Sh interface; Signalling flows and message contents".

[12]	RFC 3261 (June 2002): "SIP: Session Initiation Protocol".

[13]	RFC 3428 (December 2002): "Session Initiation Protocol (SIP) Extension for Instant Messaging".

# 3	Definitions and abbreviations

## 3.1	Definitions

For the purposes of the present document, the terms and definitions given in TR 21.905 [1] and the following apply. A term defined in the present document takes precedence over the definition of the same term, if any, in TR 21.905 [1].

SMS-over-IP sender: entity that creates a SIP MESSAGE request including a vnd.3gpp.sms payload (introduced in 3GPP TS 23.140 [4]).

Editor’s Note: MIME type "application/vnd.3gpp.sms-tl" is also available.

SMS-over-IP receiver: entity that processes the vnd.3gpp.sms payload received in a SIP MESSAGE request

For the purposes of the present document, the following terms and definitions given in RFC 3261 [12] apply.

Header

Header field

Method

Request

Response

(SIP) transaction

Status-code (see RFC 3261 [12], subclause 7.2)

Tag (see RFC 3261 [12], subclause 19.3)

For the purposes of the present document, the following terms and definitions given in 3GPP TS 23.002 [2], subclauses 4.1.1.1 and 4a.7 apply:

Call Session Control Function (CSCF)

Home Subscriber Server (HSS)

For the purposes of the present document, the following terms and definitions given in 3GPP TS 23.218 [6], subclause 3.1 apply:

Filter criteria

Initial filter criteria

For the purposes of the present document, the following terms and definitions given in 3GPP TS 23.228 [7], subclauses 4.3.3.1 and 4.6 apply:

Interrogating-CSCF (I-CSCF)

Proxy-CSCF (P-CSCF)

Serving-CSCF (S-CSCF)

## 3.2	Abbreviations

For the purposes of the present document, the abbreviations given in TR 21.905 [1] and the following apply. An abbreviation defined in the present document takes precedence over the definition of the same abbreviation, if any, in TR 21.905 [1].

AS	Application Server

IP-SM-GW	IP-Short-Message-Gateway

SM-SC	Short Message Service Centre

# 4	Overview of SMS over IP functionality

## 4.1	Introduction

SMS over IP functionality provides the UE with the capability of sending traditional SMS messages over IMS network. The architecture for the SMS over IP functionality is specified in 3GPP TS 23.204 [5].

## 4.2	SMS over IP

In order to guarantee SMS interoperability the SMS-over-IP sender, the SMS-over-IP receiver and the IP-SM-GW shall support encapsulation of RPDUs defined in 3GPP TS 24.011 [8], subclause 7.3. The SMS-over-IP sender, the SMS-over-IP receiver and the IP-SM-GW shall use the MIME type "application/vnd.3gpp.sms" for this purpose.

## 4.3	MMS over IP

For MMS over generic IP access, existing mechanisms are used (HTTP and SMTP) for transfer of the MMS itself, these mechanisms are not described in the present document. For MMS notification, SMS over generic IP access can be used, the mechanisms for this are described in the present document.

Editor’s Note: Reference to be added for MMS transfer protocols used, and a statement for the method used for MMS notification.

Editor’s Note: Annex A will include an example flow including MMS notification using SMS over IP and the MMS transfer.

# 5	SIP related procedures

## 5.1	Introduction

## 5.2	Functional entities

### 5.2.1	User Equipment (UE)

A UE may implement the role of an SMS-over-IP sender (see subclause 5.3.1) or an SMS-over-IP receiver (see subclause 5.3.2).

Editor’s Note: It is FFS whether the limitation to handle at most one UE originated SMS and one UE terminated SMS at a time is kept for SMS over IP.

### 5.2.2	Application Server (AS)

An AS may implement the role of an IP-SM-GW (see subclause 5.3.3).

## 5.3	Roles

### 5.3.1	SMS-over-IP sender

#### 5.3.1.1	General

In addition to the procedures specified in subclause 5.3.1, the SMS-over-IP sender shall support the procedures specified in 3GPP TS 24.229 [10] appropriate to the functional entity in which the SMS-over-IP sender is implemented. The SMS-over-IP sender shall be able to build and populate RP-DATA, RP-ACK, RP-SMMA and RP-ERROR messages, containing all the information that a mobile station sending an SMS according to 3GPP TS 24.011 [8] would place, for successful delivery.

#### 5.3.1.2	Sending an SMS message

When an SMS-over-IP sender wants to submit an SMS over IP, the SMS-over-IP sender shall send a SIP MESSAGE request with the following information:

a)	the Request-URI, which shall contain the destination user’s URI;

Editor’s Note: It is FFS whether UE shall insert destination user’s URI, IP-SM-GW address, or SM-SC address as R-URI. The population of the To header must be defined as well.

b)	the Content-Type header, which shall contain "application/vnd.3gpp.sms"; and

c)	the body of the request shall contain an RP-DATA message as defined in 3GPP TS 24.011 [8], including the SMS headers and the SMS text.

Editor’s Note: It is FFS whether UE can insert all elements of the RP-DATA message content or it will be inserted by the IP-SM-GW, SMS-IWMSC, or SM-SC.

NOTE 1:	The address of the SM-SC is included in the RP-DATA message content. The address of the SM-SC is configured in the SMS-over-IP sender.

NOTE 2:	The SMS-over-IP sender will use content transfer encoding of type "binary" for the encoding of the SMS in the body of the SIP MESSAGE request.

d)	the From header, which shall contain a public user identity of the SMS-over-IP sender.

NOTE 3:	The IP-SM-GW will have to use an address of the SMS-over-IP sender that the SM-SC can process (i.e. a E.164 number). This address will come from a tel URI in a P-Asserted-ID header placed in the SIP MESSAGE request by the P-CSCF or S-CSCF.

#### 5.3.1.3	Sending a delivery report

When an SMS-over-IP sender wants to send an SMS delivery report over IP, the SMS-over-IP sender shall send a SIP MESSAGE request with the following information:

a)	the Request-URI, which shall contain the IP-SM-GW;

NOTE 1:	The address of the IP-SM-GW is received in the SIP MESSAGE request including the delivered SMS message.

b)	the Content-Type header shall contain "application/vnd.3gpp.sms"; and

c)	the body of the request shall contain the RP-ACK or RP-ERROR message for the SMS delivery report, as defined in 3GPP TS 24.011 [8].

NOTE 2:	The SMS-over-IP sender will use content transfer encoding of type "binary" for the encoding of the SMS in the body of the SIP MESSAGE request.

#### 5.3.1.4	Sending a notification about UE having memory available

When a UE acting as an SMS-over-IP sender wants to submit a notification to the network that the UE has memory available to receive one or more short messages, the SMS-over-IP sender shall send a SIP MESSAGE request with the following information:

a)	the Request-URI;

Editor’s Note: It is FFS whether UE shall insert destination user’s URI, IP-SM-GW address, or SM-SC address as Request-URI. The population of the To header must be defined as well.

b)	the Content-Type header shall contain "application/vnd.3gpp.sms";

c)	the body of the request shall contain the SMS headers and the SMS text as it is defined for RP-SMMA message, see 3GPP TS 24.011 [8]; and

Editor’s Note: It is FFS whether UE can insert all elements of the RP-SMMA message content or it will be inserted by the IP-SM-GW, SMS-IWMSC, or SM-SC.

NOTE 1: The address of the SM-SC is included in the RP-SMMA message content. The address of SM-SC is configured in SMS-over-IP sender.

d)	the From header, which shall contain a public user identity of the SMS-over-IP sender.

NOTE 2: The IP-SM-GW will have to use an address of the SMS-over-IP sender that the SM-SC can process (i.e. a E.164 number). This address will come from a tel URI in a P-Asserted-ID header placed in the SIP MESSAGE request by the P-CSCF or S-CSCF

### 5.3.2	SMS-over-IP receiver

#### 5.3.2.1	General

In addition to the procedures specified in subclause 5.3.2, the SMS-over-IP receiver shall support the procedures specified in 3GPP TS 24.229 [10] appropriate to the functional entity in which the SMS-over-IP receiver is implemented. The SMS-over-IP receiver shall be able to parse and interpret RP- DATA, RP-ACK and RP-ERROR messages, containing all the information that a mobile station receiving an SMS according to 3GPP TS 24.011 [8] would see, in a SMS delivery.

#### 5.3.2.2	Receiving an SMS message

When a SIP MESSAGE request including a short message in the "vnd.3gpp.sms" payload is received, the SMS-over-IP receiver shall:

Editor’s Note: It is FFS whether UE can determine if the request is received from an IP-SM-GW. UDH Source Indicator is a possible candidate, to be checked.

-	generate a SIP response according to RFC 3428 [13];

-	extract the payload encoded according to 3GPP TS 24.011 [8]; and

-	create a delivery report as described in subclause 5.3.1.3. The content of the report is defined in 3GPP TS 24.011 [8].

#### 5.3.2.3	Receiving a submit report

When a SIP MESSAGE request including a submit report in the "vnd.3gpp.sms" payload is received, the SMS-over-IP receiver shall:

Editor’s Note: It is FFS whether UE can determine if the request is received from an IP-SM-GW. UDH Source Indicator is a possible candidate, to be checked.

-	generate a SIP response according to RFC 3428 [13]; and

-	extract the payload encoded according to 3GPP TS 24.011 [8] for RP-ACK or RP-ERROR.

### 5.3.3	IP-Short-Message-Gateway (IP-SM-GW)

#### 5.3.3.1	General

An IP-SM-GW is an entity that provides the protocol interworking for delivery of the short message between the IP-based UE and the SM-SC.

In addition to the procedures specified in subclause 5.3.3, the IP-SM-GW shall support the procedures specified in subclause 5.7 in 3GPP TS 24.229 [10].

#### 5.3.3.2	Indication of UE availability for receiving SMS messages

Upon receipt of a third-party REGISTER request (public user ID is (re-)registered), the IP-SM-GW should send a 200 (OK) response for the REGISTER request and start a data update procedure to the HSS as specified in 3GPP TS 29.328 [11] to indicate that the registering public user ID is registered with it for delivery of SMS.

Editor’s Note: It is FFS whether IP-SM-GW must subscribe to reg event package.

Editor’s Note: It is FFS whether the interface between IP-SM-GW and HSS will be Sh or MAP.

#### 5.3.3.3	Indication of UE unavailability for receiving SMS messages

Upon receipt of a third-party REGISTER request (public user ID is deregistered), the IP-SM-GW should send a 200 (OK) response for the REGISTER request and start the data update procedure to the HSS as specified in 3GPP TS 29.328 [11] to indicate that the deregistering public user ID is not registered with it any more for delivery of SMS.

Editor’s Note: It is FFS whether the interface between IP-SM-GW and HSS will be Sh or MAP.

Editor’s Note: It is FFS in stage 2 if data update procedure to the HSS is needed.

#### 5.3.3.4	Forwarding SMS over IP – UE sends SIP MESSAGE request

NOTE: The SIP MESSAGE received from the UE will include a P-Asserted-ID header containing a tel URI of the UE and will contain either a short message (RP-DATA), or a delivery report (RP-ACK).

Editor’s Note: RP-SM-MEMORY-AVAILABLE is FFS.

If a SIP MESSAGE request including "vnd.3gpp.sms" payload is received from the SMS-over-IP sender, the IP-SM-GW shall:

- extract and validate the format of the SM-SC address from the received payload as defined in 3GPP TS 24.011 [8] and 3GPP TS 23.040 [3];

- extract the RPDU type (see 3GPP TS 24.011 [8]) from the received payload and include it in the appropriate message to SM-SC via SMS-IWMSC; and

- if any of the steps above fails, respond to the SIP MESSAGE request with an appropriate 4xx response; otherwise, respond with a 202 (Accepted) response.

#### 5.3.3.5	Forwarding SMS over IP – UE receives SIP MESSAGE request

If a short message is received from the SMS-GMSC, the IP-SM-GW shall extract the IMSI of the SMS-over-IP receiver (destination UE) from the received message. If an SMS submit report is received from the SMS-GMSC, the IP-SM-GW shall retrieve the IMSI from the existing MAP context. Then the IP-SM-GW shall obtain a corresponding public user identity and send a SIP MESSAGE request with the following information:

a)	the Request-URI, which shall contain a public user identity of the SMS-over-IP receiver;

b)	the Content-Type header which shall contain "application/vnd.3gpp.sms"; and

c)	the body of the request which shall either contain an RP-DATA message as defined in 3GPP TS 24.011 [8], including the SMS headers and the SMS text, or an RP-ACK or RP-ERROR message as defined in 3GPP TS 24.011 [8], including the SMS submit report.

Annex A (informative):
Example signalling flows of SMS over IP functionality

# A.1	Scope of signalling flows

This annex gives examples of signalling flows for the SMS over IP within the IP Multimedia (IM) Core Network (CN) subsystem based on the Session Initiation Protocol (SIP) and SIP Events.

These signalling flows provide detailed signalling flows, which expand on the overview information flows provided in 3GPP TS 23.204 [5].

# A.2	Introduction

## A.2.1	General

The signalling flows provided in this annex follow the methodology developed in 3GPP TS 24.228 [9]. The following additional considerations apply:

a)	3GPP TS 24.228 [9] shows separate signalling flows with no configuration hiding between networks, and with configuration hiding between networks. There is no SMS over IP specific functionality associated with this hiding, and therefore such separate signalling flows are not show in the present document; and

b)	3GPP TS 24.228 [9] does not show the functionality between the S-CSCF and the AS. As the SMS over IP functionality depends on the functionality provided by an AS, the signalling flows between S-CSCF and AS are shown in the present document.

## A.2.2	Key required to interpret signalling flows

The key to interpret signalling flows specified in 3GPP TS 24.228 [9] subclauses 4.1 and 4.2 applies with the additions specified below.

- ipsmgw.home1.net: an IP-SM-GW in the home network of the SMS-over-IP sender/receiver;

- user1_public1@home1.net: SMS-over-IP sender/receiver;

- user2_public2@home2.net: SMS-over-IP sender/receiver.

As in 3GPP TS 24.228 [9], in order to differentiate between SIP methods and other protocol messages, the message name is preceded with the associated protocol for all non-SIP messages.

Each signalling flow table contains descriptions for headers where the content of the header is new to that signalling flow, as is already performed in 3GPP TS 24.228 [9].

However, 3GPP TS 24.228 [9] includes extensive descriptions for the contents of various headers following each of the tables representing the contents of the signalling flows. Where the operation of the header is identical to that shown in 3GPP TS 24.228 [9], then such text is not reproduced in the present document.

Additional text may also be found on the contents of headers within 3GPP TS 24.228 [9] in addition to the material shown in the present document.

# A.3	Signalling flows demonstrating how IP-SM-GW indicates to HSS the availability of UE for receiving SMS messages

Figure A.3-1: IP-SM-GW registration signalling

Figure A.3-1 shows the registration signalling flow for the scenario when IP-SM-GW registers to HSS. The details of the signalling flows are as follows:

1.	See 3GPP TS 24.228 [9], subclause 6.2 steps 1 through 22

Editor’s Note: 3GPP TS 24.228 [9] contains Rel-5 registration, additional parameters might appear in Rel-7 registration.

2.	Initial filter criteria

The S-CSCF analyses the incoming request against the initial filter criteria and decides to send a third-party REGISTER request to the IP-SM-GW.

3.	REGISTER request (S-CSCF to IP-SM-GW) - see example in table A.3-1

This signalling flow forwards the REGISTER request from the S-CSCF to the IP-SM-GW.

Table A.3-1: REGISTER request (S-CSCF to IP-SM-GW)

REGISTER sip:ipsmgw.home1.net SIP/2.0

Via: SIP/2.0/UDP sip:scscf1.home1.net

Max-Forwards: 70

P-Access-Network-Info:

P-Visited-Network-ID:

P-Charging-Vector:

P-Charging-Function-Addresses:

From: sip:scscf1.home1.net

To: <sip:user1_public1@home1.net>

Contact: <sip:scscf1.home1.net>

Expires: 600000

Call-ID: apb03a0s09dkjdfglkj49112

CSeq: 43 REGISTER

Content-Length: 0

4.	200 OK response (IP-SM-GW to S-CSCF) - see example in table A.3-2

The PNA sends a 200 (OK) response to the S-CSCF indicating that Registration was successful.

Table A.3-2: 200 OK response (IP-SM-GW to S-CSCF)

SIP/2.0 200 OK

Via: SIP/2.0/UDP sip:scscf1.home1.net

From:

To:

Call-ID:

Contact: <sip:scscf1.home1.net>;expires=600000

CSeq:

Date: Wed, 11 July 2001 08:49:37 GMT

Content-Length:

5.	Sh: Data Update

Editor’s Note: It is FFS whether the interface between the IP-SM-GW and the HSS will be Sh or MAP.

The IP-SM-GW sends a request to the HSS to update profile. The HSS response includes a successful result code.

For detailed message flows see 3GPP TS 29.328 [11].

Table A.3-2a provides the parameters in the Sh data update procedure, which are sent to the HSS.

Table A.3-2a: Sh: Data update procedure (IP-SM-GW to HSS)

| Message source and destination | Sh: Information element name | Information source | Description |
| --- | --- | --- | --- |
| IP-SM-GW to HSS | User Identity | To header in SIP REGISTER request | This information element indicates the public user identity |
| IP-SM-GW to HSS | Data Reference | 14 (static, Location Information) | See Table 7.6.1 in 3GPP TS 29.328 [11] |
| IP-SM-GW to HSS | User Data | (static) IP-SM-GW address | HSS should return this address to SM-SC when SM-SC |
| IP-SM-GW to HSS | User Identity | (static) IP-SM-GW | This information element indicates the public user identity |

Editor’s Note: Data Reference information element is FFS.

Table A.3-2b provides the parameters sent from the HSS that need to be stored? In IP-SM-GW.

Table A.3-2b: Sh: Data update procedure (HSS to IP-SM-GW)

| Message source and destination | Sh: Information element name | Value | Description |
| --- | --- | --- | --- |
| HSS to IP-SM-GW | Result Code | DIAMETER_SUCCESS | This information indicates that update was successful |

# A.4	Signalling flows demonstrating how IP-SM-GW indicates to HSS the unavailability of UE for receiving SMS messages

Editor’s Note: IP-SM-GW deregistration from HSS is FFS in SA2. If it is removed, then there is no need for deregistration example. Otherwise the example will be inserted.

# A.5	Signalling flows demonstrating successful UE originated SMS submission over IP procedure

Figure A.5-1: UE originated SMS delivery over IP signalling

Editor’s Note: It is FFS how the delivery report will find the same UE. Also how to avoid forking at UE terminated SMS delivery.

Figure A.5-1 shows a successful UE originated SMS over IP submission. For simplicity it is assumed that IP-SM-GW has direct access to SM-SC. The details of the signalling flows are as follows:

1.	MESSAGE request (UE to P-CSCF) - see example in table A.5-1

This request includes a vnd.3gpp.sms payload that includes the short message and routing information for the IP-SM-GW to forward the short message.

Table A.5-1: MESSAGE request (UE to P-CSCF)

MESSAGE sip:TBD@TBD.net SIP/2.0

Via: SIP/2.0/UDP [5555::aaa:bbb:ccc:ddd]:1357;comp=sigcomp; branch=z9hG4bKnashds7

Max-Forwards: 70

Route: <sip:pcscf1.visited1.net:7531;lr;comp=sigcomp>, <sip:orig@scscf1.home1.net;lr>

P-Preferred-Identity: "John Doe" <sip:user1_public1@home1.net>

From: <sip:user1_public1@home1.net>; tag=171828

To: <sip:TBD@hTBD.net>

Call-ID: cb03a0s09a2sdfglkj490333

Cseq: 666 MESSAGE

Content-Type: application/vnd.3gpp.sms

Content-Length: (…)

Request-URI:	This is FFS.

Editor’s Note: It is FFS whether UE shall insert destination user’s URI, IP-SM-GW address, or SM-SC address as R-URI. The population of To header must be defined as well.

The payload includes an RP-DATA message (see 3GPP TS 24.011 [8]). It includes:

-	Address of the originating UE, i.e., the public user identity sending the SMS;

Editor’s Note: This field includes the length indicator only.

-	Address of the destination SM-SC, which is configured in the UE; and

-	RP-User-Data (see 3GPP TS 23.040 [3]), which includes SMS-SUBMIT as type indicator.

2.	MESSAGE request (P-CSCF to S-CSCF) - see example in table A.5-2

Table A.5-2: MESSAGE request (P-CSCF to S-CSCF)

MESSAGE sip:TBD@TBD.net SIP/2.0

Via: SIP/2.0/UDP pcscf1.visited1.net;branch=z9hG4bK240f341, SIP/2.0/UDP [5555::aaa:bbb:ccc:ddd]:1357;comp=sigcomp; branch=z9hG4bKnashds7

Max-Forwards: 69

Route: <sip:orig@scscf1.home1.net;lr>

P-Asserted-Identity: "John Doe" <sip:user1_public1@home1.net>

From: <sip:user1_public1@home1.net>; tag=171828

To: <sip:TBD@TBD.net>

Call-ID: cb03a0s09a2sdfglkj490333

Cseq: 666 MESSAGE

Content-Type: application/vnd.3gpp.sms

Content-Length: (…)

3.	Initial filter criteria

The S-CSCF analyses the incoming request against the initial filter criteria and decides to send the SIP MESSAGE request to the IP-SM-GW.

Editor’s Note: The SPT is FFS.

4.	MESSAGE request (S-CSCF to IP-SM-GW) - see example in table A.5-3

Table A.5-3: MESSAGE request (S-CSCF to IP-SM-GW)

MESSAGE sip:TBD@TBD.net SIP/2.0

Via: SIP/2.0/UDP scscf1.home1.net;branch=z9hG4bK344a651, SIP/2.0/UDP pcscf1.visited1.net;branch=z9hG4bK240f341, SIP/2.0/UDP [5555::aaa:bbb:ccc:ddd]:1357;comp=sigcomp; branch=z9hG4bKnashds7

Max-Forwards: 68

Route: <sip:ipsmgw.home1.net;lr>, <sip:cb03a0s09a2sdfglkj490333@scscf1.home1.net;lr>

P-Asserted-Identity: "John Doe" <sip:user1_public1@home1.net>

From: <sip:user1_public1@home1.net>; tag=171828

To: <sip:TBD@TBD.net>

Call-ID: cb03a0s09a2sdfglkj490333

Cseq: 666 MESSAGE

Content-Type: application/vnd.3gpp.sms

Content-Length: (…)

5.	202 (Accepted) response (IP-SM-GW to S-CSCF) - see example in table A.5-4

Table A.5-4: 202 (Accepted) response (IP-SM-GW to S-CSCF)

SIP/2.0 202 Accepted

Via: SIP/2.0/UDP scscf1.home1.net;branch=z9hG4bK344a651, SIP/2.0/UDP pcscf1.visited1.net;branch=z9hG4bK240f341, SIP/2.0/UDP [5555::aaa:bbb:ccc:ddd]:1357;comp=sigcomp; branch=z9hG4bKnashds7

From:

To:

Call-ID:

Cseq:

6.	202 (Accepted) response (S-CSCF to P-CSCF) - see example in table A.5-5

Table A.5-5: 202 (Accepted) response (S-CSCF to P-CSCF)

SIP/2.0 202 Accepted

Via: SIP/2.0/UDP pcscf1.visited1.net;branch=z9hG4bK240f341, SIP/2.0/UDP [5555::aaa:bbb:ccc:ddd]:1357;comp=sigcomp; branch=z9hG4bKnashds7

From:

To:

Call-ID:

Cseq:

7.	202 (Accepted) response (P-CSCF to UE) - see example in table A.5-6

Table A.5-6: 202 (Accepted) response (P-CSCF to UE)

SIP/2.0 202 Accepted

Via: SIP/2.0/UDP [5555::aaa:bbb:ccc:ddd]:1357;comp=sigcomp; branch=z9hG4bKnashds7

From:

To:

Call-ID:

Cseq:

8.	Extracting and forwarding the short message, waiting and processing report

NOTE: This step can be done right after step 5, in parallel with step 6 and 7.

The IP-SM-GW forwards the short message TPDU (SMS-SUBMIT) to the SM-SC. The SM-SC returns a submit report which includes SMS-SUBMIT-REPORT as type indicator.

9.	MESSAGE request (IP-SM-GW to S-CSCF) - see example in table A.5-7

This request includes a vnd.3gpp.sms payload that includes the short message submission report and routing information for the IP-SM-GW to forward the submission report.

Table A.5-7: MESSAGE request (IP-SM-GW to S-CSCF)

MESSAGE sip:user1_public1@home1.net SIP/2.0

Via: SIP/2.0/UDP ipsmgw.home1.net; branch=z9hG4bK876ffa3

Max-Forwards: 70

Route: <sip:orig@scscf1.home1.net;lr>

From: <sip:ipsmgw.home1.net>; tag=583558

To: <sip:user1_public1@home1.net>

Call-ID: fy365h43g3f36f3f6fth74g3

Cseq: 888 MESSAGE

Content-Type: application/vnd.3gpp.sms

Content-Length: (…)

Request-URI:	Public user identity receiving the submission report.

The payload includes an RP-ACK message (see 3GPP TS 24.011 [8]). It includes RP-User-Data (see 3GPP TS 23.040 [3]), which includes SMS-SUBMIT-REPORT as type indicator.

10.	MESSAGE request (S-CSCF to P-CSCF) - see example in table A.5-8

Table A.5-8: MESSAGE request (S-CSCF to P-CSCF)

MESSAGE sip:[5555::aaa:bbb:ccc:ddd]:1357;comp=sigcomp SIP/2.0

Via: SIP/2.0/UDP scscf1.home1.net;branch=z9hG4bK344a651, SIP/2.0/UDP ipsmgw.home1.net; branch=z9hG4bK876ffa3

Max-Forwards: 69

Route: <sip:pcscf1.visited1.net:7531;lr;comp=sigcomp>

From: <sip:ipsmgw.home1.net>; tag=583558

To: <sip:user1_public1@home1.net>

Call-ID: fy365h43g3f36f3f6fth74g3

Cseq: 888 MESSAGE

Content-Type: application/vnd.3gpp.sms

Content-Length: (…)

11.	MESSAGE request (P-CSCF to UE) - see example in table A.5-9

Table A.5-9: MESSAGE request (P-CSCF to UE)

MESSAGE sip:[5555::aaa:bbb:ccc:ddd]:1357;comp=sigcomp SIP/2.0

Via: SIP/2.0/UDP pcscf1.visited1.net;branch=z9hG4bK2524fd2, SIP/2.0/UDP scscf1.home1.net;branch=z9hG4bK344a651, SIP/2.0/UDP ipsmgw.home1.net; branch=z9hG4bK876ffa3

Max-Forwards: 68

From: <sip:ipsmgw.home1.net>; tag=583558

To: <sip:user1_public1@home1.net>

Call-ID: fy365h43g3f36f3f6fth74g3

Cseq: 888 MESSAGE

Content-Type: application/vnd.3gpp.sms

Content-Length: (…)

12.	200 (OK) response (IP-SM-GW to S-CSCF) - see example in table A.5-10

Table A.5-10: 20 (OK) response (UE to P-S-CSCF)

SIP/2.0 200 OK

Via: SIP/2.0/UDP pcscf1.visited1.net;branch=z9hG4bK2524fd2, SIP/2.0/UDP scscf1.home1.net;branch=z9hG4bK344a651, SIP/2.0/UDP ipsmgw.home1.net; branch=z9hG4bK876ffa3

From:

To:

Call-ID:

Cseq:

13.	200 (OK) response (P-CSCF to S-CSCF) - see example in table A.5-11

Table A.5-11: 200 (OK) response (P-CSCF to S-CSCF)

SIP/2.0 200 OK

Via: SIP/2.0/UDP scscf1.home1.net;branch=z9hG4bK344a651, SIP/2.0/UDP ipsmgw.home1.net; branch=z9hG4bK876ffa3

From:

To:

Call-ID:

Cseq:

14.	200 (OK) response (S-CSCF to IP-SM-GW) - see example in table A.5-12

Table A.5-12: 200 (OK) response (S-CSCF to IP-SM-GW)

SIP/2.0 200 OK

Via: SIP/2.0/UDP ipsmgw.home1.net; branch=z9hG4bK876ffa3

From:

To:

Call-ID:

Cseq:

# A.6	Signalling flows demonstrating successful UE terminated SMS delivery over IP procedure (including delivery report)

Figure A.6-1: UE originated SMS delivery over IP signalling

Editor’s Note: It is FFS how to avoid forking at UE terminated SMS delivery

Editor’s Note: Steps 8 to 14 are FFS in 3GPP SA2 WG.

Figure A.6-1 shows a successful UE terminated SMS over IP delivery. The details of the signalling flows are as follows:

1.	Receiving SMS from SM-SC

The IP-SM-GW receives a short message from SM-SC (smsc@home-a.net) which includes SMS-DELIVER as type indicator.

2.	MESSAGE request (IP-SM-GW to S-CSCF) - see example in table A.6-1

This request includes a vnd.3gpp.sms payload that includes the short message and routing information for the S-CSCF to forward the short message.

Table A.6-1: MESSAGE request (IP-SM-GW to S-CSCF)

MESSAGE sip:user1_public1@home1.net SIP/2.0

Via: SIP/2.0/UDP ipsmgw.home1.net; branch=z9hG4bK876ffa3

Max-Forwards: 70

Route: <sip:orig@scscf1.home1.net;lr>

From: <sip:ipsmgw.home1.net>; tag=583558

To: <sip:user1_public1@home1.net>

Call-ID: fy365h43g3f36f3f6fth74g3

Cseq: 888 MESSAGE

Content-Type: application/vnd.3gpp.sms

Content-Length: (…)

Request-URI:	Public user identity receiving the delivery report.

The payload includes the RP-DATA message (see 3GPP TS 24.011 [8]). Its RP-User-Data information element includes a TPDU of type SMS-DELIVER.

3.	MESSAGE request (S-CSCF to P-CSCF) - see example in table A.6-2

Table A.6-2: MESSAGE request (S-CSCF to P-CSCF)

MESSAGE sip:[5555::aaa:bbb:ccc:ddd]:1357;comp=sigcomp SIP/2.0

Via: SIP/2.0/UDP scscf1.home1.net;branch=z9hG4bK344a651, SIP/2.0/UDP ipsmgw.home1.net; branch=z9hG4bK876ffa3

Max-Forwards: 69

Route: <sip:pcscf1.visited1.net:7531;lr;comp=sigcomp>

From: <sip:ipsmgw.home1.net>; tag=583558

To: <sip:user1_public1@home1.net>

Call-ID: fy365h43g3f36f3f6fth74g3

Cseq: 888 MESSAGE

Content-Type: application/vnd.3gpp.sms

Content-Length: (…)

4.	MESSAGE request (P-CSCF to UE) - see example in table A.6-3

Table A.6-3: MESSAGE request (P-CSCF to UE)

MESSAGE sip:[5555::aaa:bbb:ccc:ddd]:1357;comp=sigcomp SIP/2.0

Via: SIP/2.0/UDP pcscf1.visited1.net;branch=z9hG4bK2524fd2, SIP/2.0/UDP scscf1.home1.net;branch=z9hG4bK344a651, SIP/2.0/UDP ipsmgw.home1.net; branch=z9hG4bK876ffa3

Max-Forwards: 68

From: <sip:ipsmgw.home1.net>; tag=583558

To: <sip:user1_public1@home1.net>

Call-ID: fy365h43g3f36f3f6fth74g3

Cseq: 888 MESSAGE

Content-Type: application/vnd.3gpp.sms

Content-Length: (…)

5.	200 (OK) response (UE to P-CSCF) - see example in table A.6-4

Table A.6-4: 20 (OK) response (UE to P-S-CSCF)

SIP/2.0 200 OK

Via: SIP/2.0/UDP pcscf1.visited1.net;branch=z9hG4bK2524fd2, SIP/2.0/UDP scscf1.home1.net;branch=z9hG4bK344a651, SIP/2.0/UDP ipsmgw.home1.net; branch=z9hG4bK876ffa3

From:

To:

Call-ID:

Cseq:

6.	200 (OK) response (P-CSCF to S-CSCF) - see example in table A.6-5

Table A.6-5: 200 (OK) response (P-CSCF to S-CSCF)

SIP/2.0 200 OK

Via: SIP/2.0/UDP scscf1.home1.net;branch=z9hG4bK344a651, SIP/2.0/UDP ipsmgw.home1.net; branch=z9hG4bK876ffa3

From:

To:

Call-ID:

Cseq:

7.	200 (OK) response (S-CSCF to IP-SM-GW) - see example in table A.6-6

Table A.6-6: 200 (OK) response (S-CSCF to IP-SM-GW)

SIP/2.0 200 OK

Via: SIP/2.0/UDP ipsmgw.home1.net; branch=z9hG4bK876ffa3

From:

To:

Call-ID:

Cseq:

8.	MESSAGE request (UE to P-CSCF) - see example in table A.6-7

This request includes a vnd.3gpp.sms payload that includes the SMS-DELIVER-REPORT and routing information for the IP-SM-GW to forward the delivery report.

Table A.6-7: MESSAGE request (UE to P-CSCF)

MESSAGE sip:TBD@TBD.net SIP/2.0

Via: SIP/2.0/UDP [5555::aaa:bbb:ccc:ddd]:1357;comp=sigcomp; branch=z9hG4bKnashds7

Max-Forwards: 70

Route: <sip:pcscf1.visited1.net:7531;lr;comp=sigcomp>, <sip:orig@scscf1.home1.net;lr>

P-Preferred-Identity: "John Doe" <sip:user1_public1@home1.net>

From: <sip:user1_public1@home1.net>; tag=171828

To: <sip:TBD@TBD.net>

Call-ID: cb03a0s09a2sdfglkj490333

Cseq: 999 MESSAGE

Content-Type: application/vnd.3gpp.sms

Content-Length: (…)

Request-URI:	This is FFS.

Editor’s Note: It is FFS whether UE shall insert IP-SM-GW address or SM-SC address as R-URI. The population of To header must be defined as well.

The payload includes an RP-ACK message (see 3GPP TS 24.011 [8]). Its RP-User-Data information element includes a TPDU of type SMS-DELIVER-REPORT.

9.	MESSAGE request (P-CSCF to S-CSCF) - see example in table A.6-8

Table A.6-8: MESSAGE request (P-CSCF to S-CSCF)

MESSAGE sip:TBD@TBD.net SIP/2.0

Via: SIP/2.0/UDP pcscf1.visited1.net;branch=z9hG4bK240f341, SIP/2.0/UDP [5555::aaa:bbb:ccc:ddd]:1357;comp=sigcomp; branch=z9hG4bKnashds7

Max-Forwards: 69

Route: <sip:orig@scscf1.home1.net;lr>

P-Asserted-Identity: "John Doe" <sip:user1_public1@home1.net>

From: <sip:user1_public1@home1.net>; tag=171828

To: <sip:TBD@TBD.net>

Call-ID: cb03a0s09a2sdfglkj490333

Cseq: 999 MESSAGE

Content-Type: application/vnd.3gpp.sms

Content-Length: (…)

10.	Initial filter criteria

The S-CSCF analyses the incoming request against the initial filter criteria and decides to send the SIP MESSAGE request to the IP-SM-GW.

Editor’s Note: The SPT is FFS.

11.	MESSAGE request (S-CSCF to IP-SM-GW) - see example in table A.6-9

Table A.6-9: MESSAGE request (S-CSCF to IP-SM-GW)

MESSAGE sip:TBD@TBD.net SIP/2.0

Via: SIP/2.0/UDP scscf1.home1.net;branch=z9hG4bK344a651, SIP/2.0/UDP pcscf1.visited1.net;branch=z9hG4bK240f341, SIP/2.0/UDP [5555::aaa:bbb:ccc:ddd]:1357;comp=sigcomp; branch=z9hG4bKnashds7

Max-Forwards: 68

Route: <sip:ipsmgw.home1.net;lr>, <sip:cb03a0s09a2sdfglkj490333@scscf1.home1.net;lr>

P-Asserted-Identity: "John Doe" <sip:user1_public1@home1.net>

From: <sip:user1_public1@home1.net>; tag=171828

To: <sip:TBD@TBD.net>

Call-ID: cb03a0s09a2sdfglkj490333

Cseq: 666 MESSAGE

Content-Type: application/vnd.3gpp.sms

Content-Length: (…)

12.	202 (Accepted) response (IP-SM-GW to S-CSCF) - see example in table A.6-10

Table A.6-10: 202 (Accepted) response (IP-SM-GW to S-CSCF)

SIP/2.0 202 Accepted

Via: SIP/2.0/UDP scscf1.home1.net;branch=z9hG4bK344a651, SIP/2.0/UDP pcscf1.visited1.net;branch=z9hG4bK240f341, SIP/2.0/UDP [5555::aaa:bbb:ccc:ddd]:1357;comp=sigcomp; branch=z9hG4bKnashds7

From:

To:

Call-ID:

Cseq:

13.	202 (Accepted) response (S-CSCF to P-CSCF) - see example in table A.6-11

Table A.6-11: 202 (Accepted) response (S-CSCF to P-CSCF)

SIP/2.0 202 Accepted

Via: SIP/2.0/UDP pcscf1.visited1.net;branch=z9hG4bK240f341, SIP/2.0/UDP [5555::aaa:bbb:ccc:ddd]:1357;comp=sigcomp; branch=z9hG4bKnashds7

From:

To:

Call-ID:

Cseq:

14.	202 (Accepted) response (P-CSCF to UE) - see example in table A.6-12

Table A.6-12: 202 (Accepted) response (P-CSCF to UE)

SIP/2.0 202 Accepted

Via: SIP/2.0/UDP [5555::aaa:bbb:ccc:ddd]:1357;comp=sigcomp; branch=z9hG4bKnashds7

From:

To:

Call-ID:

Cseq:

15.	Extracting and forwarding the delivery report

NOTE 1: This step can be done right after step 12, in parallel with step 13 and 14.

The IP-SM-GW forwards the short message TPDU (SMS-DELIVER-REPORT) to the SM-SC.

# A.7	Signalling flows demonstrating successful UE terminated MMS delivery using SMS over IP procedure

Annex B (informative):
Change history

| Change history |
| --- |
| Date | TSG # | TSG Doc. | CR | Rev | Subject/Comment | Old | New |
| 2006-05 |  |  |  |  | Initial version |  |  |
| 2006-05 |  |  |  |  | Version 0.1.0 incorporating results of CT1 discussions at CT1 #42. Agreed documents: C1-061049 (revised TS skeleton), C1-061050, C1-061052, C1-061053, and C1-061067. |  |  |
| 2006-07 |  |  |  |  | Version 0.2.0 incorporating results of CT1 discussions at CT1 #42bis. Agreed documents: C1-061140, C1-061329, C1-061330, C1-061333, C1-061334, C1-061335, C1-061353, C1-061354, C1-061359, and C1-061360. |  |  |