3G TR 25.924 V1.0.0 (1999-12)

Technical Report

3rd Generation Partnership Project;

Technical Specification Group Radio Access Network;

Opportunity Driven Multiple Access

(3G TR 25.924 version 1.0.0)

The present document has been developed within the 3rd Generation Partnership Project (3GPP TM) and may be further elaborated for the purposes of 3GPP.	 
The present document has not been subject to any approval process by the 3GPP Organisational Partners and shall not be implemented.	 
This Specification is provided for future development work within 3GPP only. The Organisational Partners accept no liability for any use of this Specification.
Specifications and reports for implementation of the 3GPP TM system should be obtained via the 3GPP Organisational Partners' Publications Offices.

Reference

3TR/TSGR-0225924U

Keywords

ODMA

3GPP

Postal address

3GPP support office address

650 Route des Lucioles - Sophia Antipolis

Valbonne - FRANCE

Tel.: +33 4 92 94 42 00 Fax: +33 4 93 65 47 16

Internet

http://www.3gpp.org

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© 1999, 3GPP Organizational Partners (ARIB, CWTS, ETSI, T1, TTA,TTC).

All rights reserved.

Contents

Foreword	4

1	Scope	5

2	References	5

3	Abbreviations	5

4	Opportunity Driven Multiple Access	5

4.1	ODMA Infrastructure Configurations	6

4.1.1	Systems with integrated TDD/ODMA NodeB	6

4.1.2	Systems employing Last Hop Gateway ODMA Relay Nodes	7

4.2	ODMA Probing and Route Acquisition	8

4.2.1	Different Probing States	8

4.2.1.1	Full probing	8

4.2.1.2	Duty Maintained probing	8

4.2.1.3	Relay Prohibited	8

4.3	ODMA Efficiency and Power Requirements	9

4.4	ODMA Physical Layer Burst Mapping	10

4.5	ODMA Idle Mode Procedures	10

4.6	ODMA Connected Mode Procedures	10

4.7	ODMA Synchronisation and Guard Bands	10

4.7.1	TDD Guard Period Requirements	10

Annex A: Frequently Asked Questions	11

History	13

# Foreword

This Technical Report has been produced by the 3GPP.

The contents of the present document are subject to continuing work within the TSG and may change following formal TSG approval. Should the TSG modify the contents of this TS, it will be re-released by the TSG with an identifying change of release date and an increase in version number as follows:

Version x.y.z

where:

x	the first digit:

1	presented to TSG for information;

2	presented to TSG for approval;

3	Indicates TSG approved document under change control.

y	the second digit is incremented for all changes of substance, i.e. technical enhancements, corrections, updates, etc.

z	the third digit is incremented when editorial only changes have been incorporated in the document.

# 1	Scope

The present document provides a description of Opportunity Driven Multiple Access (ODMA).

ODMA is a relay transmission protocol to be applied to UMTS TDD. ODMA will provide the ability to maintain high data rates within a TDD towards the edges of traditional TDD coverage. The main purpose of ODMA is:

-	Increase the high data rate coverage within a cell.

-	Increase the capacity of TDD.

-	Provide distributed network architecture for spot coverage and traffic hotspots.

# 2	References

[1]	3GPP Homepage: www.3GPP.org

[2] 	3G TS 25.301: "Radio Interface Protocol Architecture"

[3] 	3G TS 25.302: "Services provided by the Physical Layer"

[4] 	3G TS 25.303: "Interlayer Procedures in Connected Mode"

[5] 	3G TS 25.304: "UE Procedures in Idle Mode"

[6] 	3G TS 25.322: "RLC Protocol Specification"

[7] 	3G TS 25.331: "RRC Protocol Specification"

[8] 	3G TS 25.990: "Vocabulary"

# 3	Abbreviations

For the purposes of the present document, the following abbreviations apply:

OCCCH	ODMA Common Control Channel

ODCCH	ODMA Dedicated Control Channel

ODCH	ODMA Dedicated Channel

ODMA	Opportunity Driven Multiple Access

ORACH	ODMA Random Access Channel

ODTCH	ODMA Dedicated Traffic Channel

TDD	Time Division Duplex

UE	User Equipment

UER	User Equipment with ODMA relay operation enabled

UL	Uplink

UMTS	Universal Mobile Telecommunications System

URA	UTRAN Registration Area

UTRA	UMTS Terrestrial Radio Access

UTRAN	UMTS Terrestrial Radio Access Network

# 4	Opportunity Driven Multiple Access

ODMA is a communications relaying protocol, which may be used to increase the efficiency of UMTS. One way in which this is achieved is by increasing the range of high data rate services. The concept of ODMA was introduced at ETSI SMG2 in 1996, after which a number of contributions have been presented.

In summary, in an ideal telecommunications system the minimum amount of transmit power that can provide satisfactory service will always be used to overcome the radio path. In wireless telecommunications systems that have a large number of subscribers, an opportunistic method of transmission can take place where information is relayed between a number of nodes. It has been shown that the most efficient method of communicating is to break a larger path down into a number of smaller hops. However, the efficient routing of data in such a system without incurring the large overhead that is usually associated with ad-hoc routing systems is not trivial. ODMA is a relay protocol designed to address this shortfall.

ODMA may be regarded as an expansion of the current UMTS TDD mode[, although further studies are taking place to examine is application to UMTS FDD environments]. One of the aims of ODMA is to increase the capacity and efficiency of radio transmissions towards the boundaries of the cell. At these regions due to the hostile losses in the channel only relatively low data rates can normally be achieved. ODMA provides TDD with a mechanism to provide high data rate coverage by relaying these transmissions over a number of hops.

Each relaying node must be within the planned coverage of the cell, so that it may receive essential layer 1 synchronisation information. Each node also has to authenticate itself with the network, which will enable it to be used as a relay. Therefore, any ODMA relay node that is within the planned coverage area may be used to relay communication, but any ODMA relay node outside of the planned coverage area will not be able to be used to relay communications; as shown in Figure 1. Therefore, the regulation of ODMA transmissions at the border regions should be NO more complex than the planning that will have to be applied to the TDD mode of operation.

Figure 1: ODMA Border Coverage

## 4.1	ODMA Infrastructure Configurations

The UTRAN consists of three core elements; UE, NodeB, and RNC. However, ODMA may be introduced into this core infrastructure via a number of configurations. The configurations are systems with integrated TDD/ODMA NodeB, and systems employing last hop Gateway ODMA relay nodes.

### 4.1.1	Systems with integrated TDD/ODMA NodeB

One implementation of ODMA would be to use an integrated TDD system that contains ODMA procedures built into the infrastructure. This implementation results in system information such as synchronisation and paging messages being readily available from the standard TDD system.

One of the aims of ODMA is to extend the range of the high rate data coverage, e.g. to match that offered by TDD and FDD for speech coverage.  Increased high data rate coverage can be achieved both by deployed seeds and relay terminals that happen to fall into the regions requiring increased capacity. A simplistic view of this concept is illustrated in Figure 2.

Figure 2: ODMA concept diagram with integrated TDD/ODMA NodeB

Figure 2 illustrates a scenario where the Node B may provide extended data service coverage directly through the use of ODMA.

### 4.1.2	Systems employing Last Hop Gateway ODMA Relay Nodes

In systems where FDD infrastructure may be extensive but limited TDD infrastructure is available then last hop gateway ODMA relay nodes should be deployed. Last Hop Gateway ODMA Relay Nodes provide the ability to extend high data rate communications within 3G systems by interworking ODMA functionality with standard FDD infrastructure (requiring only nominal changes to the RNC). A simplistic view of this concept is illustrated in Figure 3.

Figure 3: ODMA concept diagram with last hop

NOTE:	This approach is equally applicable to TDD NodeB's if it does not have ODMA capability.

## 4.2	ODMA Probing and Route Acquisition

Probing is a mechanism used by a relay to build a neighbour list which should contain at least a predefined minimum number of neighbours. This probing mechanism will be defined within the idle mode cell selection. In order to optimise power consumption the relay terminal will regulate probing activity.

A relays probing activity levels will be influenced by a number of key parameters such as

-	Number of neighbours

-	Gradient to the base information of the neighbours

-	Speed of the terminal - This may indeed represent a simplification for vehicle-mounted UER for which battery consumption is not at stake.

-	Battery power level

These probing activity levels will be characterised by three states. The probing states are full probing, duty maintained probing, relay prohibited.

### 4.2.1	Different Probing States

One aim of assigning probing rates is to ensure efficient power consumption. The functional difference between these states may generally be determined by the number of ORACH slots that may be used for probing within a superframe.

#### 4.2.1.1	Full probing

The full probing mode is the case where the relay constantly uses the ORACH by monitoring and transmitting probe bursts. When this mode is chosen by a relay, then it means that the probing messages for the neighbours of that local area may be sent and received on any ORACH slot within a superframe.

#### 4.2.1.2	Duty Maintained probing

This is the "normal" probing mode. This mode is designed to cope with dynamic changes within the terminals local connectivity and scheduling the probing accordingly. Note the assignment of the slots in a superframe allocated as an ORACH does not have to be consecutive.

#### 4.2.1.3	Relay Prohibited

In this mode the relay ceases all its probing activities and would fall into non-relay TDD or FDD operation. Figure 4 illustrates probing on the ORACH during a 72-superframe cycle.

Figure 4: ORACH Superframe selection

Typical activity levels within an ODMA system are illustrated in Figure 5.

Figure 5: UERs with different probing states

## 4.3	ODMA Efficiency and Power Requirements

FFS

## 4.4	ODMA Physical Layer Burst Mapping

FFS

## 4.5	ODMA Idle Mode Procedures

Neighbour Gathering

The concept of neighbour gathering must be understood for the ODMA routing process to become clear. Neighbour gathering is a process where the local connectivity of an ODMA relay node is assessed through the use of a background probing messages. This neighbour information is stored within a neighbour table. Gradient tables are also derived from the neighbour messages but are used to evaluate the end-to-end connectivity. [Example routeing tables are described in Tdoc180.]  Gradients are effectively a cost function of the routeing messages over a particular path in terms of propagation conditions, number of hops, and other system parameters. In practice each mobile should have at least one gradient to a NodeB which will allow any call set-up procedures to be executed allowing for route acquisition.

## 4.6	ODMA Connected Mode Procedures

FFS

## 4.7	ODMA Synchronisation and Guard Bands

ODMA will operate in the TDD mode without adding any further constraints on the synchronisation of the TDD mode. This section highlights guard period requirements for the UMTS-TDD mode and the corresponding impact on ODMA.

### 4.7.1	TDD Guard Period Requirements

For the UMTS-TDD mode, where it is possible to have multiple switching points, this suggests that guard periods must be inserted at the end of every slot to avoid receiver capture. The guard period specified for each slot in the UMTS TDD mode is 96-chip duration, which allows a maximum two-way communication of approximately 3.5 km.

Since ODMA is intended for relatively short distances between ODMA nodes, which are adequately covered by the GP available within a slot. This means ODMA does not place any further constraints on the synchronisation or the GP requirements of TDD.

Due to the relatively short range of transmissions, the inclusion of ODMA does not impose any additional guard period or frame synchronisation requirements over those discussed above for standard TDD.

Any potential overlap caused by relay transmissions will be localised to a node and its neighbours by the ODMA protocol.

The inclusion of ODMA could relax the guard period requirements of a TDD system since neighbouring mobiles are regarded as relay opportunities and any communications between neighbours (on an ODCH) could be synchronised further

Annex A: Frequently Asked Questions

Question 1

In highly connected networks, delay per hop decreases. Is it not likely in such cases the mean distance covered by each hop is shortened so that the reduced delay per hop is offset by an increase in the number of hops per path. The total end to end delay may actually increase. Have we examined this?

Answer 1

As the density of stations increases, the path loss between stations typically reduces as a 40 log D relationship.  Therefore the data rate that can be used between stations increases at the same rate.  The delay of a multi-hop network reduces as the density goes up, even if there are more relays.  For example if the relay distance is halved, the number of hops is doubled, the path loss per hop is reduced by 12 dB and the data rate can be increased by ten times or so (at the same power level), and therefore overall delay is reduced by five.  This is a non-intuitive conclusion and holds, providing the data rate can be continually increased.  In addition, the amount of joules of energy required to move the data over the relays is reduced in total by five times.  Overall there is an improvement in performance through using more relay hops.

At some point the maximum data rate is reached, due to bandwidth allocation or complexity problems, at which point the number of hops needs to be curtailed based upon the maximum delay.

Question 2

ODMA should not focus entirely on urban deployments. The large increase in the number of basestations that we suggest UMTS needs compared with GSM actually only applies to the rural (i.e. noise-limited) case - hence "universal" UMTS remains uneconomic. Surely if ODMA sticks to the non-fading wideband relaying the required ranges can be achieved - albeit at 100mW mean power?

Answer 2

Wide area coverage in the rural environment, particularly if this is used as an extension of the high data rate services within a rural cell, is an important application of ODMA. Particularly in rural environments where there are sparse population densities strung out along roads or in clusters, the use of seeds and subscriber relay to fixed subscribers or via fixed subscribers will provide significant advantages.

Question 3

What are the average sleeping patterns on 720 ms multi-frame?

Answer 3

FFS

Question 4

How many times and during how many slots and frames does the UE listen to the RACH, ORACH?

Answer 4

FFS

Question 5

What is the duty cycle of probing on the RACH, ORACH?

Answer 5

FFS

Question 6

Over how many slots are receive and transmit associated with relaying functionality?

Answer 6

FFS

# History

| Document history |
| --- |
| 0.0.1 | April 1999 | Report was created with initial headings included from document R2-99287 |
| 0.0.2 | May 1999 | References to 3GPP documents number numbers within the report were updated. |
| 0.1.0 | June 1999 | Version 0.0.2 approved by WG2 over email. |
| 0.1.1 | July 1999 | Expansion of sections ODMA, Probing and Route Acquisition, TDD Guard Period Requirements, and Idle Mode Procedures. |
| 0.1.2 | August 1999 | Approved changes proposed during email ad-hoc on ODMA. |
| 0.2.0 | September 1999 | Changes approved to 0.1.2. |
| 1.0.0 | December 1999 | Raised to document number for presentation to RAN#6. |
| V2.0.0 |  |  |
| V3.0.0 | <MMMM yyyy> | Publication |

Rapporteur for 3GPP TSG RAN WG2 25.924 is:

Alan Law

Communications Security and Advanced Development

Vodafone Ltd

The Courtyard

2-4 London Road

Newbury

Berkshire

RG141JX

United Kingdom

Tel: +44 (0)1635 676470

Fax: +44 (0)1635 234895

Email: alan.law@vf.vodafone.co.uk