3GPP TS 29.198-6 V6.6.1 (2006-07)

Technical Specification

3rd Generation Partnership Project;

Technical Specification Group Core Network and Terminals;

Open Service Access (OSA);

Application Programming Interface (API);

Part 6: Mobility Service Capability Feature (SCF)

(Release 6)

The present document has been developed within the 3rd Generation Partnership Project (3GPP TM) and may be further elaborated for the purposes of 3GPP.	 
The present document has not been subject to any approval process by the 3GPP Organizational Partners and shall not be implemented.	 
This Specification is provided for future development work within 3GPP only. The Organizational Partners accept no liability for any use of this Specification.
Specifications and reports for implementation of the 3GPP TM system should be obtained via the 3GPP Organizational Partners' Publications Offices.

Keywords

UMTS, API, OSA

3GPP

Postal address

3GPP support office address

650 Route des Lucioles - Sophia Antipolis

Valbonne - FRANCE

Tel.: +33 4 92 94 42 00 Fax: +33 4 93 65 47 16

Internet

http://www.3gpp.org

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© 2006, 3GPP Organizational Partners (ARIB, ATIS, CCSA, ETSI, TTA, TTC).

All rights reserved.

Contents

Foreword	8

Introduction	8

1	Scope	10

2	References	10

3	Definitions and abbreviations	11

3.1	Definitions	11

3.2	Abbreviations	11

4	Mobility SCF	11

4.1	General requirements on support of methods	11

5	Sequence Diagrams	11

5.1	User Location Sequence Diagrams	11

5.1.1	User Location Interrogation - Triggered Request	11

5.1.2	User Location Interrogation - Periodic Request	12

5.1.3	User Location Interrogation - Interactive Request	13

5.2	User Location Camel Sequence Diagrams	14

5.2.1	User Location Camel Interrogation - Triggered Request	14

5.2.2	User Location Camel Interrogation - Periodic Request	15

5.2.3	User Location Camel Interrogation - Interactive Request	16

5.3	User Status Sequence Diagrams	17

5.3.1	Triggered Reporting	17

5.3.2	Interactive Request	18

6	Class Diagrams	19

6.1	User Location Class Diagrams	19

6.2	User Location Camel Class Diagrams	20

6.3	User Status Class Diagrams	21

7	The Service Interface Specifications	22

7.1	Interface Specification Format	22

7.1.1	Interface Class	22

7.1.2	Method descriptions	22

7.1.3	Parameter descriptions	23

7.1.4	State Model	23

7.2	Base Interface	23

7.2.1	Interface Class IpInterface	23

7.3	Service Interfaces	23

7.3.1	Overview	23

7.4	Generic Service Interface	23

7.4.1	Interface Class IpService	23

7.4.1.1	Method setCallback()	24

7.4.1.2	Method setCallbackWithSessionID()	24

8	Mobility Interface Classes	24

8.1	User Location Interface Classes	24

8.1.1	Interface Class IpUserLocation	25

8.1.1.1	Method locationReportReq()	25

8.1.1.2	Method extendedLocationReportReq()	26

8.1.1.3	Method periodicLocationReportingStartReq()	26

8.1.1.4	Method periodicLocationReportingStop()	27

8.1.1.5	Method <<new>> getNextPeriodicLocationRequest()	27

8.1.2	Interface Class IpAppUserLocation	28

8.1.2.1	Method locationReportRes()	28

8.1.2.2	Method locationReportErr()	28

8.1.2.3	Method extendedLocationReportRes()	29

8.1.2.4	Method extendedLocationReportErr()	29

8.1.2.5	Method periodicLocationReport()	29

8.1.2.6	Method periodicLocationReportErr()	30

8.1.3	Interface Class IpTriggeredUserLocation	30

8.1.3.1	Method triggeredLocationReportingStartReq()	30

8.1.3.2	Method triggeredLocationReportingStop()	31

8.1.3.3	Method <<new>> getNextTriggeredLocationRequest()	31

8.1.4	Interface Class IpAppTriggeredUserLocation	32

8.1.4.1	Method triggeredLocationReport()	32

8.1.4.2	Method triggeredLocationReportErr()	33

8.1.4.3	Method <<new>> triggeredReportingEnded()	33

8.2	User Location Camel Interface Classes	33

8.2.1	Interface Class IpUserLocationCamel	33

8.2.1.1	Method locationReportReq()	34

8.2.1.2	Method periodicLocationReportingStartReq()	34

8.2.1.3	Method periodicLocationReportingStop()	35

8.2.1.4	Method triggeredLocationReportingStartReq()	35

8.2.1.5	Method triggeredLocationReportingStop()	36

8.2.1.6	Method <<new>> getNextPeriodicLocationRequest()	36

8.2.1.7	Method <<new>> getNextTriggeredLocationRequest()	37

8.2.2	Interface Class IpAppUserLocationCamel	37

8.2.2.1	Method locationReportRes()	38

8.2.2.2	Method locationReportErr()	38

8.2.2.3	Method periodicLocationReport()	39

8.2.2.4	Method periodicLocationReportErr()	39

8.2.2.5	Method triggeredLocationReport()	39

8.2.2.6	Method triggeredLocationReportErr()	39

8.2.2.7	Method <<new>> triggeredReportingEnded()	40

8.3	User Status Interface Classes	40

8.3.1	Interface Class IpAppUserStatus	40

8.3.1.1	Method statusReportRes()	41

8.3.1.2	Method statusReportErr()	41

8.3.1.3	Method triggeredStatusReport()	42

8.3.1.4	Method triggeredStatusReportErr()	42

8.3.1.5	Method <<new>> extendedStatusReportRes()	42

8.3.1.6	Method <<new>> extendedStatusReportErr()	42

8.3.1.7	Method <<new>> extTriggeredStatusReport()	43

8.3.1.8	Method <<new>> extTriggeredStatusReportErr()	43

8.3.1.9	Method <<new>> triggeredReportingEnded()	43

8.3.2	Interface Class IpUserStatus	43

8.3.2.1	Method statusReportReq()	44

8.3.2.2	Method triggeredStatusReportingStartReq()	45

8.3.2.3	Method triggeredStatusReportingStop()	45

8.3.2.4	Method <<new>> getNextTriggeredStatusRequest()	45

8.3.2.5	Method <<new>> extendedStatusReportReq()	46

8.3.2.6	Method <<new>> extTriggeredStatusReportingStartReq()	46

8.3.2.7	Method <<new>> extTriggeredStatusReportingStop()	47

9	State Transition Diagrams	47

9.1	User Location	47

9.2	User Location Camel	47

9.2.1	State Transition Diagrams for IpUserLocationCamel	47

9.2.1.1	Active State	48

9.3	User Status	48

9.3.1	State Transition Diagrams for IpUserStatus	48

9.3.1.1	Active State	49

10	Service Properties	49

10.1	Mobility Properties	49

10.1.1	Emergency Application Subtypes	49

10.1.2	Value Added Application Subtypes	49

10.1.3	PLMN Operator Application Subtypes	50

10.1.4	Lawful Intercept Application Subtypes	50

10.1.5	Altitude Obtainable	50

10.1.6	Location Methods	50

10.1.7	Priorities	50

10.1.8	Max Interactive Requests	51

10.1.9	Max Triggered Users	51

10.1.10	Max Periodic Users	51

10.1.11	Min Periodic Interval Duration	51

10.1.12	Initial Report	51

10.1.13	Max Life Time	51

10.2	User Location Service Properties	51

10.3	User Location Camel Service Properties	52

10.4	User Status Service Properties	52

11	Data Definitions	53

11.1	Common Mobility Data Definitions	53

11.1.1	TpGeographicalPosition	53

11.1.2	TpLocationPriority	54

11.1.3	TpLocationRequest	55

11.1.4	TpLocationResponseIndicator	55

11.1.5	TpLocationResponseTime	55

11.1.6	TpLocationType	55

11.1.7	TpLocationUncertaintyShape	56

11.1.8	TpMobilityDiagnostic	56

11.1.9	TpMobilityError	57

11.1.10	TpMobilityStopAssignmentData	57

11.1.11	TpMobilityStopScope	57

11.1.12	TpTerminalType	57

11.2	User Location Data Definitions	58

11.2.1	IpUserLocation	58

11.2.2	IpUserLocationRef	58

11.2.3	IpAppUserLocation	58

11.2.4	IpAppUserLocationRef	58

11.2.5	IpTriggeredUserLocation	58

11.2.6	IpTriggeredUserLocationRef	58

11.2.7	IpAppTriggeredUserLocation	58

11.2.8	IpAppTriggeredUserLocationRef	58

11.2.9	TpUlExtendedData	58

11.2.10	TpUlExtendedDataSet	58

11.2.11	TpUserLocationExtended	59

11.2.12	TpUserLocationExtendedSet	59

11.2.13	TpLocationTrigger	59

11.2.14	TpLocationTriggerSet	59

11.2.15	TpLocationTriggerCriteria	59

11.2.16	TpUserLocation	59

11.2.17	TpUserLocationSet	60

11.2.18	TpTriggeredLocationRequestSetEntry	60

11.2.19	TpTriggeredLocationRequestSet	60

11.2.20	TpTriggeredLocationRequest	60

11.2.21	TpPeriodicLocationRequestSetEntry	60

11.2.22	TpPeriodicLocationRequestSet	60

11.2.23	TpPeriodicLocationRequest	60

11.3	User Location Camel Data Definitions	61

11.3.1	IpUserLocationCamel	61

11.3.2	IpUserLocationCamelRef	61

11.3.3	IpAppUserLocationCamel	61

11.3.4	IpAppUserLocationCamelRef	61

11.3.5	TpLocationCellIDOrLAI	61

11.3.6	TpLocationTriggerCamel	61

11.3.7	TpUserLocationCamel	62

11.3.8	TpUserLocationCamelSet	62

11.4	User Location Emergency Data Definitions	62

11.4.1	IpUserLocationEmergency	62

11.4.2	IpUserLocationEmergencyRef	62

11.4.3	IpAppUserLocationEmergency	62

11.4.4	IpAppUserLocationEmergencyRef	62

11.4.5	TpIMEI	62

11.4.6	TpNaESRD	62

11.4.7	TpNaESRK	63

11.4.8	TpUserLocationEmergencyRequest	63

11.4.9	TpUserLocationEmergency	63

11.4.10	TpUserLocationEmergencyTrigger	64

11.5	User Status Data Definitions	64

11.5.1	IpUserStatus	64

11.5.2	IpUserStatusRef	64

11.5.3	IpAppUserStatus	64

11.5.4	IpAppUserStatusRef	64

11.5.5	TpUserStatus	64

11.5.6	TpUserStatusSet	64

11.5.7	TpUserStatusIndicator	64

11.5.8	TpTriggeredStatusRequestSetEntry	65

11.5.9	TpTriggeredStatusRequestSet	65

11.5.10	TpTriggeredStatusRequest	65

11.5.11	TpUserStatusExtended	65

11.5.12	TpUserStatusExtendedSet	65

11.5.13	TpUserStatusIndicatorExtended	66

11.5.14	TpAuthStatusIndicator	66

11.5.15	TpUserInfo	66

11.5.16	TpNetworkStatusIndicator	66

11.5.17	TpAccessTechnology	66

11.5.18	TpRoamingStatus	66

11.6	User Binding Data Definitions	67

11.6.1	TpBindingSet	67

11.6.2	TpBindingEntrySet	67

11.6.3	TpBindingEntry	67

11.6.4	TpBindingEntryType	67

11.6.5	TpBindingNotificationCriteriaSet	67

11.6.6	TpBindingNotificationCriteria	68

11.6.7	TpBindingNotificationCriteriaType	68

11.7	Units and Validations of Parameters	68

12	Exception Classes	69

Annex A (normative):	OMG IDL Description of Mobility SCF	70

Annex B (informative):	W3C WSDL Description of Mobility SCF	71

Annex C (informative):	Java API Description of the Mobility SCFs	72

Annex D (informative):	Description of Mobility SCF for 3GPP2 cdma2000 networks	73

D.1	General Exceptions	73

D.2	Specific Exceptions	73

D.2.1	Clause 1: Scope	73

D.2.2	Clause 2: References	73

D.2.3	Clause 3: Definitions and abbreviations	73

D.2.4	Clause 4: Mobility SCF	73

D.2.5	Clause 5: Sequence Diagrams	73

D.2.6	Clause 6 Class Diagrams	74

D.2.7	Clause 7: The Service Interface Specifications	74

D.2.8	Clause 8: Mobility Interface Classes	74

D.2.9	Clause 9: State Transition Diagrams	74

D.2.10	Clause 10: Service Properties	74

D.2.11	Clause 11: Data Definitions	74

D.2.12	Clause 12: Exception Classes	74

D.2.13	Annex A (normative): OMG IDL Description of Mobility SCF	74

D.2.14	Annex B (informative): W3C WSDL Description of Mobility SCF	74

D.2.15	Annex C (informative): Java™ API Description of Mobility SCF	74

Annex E (informative):	Change history	75

# Foreword

This Technical Specification has been produced by the 3rd Generation Partnership Project (3GPP).

The contents of the present document are subject to continuing work within the TSG and may change following formal TSG approval. Should the TSG modify the contents of the present document, it will be re-released by the TSG with an identifying change of release date and an increase in version number as follows:

Version x.y.z

where:

x	the first digit:

1	presented to TSG for information;

2	presented to TSG for approval;

3	or greater indicates TSG approved document under change control.

y	the second digit is incremented for all changes of substance, i.e. technical enhancements, corrections, updates, etc.

z	the third digit is incremented when editorial only changes have been incorporated in the document.

# Introduction

The present document is part 6 of a multi-part TS covering the 3rd Generation Partnership Project: Technical Specification Group Core Network and Terminals; Open Service Access (OSA); Application Programming Interface (API), as identified below. The API specification (3GPP TS 29.198) is structured in the following Parts:

Part 1: 	"Overview";

Part 2: 	"Common Data Definitions";

Part 3:	"Framework";

Part 4:	"Call Control";

Sub-part 1: "Call Control Common Definitions";

Sub-part 2: "Generic Call Control SCF";

Sub-part 3: "Multi-Party Call Control SCF";

Sub-part 4: "Multi-Media Call Control SCF";

Sub-part 5: "Conference Call Control SCF";	(not part of 3GPP Release 6)

Part 5:	"User Interaction SCF";

Part 6:	"Mobility SCF";

Part 7:	"Terminal Capabilities SCF";

Part 8:	"Data Session Control SCF";

Part 9:	"Generic Messaging SCF";	(not part of 3GPP Release 6)

Part 10:	"Connectivity Manager SCF";	(not part of 3GPP Release 6)

Part 11:	"Account Management SCF";

Part 12:	"Charging SCF".

Part 13:	"Policy Management SCF";

Part 14:	"Presence and Availability Management SCF";

Part 15:	"Multi Media Messaging SCF";	(new in Release 6)

The Mapping specification of the OSA APIs and network protocols (3GPP TR 29.998) is also structured as above. A mapping to network protocols is however not applicable for all Parts, but the numbering of Parts is kept.
Also in case a Part is not supported in a Release, the numbering of the parts is maintained.

Table: Overview of the OSA APIs & Protocol Mappings 29.198 & 29.998-family

| OSA API specifications 29.198-family | OSA API Mapping - 29.998-family |
| --- | --- |
| 29.198-01 | Overview | 29.998-01 | Overview |
| 29.198-02 | Common Data Definitions | 29.998-02 | Not Applicable |
| 29.198-03 | Framework | 29.998-03 | Not Applicable |
| Call Control (CC) SCF | 29.198-04-1 Common CC data definitions | 29.198-04-2 Generic CC SCF | 29.198-04-3 Multi-Party CC SCF | 29.198-04-4 Multi-media CC SCF | 29.998-04-1 | Generic Call Control – CAP mapping |
|  |  |  |  |  | 29.998-04-2 | Generic Call Control – INAP mapping |
|  |  |  |  |  | 29.998-04-3 | Generic Call Control – Megaco mapping |
|  |  |  |  |  | 29.998-04-4 | Multiparty Call Control – ISC mapping |
| 29.198-05 | User Interaction SCF | 29.998-05-1 | User Interaction – CAP mapping |
|  |  | 29.998-05-2 | User Interaction – INAP mapping |
|  |  | 29.998-05-3 | User Interaction – Megaco mapping |
|  |  | 29.998-05-4 | User Interaction – SMS mapping |
| 29.198-06 | Mobility SCF | 29.998-06 | User Status and User Location – MAP mapping |
| 29.198-07 | Terminal Capabilities SCF | 29.998-07 | Not Applicable |
| 29.198-08 | Data Session Control SCF | 29.998-08 | Data Session Control – CAP mapping |
| 29.198-09 | Generic Messaging SCF | 29.998-09 | Not Applicable |
| 29.198-10 | Connectivity Manager SCF | 29.998-10 | Not Applicable |
| 29.198-11 | Account Management SCF | 29.998-11 | Not Applicable |
| 29.198-12 | Charging SCF | 29.998-12 | Not Applicable |
| 29.198-13 | Policy Management SCF | 29.998-13 | Not Applicable |
| 29.198-14 | Presence & Availability Management SCF | 29.998-14 | Not Applicable |
| 29.198-15 | Multi-media Messaging SCF | 29.998-15 | Not Applicable |

# 1	Scope

The present document is Part 6 of the Stage 3 specification for an Application Programming Interface (API) for Open Service Access (OSA).

The OSA specifications define an architecture that enables application developers to make use of network functionality through an open standardised interface, i.e. the OSA APIs. The concepts and the functional architecture for the OSA are contained in 3GPP TS 23.198 [3]. The requirements for OSA are contained in 3GPP TS 22.127 [2].

The present document specifies the Mobility Service Capability Feature (SCF) aspects of the interface. All aspects of the Mobility SCF are defined here, these being:

-	Sequence Diagrams

-	Class Diagrams

-	Interface specification plus detailed method descriptions

-	State Transition diagrams

-	Data definitions

- IDL Description of the interfaces

- WSDL Description of the interfaces

- Reference to the Java™ API description of the interfaces

The process by which this task is accomplished is through the use of object modelling techniques described by the Unified Modelling Language (UML).

This specification has been defined jointly between 3GPP TSG CT WG5, ETSI TISPAN and the Parlay Group, in co-operation with a number of JAIN™ Community member companies.

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

- References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

- For a specific reference, subsequent revisions do not apply.

- For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TS 29.198-01: "Open Service Access (OSA) Application Programming Interface (API); Part 1: Overview".

[2]	3GPP TS 22.127: "Service Requirement for the Open Services Access (OSA); Stage 1".

[3]	3GPP TS 23.198: "Open Service Access (OSA); Stage 2".

[4]	3GPP TS 29.002: "Mobile Application Part (MAP) specification".

# 3	Definitions and abbreviations

## 3.1	Definitions

For the purposes of the present document, the terms and definitions given in TS 29.198-1 [1] apply.

## 3.2	Abbreviations

For the purposes of the present document, the abbreviations given in TS 29.198-1 [1] apply.

# 4	Mobility SCF

The following clauses describe each aspect of the Mobility Service Capability Feature (SCF).

The order is as follows:

The Sequence diagrams give the reader a practical idea of how each of the SCFs is implemented.

The Class relationships clause shows how each of the interfaces applicable to the SCF, relate to one another.

The Interface specification clause describes in detail each of the interfaces shown within the Class diagram part.

The State Transition Diagrams (STD) show the transition between states in the SCF. The states and transitions are well-defined; either methods specified in the Interface specification or events occurring in the underlying networks cause state transitions.

The Data Definitions clause shows a detailed expansion of each of the data types associated with the methods within the classes. Note that some data types are used in other methods and classes and are therefore defined within the Common Data types part of this specification.

## 4.1	General requirements on support of methods

An implementation of this API which supports or implements a method described in the present document, shall support or implement the functionality described for that method, for at least one valid set of values for the parameters of that method.

Where a method is not supported by an implementation of a Service interface, the exception P_METHOD_NOT_SUPPORTED shall be returned to any call of that method.

Where a method is not supported by an implementation of an Application interface, a call to that method shall be possible, and no exception shall be returned.

# 5	Sequence Diagrams

## 5.1	User Location Sequence Diagrams

### 5.1.1	User Location Interrogation - Triggered Request

The following sequence diagram shows how an application requests triggered location reports from the User Location service. When users location changes, the service reports this to the application.

1:	This message is used to start triggered location reporting for one or several users.

2:	When the trigger condition is fulfilled then this message passes the location of the affected user to its callback object.

3:	This is repeated until the application stops triggered location reporting (see next message).

4:	This message is used to stop triggered location reporting.

### 5.1.2	User Location Interrogation - Periodic Request

The following sequence diagram shows how an application requests periodic location reports from the User Location service.

1:	This message is used to start periodic location reporting for one or several users.

2:	This message passes the location of one or several users to its callback object.

3:	This message passes the location of one or several users to its callback object.

This is repeated at regular intervals until the application stops periodic location reporting (see next message).

4:	This message is used to stop periodic location reporting.

### 5.1.3	User Location Interrogation - Interactive Request

The following sequence diagram shows how an application requests a location report from the User Location service.

1:	This message is used to request the location of one or several users.

2:	This message passes the result of the location request for one or several users to its callback object.

## 5.2	User Location Camel Sequence Diagrams

### 5.2.1	User Location Camel Interrogation - Triggered Request

The following sequence diagram shows how an application requests triggered location reports from the User Location Camel service. When users location changes, the service reports this to the application.

1:	This message is used to start triggered location reporting for one or several users.

2:	When the trigger condition is fulfilled then this message passes the location of the affected user to its callback object.

3:	This is repeated until the application stops triggered location reporting (see next message).

4:	This message is used to stop triggered location reporting.

### 5.2.2	User Location Camel Interrogation - Periodic Request

The following sequence diagram shows how an application requests periodic location reports from the User Location Camel service.

1:	This message is used to start periodic location reporting for one or several users.

2:	This message passes the location of one or several users to its callback object.

3:	This message passes the location of one or several users to its callback object.

This is repeated at regular intervals until the application stops periodic location reporting (see next message).

4:	This message is used to stop periodic location reporting.

### 5.2.3	User Location Camel Interrogation - Interactive Request

The following sequence diagram shows how an application requests a location report from the User Location Camel service.

1:	This message is used to request the location of one or several users.

2:	This message passes the result of the location request for one or several users to its callback object.

## 5.3	User Status Sequence Diagrams

### 5.3.1	Triggered Reporting

The following sequence diagram shows how an application requests triggered status reports from the Status Location service. When user's status changes, the service reports this to the application.

1:	This message is used to start triggered status reporting for one or several users.

2:	When a user's status changes,  this message passes the status to its callback object.

3:	This is repeated until the application stops triggered status reporting (see next message).

4:	This message is used to stop triggered status reporting.

### 5.3.2	Interactive Request

The following sequence diagram shows how an application requests a status report from the User Status service.

1:	This message is used to request the status of one or several users.

2:	This message passes the result of the status request to its callback object.

# 6	Class Diagrams

## 6.1	User Location Class Diagrams

This class diagram shows the relationship between the interfaces in the User Location service. IpTriggeredUserLocation inherits from IpUserLocation, and IpAppTriggeredUserLocation inherits from IpAppUserLocation.

Figure: User Location Class Diagram

## 6.2	User Location Camel Class Diagrams

This class diagram shows the interfaces for the User Location Camel service.

Figure: User Location Camel Class Diagram

## 6.3	User Status Class Diagrams

This class diagram shows the interfaces for the User Status service.

Figure: User Status Class Diagram

# 7	The Service Interface Specifications

## 7.1	Interface Specification Format

This clause defines the interfaces, methods and parameters that form a part of the  API specification. The Unified Modelling Language (UML) is used to specify the interface classes. The general format of an interface specification is described below.

### 7.1.1	Interface Class

This shows a UML interface class description of the methods supported by that interface, and the relevant parameters and types. The Service and Framework interfaces for enterprise-based client applications are denoted by classes with name Ip<name>. The callback interfaces to the applications are denoted by classes with name IpApp<name>.  For the interfaces between a Service and the Framework, the Service interfaces are typically denoted by classes with name IpSvc<name>, while the Framework interfaces are denoted by classes with name IpFw<name>.

### 7.1.2	Method descriptions

Each method (API method “call”) is described. Both synchronous and asynchronous methods are used in the  API. Asynchronous methods are identified by a 'Req' suffix for a method request, and, if applicable, are served by asynchronous methods identified by either a 'Res' or 'Err' suffix for method results and errors, respectively. To handle responses and reports, the application or service developer must implement the relevant IpApp<name> or IpSvc<name> interfaces to provide the callback mechanism.

### 7.1.3	Parameter descriptions

Each method parameter and its possible values are described. Parameters described as 'in' represent those that must have a value when the method is called. Those described as 'out' are those that contain the return result of the method when the method returns.

### 7.1.4	State Model

If relevant, a state model is shown to illustrate the states of the objects that implement the described interface.

## 7.2	Base Interface

### 7.2.1	Interface Class IpInterface

All application, framework and service interfaces inherit from the following interface. This API Base  Interface does not provide any additional methods.

<<Interface>> IpInterface

## 7.3	Service Interfaces

### 7.3.1	Overview

The Service Interfaces provide the interfaces into the capabilities of the underlying network - such as call control, user interaction, messaging, mobility and connectivity management.

The interfaces that are implemented by the services are denoted as 'Service Interface'. The corresponding interfaces that must be implemented by the application (e.g. for API callbacks) are denoted as 'Application Interface'.

## 7.4	Generic Service Interface

### 7.4.1	Interface Class IpService

Inherits from: IpInterface

All service interfaces inherit from the following interface.

<<Interface>> IpService

setCallback (appInterface : in IpInterfaceRef) : void setCallbackWithSessionID (appInterface : in IpInterfaceRef, sessionID : in TpSessionID) : void

#### 7.4.1.1	Method setCallback()

This method specifies the reference address of the callback interface that a service uses to invoke methods on the application.  It is not allowed to invoke this method on an interface that uses SessionIDs.  Multiple invocations of this method on an interface shall result in multiple callback references being specified. The SCS shall use the most recent callback interface provided by the application using this method. In the event that a callback reference fails or is no longer available, the next most recent callback reference available shall be used.

Parameters

appInterface : in IpInterfaceRef

Specifies a reference to the application interface, which is used for callbacks.

Raises

TpCommonExceptions, P_INVALID_INTERFACE_TYPE

#### 7.4.1.2	Method setCallbackWithSessionID()

This method specifies the reference address of the application's callback interface that a service uses for interactions associated with a specific session ID: e.g. a specific call, or call leg.  It is not allowed to invoke this method on an interface that does not use SessionIDs.  Multiple invocations of this method on an interface shall result in multiple callback references being specified. The SCS shall use the most recent callback interface provided by the application using this method. In the event that a callback reference fails or is no longer available, the next most recent callback reference available shall be used.

Parameters

appInterface : in IpInterfaceRef

Specifies a reference to the application interface, which is used for callbacks.

sessionID : in TpSessionID

Specifies the session for which the service can invoke the application's callback interface.

Raises

TpCommonExceptions, P_INVALID_SESSION_ID, P_INVALID_INTERFACE_TYPE

# 8	Mobility Interface Classes

## 8.1	User Location Interface Classes

The User Location service (UL) provides a general geographic location service. UL has functionality to allow applications to obtain the geographical location and the status of fixed, mobile and IP based telephony users.

UL is supplemented by User Location Camel service (ULC) to provide information about network related information. There is also some specialised functionality to handle emergency calls in the User Location Emergency service (ULE).

The UL service provides the IpUserLocation and IpTriggeredUserLocation interfaces. Most methods are asynchronous, in that they do not lock a thread into waiting whilst a transaction performs. In this way, the client machine can handle many more calls, than one that uses synchronous message calls. To handle responses and reports, the developer must implement IpAppUserLocation and IpAppTriggeredUserLocation interfaces to provide the callback mechanism.

When periodic or triggered location reporting is used, errors may be reported either when the recurrent reporting is requested, as an error per user in reports or in the corresponding err-method when the error concerns all subscribers in an assignment.

### 8.1.1	Interface Class IpUserLocation

Inherits from: IpService.

This interface is the 'service manager' interface for the User Location Service.

The user location interface provides the management functions to the user location service. The application programmer can use this interface to obtain the geographical location of users.

This interface, or IpTriggeredUserLocation, shall be implemented by a User Location SCF as a minimum requirement.

The locationReportReq() method, or the extendedLocationReportReq() method, or both the periodicLocationReportingStartReq() and periodicLocationReportingStop() methods shall be implemented as a minimum requirement, if this interface is implemented.

<<Interface>> IpUserLocation

locationReportReq (appLocation : in IpAppUserLocationRef, users : in TpAddressSet) : TpAssignmentID extendedLocationReportReq (appLocation : in IpAppUserLocationRef, users : in TpAddressSet, request : in TpLocationRequest) : TpAssignmentID periodicLocationReportingStartReq (appLocation : in IpAppUserLocationRef, users : in TpAddressSet, request : in TpLocationRequest, reportingInterval : in TpDuration) : TpAssignmentID periodicLocationReportingStop (stopRequest : in TpMobilityStopAssignmentData) : void <<new>> getNextPeriodicLocationRequest (reset : in TpBoolean) : TpPeriodicLocationRequestSetEntry

#### 8.1.1.1	Method locationReportReq()

Request of a report on the location for one or several users.

Returns: assignmentId.

Specifies the assignment ID of the location-report request.

Parameters

appLocation : in IpAppUserLocationRef

Specifies the application interface for callbacks from the User Location service.

users : in TpAddressSet

Specifies the user(s) for which the location shall be reported.

Returns

TpAssignmentID

Raises

TpCommonExceptions, P_APPLICATION_NOT_ACTIVATED, P_INFORMATION_NOT_AVAILABLE, P_INVALID_INTERFACE_TYPE

#### 8.1.1.2	Method extendedLocationReportReq()

Advanced request of report on the location for one or several users.

Returns: assignmentId.

Specifies the assignment ID of the extended location-report request.

Parameters

appLocation : in IpAppUserLocationRef

Specifies the application interface for callbacks from the User Location service.

users : in TpAddressSet

Specifies the user(s) for which the location shall be reported

request : in TpLocationRequest

Specifies among others the requested location type, accuracy, response time and priority.

Returns

TpAssignmentID

Raises

TpCommonExceptions, P_APPLICATION_NOT_ACTIVATED, P_REQUESTED_ACCURACY_CANNOT_BE_DELIVERED, P_REQUESTED_RESPONSE_TIME_CANNOT_BE_DELIVERED, P_INFORMATION_NOT_AVAILABLE, P_INVALID_INTERFACE_TYPE

#### 8.1.1.3	Method periodicLocationReportingStartReq()

Request of periodic reports on the location for one or several users.

Returns: assignmentId.

Specifies the assignment ID of the periodic location-reporting request.

Parameters

appLocation : in IpAppUserLocationRef

Specifies the application interface for callbacks from the User Location service.

users : in TpAddressSet

Specifies the user(s) for which the location shall be reported.

request : in TpLocationRequest

Specifies among others the requested location type, accuracy, response time and priority.

reportingInterval : in TpDuration

Specifies the requested interval in milliseconds between the reports.

Returns

TpAssignmentID

Raises

TpCommonExceptions, P_INVALID_REPORTING_INTERVAL, P_REQUESTED_ACCURACY_CANNOT_BE_DELIVERED, P_REQUESTED_RESPONSE_TIME_CANNOT_BE_DELIVERED, P_APPLICATION_NOT_ACTIVATED, P_INFORMATION_NOT_AVAILABLE, P_INVALID_INTERFACE_TYPE

#### 8.1.1.4	Method periodicLocationReportingStop()

Termination of periodic reports on the location for one or several users.

Parameters

stopRequest : in TpMobilityStopAssignmentData

Specifies how the assignment shall be stopped, i.e. if whole or just parts of the assignment should be stopped.

Raises

TpCommonExceptions, P_INVALID_ASSIGNMENT_ID

#### 8.1.1.5	Method <<new>> getNextPeriodicLocationRequest()

This method is used by the application to query the request set created with periodicLocationReportingStartReq. Since a lot of data can potentially be returned (which might cause problem in the middleware), this method must be used in an iterative way. Each method invocation  may return part of the total set of requests if the set is too large to return it at once. The reset parameter permits the application to indicate whether an invocation to getNextPeriodicLocationRequest  is requesting more requests from the total set of requests or is requesting that the total set of requests shall be returned from the beginning.

Returns the set of requests and an indication whether all off the requests have been obtained or if more requests are available that have not yet been obtained by  the application.

Note that the (maximum) number of items provided to the application is determined by the gateway.

Parameters

reset : in TpBoolean

TRUE: indicates that the application is intended to obtain the set of requests starting at the beginning.

FALSE: indicates that the application requests the next set of requests that have not (yet) been obtained since the last call to this method with this parameter set to TRUE.

The first time this method is invoked, reset shall be set to TRUE. Following the receipt of a final indication, for the next call to this method reset shall be set to TRUE. P_TASK_REFUSED may be thrown if these conditions are not met.

Returns

TpPeriodicLocationRequestSetEntry

Raises

TpCommonExceptions

### 8.1.2	Interface Class IpAppUserLocation

Inherits from: IpInterface.

The user-location application interface is implemented by the client application developer and is used to handle user location request responses.

<<Interface>> IpAppUserLocation

locationReportRes (assignmentId : in TpAssignmentID, locations : in TpUserLocationSet) : void locationReportErr (assignmentId : in TpAssignmentID, cause : in TpMobilityError, diagnostic : in TpMobilityDiagnostic) : void extendedLocationReportRes (assignmentId : in TpAssignmentID, locations : in TpUserLocationExtendedSet) : void extendedLocationReportErr (assignmentId : in TpAssignmentID, cause : in TpMobilityError, diagnostic : in TpMobilityDiagnostic) : void periodicLocationReport (assignmentId : in TpAssignmentID, locations : in TpUserLocationExtendedSet) : void periodicLocationReportErr (assignmentId : in TpAssignmentID, cause : in TpMobilityError, diagnostic : in TpMobilityDiagnostic) : void

#### 8.1.2.1	Method locationReportRes()

A report containing locations for one or several users is delivered.

Parameters

assignmentId : in TpAssignmentID

Specifies the assignment ID of the location-report request.

locations : in TpUserLocationSet

Specifies the location(s) of one or several users.

#### 8.1.2.2	Method locationReportErr()

This method indicates that the location report request has failed.

Parameters

assignmentId : in TpAssignmentID

Specifies the assignment ID of the failed location report request.

cause : in TpMobilityError

Specifies the error that led to the failure.

diagnostic : in TpMobilityDiagnostic

Specifies additional information about the error that led to the failure.

#### 8.1.2.3	Method extendedLocationReportRes()

A report containing extended location information for one or several users is delivered.

Parameters

assignmentId : in TpAssignmentID

Specifies the assignment ID of the extended location-report request.

locations : in TpUserLocationExtendedSet

Specifies the location(s) of one or several users.

#### 8.1.2.4	Method extendedLocationReportErr()

This method indicates that the extended location report request has failed.

Parameters

assignmentId : in TpAssignmentID

Specifies the assignment ID of the failed extended location report request.

cause : in TpMobilityError

Specifies the error that led to the failure.

diagnostic : in TpMobilityDiagnostic

Specifies additional information about the error that led to the failure.

#### 8.1.2.5	Method periodicLocationReport()

A report containing periodic location information for one or several users is delivered.

Parameters

assignmentId : in TpAssignmentID

Specifies the assignment ID of the periodic location-reporting request.

locations : in TpUserLocationExtendedSet

Specifies the location(s) of one or several users.

#### 8.1.2.6	Method periodicLocationReportErr()

This method indicates that a requested periodic location report has failed. Note that errors only concerning individual users are reported in the ordinary periodicLocationReport() message.

Parameters

assignmentId : in TpAssignmentID

Specifies the assignment ID of the failed periodic location reporting start request.

cause : in TpMobilityError

Specifies the error that led to the failure.

diagnostic : in TpMobilityDiagnostic

Specifies additional information about the error that led to the failure.

### 8.1.3	Interface Class IpTriggeredUserLocation

Inherits from: IpUserLocation.

This interface can be used as an extended version of the User Location: Service Interface.

The triggered user location interface represents the interface to the triggered user location functions. The application programmer can use this interface to request user location reports that are triggered by location change.

This interface, or IpUserLocation, shall be implemented by a User Location SCF as a minimum requirement.

The triggeredLocationReportingStartReq() and triggeredLocationReportingStop() methods shall be implemented as a minimum requirement. An implementation of IpTriggeredUserLocation is not required to implement the minimum mandatory methods of IpUserLocation.

<<Interface>> IpTriggeredUserLocation

triggeredLocationReportingStartReq (appLocation : in IpAppTriggeredUserLocationRef, users : in TpAddressSet, request : in TpLocationRequest, triggers : in TpLocationTriggerSet) : TpAssignmentID triggeredLocationReportingStop (stopRequest : in TpMobilityStopAssignmentData) : void <<new>> getNextTriggeredLocationRequest (reset : in TpBoolean) : TpTriggeredLocationRequestSetEntry

#### 8.1.3.1	Method triggeredLocationReportingStartReq()

Request for user location reports when the location is changed (reports are triggered by location change).

Returns: assignmentId.

Specifies the assignment ID of the triggered location-reporting request.

Parameters

appLocation : in IpAppTriggeredUserLocationRef

Specifies the application interface for callbacks from the User Location service.

users : in TpAddressSet

Specifies the user(s) for which the location shall be reported.

request : in TpLocationRequest

Specifies among others the requested location type, accuracy, response time and priority.

triggers : in TpLocationTriggerSet

Specifies the trigger conditions.

Returns

TpAssignmentID

Raises

TpCommonExceptions, P_REQUESTED_ACCURACY_CANNOT_BE_DELIVERED, P_REQUESTED_RESPONSE_TIME_CANNOT_BE_DELIVERED, P_TRIGGER_CONDITIONS_NOT_SUBSCRIBED, P_UNKNOWN_SUBSCRIBER, P_APPLICATION_NOT_ACTIVATED, P_INFORMATION_NOT_AVAILABLE, P_INVALID_INTERFACE_TYPE

#### 8.1.3.2	Method triggeredLocationReportingStop()

Stop triggered user location reporting.

Parameters

stopRequest : in TpMobilityStopAssignmentData

Specifies how the assignment shall be stopped, i.e. if whole or just parts of the assignment should be stopped.

Raises

TpCommonExceptions, P_INVALID_ASSIGNMENT_ID

#### 8.1.3.3	Method <<new>> getNextTriggeredLocationRequest()

This method is used by the application to query the request set created with triggeredLocationReportingStartReq. Since a lot of data can potentially be returned (which might cause problem in the middleware), this method must be used in an iterative way. Each method invocation  may return part of the total set of requests if the set is too large to return it at once. The reset parameter permits the application to indicate whether an invocation to getNextTriggeredLocationRequest  is requesting more requests from the total set of requests or is requesting that the total set of requests shall be returned from the beginning.

Returns the set of requests and an indication whether all off the requests have been obtained or if more requests are available that have not yet been obtained by  the application.

Note that the (maximum) number of items provided to the application is determined by the gateway.

Parameters

reset : in TpBoolean

TRUE: indicates that the application is intended to obtain the set of requests starting at the beginning.

FALSE: indicates that the application requests the next set of requests that have not (yet) been obtained since the last call to this method with this parameter set to TRUE.

The first time this method is invoked, reset shall be set to TRUE. Following the receipt of a final indication, for the next call to this method reset shall be set to TRUE. P_TASK_REFUSED may be thrown if these conditions are not met.

Returns

TpTriggeredLocationRequestSetEntry

Raises

TpCommonExceptions

### 8.1.4	Interface Class IpAppTriggeredUserLocation

Inherits from: IpAppUserLocation.

This interface must be used as a specialised version of the User Location: Application Interface if the Triggered User Location: Service Interface is used.

The triggered user location application interface is implemented by the client application developer and is used to handle triggered location reports.

<<Interface>> IpAppTriggeredUserLocation

triggeredLocationReport (assignmentId : in TpAssignmentID, location : in TpUserLocationExtended, criterion : in TpLocationTriggerCriteria) : void triggeredLocationReportErr (assignmentId : in TpAssignmentID, cause : in TpMobilityError, diagnostic : in TpMobilityDiagnostic) : void <<new>> triggeredReportingEnded (assignmentId : in TpAssignmentID) : void

#### 8.1.4.1	Method triggeredLocationReport()

A triggered report containing location for a user is delivered.

Parameters

assignmentId : in TpAssignmentID

Specifies the assignment ID of the triggered location-reporting request.

location : in TpUserLocationExtended

Specifies the location of the user.

criterion : in TpLocationTriggerCriteria

Specifies the criterion that triggered the report.

#### 8.1.4.2	Method triggeredLocationReportErr()

This method indicates that a requested triggered location report has failed. Note that errors only concerning individual users are reported in the ordinary triggeredLocationReport() message.

Parameters

assignmentId : in TpAssignmentID

Specifies the assignment ID of the failed triggered location reporting start request.

cause : in TpMobilityError

Specifies the error that led to the failure.

diagnostic : in TpMobilityDiagnostic

Specifies additional information about the error that led to the failure.

#### 8.1.4.3	Method <<new>> triggeredReportingEnded()

The user status or user location triggering has stopped because the max life time allowed for this triggering has exceeded.

Parameters

assignmentId : in TpAssignmentID

Specifies the assignment ID of the triggered request.

## 8.2	User Location Camel Interface Classes

The ULC provides location information, based on network-related information, rather than the geographical co-ordinates that can be retrieved via the general User Location Service.

Using the ULC functions, an application programmer can request the VLR Number, the location Area Identification and the Cell Global Identification and other mobile-telephony-specific location information.

The ULC provides the IpUserLocationCamel interface. Most methods are asynchronous, in that they do not lock a thread into waiting whilst a transaction performs. In this way, the client machine can handle many more calls, than one that uses synchronous message calls. To handle responses and reports, the developer must implement IpAppUserLocationCamel interface to provide the callback mechanism.

### 8.2.1	Interface Class IpUserLocationCamel

Inherits from: IpService.

This interface is the 'service manager' interface for ULC.

This interface shall be implemented by a User Location Camel SCF.

The locationReportReq() method, or both the periodicLocationReportingStartReq() and periodicLocationReportingStop() methods, or both the triggeredLocationReportingStartReq() and triggeredLocationReportingStop() methods shall be implemented as a minimum requirement.

<<Interface>> IpUserLocationCamel

locationReportReq (appLocationCamel : in IpAppUserLocationCamelRef, users : in TpAddressSet) : TpAssignmentID periodicLocationReportingStartReq (appLocationCamel : in IpAppUserLocationCamelRef, users : in TpAddressSet, reportingInterval : in TpDuration) : TpAssignmentID periodicLocationReportingStop (stopRequest : in TpMobilityStopAssignmentData) : void triggeredLocationReportingStartReq (appLocationCamel : in IpAppUserLocationCamelRef, users : in TpAddressSet, trigger : in TpLocationTriggerCamel) : TpAssignmentID triggeredLocationReportingStop (stopRequest : in TpMobilityStopAssignmentData) : void <<new>> getNextPeriodicLocationRequest (reset : in TpBoolean) : TpPeriodicLocationRequestSetEntry <<new>> getNextTriggeredLocationRequest (reset : in TpBoolean) : TpTriggeredLocationRequestSetEntry

#### 8.2.1.1	Method locationReportReq()

Request for mobile-related location information on one or several camel users.

Returns: assignmentId.

Specifies the assignment ID of the location-report request.

Parameters

appLocationCamel : in IpAppUserLocationCamelRef

Specifies the application interface for callbacks from the User Location Camel service.

users : in TpAddressSet

Specifies the user(s) for which the location shall be reported.

Returns

TpAssignmentID

Raises

TpCommonExceptions, P_UNKNOWN_SUBSCRIBER, P_APPLICATION_NOT_ACTIVATED, P_INFORMATION_NOT_AVAILABLE, P_INVALID_INTERFACE_TYPE

#### 8.2.1.2	Method periodicLocationReportingStartReq()

Request for periodic mobile location reports on one or several users.

Returns: assignmentId.

Specifies the assignment ID of the periodic location-reporting request.

Parameters

appLocationCamel : in IpAppUserLocationCamelRef

Specifies the application interface for callbacks from the User Location Camel service.

users : in TpAddressSet

Specifies the user(s) for which the location shall be reported.

reportingInterval : in TpDuration

Specifies the requested interval in milliseconds between the reports.

Returns

TpAssignmentID

Raises

TpCommonExceptions, P_INVALID_REPORTING_INTERVAL, P_UNKNOWN_SUBSCRIBER, P_APPLICATION_NOT_ACTIVATED, P_INFORMATION_NOT_AVAILABLE, P_INVALID_INTERFACE_TYPE

#### 8.2.1.3	Method periodicLocationReportingStop()

This method stops the sending of periodic mobile location reports for one or several users.

Parameters

stopRequest : in TpMobilityStopAssignmentData

Specifies how the assignment shall be stopped, i.e. if whole or just parts of the assignment should be stopped.

Raises

TpCommonExceptions, P_INVALID_ASSIGNMENT_ID

#### 8.2.1.4	Method triggeredLocationReportingStartReq()

Request for user location reports, containing mobile related information, when the location is changed (the report is triggered by the location change).

Returns: assignmentId.

Specifies the assignment ID of the triggered location-reporting request.

Parameters

appLocationCamel : in IpAppUserLocationCamelRef

Specifies the application interface for callbacks from the User Location Camel service.

users : in TpAddressSet

Specifies the user(s) for which the location shall be reported.

trigger : in TpLocationTriggerCamel

Specifies the trigger conditions.

Returns

TpAssignmentID

Raises

TpCommonExceptions, P_UNKNOWN_SUBSCRIBER, P_APPLICATION_NOT_ACTIVATED, P_INFORMATION_NOT_AVAILABLE, P_INVALID_INTERFACE_TYPE

#### 8.2.1.5	Method triggeredLocationReportingStop()

Request that triggered mobile location reporting should stop.

Parameters

stopRequest : in TpMobilityStopAssignmentData

Specifies how the assignment shall be stopped, i.e. if whole or just parts of the assignment should be stopped.

Raises

TpCommonExceptions, P_INVALID_ASSIGNMENT_ID

#### 8.2.1.6	Method <<new>> getNextPeriodicLocationRequest()

This method is used by the application to query the request set created with periodicLocationReportingStartReq. Since a lot of data can potentially be returned (which might cause problem in the middleware), this method must be used in an iterative way. Each method invocation  may return part of the total set of requests if the set is too large to return it at once. The reset parameter permits the application to indicate whether an invocation to getNextPeriodicLocationRequest  is requesting more requests from the total set of requests or is requesting that the total set of requests shall be returned from the beginning.

Returns the set of requests and an indication whether all off the requests have been obtained or if more requests are available that have not yet been obtained by  the application.

Note that the (maximum) number of items provided to the application is determined by the gateway.

Parameters

reset : in TpBoolean

TRUE: indicates that the application is intended to obtain the set of requests starting at the beginning.

FALSE: indicates that the application requests the next set of requests that have not (yet) been obtained since the last call to this method with this parameter set to TRUE.

The first time this method is invoked, reset shall be set to TRUE. Following the receipt of a final indication, for the next call to this method reset shall be set to TRUE. P_TASK_REFUSED may be thrown if these conditions are not met.

Returns

TpPeriodicLocationRequestSetEntry

Raises

TpCommonExceptions

#### 8.2.1.7	Method <<new>> getNextTriggeredLocationRequest()

This method is used by the application to query the request set created with triggeredLocationReportingStartReq. Since a lot of data can potentially be returned (which might cause problem in the middleware), this method must be used in an iterative way. Each method invocation  may return part of the total set of requests if the set is too large to return it at once. The reset parameter permits the application to indicate whether an invocation to getNextTriggeredLocationRequest  is requesting more requests from the total set of requests or is requesting that the total set of requests shall be returned from the beginning.

Returns the set of requests and an indication whether all off the requests have been obtained or if more requests are available that have not yet been obtained by  the application.

Note that the (maximum) number of items provided to the application is determined by the gateway.

Parameters

reset : in TpBoolean

TRUE: indicates that the application is intended to obtain the set of requests starting at the beginning.

FALSE: indicates that the application requests the next set of requests that have not (yet) been obtained since the last call to this method with this parameter set to TRUE.

The first time this method is invoked, reset shall be set to TRUE. Following the receipt of a final indication, for the next call to this method reset shall be set to TRUE. P_TASK_REFUSED may be thrown if these conditions are not met.

Returns

TpTriggeredLocationRequestSetEntry

Raises

TpCommonExceptions

### 8.2.2	Interface Class IpAppUserLocationCamel

Inherits from: IpInterface.

The user location Camel application interface is implemented by the client application developer and is used to handle location reports that are specific for mobile telephony users.

<<Interface>> IpAppUserLocationCamel

locationReportRes (assignmentId : in TpAssignmentID, locations : in TpUserLocationCamelSet) : void locationReportErr (assignmentId : in TpAssignmentID, cause : in TpMobilityError, diagnostic : in TpMobilityDiagnostic) : void periodicLocationReport (assignmentId : in TpAssignmentID, locations : in TpUserLocationCamelSet) : void periodicLocationReportErr (assignmentId : in TpAssignmentID, cause : in TpMobilityError, diagnostic : in TpMobilityDiagnostic) : void triggeredLocationReport (assignmentId : in TpAssignmentID, location : in TpUserLocationCamel, criterion : in TpLocationTriggerCamel) : void triggeredLocationReportErr (assignmentId : in TpAssignmentID, cause : in TpMobilityError, diagnostic : in TpMobilityDiagnostic) : void <<new>> triggeredReportingEnded (assignmentId : in TpAssignmentID) : void

#### 8.2.2.1	Method locationReportRes()

Delivery of a mobile location report. The report is containing mobile-related location information for one or several users.

Parameters

assignmentId : in TpAssignmentID

Specifies the assignment ID of the location-report request.

locations : in TpUserLocationCamelSet

Specifies the location(s) of one or several users.

#### 8.2.2.2	Method locationReportErr()

This method indicates that the location report request has failed.

Parameters

assignmentId : in TpAssignmentID

Specifies the assignment ID of the failed location report request.

cause : in TpMobilityError

Specifies the error that led to the failure.

diagnostic : in TpMobilityDiagnostic

Specifies additional information about the error that led to the failure.

#### 8.2.2.3	Method periodicLocationReport()

Periodic delivery of mobile location reports. The reports are containing mobile-related location information for one or several users.

Parameters

assignmentId : in TpAssignmentID

Specifies the assignment ID of the periodic location-reporting request.

locations : in TpUserLocationCamelSet

Specifies the location(s) of one or several users.

#### 8.2.2.4	Method periodicLocationReportErr()

This method indicates that a requested periodic location report has failed. Note that errors only concerning individual users are reported in the ordinary periodicLocationReport() message.

Parameters

assignmentId : in TpAssignmentID

Specifies the assignment ID of the failed periodic location reporting start request.

cause : in TpMobilityError

Specifies the error that led to the failure.

diagnostic : in TpMobilityDiagnostic

Specifies additional information about the error that led to the failure.

#### 8.2.2.5	Method triggeredLocationReport()

Delivery of a report that is indicating that the user's mobile location has changed.

Parameters

assignmentId : in TpAssignmentID

Specifies the assignment ID of the triggered location-reporting request.

location : in TpUserLocationCamel

Specifies the location of the user.

criterion : in TpLocationTriggerCamel

Specifies the criterion that triggered the report.

#### 8.2.2.6	Method triggeredLocationReportErr()

This method indicates that a requested triggered location report has failed. Note that errors only concerning individual users are reported in the ordinary triggeredLocationReport() message.

Parameters

assignmentId : in TpAssignmentID

Specifies the assignment ID of the failed triggered location reporting start request.

cause : in TpMobilityError

Specifies the error that led to the failure.

diagnostic : in TpMobilityDiagnostic

Specifies additional information about the error that led to the failure.

#### 8.2.2.7	Method <<new>> triggeredReportingEnded()

The user status or user location triggering has stopped because the max life time allowed for this triggering has exceeded.

Parameters

assignmentId : in TpAssignmentID

Specifies the assignment ID of the triggered request.

## 8.3	User Status Interface Classes

The User Status Service (US) provides a general user status service. US allow applications to obtain the status of fixed, mobile and IP-based telephony users.

The US provides the IpUserStatus interface. Most methods are asynchronous, in that they do not lock a thread into waiting whilst a transaction performs. In this way, the client machine can handle many more calls, than one that uses synchronous message calls. To handle responses and reports, the developer must implement IpAppUserStatus interface to provide the callback mechanism.

### 8.3.1	Interface Class IpAppUserStatus

Inherits from: IpInterface.

The user-status application interface is implemented by the client application developer and is used to handle user status reports.

<<Interface>> IpAppUserStatus

statusReportRes (assignmentId : in TpAssignmentID, status : in TpUserStatusSet) : void statusReportErr (assignmentId : in TpAssignmentID, cause : in TpMobilityError, diagnostic : in TpMobilityDiagnostic) : void triggeredStatusReport (assignmentId : in TpAssignmentID, status : in TpUserStatus) : void triggeredStatusReportErr (assignmentId : in TpAssignmentID, cause : in TpMobilityError, diagnostic : in TpMobilityDiagnostic) : void <<new>> extendedStatusReportRes (assignmentId : in TpAssignmentID, status : in TpUserStatusExtendedSet) : void <<new>> extendedStatusReportErr (assignmentId : in TpAssignmentID, cause : in TpMobilityError, diagnostic : in TpMobilityDiagnostic) : void <<new>> extTriggeredStatusReport (assignmentId : in TpAssignmentID, status : in TpUserStatusExtended) : void <<new>> extTriggeredStatusReportErr (assignmentId : in TpAssignmentID, cause : in TpMobilityError, diagnostic : in TpMobilityDiagnostic) : void <<new>> triggeredReportingEnded (assignmentId : in TpAssignmentID) : void

#### 8.3.1.1	Method statusReportRes()

Delivery of a report, that is containing one or several user's status.

Parameters

assignmentId : in TpAssignmentID

Specifies the assignment ID of the status-report request.

status : in TpUserStatusSet

Specifies the status of one or several users.

#### 8.3.1.2	Method statusReportErr()

This method indicates that the status report request has failed.

Parameters

assignmentId : in TpAssignmentID

Specifies the assignment ID of the failed status report request.

cause : in TpMobilityError

Specifies the error that led to the failure.

diagnostic : in TpMobilityDiagnostic

Specifies additional information about the error that led to the failure.

#### 8.3.1.3	Method triggeredStatusReport()

Delivery of a report that is indicating that a user's status has changed.

Parameters

assignmentId : in TpAssignmentID

Specifies the assignment ID of the triggered status-reporting request.

status : in TpUserStatus

Specifies the status of the user.

#### 8.3.1.4	Method triggeredStatusReportErr()

This method indicates that a requested triggered status reporting has failed. Note that errors only concerning individual users are reported in the ordinary triggeredStatusReport() message.

Parameters

assignmentId : in TpAssignmentID

Specifies the assignment ID of the failed triggered status reporting start request.

cause : in TpMobilityError

Specifies the error that led to the failure.

diagnostic : in TpMobilityDiagnostic

Specifies additional information about the error that led to the failure.

#### 8.3.1.5	Method <<new>> extendedStatusReportRes()

Delivery of a report, that is containing one or several user's status.

Parameters

assignmentId : in TpAssignmentID

Specifies the assignment ID of the status-report request.

status : in TpUserStatusExtendedSet

Specifies the status of one or several users.

#### 8.3.1.6	Method <<new>> extendedStatusReportErr()

This method indicates that the status report request has failed.

Parameters

assignmentId : in TpAssignmentID

Specifies the assignment ID of the failed status report request.

cause : in TpMobilityError

Specifies the error that led to the failure.

diagnostic : in TpMobilityDiagnostic

Specifies additional information about the error that led to the failure.

#### 8.3.1.7	Method <<new>> extTriggeredStatusReport()

Delivery of a report that is indicating that a user's status has changed.

Parameters

assignmentId : in TpAssignmentID

Specifies the assignment ID of the triggered status-reporting request.

status : in TpUserStatusExtended

Specifies the status of the user.

#### 8.3.1.8	Method <<new>> extTriggeredStatusReportErr()

This method indicates that a requested triggered status reporting has failed. Note that errors only concerning individual users are reported in the ordinary extTriggeredStatusReport() message.

Parameters

assignmentId : in TpAssignmentID

Specifies the assignment ID of the failed triggered status reporting start request.

cause : in TpMobilityError

Specifies the error that led to the failure.

diagnostic : in TpMobilityDiagnostic

Specifies additional information about the error that led to the failure.

#### 8.3.1.9	Method <<new>> triggeredReportingEnded()

The user status or user location triggering has stopped because the max life time allowed for this triggering has exceeded.

Parameters

assignmentId : in TpAssignmentID

Specifies the assignment ID of the triggered request.

### 8.3.2	Interface Class IpUserStatus

Inherits from: IpService.

The application programmer can use this interface to obtain the status of fixed, mobile and IP-based telephony users.

This interface shall be implemented by a User Status SCF.

The statusReportReq() method, or both the triggeredStatusReportingStartReq() and trigggeredStatusReportingStop() methods shall be implemented as a minimum requirement.

<<Interface>> IpUserStatus

statusReportReq (appStatus : in IpAppUserStatusRef, users : in TpAddressSet) : TpAssignmentID triggeredStatusReportingStartReq (appStatus : in IpAppUserStatusRef, users : in TpAddressSet) : TpAssignmentID triggeredStatusReportingStop (stopRequest : in TpMobilityStopAssignmentData) : void <<new>> getNextTriggeredStatusRequest (reset : in TpBoolean) : TpTriggeredStatusRequestSetEntry <<new>> extendedStatusReportReq (appStatus : in IpAppUserStatusRef, users : in TpAddressSet) : TpAssignmentID <<new>> extTriggeredStatusReportingStartReq (appStatus : in IpAppUserStatusRef, users : in TpAddressSet) : TpAssignmentID <<new>> extTriggeredStatusReportingStop (stopRequest : in TpMobilityStopAssignmentData) : void

#### 8.3.2.1	Method statusReportReq()

Request for a report on the status of one or several users.

Returns: assignmentId.

Specifies the assignment ID of the status-report request.

Parameters

appStatus : in IpAppUserStatusRef

Specifies the application interface for callbacks from the User Status service.

users : in TpAddressSet

Specifies the user(s) for which the status shall be reported.

Returns

TpAssignmentID

Raises

TpCommonExceptions, P_UNKNOWN_SUBSCRIBER, P_INFORMATION_NOT_AVAILABLE, P_APPLICATION_NOT_ACTIVATED, P_INVALID_INTERFACE_TYPE

#### 8.3.2.2	Method triggeredStatusReportingStartReq()

Request for triggered status reports when one or several user's status is changed. The user status service will send a report when the status changes.

Returns: assignmentId.

Specifies the assignment ID of the triggered status-reporting request.

Parameters

appStatus : in IpAppUserStatusRef

Specifies the application interface for callbacks from the User Status service.

users : in TpAddressSet

Specifies the user(s) for which the status changes shall be reported.

Returns

TpAssignmentID

Raises

TpCommonExceptions, P_UNKNOWN_SUBSCRIBER, P_INFORMATION_NOT_AVAILABLE, P_APPLICATION_NOT_ACTIVATED, P_INVALID_INTERFACE_TYPE

#### 8.3.2.3	Method triggeredStatusReportingStop()

This method stops the sending of status reports for one or several users.

Parameters

stopRequest : in TpMobilityStopAssignmentData

Specifies how the assignment shall be stopped, i.e. if whole or just parts of the assignment should be stopped.

Raises

TpCommonExceptions, P_INVALID_ASSIGNMENT_ID

#### 8.3.2.4	Method <<new>> getNextTriggeredStatusRequest()

This method is used by the application to query the request set created with triggeredStatusReportingStartReq. Since a lot of data can potentially be returned (which might cause problem in the middleware), this method must be used in an iterative way. Each method invocation  may return part of the total set of requests if the set is too large to return it at once. The reset parameter permits the application to indicate whether an invocation to getNextTriggeredStatusRequest  is requesting more requests from the total set of requests or is requesting that the total set of requests shall be returned from the beginning.

Returns the set of requests and an indication whether all off the requests have been obtained or if more requests are available that have not yet been obtained by  the application.

Note that the (maximum) number of items provided to the application is determined by the gateway.

Parameters

reset : in TpBoolean

TRUE: indicates that the application is intended to obtain the set of requests starting at the beginning.

FALSE: indicates that the application requests the next set of requests that have not (yet) been obtained since the last call to this method with this parameter set to TRUE.

The first time this method is invoked, reset shall be set to TRUE. Following the receipt of a final indication, for the next call to this method reset shall be set to TRUE. P_TASK_REFUSED may be thrown if these conditions are not met.

Returns

TpTriggeredStatusRequestSetEntry

Raises

TpCommonExceptions

#### 8.3.2.5	Method <<new>> extendedStatusReportReq()

Request for a report on the status of one or several users.

A user can be identified by the following address types:

- MSISDN     indicated with address plan P_ADDRESS_PLAN_E164.

- IP Address  indicated with address plan P_ADDRESS_PLAN_IP.

- User Name indicated with address plan P_ADDRESS_PLAN_UNDEFINED.

Returns: assignmentID.

Parameters

appStatus : in IpAppUserStatusRef

Specifies the application interface for callbacks from the  User Status service.

users : in TpAddressSet

Specifies the user(s) for which the status shall be reported.

Returns

TpAssignmentID

Raises

TpCommonExceptions, P_UNKNOWN_SUBSCRIBER, P_INFORMATION_NOT_AVAILABLE, P_APPLICATION_NOT_ACTIVATED, P_INVALID_INTERFACE_TYPE

#### 8.3.2.6	Method <<new>> extTriggeredStatusReportingStartReq()

Request for triggered status reports when one or several user's status is changed. The user status service will send a report when the status changes.

Returns: assignmentId.

Specifies the assignment ID of the triggered status-reporting request.

Parameters

appStatus : in IpAppUserStatusRef

Specifies the application interface for callbacks from the User Status service.

users : in TpAddressSet

Specifies the user(s) for which the status changes shall be reported.

Returns

TpAssignmentID

Raises

TpCommonExceptions, P_UNKNOWN_SUBSCRIBER, P_INFORMATION_NOT_AVAILABLE, P_APPLICATION_NOT_ACTIVATED, P_INVALID_INTERFACE_TYPE

#### 8.3.2.7	Method <<new>> extTriggeredStatusReportingStop()

This method stops the sending of status reports for one or several users.

Parameters

stopRequest : in TpMobilityStopAssignmentData

Specifies how the assignment shall be stopped, i.e. if whole or just parts of the assignment should be stopped.

Raises

TpCommonExceptions, P_INVALID_ASSIGNMENT_ID

# 9	State Transition Diagrams

## 9.1	User Location

There are no State Transition Diagrams for User Location.

## 9.2	User Location Camel

### 9.2.1	State Transition Diagrams for IpUserLocationCamel

During the signServiceAgreement a new  user location interface reference is created, which is user as the initial point of contact for the application.

Figure : State Transition Diagram for User Location Camel

#### 9.2.1.1	Active State

In this state, a relation between the Application and the Network User Location Service Capability Feature has been established. It allows the application to request a specific user location reports, subscribe to periodic user location reports or subscribe to triggers that generate location report when a location update occurs inside the current VLR area or when the user moves to another VLR area or both.

## 9.3	User Status

### 9.3.1	State Transition Diagrams for IpUserStatus

Figure : State Transition Diagram for User Status

#### 9.3.1.1	Active State

In this state, a relation between the Application and the User Status Service Capability Feature has been established. It allows the application to request a specific user status report or subscribe to triggers that generate status reports when the status of one of the monitored user changes.

# 10	Service Properties

## 10.1	Mobility Properties

### 10.1.1	Emergency Application Subtypes

Emergency (see definition of ‘LCS Client Type’ in 3GPP TS 23.271) Application Subtypes;

This property contains a list of application subtypes that are permitted to use the service. The possible subtypes are (see definition of ‘LCS Client Internal ID’ in 3GPP TS 23.271):

- “Broadcast service”
- “O&M HPLMN service”
- “O&M VPLMN service”
- “Anonymous location”
- “Target MS subscribed service”

### 10.1.2	Value Added Application Subtypes

Value Added (see definition of ‘LCS Client Type’ in 3GPP TS 23.271) Application Subtypes.

This property contains a list of application subtypes that are permitted to use the service. The possible subtypes are (see definition of ‘LCS Client Internal ID’ in 3GPP TS 23.271):

- “Broadcast service”
- “O&M HPLMN service”
- “O&M VPLMN service”
- “Anonymous location”
- “Target MS subscribed service”

### 10.1.3	PLMN Operator Application Subtypes

PLMN Operator (see definition of ‘LCS Client Type’ in 3GPP TS 23.271.) Application Subtypes.

This property contains a list of application subtypes that are permitted to use the service. The possible subtypes are (see definition of ‘LCS Client Internal ID’ in 3GPP TS 23.271):

- “Broadcast service”
- “O&M HPLMN service”
- “O&M VPLMN service”
- “Anonymous location”
- “Target MS subscribed service”

### 10.1.4	Lawful Intercept Application Subtypes

Lawful Intercept (See definition of ‘LCS Client Type’ in 3GPP TS 23.271.) Application Subtypes.

This property contains a list of application subtypes that are permitted to use the service. The possible subtypes are (see definition of ‘LCS Client Internal ID’ in 3GPP TS 23.271):

- “Broadcast service”
- “O&M HPLMN service”
- “O&M VPLMN service”
- “Anonymous location”
- “Target MS subscribed service”

### 10.1.5	Altitude Obtainable

Indicates whether it is possible to obtain a user’s altitude.

### 10.1.6	Location Methods

List of supported location methods. Possible values (other values are permitted):

- “Time of Arrival”

- “Timing Advance”

- “GPS”

- “User Data Lookup”

- “Any Time Interrogation”

### 10.1.7	Priorities

List of supported priorities for location requests. Possible values (no other values are permitted):

- “Normal”

- “High”

### 10.1.8	Max Interactive Requests

The maximum number of parallel outstanding location or status requests allowed per application. It shall be possible to convert the value to a 32-bit integer.

### 10.1.9	Max Triggered Users

The maximum number of users allowed per application for which triggered location reporting can be requested. It shall be possible to convert the value to a 32-bit integer.

### 10.1.10	Max Periodic Users

The maximum number of users allowed per application for which periodic location reporting can be requested. It shall be possible to convert the value to a 32-bit integer.

### 10.1.11	Min Periodic Interval Duration

The minimal time in seconds allowed between two periodic reports. It shall be possible to convert the value to a 32-bit integer.  Note however that the reportingInterval parameter, which is used in methods pertaining to periodic location reporting, is of common data type TpDuration, i.e. a signed 32-bit integer representing a time interval in milliseconds.

### 10.1.12	Initial Report

Indicates whether a triggered service should generate an initial triggered report immediately after a triggered start request.

- Triggered Status – If this property is set to “True”, the initial status of the end user is reported immediately after the triggeredStatusReportingStartReq.

- Triggered Location – If this property is set to “True”, the initial location of the end user is reported immediately after the triggeredLocationReportingStartReq, if the trigger criteria is met i.e. if the end user is within the location area and the Criterion is P_UL_ENTERING_AREA or the end user is outside the location area and the Criterion is P_UL_LEAVING_AREA.

### 10.1.13	Max Life Time

Specifies the maximum life time in milliseconds of a triggered or periodic reporting. It is of common data type TpDuration, i.e. a signed 32-bit integer representing a time interval in milliseconds. A value of zero means infinite life time.

- The periodic or triggered reporting will stop when a stop method associated with the triggering is received by the SCS or when the life time has expired.

## 10.2	User Location Service Properties

A specific  User Location service shall set the following properties:

General Properties applicable to all SCFs (in Framework)

Permitted application types

Permitted application subtypes

Priorities (see definition of ‘LCSClientType’ in 3GPP TS 23.271.)

Altitude obtainable

Location methods

Max interactive requests

Max triggered users

Max periodic users

Min periodic interval duration

Initial Report

Max Life Time

EXAMPLE:	The example below describes the capabilities of two fictive User Location services:

| Property Name | Property Value Service 1 | Property Value Service 2 |
| --- | --- | --- |
| Service instance ID | 0x80923AD0 | 0xF0ED85CB |
| Service name | UserLocation | UserLocation |
| Service version | 2.1 | 2.1 |
| Service description | Basic User Location service | Advanced high-performance User Location service |
| Product name | Find It | Locate.com |
| Product version | 1.3 | 3.1 |
| Supported interfaces | “IpUserLocation” | “IpUserLocation” |
| Permitted application types | “Emergency service”, “Value added service” | “Emergency service”, “Value added service”, “Lawful intercept service” |
| Permitted application subtypes | ? | ? |
| Priorities | “Normal” | “Normal”, “High” |
| Altitude obtainable | False | True |
| Location methods | “Timing Advance” | “GPS”, “Time Of Arrival” |
| Max interactive requests | 2000 | 10000 |
| Max triggered users | 0 | 2000 |
| Max periodic users | 300 | 2000 |
| Min periodic interval duration | 600 | 30 |
| Initial Report | True | True |

## 10.3	User Location Camel Service Properties

A specific  User Location Camel service shall set the following properties:

General Properties applicable to all SCFs (in Framework)

Max interactive requests

Max triggered users

Max periodic users

Min periodic interval duration

Initial Report

Max Life Time

## 10.4	User Status Service Properties

A specific  User Location service shall set the following properties:

General Properties applicable to all SCFs (in Framework)

Max interactive requests

Max triggered users

Initial Report

Max Life Time

# 11	Data Definitions

All data types referenced but not defined in this clause are common data definitions which may be found in 3GPP TS 29.198-2.

## 11.1	Common Mobility Data Definitions

The following data definitions are used for several of the mobility services.

### 11.1.1	TpGeographicalPosition

Defines the Sequence of Data Elements that specify a geographical position.

The horizontal location is defined by an “ellipsoid point with uncertainty shape”. The reference system chosen for the coding of locations is the World Geodetic System 1984 (WGS 84).

TypeOfUncertaintyShape describes the type of the uncertainty shape and Longitude/Latitude defines the position of the uncertainty shape. The following table defines the meaning of the data elements that describe the uncertainty shape for each uncertainty shape type.

| Type of uncertainty shape | Uncertainty Outer Semi Major | Uncertainty Outer Semi Minor | Uncertainty Inner Semi Major | Uncertainty Inner Semi Minor | Angle Of Semi Major | Segment Start Angle | Segment End Angle |
| --- | --- | --- | --- | --- | --- | --- | --- |
| None | - | - | - | - | - | - | - |
| Circle | radius of circle | - | - | - | - | - | - |
| Circle Sector | radius of circle | - | - | - | - | start angle of circle segment | end angle of circle segment |
| Circle Arc Stripe | radius of outer circle | - | radius of inner circle | - | - | start angle of circle arc stripe | end angle of circle arc stripe |
| Ellipse | length of semi-major axis | length of semi-minor axis | - | - | rotation of ellipse measured clockwise from north | - | - |
| Ellipse Sector | length of semi-major axis | length of semi-minor axis | - | - | rotation of ellipse measured clockwise from north | start angle of ellipse segment | end angle of ellipse segment |
| Ellipse Arc Stripe | length of semi-major axis, outer ellipse | length of semi-minor axis, outer ellipse | length of semi-major axis, inner ellipse | length of semi-minor axis, inner ellipse | rotation of ellipse measured clockwise from north | start angle of ellipse arc stripe | end angle of ellipse arc stripe |

Figure 1 Description of an Ellipse Arc

TpGeographicalPosition:

| Sequence Element Name | Sequence Element Type |
| --- | --- |
| Longitude | TpFloat |
| Latitude | TpFloat |
| TypeOfUncertaintyShape | TpLocationUncertaintyShape |
| UncertaintyInnerSemiMajor | TpFloat |
| UncertaintyOuterSemiMajor | TpFloat |
| UncertaintyInnerSemiMinor | TpFloat |
| UncertaintyOuterSemiMinor | TpFloat |
| AngleOfSemiMajor | TpInt32 |
| SegmentStartAngle | TpInt32 |
| SegmentEndAngle | TpInt32 |

### 11.1.2	TpLocationPriority

Defines the priority of a location request.

| Name | Value | Description |
| --- | --- | --- |
| P_M_NORMAL | 0 | Normal |
| P_M_HIGH | 1 | High |

### 11.1.3	TpLocationRequest

Defines the Sequence of Data Elements that specify a location request.

| Sequence Element Name | Sequence Element Type | Description |
| --- | --- | --- |
| RequestedAccuracy | TpFloat | Requested accuracy in meters. |
| RequestedResponseTime | TpLocationResponseTime | Requested response time as a classified requirement or as an absolute timer. |
| AltitudeRequested | TpBoolean | Altitude request flag. |
| Type | TpLocationType | The kind of location that is requested. |
| Priority | TpLocationPriority | Priority of location request. |
| RequestedLocationMethod | TpString | The kind of location method that is requested. |

### 11.1.4	TpLocationResponseIndicator

Defines a response time requirement.

| Name | Value | Description |
| --- | --- | --- |
| P_M_NO_DELAY | 0 | No delay: return either initial or last known location of the user. |
| P_M_LOW_DELAY | 1 | Low delay: return the current location with minimum delay. The mobility service shall attempt to fulfil any accuracy requirement, but in doing so shall not add any additional delay. |
| P_M_DELAY_TOLERANT | 2 | Delay tolerant: obtain the current location with regard to fulfilling the accuracy requirement. |
| P_M_USE_TIMER_VALUE | 3 | Use timer value: obtain the current location with regard to fulfilling the response time requirement. |

### 11.1.5	TpLocationResponseTime

Defines the Sequence of Data Elements that specify the application’s requirements on the mobility service’s response time.

| Sequence Element Name | Sequence Element Type | Description |
| --- | --- | --- |
| ResponseTime | TpLocationResponseIndicator | Indicator for which kind of response time that is required, see TpLocationResponseIndicator. |
| TimerValue | TpInt32 | Optional timer used in combination when ResponseTime equals P_M_USE_TIMER_VALUE. Units are seconds. |

### 11.1.6	TpLocationType

Defines the type of location requested.

| Name | Value | Description |
| --- | --- | --- |
| P_M_CURRENT | 0 | Current location |
| P_M_CURRENT_OR_LAST_KNOWN | 1 | Current or last known location |
| P_M_INITIAL | 2 | Initial location for an emergency services call |

### 11.1.7	TpLocationUncertaintyShape

Defines the type of uncertainty shape.

| Name | Value | Description |
| --- | --- | --- |
| P_M_SHAPE_NONE | 0 | No uncertainty shape present. |
| P_M_SHAPE_CIRCLE | 1 | Uncertainty shape is a circle. |
| P_M_SHAPE_CIRCLE_SECTOR | 2 | Uncertainty shape is a circle sector. |
| P_M_SHAPE_CIRCLE_ARC_STRIPE | 3 | Uncertainty shape is a circle arc stripe. |
| P_M_SHAPE_ELLIPSE | 4 | Uncertainty shape is an ellipse. |
| P_M_SHAPE_ELLIPSE_SECTOR | 5 | Uncertainty shape is an ellipse sector. |
| P_M_SHAPE_ELLIPSE_ARC_STRIPE | 6 | Uncertainty shape is an ellipse arc stripe. |

### 11.1.8	TpMobilityDiagnostic

Defines a diagnostic value that is reported in addition to an error by one of the mobility services.

| Name | Value | Description |
| --- | --- | --- |
| P_M_NO_INFORMATION | 0 | No diagnostic information present. Valid for all type of errors. |
| P_M_APPL_NOT_IN_PRIV_EXCEPT_LST | 1 | Application not in privacy exception list. Valid for ‘Unauthorised Application’ error. |
| P_M_CALL_TO_USER_NOT_SETUP | 2 | Call to user not set-up. Valid for ‘Unauthorised Application’ error. |
| P_M_PRIVACY_OVERRIDE_NOT_APPLIC | 3 | Privacy override not applicable. Valid for ‘Unauthorised Application’ error. |
| P_M_DISALL_BY_LOCAL_REGULAT_REQ | 4 | Disallowed by local regulatory requirements. Valid for ‘Unauthorised Application’ error. |
| P_M_CONGESTION | 5 | Congestion. Valid for ‘Position Method Failure’ error. |
| P_M_INSUFFICIENT_RESOURCES | 6 | Insufficient resources. Valid for ‘Position Method Failure’ error. |
| P_M_INSUFFICIENT_MEAS_DATA | 7 | Insufficient measurement data. Valid for ‘Position Method Failure’ error. |
| P_M_INCONSISTENT_MEAS_DATA | 8 | Inconsistent measurement data. Valid for ‘Position Method Failure’ error. |
| P_M_LOC_PROC_NOT_COMPLETED | 9 | Location procedure not completed. Valid for ‘Position Method Failure’ error. |
| P_M_LOC_PROC_NOT_SUPP_BY_USER | 10 | Location procedure not supported by user. Valid for ‘Position Method Failure’ error. |
| P_M_QOS_NOT_ATTAINABLE | 11 | Quality of service not attainable. Valid for ‘Position Method Failure’ error. |

### 11.1.9	TpMobilityError

Defines an error that is reported by one of the mobility services.

| Name | Value | Description | Fatal |
| --- | --- | --- | --- |
| P_M_OK | 0 | No error occurred while processing the request. | N/A |
| P_M_SYSTEM_FAILURE | 1 | System failure. The request cannot be handled because of a general problem in the mobility service or the underlying network. | Yes |
| P_M_UNAUTHORIZED_NETWORK | 2 | Unauthorised network. The requesting network is not authorised to obtain the user’s binding details, location or status. | No |
| P_M_UNAUTHORIZED_APPLICATION | 3 | Unauthorised application. The application is not authorised to obtain the user’s binding details, location or status. | Yes |
| P_M_UNKNOWN_SUBSCRIBER | 4 | Unknown subscriber. The user is unknown, i.e. no such subscription exists. | Yes |
| P_M_ABSENT_SUBSCRIBER | 5 | Absent subscriber. The user is currently not reachable. | No |
| P_M_POSITION_METHOD_FAILURE | 6 | Position method failure. The mobility service failed to obtain the user’s position. | No |

### 11.1.10	TpMobilityStopAssignmentData

Defines the Sequence of Data Elements that specify a request to stop whole or parts of an assignment. Assignments are used for periodic or triggered reporting of a user's location or status.

Note that the parameter ‘Users’ is optional. If the parameter ‘StopScope’ is set to P_M_ALL_IN_ASSIGNMENT the parameter ‘Users’ is undefined. If the parameter 'StopScope' is set to P_M_SPECIFIED_USERS, then the assignment shall be stopped only for those users specified in the ‘Users’ list.

| Sequence Element Name | Sequence Element Type | Description |
| --- | --- | --- |
| AssignmentId | TpAssignmentID | Identity of the assignment that shall be stopped. |
| StopScope | TpMobilityStopScope | Specify if only a part of the assignment or if all the assignment shall be stopped. |
| Users | TpAddressSet | Optional parameter describing which users a stop request is addressing, when only a part of an assignment is to be stopped. |

### 11.1.11	TpMobilityStopScope

This enumeration is used in requests to stop mobility reports that are sent from a mobility service to an application.

| Name | Value | Description |
| --- | --- | --- |
| P_M_ALL_IN_ASSIGNMENT | 0 | The request concerns all users in an assignment. |
| P_M_SPECIFIED_USERS | 1 | The request concerns only the users that are explicitly specified in a list. |

### 11.1.12	TpTerminalType

Defines which kind of terminal is used.

| Name | Value | Description |
| --- | --- | --- |
| P_M_FIXED | 0 | Fixed terminal. |
| P_M_MOBILE | 1 | Mobile terminal. |
| P_M_IP | 2 | IP terminal. |

## 11.2	User Location Data Definitions

### 11.2.1	IpUserLocation

Defines the address of an IpUserLocation Interface.

### 11.2.2	IpUserLocationRef

Defines a Reference to type IpUserLocation.

### 11.2.3	IpAppUserLocation

Defines the address of an IpAppUserLocation Interface.

### 11.2.4	IpAppUserLocationRef

Defines a Reference to type IpAppUserLocation.

### 11.2.5	IpTriggeredUserLocation

Defines the address of an IpTriggeredUserLocation Interface.

### 11.2.6	IpTriggeredUserLocationRef

Defines a Reference to type IpTriggeredUserLocation.

### 11.2.7	IpAppTriggeredUserLocation

Defines the address of an IpAppTriggeredUserLocation Interface.

### 11.2.8	IpAppTriggeredUserLocationRef

Defines a Reference to type IpAppTriggeredUserLocation.

### 11.2.9	TpUlExtendedData

Defines the Sequence of Data Elements that specify a location (extended format).

The optional vertical location is defined by the data element Altitude, which contains the altitude in meters above sea level, and the data element AltitudeAccuracy, which contains the accuracy of the altitude.

| Sequence Element Name | Sequence Element Type | Description |
| --- | --- | --- |
| GeographicalPosition | TpGeographicalPosition | Specification of a position and an area of uncertainty. |
| TerminalType | TpTerminalType | Kind of terminal. |
| AltitudePresent | TpBoolean | Flag indicating if the altitude is present. |
| Altitude | TpFloat | Decimal altitude in meters. |
| UncertaintyAltitude | TpFloat | Uncertainty of the altitude. |
| TimestampPresent | TpBoolean | Flag indicating if the timestamp is present. |
| Timestamp | TpDateAndTime | Timestamp indicating when the position was measured. |
| UsedLocationMethod | TpString | Specifying which location method was used. |

### 11.2.10	TpUlExtendedDataSet

Defines a Numbered Set of Data Elements of TpUlExtendedData.

### 11.2.11	TpUserLocationExtended

Defines the Sequence of Data Elements that specify the identity and location(s) of a user (extended format). In general the data element Locations will contain only one location, but in case of IP-telephony users this data element might continue several locations (the locations of all communication end-points, where the user is currently registered).

| Sequence Element Name | Sequence Element Type | Description |
| --- | --- | --- |
| UserID | TpAddress | The address of the user. |
| StatusCode | TpMobilityError | Indicator of error. |
| Locations | TpUlExtendedDataSet | Optional list of locations. If StatusCode is indicating an error, this value is undefined. |

### 11.2.12	TpUserLocationExtendedSet

Defines a Numbered Set of Data Elements of TpUserLocationExtended.

### 11.2.13	TpLocationTrigger

Defines the Sequence of Data Elements that specify the criteria for a triggered location report to be generated. The area is defined by an ellipse.

| Sequence Element Name | Sequence Element Type | Description |
| --- | --- | --- |
| Longitude | TpFloat | Longitude of the position used in the trigger. |
| Latitude | TpFloat | Latitude of the position used in the trigger. |
| AreaSemiMajor | TpFloat | Semi major of ellipse area used in the trigger. |
| AreaSemiMinor | TpFloat | Semi minor of ellipse area used in the trigger. |
| AngleOfSemiMajor | TpInt32 | Angle of the semi major of the ellipse area used in the trigger. |
| Criterion | TpLocationTriggerCriteria | Trigger criteria with regard to the ellipse area. |
| ReportingInterval | TpDuration | Duration between generated location reports. Notes: Units are milliseconds. Denotes the minimum time between invocations of the IpAppTriggeredUserLocation. triggeredLocationReport method, for this specific location ellipse area and trigger criterion. |

### 11.2.14	TpLocationTriggerSet

Defines a Numbered Set of Data Elements of TpLocationTrigger.

### 11.2.15	TpLocationTriggerCriteria

Defines the criteria that trigger a location report.

| Name | Value | Description |
| --- | --- | --- |
| P_UL_ENTERING_AREA | 0 | User enters the area |
| P_UL_LEAVING_AREA | 1 | User leaves the area |

### 11.2.16	TpUserLocation

Defines the Sequence of Data Elements that specify the identity and location of a user (basic format).

| Sequence Element Name | Sequence Element Type | Description |
| --- | --- | --- |
| UserID | TpAddress | The address of the user. |
| StatusCode | TpMobilityError | Indicator of error. |
| GeographicalPosition | TpGeographicalPosition | Specification of a position and an area of uncertainty. If StatusCode is indicating an error, this value is undefined. |

### 11.2.17	TpUserLocationSet

Defines a Numbered Set of Data Elements of TpUserLocation.

### 11.2.18	TpTriggeredLocationRequestSetEntry

Defines the Sequence of Data Elements that specify a set of triggered requests and an indication whether more triggered location requests can be requested.

| Sequence Element Name | Sequence Element Type | Description |
| --- | --- | --- |
| Requests | TpTriggeredLocationRequestSet | Numbered set of requests. |
| Final | TpBoolean | Indication whether the set of triggered requests is the final set (TRUE) or if there are more triggered requests (FALSE). |

### 11.2.19	TpTriggeredLocationRequestSet

Defines a numbered Set of Data Elements of TpTriggeredLocationRequest.

### 11.2.20	TpTriggeredLocationRequest

Defines the Sequence of Data Elements that specify the criteria relating to triggered location requests.

| Sequence Element Name | Sequence Element Type |
| --- | --- |
| Users | TpAddressSet |
| Request | TpLocationRequest |
| AssignmentID | TpAssignmentID |

### 11.2.21	TpPeriodicLocationRequestSetEntry

Defines the Sequence of Data Elements that specify a set of triggered requests and an indication whether more periodic location requests can be requested.

| Sequence Element Name | Sequence Element Type | Description |
| --- | --- | --- |
| Requests | TpPeriodicLocationRequestSet | Numbered set of requests. |
| Final | TpBoolean | Indication whether the set of triggered requests is the final set (TRUE) or if there are more triggered requests (FALSE). |

### 11.2.22	TpPeriodicLocationRequestSet

Defines a numbered Set of Data Elements of TpPeriodicLocationRequest.

### 11.2.23	TpPeriodicLocationRequest

Defines the Sequence of Data Elements that specify the criteria relating to periodic location requests.

| Sequence Element Name | Sequence Element Type |
| --- | --- |
| Users | TpAddressSet |
| Request | TpLocationRequest |
| ReportingInterval | TpDuration |
| AssignmentID | TpAssignmentID |

## 11.3	User Location Camel Data Definitions

### 11.3.1	IpUserLocationCamel

Defines the address of an IpUserLocationCamel Interface.

### 11.3.2	IpUserLocationCamelRef

Defines a Reference to type IpUserLocationCamel.

### 11.3.3	IpAppUserLocationCamel

Defines the address of an IpAppUserLocationCamel Interface.

### 11.3.4	IpAppUserLocationCamelRef

Defines a Reference to type IpAppUserLocationCamel.

### 11.3.5	TpLocationCellIDOrLAI

This data type is identical to a TpString. It specifies the Cell Global Identification or the Location Area Identification (LAI).

The Cell Global Identification (CGI) is defined as a string of characters in the following format:

MCC-MNC-LAC-CI

where:

MCC	Mobile Country Code (three decimal digits)

MNC	Mobile Network Code (two or three decimal digits)

LAC	Location Area Code (four hexadecimal digits)

CI	Cell Identification (four hexadecimal digits)

The Location Area Identification (LAI) is defined as a string of characters in the following format:

MCC-MNC-LAC

where:

MCC	Mobile Country Code (three decimal digits)

MNC	Mobile Network Code (two or three decimal digits)

LAC	Location Area Code (four hexadecimal digits)

The length of the parameter indicates, which format is used. See 3GPP TS 29.002 [4] for the detailed coding.

### 11.3.6	TpLocationTriggerCamel

Defines the Sequence of Data Elements that specify the criteria for a triggered location report to be generated.

| Sequence Element Name | Sequence Element Type | Description |
| --- | --- | --- |
| UpdateInsideVlr | TpBoolean | Generate location report, when a location update occurs inside the current VLR area. |
| UpdateOutsideVlr | TpBoolean | Generate location report, when the user moves to another VLR area. |

### 11.3.7	TpUserLocationCamel

Defines the Sequence of Data Elements that specify the location of a mobile telephony user. Note that if the StatusCode is indicating an error , then neither GeographicalPosition, Timestamp, VlrNumber, LocationNumber, CellIdOrLai nor their associated presence flags are defined.

| Sequence Element Name | Sequence Element Type | Description |
| --- | --- | --- |
| UserID | TpAddress | The address of the user. |
| StatusCode | TpMobilityError | Indicator of error. |
| GeographicalPositionPresent | TpBoolean | Flag indicating if the geographical position is present. |
| GeographicalPosition | TpGeographicalPosition | Specification of a position and an area of uncertainty. |
| TimestampPresent | TpBoolean | Flag indicating if the timestamp is present. |
| Timestamp | TpDateAndTime | Timestamp indicating when the request was processed. |
| VlrNumberPresent | TpBoolean | Flag indicating if the VLR number is present. |
| VlrNumber | TpAddress | Current VLR number for the user. |
| LocationNumberPresent | TpBoolean | Flag indicating if the location number is present. |
| LocationNumber (see Note) | TpAddress | Current location number. |
| CellIdOrLaiPresent | TpBoolean | Flag indicating if cell-id or LAI of the user is present. |
| CellIdOrLai | TpLocationCellIDOrLAI | Cell-id or LAI of the user. |
| NOTE: The location number is the number to the MSC or in rare cases the roaming number. |

### 11.3.8	TpUserLocationCamelSet

Defines a Numbered Set of Data Elements of TpUserLocationCamel.

## 11.4	User Location Emergency Data Definitions

### 11.4.1	IpUserLocationEmergency

Defines the address of an IpUserLocationEmergency Interface.

### 11.4.2	IpUserLocationEmergencyRef

Defines a Reference to type IpUserLocationEmergency.

### 11.4.3	IpAppUserLocationEmergency

Defines the address of an IpAppUserLocationEmergency Interface.

### 11.4.4	IpAppUserLocationEmergencyRef

Defines a Reference to type IpAppUserLocationEmergency.

### 11.4.5	TpIMEI

This data type is identical to a TpString. It specifies the International Mobile Equipment Identity (IMEI).

### 11.4.6	TpNaESRD

This data type is identical to a TpString. It specifies the North American Emergency Services Routing Digits (NA-ESRD). 
NA-ESRD is a telephone number in the North American Numbering Plan that can be used to identify a North American emergency services provider and its associated Location Services client. The NA-ESRD also identifies the base station, cell site or sector from which a North American emergency call originates.

### 11.4.7	TpNaESRK

This data type is identical to a TpString. It specifies the North American Emergency Services Routing Key (NA-ESRK). 
NA-ESRK is a telephone number in the North American Numbering Plan that is assigned to an emergency services call for the duration of the call. The NA-ESRK is used to identify (e.g. route to) both, the emergency services provider and the switch, currently serving the emergency caller. During the lifetime of an emergency services call, the NA-ESRK also identifies the calling subscriber.

### 11.4.8	TpUserLocationEmergencyRequest

Defines the Sequence of Data Elements that specify the request for the location of an emergency service user. The emergency service user is identified by a combination of user address, NaESRD, NaESRK and IMEI. NaESRD, NaESRK and IMEI may be provided, if the emergency service user has originated the emergency service call in North America.

| Sequence Element Name | Sequence Element Type | Description |
| --- | --- | --- |
| UserAddressPresent | TpBoolean | Flag indicating if the user address is present. |
| UserAddress | TpAddress | The address of the user. |
| NaEsrdPresent | TpBoolean | Flag indicating if the NaESRD is present. |
| NaEsrd | TpNaESRD | Current NaESRD for the user. |
| NaEsrkPresent | TpBoolean | Flag indicating if the NaESRK is present. |
| NaEsrk | TpNaESRK | Current NaESRK for the user. |
| ImeiPresent | TpBoolean | Flag indicating if the IMEI is present. |
| Imei | TpIMEI | IMEI for the user. |
| LocationReq | TpLocationRequest | The actual location request. |

### 11.4.9	TpUserLocationEmergency

Defines the Sequence of Data Elements that specify the identity and location of an emergency service user.
The emergency service user is identified by a combination of UserID, NaESRD, NaESRK and IMEI.
NaESRD, NaESRK and IMEI may be provided, if the emergency service user has originated the emergency service call in North America.
The horizontal location is defined by an “ellipsoid point with uncertainty ellipse” (see TpUlExtendedData).

| Sequence Element Name | Sequence Element Type | Description |
| --- | --- | --- |
| StatusCode | TpMobilityError | Indicator of error. |
| UserIdPresent | TpBoolean | Flag indicating if the user address is present. |
| UserId | TpAddress | The user address. |
| NaEsrdPresent | TpBoolean | Flag indicating if the NaESRD is present. |
| NaEsrd | TpNaESRD | Current NaESRD for the user. |
| NaEsrkPresent | TpBoolean | Flag indicating if the NaESRK is present. |
| NaEsrk | TpNaESRK | Current NaESRK for the user. |
| ImeiPresent | TpBoolean | Flag indicating if the IMEI is present. |
| Imei | TpIMEI | IMEI for the user. |
| TriggeringEvent | TpUserLocationEmergencyTrigger | The reason for this location report. |
| GeographicalPositionPresent | TpBoolean | Flag indicating if the geographical position is present. |
| GeographicalPosition | TpGeographicalPosition | Specification of a position and an area of uncertainty. |
| AltitudePresent | TpBoolean | Flag indicating if the altitude is present. |
| Altitude | TpFloat | Decimal altitude in meters. |
| UncertaintyAltitude | TpFloat | Uncertainty of the altitude. |
| TimestampPresent | TpBoolean | Flag indicating if a timestamp is present. |
| Timestamp | TpDateAndTime | Timestamp indicating when the request was processed. |
| UsedLocationMethod | TpString | Specifying which location method was used. |

### 11.4.10	TpUserLocationEmergencyTrigger

Defines which event triggered the emergency User Location report.

| Name | Value | Description |
| --- | --- | --- |
| P_ULE_CALL_ORIGINATION | 0 | An emergency service user originated an emergency call. |
| P_ULE_CALL_RELEASE | 1 | An emergency service user released an emergency call. |
| P_ULE_LOCATION_REQUEST | 2 | The report is a response to an emergency location report request. |

## 11.5	User Status Data Definitions

### 11.5.1	IpUserStatus

Defines the address of an IpUserStatus Interface.

### 11.5.2	IpUserStatusRef

Defines a Reference to type IpUserStatus.

### 11.5.3	IpAppUserStatus

Defines the address of an IpAppUserStatus Interface.

### 11.5.4	IpAppUserStatusRef

Defines a Reference to type IpAppUserStatus.

### 11.5.5	TpUserStatus

Defines the Sequence of Data Elements that specify the identity and status of a user.

| Sequence Element Name | Sequence Element Type | Description |
| --- | --- | --- |
| UserID | TpAddress | The user address. |
| StatusCode | TpMobilityError | Indicator of error. |
| Status | TpUserStatusIndicator | The current status of the user. |
| TerminalType | TpTerminalType | The kind of terminal used by the user. |

### 11.5.6	TpUserStatusSet

Defines a Numbered Set of Data Elements of TpUserStatus.

### 11.5.7	TpUserStatusIndicator

Defines the status of a user.

| Name | Value | Description |
| --- | --- | --- |
| P_US_REACHABLE | 0 | User is reachable |
| P_US_NOT_REACHABLE | 1 | User is not reachable |
| P_US_BUSY (see Note) | 2 | User is busy (only applicable for interactive user status request, not when triggers are used) |
| NOTE: Only applicable to mobile (Camel) telephony users. |

### 11.5.8	TpTriggeredStatusRequestSetEntry

Defines the Sequence of Data Elements that specify a set of triggered requests and an indication whether more triggered status requests can be requested.

| Sequence Element Name | Sequence Element Type | Description |
| --- | --- | --- |
| Requests | TpTriggeredStatusRequestSet | Numbered set of requests. |
| Final | TpBoolean | Indication whether the set of triggered requests is the final set (TRUE) or if there are more triggered requests (FALSE). |

### 11.5.9	TpTriggeredStatusRequestSet

Defines a numbered Set of Data Elements of TpTriggeredStatusRequest.

### 11.5.10	TpTriggeredStatusRequest

Defines the Sequence of Data Elements that specify the criteria relating to triggered status requests.

| Sequence Element Name | Sequence Element Type |
| --- | --- |
| Users | TpAddressSet |
| AssignmentID | TpAssignmentID |

### 11.5.11	TpUserStatusExtended

Defines the Sequence of Data Elements that specify the identity and status of a user.

| Sequence Element Name | Sequence Element Type | Description |
| --- | --- | --- |
| UserID | TpAddress | The user address. |
| StatusCode | TpMobilityError | Indicator of error. |
| Status | TpUserStatusIndicatorExtended | The current status of the user. |
| TerminalType | TpTerminalType | The kind of terminal used by the user. |
| AuthenticationStatus | TpAuthStatusIndicator | The current authentication status of the user |
| NetworkStatus | TpNetworkStatusIndicator | Country code, Mobile network code, technology and Roaming status. |
| UserIPAddress | TpString | The allocated IP address for the user. If there is no IPAddress allocated then this is represented with the empty string. |
| UserMSISDN | TpString | The user MSISDN. If the MSISDN address is not known, then this is represented with the empty string. |
| UserInfo | TpUserInfo | Used to reference the user name and password supplied by the user during user-network authentication, if known by the network. |
| UserConnectionID | TpString | Combination of User IP Address and TCP port. This combination uniquely identifies the user’s TCP connection, because one user can have several TCP connections ongoing at the same time. The User IP Address contained in UserConnectionID can be the same as the userIPAddress, but this is not always the case since a router in the data network might have translated the UserIPAddress to another IP-address. The latter is then contained in UserConnectionID. |
| AccessPointName | TpString | Provides the Access Point Name of the Internet Service Provider |

### 11.5.12	TpUserStatusExtendedSet

Defines a Numbered Set of Data Elements of TpUserStatusExtended.

### 11.5.13	TpUserStatusIndicatorExtended

Defines the status of a user.

| Sequence Element Name | Sequence Element Type | Description |
| --- | --- | --- |
| UserStatusIndicator | TpUserStatusIndicator | Indication whether the user is busy, reachable or not reachable |
| PDPContextActive | TpBoolean | Indication whether the user currently has an ongoing data session (i.e. PDP context established) |

### 11.5.14	TpAuthStatusIndicator

Used to indicate if and how the user has been authenticated during data session establishment

| Name | Value | Description |
| --- | --- | --- |
| P_AUTHENTICATED_FOR_NETWORK_ONLY | 0 | Authenticated only for the network |
| P_AUTHENTICATED_FOR_NETWORK_AND_IP_SERVICES | 1 | Authenticated for the network and IP services |
| P_NOT_AUTHENTICATED | 2 | Not authenticated |

### 11.5.15	TpUserInfo

Used to reference the user name and password supplied by the user, if known by the network.

| Name | Structure Element Type | Description |
| --- | --- | --- |
| UserName | TpString | User name as provided in a PPP/CHAP message. |
| Password | TpString | Password as provided in a PPP/CHAP message. |

### 11.5.16	TpNetworkStatusIndicator

Specifies the country code, mobile network code, access network technology used by the user for the data session and roaming status.

| Name | Structure Element Type | Description |
| --- | --- | --- |
| CountryCode | TpString | Network CC Identification, Country code |
| MobileNetworkCode | TpString | Network MNC Identification, Mobile network code |
| AccessTechnology | TpAccessTechnology | Network access technology used by the user to connect |
| RoamingStatus | TpRoamingStatus | Roaming Status |

### 11.5.17	TpAccessTechnology

Defines the derived access technology utilised by the user.

| Name | Value | Description |
| --- | --- | --- |
| P_MOBILE_ACCESS_PS | 0 | Access via packet switched connection in mobile network |
| P_MOBILE_ACCESS_CS | 1 | Access via a circuit switched connection in mobile network |
| P_FIXED_ACCESS | 2 | Access via a fixed network |

### 11.5.18	TpRoamingStatus

Defines the roaming status of the user.

| Name | Value | Description |
| --- | --- | --- |
| P_UNKNOWN_ROAMING_STATUS | 0 | No information on Roaming status has been found |
| P_HOME_USER | 1 | User is in the home network |
| P_NATIONAL_ROAMING | 2 | User has roamed to another operator in the same country |
| P_INTERNATIONAL_ROAMING | 3 | User has roamed to another operator abroad |
| P_OPERATOR_ROAMING | 4 | User has roamed to a partner operator abroad |

## 11.6	User Binding Data Definitions

### 11.6.1	TpBindingSet

Defines a Numbered Set of Data Elements of TpBindingEntrySet.

### 11.6.2	TpBindingEntrySet

Defines a Numbered Set of Data Elements of TpBindingEntry.

### 11.6.3	TpBindingEntry

Defines the Tagged Choice of Data Elements that specifies binding information.

|  | Tag Element Type |  |
| --- | --- | --- |
|  | TpBindingEntryType |  |

| Tag Element Value | Choice Element Type | Choice Element Name | Description |
| --- | --- | --- | --- |
| P_UB_EXPIRES | TpInt32 | UBExpires | This field can be used to enforce time limits on session duration and is defined as an integral number of seconds. |
| P_UB_CONTACT_ADDRESS | TpAddress | UBContactAddress | This field informs the network of the subscriber's desired binding address. |
| P_UB_PREFERENCE | TpFloat | UBPreference | This field conveys a relative order among subscriber bindings. |

### 11.6.4	TpBindingEntryType

Defines the type of binding information.

| Name | Value | Description |
| --- | --- | --- |
| P_UB_UNDEFINED | 0 | Undefined |
| P_UB_EXPIRES | 1 | A number indicating the number of seconds the binding is valid |
| P_UB_CONTACT_ADDRESS | 2 | The address representing the user's contact address |
| P_UB_PREFERENCE | 3 | A number between 0 and 1 indicating the contact address' relative preference |

### 11.6.5	TpBindingNotificationCriteriaSet

Defines a Numbered Set of Data Elements of TpBindingNotificationCriteria.

### 11.6.6	TpBindingNotificationCriteria

Defines the Sequence of Data Elements that specifies the criteria relating to binding report requests.

| Sequence Element Name | Sequence Element Type |
| --- | --- |
| NotificationCriteriaType | TpBindingNotificationCriteriaType |
| ContactAddressSet | TpAddressSet |

### 11.6.7	TpBindingNotificationCriteriaType

Defines the binding operations to be reported. The values may be combined by a logical 'OR' function.

| Name | Value | Description |
| --- | --- | --- |
| P_UB_NEW | 1 | Indicates attempt to create a new binding |
| P_UB_REMOVE | 2 | Indicates removal of an existing binding |
| P_UB_UPDATE | 4 | Indicates attempt to update an existing binding |

## 11.7	Units and Validations of Parameters

This clause describes the units that shall be used for data elements, where this is not obvious.

Altitude

Unit: Metric meter

Angle

Unit: Degrees

Value constraint: 0 ( 'Angle' ( 360

AreaSemiMajor and AreaSemiMinor

Unit: Metric meter

Value constraint: 0 ( 'AreaSemi…'

ReportingInterval

Unit: Milliseconds

Value constraint: 0 < 'ReportingInterval'

UncertaintyAltitude

Unit: Metric meter

Value constraint: 0 ( 'UncertaintyAltitude'

Semantic: (Altitude – UncertaintyAltitude) ( 'Terminal actual altitude' ( ('Altitude' + 'UncertaintyAltitude')

UncertaintyInnerSemiMajor and UncertaintyInnerSemiMinor

Unit: Metric meter

Value constraint: 0 ( 'UncertaintyInner…'

UncertaintyOuterSemiMajor and UncertaintyOuterSemiMinor

Unit: Metric meter

Value constraint: 0 ( 'UncertaintyInner…'

UsedLocationMethod

Predefined strings are listed in clause Location Methods.

# 12	Exception Classes

The following are the list of exception classes which are used in this interface of the API.

| Name | Description |
| --- | --- |
| P_INVALID_REPORTING_INTERVAL | The requested reporting interval is not valid |
| P_REQUESTED_ACCURACY_CANNOT_BE_DELIVERED | The requested location accuracy cannot be delivered |
| P_REQUESTED_RESPONSE_TIME_CANNOT_BE_DELIVERED | The requested response time cannot be delivered |
| P_TRIGGER_CONDITIONS_NOT_SUBSCRIBED | Trigger conditions not subscribed |

Each exception class contains the following structure:

| Structure Element Name | Structure Element Type | Structure Element Description |
| --- | --- | --- |
| ExtraInformation | TpString | Carries extra information to help identify the source of the exception, e.g. a parameter name |

Annex A (normative):
OMG IDL Description of Mobility SCF

The OMG IDL representation of this interface specification is contained in a text file (mm.idl contained in archive 2919806V660IDL.ZIP) which accompanies the present document.

Annex B (informative):
W3C WSDL Description of Mobility SCF

The W3C WSDL representation of this interface specification is contained in zip file 2919806V660WSDL.ZIP, which accompanies the present document.

Annex C (informative):
Java API Description of the Mobility SCFs

The Java API realisation of this interface specification is produced in accordance with the Java Realisation rules defined in Part 1 of this specification. These rules aim to deliver for Java, a developer API, provided as a realisation, supporting a Java API that represents the UML specifications. The rules support the production of both J2SE and J2EE versions of the API from the common UML specifications.

The J2SE representation of this interface specification is provided as Java Code, contained in archive 2919806V660J2SE.ZIP that accompanies the present document.

The J2EE representation of this interface specification is provided as Java Code, contained in archive 2919806V660J2EE.ZIP that accompanies the present document.

Annex D (informative):
Description of Mobility SCF for 3GPP2 cdma2000 networks

This annex is intended to define the OSA API Stage 3 interface definitions and it provides the complete OSA specifications. It is an extension of OSA API specifications capabilities to enable operation in cdma2000 systems environment. They are in alignment with 3GPP2 Stage 1 requirements and Stage 2 architecture defined in

[1]	3GPP2 P.S0001-B: "Wireless IP Network Standard", Version 1.0, September 2000;

[2]	3GPP2 S.R0037-0:  "IP Network Architecture Model for cdma2000 Spread Spectrum Systems", Version 2.0, May 14, 2002;

[3]	3GPP2 X.S0013: "All-IP Core Network Multimedia Domain", December 2003.

These requirements are expressed as additions to and/or exclusions from the 3GPP Release 6 specification. The information given here is to be used by developers in 3GPP2 cdma2000 network architecture to interpret the 3GPP OSA specifications.

# D.1	General Exceptions

The terms 3GPP and UMTS are not applicable for the cdma2000 family of standards. Nevertheless these terms are used (3GPP TR 21.905) mostly in the broader sense of "3G Wireless System". If not stated otherwise there are no additions or exclusions required.

CAMEL and CAP mappings are not applicable for cdma2000 systems.

# D.2	Specific Exceptions

## D.2.1	Clause 1: Scope

There are no additions or exclusions.

## D.2.2	Clause 2: References

Normative references on 3GPP TS 23.078 and on 3GPP TS 29.078 are not applicable for cdma2000 systems.

## D.2.3	Clause 3: Definitions and abbreviations

There are no additions or exclusions.

## D.2.4	Clause 4: Mobility SCF

There are no additions or exclusions. UL-User Location UMTS term may be mapped onto LCS-Location Services cdma2000 term. CAMEL is not applicable for cdma2000 systems.

## D.2.5	Clause 5: Sequence Diagrams

There are no additions. User Location Camel Sequence Diagrams are not applicable for cdma2000 systems.

## D.2.6	Clause 6 Class Diagrams

There are no additions. User Location Camel Class Diagrams are not applicable for cdma2000 systems.

## D.2.7	Clause 7: The Service Interface Specifications

There are no additions or exclusions.

## D.2.8	Clause 8: Mobility Interface Classes

There are no additions. User Location Camel Interface Classes are not applicable for cdma2000 systems

## D.2.9	Clause 9: State Transition Diagrams

Since CAMEL protocol is not applicable for cdma2000 systems, User Location Camel state transition diagrams are not applicable for cdma2000 systems.

## D.2.10	Clause 10: Service Properties

Since CAMEL protocol is not applicable for cdma2000 systems, an SCS shall indicate support for the CAMEL feature through service properties. For cdma2000 systems the service properties shall be disabled (CAMEL shall be turned always off in the case of the 3GPP2 networks; e.g.: UserLocationCamel shall be set to false).

## D.2.11	Clause 11: Data Definitions

There are no additions. UserLocationCamel data definitions are not applicable for cdma2000 systems.

## D.2.12	Clause 12: Exception Classes

There are no additions or exclusions.

## D.2.13	Annex A (normative): OMG IDL Description of Mobility SCF

There are no additions or exclusions.

## D.2.14	Annex B (informative): W3C WSDL Description of Mobility SCF

There are no additions or exclusions.

## D.2.15	Annex C (informative): Java™ API Description of Mobility SCF

There are no additions or exclusions.

Annex E (informative):
Change history

| Change history |
| --- |
| Date | TSG # | TSG Doc. | CR | Rev | Subject/Comment | Old | New |
| Mar 2001 | CN_11 | NP-010134 | 0047 | - | CR 29.198: for moving TS 29.198 from R99 to Rel 4 (N5-010158) | 3.2.0 | 4.0.0 |
| Jun 2001 | CN_12 | NP-010330 | 0001 | -- | Corrections to OSA API Rel4 | 4.0.0 | 4.1.0 |
| Jul 2001 | -- | -- | -- | -- | 29198-06-410.zip archive was packaged with the wrong accompanying IDL zip file, which should be mm.idl and not Call Control IDLs (04). | 4.1.0 | 4.1.1 |
| Sep 2001 | CN_13 | NP-010520 | 0002 | -- | Changing references to JAIN | 4.1.1 | 4.2.0 |
| Sep 2001 | CN_13 | NP-010520 | 0003 | -- | Introduction of missing mobility exceptions | 4.1.1 | 4.2.0 |
| Oct 2001 | -- | -- | -- | -- | Correction to ToC | 4.2.0 | 4.2.1 |
| Dec 2001 | CN_14 | NP-010599 | 0004 | -- | Replace Out Parameters with Return Types | 4.2.1 | 4.3.0 |
| Dec 2001 | CN_14 | NP-010599 | 0005 | -- | Methods accepting an interface as a parameter need to be able to raise P_INVALID_INTERFACE_TYPE | 4.2.1 | 4.3.0 |
| Dec 2001 | CN_14 | NP-010599 | 0006 | -- | Correction of references to 3GPP specifications | 4.2.1 | 4.3.0 |
| Dec 2001 | CN_14 | NP-010599 | 0007 | -- | Correction to callback interface reference in method IpTriggeredUserLocation.triggeredLocationReportingStartReq | 4.2.1 | 4.3.0 |
| Mar 2002 | CN_15 | NP-020108 | 0008 | -- | Add P_INVALID_INTERFACE_TYPE exception to IpService.setCallback() and IpService.setCallbackWithSessionID() | 4.3.0 | 4.4.0 |
| Jun 2002 | CN_16 | NP-020181 | 0009 | -- | Addition of support for Java API technology realisation | 4.4.0 | 5.0.0 |
| Jun 2002 | CN_16 | NP-020182 | 0010 | -- | Addition of support for WSDL realisation | 4.4.0 | 5.0.0 |
| Jun 2002 | CN_16 | NP-020190 | 0011 | -- | Delete the repetitive description of P_APPLICATION_NOT_ACTIVATED and other exceptions | 4.4.0 | 5.0.0 |
| Jun 2002 | CN_16 | NP-020190 | 0012 | -- | Correcting type of assignmentID parameters from TpSessionID to TpAssignmentID | 4.4.0 | 5.0.0 |
| Jun 2002 | CN_16 | NP-020190 | 0013 | -- | Correcting erroneous references to Service Factory | 4.4.0 | 5.0.0 |
| Sep 2002 | CN_17 | NP-020433 | 0014 | -- | Remove all parameter error and network error sequence diagrams | 5.0.0 | 5.1.0 |
| Sep 2002 | CN_17 | NP-020433 | 0015 | -- | Removal of unnecessary exception from IpUserLocation.LocationReportReq(), IpUserLocation.extendedLocationReportReq(), IpUserLocation.periodicLocationReportingStartReq() | 5.0.0 | 5.1.0 |
| Sep 2002 | CN_17 | NP-020433 | 0016 | -- | Remove unusable exceptions from IpUserLocationCamel.periodicLocationReportingStartReq() | 5.0.0 | 5.1.0 |
| Sep 2002 | CN_17 | NP-020433 | 0017 | -- | Add text to clarify requirements on support of methods | 5.0.0 | 5.1.0 |
| Sep 2002 | CN_17 | NP-020395 | 0018 | -- | Add text to clarify relationship between 3GPP and ETSI/Parlay OSA specifications | 5.0.0 | 5.1.0 |
| Mar 2003 | CN_19 | NP-030022 | 0020 |  | Addition of status of methods to Mobility interfaces | 5.1.0 | 5.2.0 |
| Jun 2003 | CN_20 | NP-030249 | 0021 | -- | Add methods to prevent unnecessary strict requirements on application persistency for Mobility | 5.2.0 | 6.0.0 |
| Jun 2003 | CN_20 | NP-030249 | 0022 | -- | Extension to User Status | 5.2.0 | 6.0.0 |
| Dec 2003 | CN_22 | NP-030553 | 0024 | -- | Add OSA API support for 3GPP2 networks | 6.0.0 | 6.1.0 |
| Jun 2004 | CN_24 | NP-040270 | 0026 | -- | Correct alignment between ETSI/Parlay OSA and the 3GPP OSA by adding user binding data types | 6.1.0 | 6.2.0 |
| Sep 2004 | CN_25 | NP-040354 | 0028 | -- | Correction to Java Realisation Annex | 6.2.0 | 6.3.0 |
| Sep 2004 | CN_25 | NP-040358 | 0029 | -- | Support High Availability at API Level | 6.2.0 | 6.3.0 |
| Dec 2004 | CN_26 | NP-040485 | 0053 | -- | Removal of OSA API SCFs description in W3C WSDL | 6.3.0 | 6.4.0 |
| Dec 2004 | -- | -- | -- | -- | Some figures were not visible (deleted 2/3 SoDAError bookmarks) | 6.4.0 | 6.4.1 |
| Dec 2004 | -- | -- | -- | -- | Added missing code attachments | 6.4.0 | 6.4.1 |
| Dec 2005 | CP_30 | CP-050561 | 0056 | -- | Correct definition of time duration units and usage | 6.4.1 | 6.5.0 |
| Dec 2005 | CP_30 | CP-050563 | 0059 | -- | Correction to allow generation of an immediate triggered report | 6.4.1 | 6.5.0 |
| Jun 2006 | CT_32 | CP-060194 | 0060 | -- | Resubmission of OSA API SCFs description in W3C WSDL | 6.5.0 | 6.6.0 |
| Jun 2006 | CT_32 | CP-060196 | 0061 | -- | Add missing life_time timer for triggeredStatusReportingStartReq | 6.5.0 | 6.6.0 |
| Jul 2006 | -- | -- | -- | -- | Added missing code attachments | 6.6.0 | 6.6.1 |