3GPP TS 29.332 V7.3.0 (2006-06)

Technical Specification

3rd Generation Partnership Project;

Technical Specification Group Core Network and Terminals;

Media Gateway Control Function (MGCF) – IM Media Gateway;

Mn Interface

(Release 7)

The present document has been developed within the 3rd Generation Partnership Project (3GPP TM) and may be further elaborated for the purposes of 3GPP.	 
The present document has not been subject to any approval process by the 3GPP Organizational Partners and shall not be implemented.	 
This Specification is provided for future development work within 3GPP only. The Organizational Partners accept no liability for any use of this Specification.
Specifications and reports for implementation of the 3GPP TM system should be obtained via the 3GPP Organizational Partners' Publications Offices.

Keywords

UMTS, IP, Multimedia

3GPP

Postal address

3GPP support office address

650 Route des Lucioles - Sophia Antipolis

Valbonne - FRANCE

Tel.: +33 4 92 94 42 00 Fax: +33 4 93 65 47 16

Internet

http://www.3gpp.org

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© 2006, 3GPP Organizational Partners (ARIB, ATIS, CCSA, ETSI, TTA, TTC).

All rights reserved.

Contents

Foreword	6

1	Scope	6

2	References	6

3	Definitions, symbols and abbreviations	8

3.1	Definitions	8

3.2	Symbols	8

3.3	Abbreviations	8

4	UMTS capability set	8

4.1	Void	9

5	Naming conventions	9

5.1	MGCF/IM-MGW naming conventions	9

5.2	Termination names	9

5.2.1 	Termination naming convention	9

5.2.2 	Termination naming convention for TDM terminations	9

6	Topology descriptor	9

7	Transaction timers	9

8	Transport	9

9	Multiple Virtual MG.	9

10	Formats and codes	9

10.1	Signalling Objects	9

10.2	Codec Parameters	10

10.2.1	AMR Codec	10

10.2.1	DTMF Codec	11

11	Mandatory Support of SDP and H.248 Annex C information elements	11

12	General on packages and Transactions	11

12.1	Profile Details	11

13	Void	12

14	Call independent H.248 transactions	12

15	Transactions towards IM CN Subsystem	12

15.1	Procedures related to a termination towards IM CN Subsystem	12

15.1.1	Reserve IMS Connection Point	13

15.1.2	Configure IMS Resources	14

15.1.3	Reserve IMS Connection Point and configure remote resources	15

15.1.4	Release IMS Termination	16

15.1.5	Termination heartbeat indication	17

15.2	IMS packages	17

16	Transactions towards ISUP	18

16.1	Procedures related to a termination towards ISUP	19

16.1.1	Reserve TDM Circuit	19

16.1.2	Release TDM Termination	19

16.1.3	Termination heartbeat indication	20

16.2	ISUP packages	20

17	Transactions towards BICC	21

17.1	Procedures related to a termination towards BICC	21

17.2	BICC packages	22

Annex A (Normative):	Profile Description	22

A.1	Profile Identification	22

A.2 	Summary	22

A.3 	Gateway Control Protocol Version	23

A.4	Connection Model	23

A.5	Context Attributes	23

A.6	Terminations	23

A.6.1	Termination Names	23

A.6.1.1	ASN.1 Encoding	23

A.6.1.2	ABNF coding:	24

A.6.1.2.1	Termination Naming Convention for TDM Terminations	24

A.6.1.2.1.1	Syntactical Specification	25

A.6.1.2.1.1	Wildcarding	25

A.6.1.2.1.2	Heterogeneous TDM Port Configurations	25

A.6.1.2.2	Termination Naming Convention for IMS/NGN Terminations	26

A.6.1.2.2.1	Syntactical Specification	26

A.6.2	Multiplexed terminations	26

A.7	Descriptors	26

A.7.1	Stream Descriptor	26

A.7.1.1	Local Control Descriptor	26

A.7.2	Events Descriptor	27

A.7.3	EventBuffer Descriptor	28

A.7.4	Signals Descriptor	28

A.7.5	DigitMap Descriptor	29

A.7.6	Statistics Descriptor	29

A.7.7	ObservedEvents Descriptor	29

A.7.8	Topology Descriptor	29

A.7.9	Error Descriptor	29

A.8	Command API	30

A.8.1	Add	30

A.8.2	Modify	30

A.8.3	Subtract	31

A.8.4	Move	31

A.8.5	Auditvalue	31

A.8.6	Auditcapabilities	32

A.8.7	Notify	32

A.8.8	Service Change	32

A.8.9	Manipulating and auditing context attributes	33

A.9	Generic command syntax and encoding	33

A.10	Transactions	33

A.11	Messages	34

A.12	Transport	34

A.13	Security	35

A.14	 Packages	35

A.14.1 Generic Package	37

A.14.2 Base Root Package	38

A.14.3 Basic DTMF Generator Package	39

A.14.4 Basic DTMF Detection Package	40

A.14.5 TDM Circuit Package	40

A.14.6 MGW Congestion Package	41

A.14.7 Continuity Package	41

A.14.8 Announcement Package	42

A.14.9 Bearer Characteristics Package	42

A.14.10 Generic Bearer Connection Package	43

A.14.11 Call Progress Tones Generator Package v1	44

A.14.12 Basic Call Progress Tones Generator with Directionality	44

A.14.13 Expanded Call Progress Tones Generator Package	45

A.14.14 Basic Services Tones Generation Package	46

A.14.15 Bearer Control Tunnelling Package	46

A.14.16 Expanded Services Tones Generation Package	47

A.14.17 Intrusion Tones Generation Package	47

A.14.18 3GUP Package	48

A.14.19 Modification of Link Characteristics Bearer Capability	49

A.14.20 Hanging Termination Detection Package	49

A.14.21 TFO package	50

A.14.22 Media Gateway Overload Control Package	51

A.14.23 Inactivity Timer Package	51

A.14.24 MGC Information Package	52

A.14.25 RTP Package	52

A.15	 Mandatory support of SDP and Annex C information elements	54

A.16	 Optional support of SDP and Annex C information elements	55

A.17	Procedures	55

A.17.1Call Independent Procedures	55

A.17.2 IMS Terminations Procedures	55

A.17.3 TDM Terminations Procedures	55

A.17.4 BICC Terminations Procedures	55

Annex B (informative):	Change history	56

# Foreword

This Technical Specification has been produced by the 3rd Generation Partnership Project (3GPP).

The contents of the present document are subject to continuing work within the TSG and may change following formal TSG approval. Should the TSG modify the contents of the present document, it will be re-released by the TSG with an identifying change of release date and an increase in version number as follows:

Version x.y.z

where:

x	the first digit:

1	presented to TSG for information;

2	presented to TSG for approval;

3	or greater indicates TSG approved document under change control.

y	the second digit is incremented for all changes of substance, i.e. technical enhancements, corrections, updates, etc.

z	the third digit is incremented when editorial only changes have been incorporated in the document.

# 1	Scope

The present document describes the protocol to be used on the Media Gateway Control Function (MGCF) – IM Media Gateway (IM-MGW) interface. The basis for this protocol is the H.248 protocol as specified in ITU-T. The IMS architecture is described in 23.228. The interaction of the MGCF-IM MGW interface signalling procedures in relation to the SIP, and BICC/ISUP signalling at the MGCF are described in 29.163[4].

This specification describes the application of H.248 on the Mn interface. Required extensions use the H.248 standard extension mechanism. In addition certain aspects of the base protocol H.248 are not needed for this interface and thus excluded by this profile.

In addition this profile provides support for PSTN/ISDN Emulation as required by ETSI TISPAN.

The present document is valid for a 3rd generation PLMN (UMTS) complying with Release 6 and later.

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

- References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

- For a specific reference, subsequent revisions do not apply.

- For a non-specific reference, the latest version applies.  In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TS 23.228: "IP Multimedia Subsystem (IMS); Stage 2".

[2]	3GPP TS 29.007: "General requirements on interworking between the Public Land Mobile Network (PLMN) and the Integrated Services Digital Network (ISDN) or Public Switched Telephone Network (PSTN)".

[3]	3GPP TS 29.205: "Application of Q.1900 series to Bearer Independent CS Network architecture; Stage 3"

[4]	3GPP TS 29.163: "Interworking between the IM CN subsystem and CS networks – Stage 3".

[5]	3GPP TS 29.232: "Media Gateway Controller (MGC); Media Gateway (MGW) interface; Stage 3".

[6]	3GPP TS 26.226: "Cellular Text Telephone Modem; General Description".

[7]	3GPP TS 26.103:  "Speech codec list for GSM and UMTS".

[8]	3GPP TS 29.202: "Application of Q.1900 series to Bearer Independent CS Network architecture; Stage 3".

[9]	ITU-T Recommendation H.248.1 (05/02): "Gateway Control Protocol: Version 2" including the Corrigendum1 for Version 2 (03/04).

[10]	ITU-T Recommendation H.248.8: "Error Codes and Service Change Reason Description".

[11] 	ITU-T Recommendation H.248.2: "Facsimile, text conversation and call discrimination packages".

[12] 	ITU-T Recommendation H.248.10: "Media Gateway Resource Congestion Handling Package".

[13]	ITU-T Recommendation T.140: "Text conversation protocol for multimedia application".

[14]	ITU-T Recommendation Q.1950 (12/2002) "Call Bearer Control Protocol".

[15]	IETF RFC 2960: "Stream Control Transmission Protocol".

[16]	IETF RFC 3267: "Real-Time Transport Protocol (RTP) Payload Format and File Storage Format for the Adaptive Multi-Rate (AMR) and Adaptive Multi-Rate Wideband (AMR-WB) Audio Codecs".

[17]	IETF RFC 2327: "SDP: Session Description Protocol".

[18]	IETF RFC 2833: "RTP Payload for DTMF Digits, Telephony Tones and Telephony Signals".

[20]	3GPP TS 26.236: "Packet switched conversational multimedia applications; Transport protocols".

[21]	3GPP TS 29.415: "Core Network Nb Interface User Plane Protocols".

[22]	3GPP TS 23.153: "Out of band transcoder control".

[23]	IETF RFC 768: "User Datagram Protocol".

[24]	IETF RFC 3332: "Signaling System 7 (SS7) Message Transfer Part 3 (MTP3) - User Adaptation Layer (M3UA)".

[25]	3GPP TS 29.202: "SS7 Signalling Transport in Core Network".

[26] 	ITU-T Recommendation H.248.7: "Generic Announcement Package".

[27] 	ITU-T Recommendation H.248.36: " Hanging Termination Detection Package ".

[28]	ITU-T Recommendation H.248.11 (11/03):"Media gateway overload control package".

[29]	ITU-T Recommendation H.248.14 (03/02):"Inactivity timer package".

[30]	ETSI TS 183 022 v1.1.1: "Telecommunications and Internet converged Services and Protocols for Advanced Networking (TISPAN); MGC Information Package".

[31]		ETSI ES 283 024 V1.0.14 (2005-12);TISPAN NGN Release 1; PSTN/ISDN Emulation Subsystem; H.248 Profile for controlling Trunking Media Gateways

# 3	Definitions, symbols and abbreviations

## 3.1	Definitions

For the purposes of the present document, the [following] terms and definitions [given in ... and the following] apply.

Context (H.248): A context is an association between a number of Terminations. The context describes the topology (who hears/sees whom) and the media mixing and/or switching parameters if more than two terminations are involved in the association.

Package (H.248): Different types of gateways may implement terminations which have differing characteristics. Variations in terminations are accommodated in the protocol by allowing terminations to have optional properties. Such options are grouped into packages, and a termination may realise a set of such packages.

Termination (H.248): A termination is a logical entity on an MGW which is the source and/or sink of media and/or control streams. A termination is described by a number of characterising properties, which are grouped in a set of descriptors which are included in commands. Each termination has a unique identity (TerminationID).

Termination Property (H.248): Termination properties are used to describe terminations. Related properties are grouped into descriptors. Each termination property has a unique identity (PropertyID).

## 3.2	Symbols

For the purposes of the present document, the following symbols apply:

Mn	Interface between the media gateway control function and the IMS media gateway.

## 3.3	Abbreviations

For the purposes of the present document, the following abbreviations apply:

BICC	Bearer Independent Call Control

IM-MGW	IP Multimedia Media Gateway

ISUP	ISDN User Part

MGCF	Media Gateway Control Function

RFC	Request For Comment; this includes both discussion documents and specifications in the IETF domain

SCTP	Stream Control Transmission Protocol

# 4	UMTS capability set

The support of the Mn interface capability set shall be identified by the Mn profile and support of this profile shall be indicated in ServiceChange procedure.

The mandatory parts of this  capability set shall be used in their entirety whenever it is used within the H.248 profile. Failure to do so will result in a non-standard implementation.

ITU-T Recommendation H.248.1 (05/02) [9] is the basis for this Capability Set. The compatibility rules for packages, signals, events, properties and statistics and the H.248 protocol are defined in ITU-T Recommendation H.248.1 [9]. Their use or exclusion for this interface is clarified in clause 12.

## 4.1	Void

# 5	Naming conventions

## 5.1	MGCF/IM-MGW naming conventions

The MGCF shall be named according to the naming structure of the underlying transport protocol which carries the H.248 protocol.

## 5.2	Termination names

### 5.2.1 	Termination naming convention

For definition on termination naming convention see 3GPP TS 29.232 [5]

### 5.2.2 	Termination naming convention for TDM terminations

For the definition of TDM terminations see 3GPP TS 29.232[5]

# 6	Topology descriptor

The Topology Descriptor may be supported by the IM-MGW and MGCF, see Annex A.

# 7	Transaction timers

All transaction timers specified in H.248 shall be supported in this subset of the protocol.

# 8	Transport

Each implementation of the Mn interface should provide SCTP (as defined in IETF RFC2960 [14]). If using SCTP as defined in IETF RFC 2960 [12] the MGW shall always be the node to perform the "Initiation".An implementation alternative may provide UDP (as defined in IETF RFC 768 [23]). The M3UA layer may also be added to SCTP for pure IP signalling transport (as defined in IETF RFC 3332 [24] with options detailed in 3GPP TS 29.202 [25]).

See also Annex A.

# 9	Multiple Virtual MG.

The support of multiple virtual MGW outlined in the subclause "Multiple virtual MGW" in ITU-T Recommendation H.248.1 [9] is optional.

# 10	Formats and codes

## 10.1	Signalling Objects

Table 10.1 shows the parameters which are required.

The coding rules applied in ITU-T Recommendation H.248.1 [9] for the applicable coding technique shall be followed for the UMTS capability set.

Table 10.1: required parameters

| Signalling Object | H.248 Descriptor | Coding |
| --- | --- | --- |
| Codec List | Local Descriptor or Remote Descriptor | <fmt list> in a single SDP m-line. For a fixed RTP payload type, the codec type is implied by the RTP payload type. For a dynamic RTP payload type, for each codec information on the codec type shall be provided in a separate SDP “a=rtpmap”-line and possibly additional SDP “a=fmtp”-line(s). See Clause 10.2. |
| Bearer Service Characteristics | Local Descriptor or Remote Descriptor | As per Q.1950 [14]. For TMR, only values “3.1 kHz audio” or “speech” are required. |
| Context ID | NA | Binary Encoding: As per ITU-T Recommendation H.248.1 [9] Annex A. Textual Encoding: As per ITU-T Recommendation H.248.1 [9] Annex B. |
| IP Address | Local Descriptor or Remote Descriptor | <connection address> in SDP “c-line” |
| Port | Local Descriptor or Remote Descriptor | <port> in SDP m-line. <transport> in SDP m-line shall be set to value "RTP/AVP" for voice service, and set to value “UDPTL” or “TCPTL”for T.38 service. |
| mediatype | Local Descriptor or Remote Descriptor | <media> in sdp m-line “audio” for voice service, and “image” for T.38 service. |
| Reserve_Value | Local Control | ITU-T Recommendation H.248.1 [9] Mode property. Binary Encoding: Encoding as per ITU-T Recommendation H.248.1 Annex A "reserveValue" Textual Encoding: Encoding as per ITU-T Recommendation H.248.1 Annex B "reservedValueMode". |
| RtcpbwRS | Local Descriptor or Remote Descriptor | <bandwidth> in SDP “b:RS”-line. |
| RtcpbwRR | Local Descriptor or Remote Descriptor | <bandwidth> in SDP “b:RR”-line. |
| RTPpayload | Local Descriptor or Remote Descriptor | <fmt list> in SDP m-line |
| Termination ID | NA | Binary Encoding: As per ITU-T Recommendation H.248.1 [9] Annex A. Textual Encoding: As per ITU-T Recommendation H.248.1 [9] Annex B. |
| Transaction ID | NA | Binary Encoding: As per ITU-T Recommendation H.248.1 [9] Annex A. Textual Encoding: As per ITU-T Recommendation H.248.1 [9] Annex B. |
| Note For binary encoding, the SDP equivalents “SDP_V”, “SDP_M”, “SDP_C”, “SDP_A”, and SDP_B” in ITU-T Recommendation H.248.1 [9], Annex C.11, shall be used to encode the corresponding SDP lines. Other SDP equivalents may be used, for details see Annex A. The SDP equivalents shall be used in the order specified for the corresponding SDP lines in IETF RFC 2327 [17]. Rules for the usage of SDP in ITU-T Recommendation H.248.1 [9] shall also be applied to the SDP equivalents. |

## 10.2	Codec Parameters

### 10.2.1	AMR Codec

On IMS terminations, the AMR codec is transported according to the IETF AMR RTP profile, IETF RFC 3267 [16]. 3GPP TS 26.236 [20] selects options applicable within 3GPP.

IETF RFC 3267 contains the MIME registration of the IETF AMR RTP profile with media type "audio" and media subtype "AMR". The AMR codec shall be signaled accordingly in the SDP "a=rtpmap"-line and a dynamic RTP payload type shall be used.

The selected options are expressed as MIME parameters in SDP "a=fmtp"-line. The following MIME parameters shall be supported on the Mn interface:

- "mode-set"

- "mode-change-period"

For compatibility with GSM peers, the IM-MGW shall perform mode changes only in every second sent package.

### 10.2.1	DTMF Codec

On IMS terminations, DTMF is transported according to the IETF RFC 2833 [18] "telephone event" format.

IETF RFC 2833[18] contains the MIME registration with media type "audio" and media subtype "telephone-event". DTMF shall be signaled accordingly in the SDP "a=rtpmap"-line and a dynamic RTP payload type shall be used.

An IM-MGW supporting DTMF shall support the default options of the IETF RFC 2833 [18] "telephone event" format. Therefore, a support of optional MIME parameters of "telephone-event" is not required at the Mn interface.

# 11	Mandatory Support of SDP and H.248 Annex C information elements

FOR BICC termination, this section shall be in accordance with the subclause "Mandatory Support of SDP and ITU-T Recommendation H.248.1 Annex C information elements" in ITU-T Recommendation Q.1950 [14].

For IMS termination, see Annex A.

For IP the IANA ICP IDI format of the NSAP addressing format as specified in X.213 [33] shall be used.  For Ipv4 networks the IPv4 format recommended by X.213 shall be adopted.

For this application the BIR length shall be fixed at 4 Octets and the NSAP length shall be fixed at 20 Octets.

# 12	General on packages and Transactions

The base root package (0x0002) properties shall be provisioned in the MGW.

H.248 Statistics shall not be audited via the Mn interface.

The use of "Overspecified" (e.g. range of values) and "Underspecifed" (e.g. "?") parameter specification shall not be permitted except where explicitly indicated in or referenced by the Mn interface specification.

The use of wildcarding for the Termination Id shall be performed using 1 octet only.

Notifications shall not be sent by the MGW in response to Release Termination procedure.

Commands on ROOT Termination shall only use the NULL Context.

## 12.1	Profile Details

VOID.

NOTE: Profile now defined in Normative Annex A.

# 13	Void

# 14	Call independent H.248 transactions

Table 14 shows the relationship between each non call-related procedure in 3GPP TS 29.232 [5] and the corresponding procedure defined in 3GPP TS 29.163 [4].

For further description of error codes and service change reasons, refer to ITU-T Recommendation H.248.8 [14].

Table 14: Non call-related transaction reused from 3GPP TS 29.232 [5]

| Procedure defined in 3GPP TS 29.163 [4] | Procedure defined in 3GPP TS 29.232 [5] | Support | Comment |
| --- | --- | --- | --- |
| IM-MGW Out of service | MGW Out of Service | Mandatory |  |
| IM-MGW Communication Up | MGW Communication Up | Mandatory |  |
| IM-MGW Restoration | MGW Restoration | Mandatory |  |
| IM-MGW Register | MGW Register | Mandatory |  |
| IM-MGW Re-register | MGW Re-register | Mandatory |  |
| MGCF Ordered Re-register | (G)MSC Server Ordered Re-register | Mandatory |  |
| MGCF Restoration | (G)MSC Server Restoration | Optional |  |
| MGCF Out of Service | (G)MSC Server Out of Service | Optional |  |
| Termination Out-of-Service | Termination Out-of-Service | Mandatory |  |
| Termination Restoration | Termination Restoration | Mandatory |  |
| Audit Value | Audit Value | Mandatory | Only For Audit of Termination Service State. Audit of the Hanging Termination Detection Package may also be supported. |
| Audit Capability | Audit Capability | Optional |  |
| Command Rejected | Command Rejected | Mandatory | The “Command Rejected” procedure may be used in response both to call-related and non-call-related ITU-T Recommendation H.248 Commands |
| IM-MGW Capability Change | Capability Update | Optional |  |
| IM-MGW Resource Congestion Handling - Activate | MGW Resource Congestion Handling - Activate | Mandatory |  |
| IM-MGW Resource Congestion Handling - Indication | MGW Resource Congestion Handling - Indication | Mandatory |  |

# 15	Transactions towards IM CN Subsystem

## 15.1	Procedures related to a termination towards IM CN Subsystem

Table 1 shows the relationship between each call-related procedure in ITU-T Recommendation Q.1950 [14] (see 3GPP TS 29.205 [3]) or TS 29.232 [5] and the corresponding stage 2 procedure defined in 3GPP TS 29.163 [4].

Table 15.1.1: Correspondence between ITU-T Recommendation Q.1950 [13] or 29.232 [5] call-related transactions and 3GPP TS 29.163 [4] procedures

| Procedure defined in 3GPP TS 29.163 [4] | Transaction used in Q.1950 [14] | Transaction used in TS 29.232 [5] | Supported | Comment |
| --- | --- | --- | --- | --- |
| Reserve IMS Connection point | Not defined | n. a. for reuse | Mandatory | See 13.2.1.1 |
| Configure IMS Resources | Not Defined | n. a. for reuse | Mandatory | See 13.2.1.2 |
| Reserve IMS Connection Point and configure remote resources | Not defined | n. a. for reuse | Mandatory | See 13.2.1.3 |
| Release IMS termination | n. a. for reuse | n. a. for reuse | Mandatory | See 13.2.1.4 |
| Change IMS ThroughConnection | Cut Through | n. a. for reuse | Mandatory | only the Explicit (MGC Controlled Cut-Through) procedure is supported |
| Detect IMS RTP Tel Event | Detect Digit | n. a. for reuse | Optional | Only applicable if termination towards IMS is connected with a termination towards a BICC network. |
| Notify IMS RTP Tel Event | Detected digit(BIWF) | n. a. for reuse | Optional | Only applicable if termination towards IMS is connected with a termination towards a BICC network. |
| Send IMS RTP Tel Event | n.a. for reuse | Send DTMF | FFS | Restrictions defined for minimum interval to follow 3G TS 23.014. Maximum interval shall be controlled by MGW if required by network |
| Stop IMS RTP Tel Event | n.a.for reuse | Stop DTMF | FFS | The signal descriptor shall not include any signal. The MGW shall ensure the minimum duration timing and minimum interval timing is achieved in accordance with the DTMF timing defined in TS 23.014 [27]. Maximum duration shall also be controlled by the MGW if required by the network |
| Termination heartbeat Indication | Not defined | Termination hearbeat Indication | Optional (NOTE 2) |  |
| IMS Bearer Released | BNC Release | Bearer Released | Mandatory | (NOTE 3) |
| NOTE 1: A procedure defined in table 13.2.1 can be combined with another procedure in the same table. This means that they can share the same contextID and termination ID(s) and that they can be combined in the same H.248 command. NOTE 2: It is highly recommended to support this procedure to allow detection of hanging contexts and terminations in the MGW that may result e.g. from a loss of communication between the MSC-S and the MGW. NOTE 3: Termination ID shall be provided in the response. |

## 15.1.1	Reserve IMS Connection Point

When the procedure “Reserve IMS Connection Point” is required the following procedure is initiated:

The MGCF sends an Add.req command with the following information.

1    Add.req (Reserve IMS Connection Point)	MGCF to IM-MGW

Table 15.1.2: Reserve IMS Connection Point Request

| Address Information | Control information | Bearer information |
| --- | --- | --- |
| Local Descriptor { Port = ? IP Address = ? } | Transaction ID = z Termination ID = ? If Context Requested: Context ID = ? If Context Provided: Context ID = c1 If Resources for multiple Codecs shall be reserved: Reserve_Value If detection of hanging termination is requested: (NOTE 1) NotificationRequested (Event ID = x, “termination heartbeat”) If indication on Bearer Released requested: NotificationRequested (Event ID = x, "BNC Release (Cause)") – as defined in ITU-T Recommendation Q.1950 | Local Descriptor { Codec List RTP Payloads RtcpbwRS RtcpbwRR } |
| NOTE 1: It is highly recommended to request termination heartbeat notification to detect hanging context and termination in the MGW that may result e.g. from a loss of communication between the MSC-S and the MGW. |

When the processing of command (1) is complete, the IM-MGW initiates the following procedure.

2    Add.resp (Reserve IMS Connection Point Ack)

Table 15.1.3: Reserve IMS Connection Point Acknowledge

| Address Information | Control information | Bearer information |
| --- | --- | --- |
| Local Descriptor { Port IP Address } | Transaction ID Termination ID Context ID | Local Descriptor { Codec List RTP Payloads RtcpbwRS RtcpbwRR } |

## 15.1.2	Configure IMS Resources

When the procedure "Configure IMS Resources" is required the following procedure is initiated:

The MGCF sends an Mod.req command with the following information.

1    Mod.req (Configure IMS Resources)	MGCF to IM-MGW

Table 15.1.4: Configure IMS Resources Request

| Address Information | Control information | Bearer information |
| --- | --- | --- |
| If local resources are modified: Local Descriptor { Port IP Address } If remote resources are modified: Remote Descriptor { Port IP Address } | Transaction ID Termination ID Context ID If Resources for multiple Codecs shall be reserved: Reserve_Value | If local resources are modified: Local Descriptor { Codec List RTP Payloads RtcpbwRS RtcpbwRR } If remote resources are modified: Remote Descriptor { Codec List RTP Payloads RtcpbwRS RtcpbwRR } |

When the processing of command (1) is complete, the IM-MGW initiates the following procedure.

2 Mod.resp (Configure IMS Resources Ack)

Table 15.1.5: Configure IMS Resources Acknowledge

| Address Information | Control information | Bearer information |
| --- | --- | --- |
| If local resources were provided in request: Local Descriptor { Port IP Address } If remote resources were provided in request: Remote Descriptor { Port IP Address } | Transaction ID Context ID | If local resources were provided in request: Local Descriptor { Codec List RTP Payloads RtcpbwRS RtcpbwRR } If remote resources were provided in request: Remote Descriptor { Codec List RTP Payloads RtcpbwRS RtcpbwRR } |

### 15.1.3	Reserve IMS Connection Point and configure remote resources

When the procedure "Reserve IMS Connection Point and configure remote resources" is required the following procedure is initiated:

The MGCF sends a Mod.req command with the following information.

1   Add.req (Reserve IMS Connection Point and configure remote resources) MGCF to IM-MGW

Table 15.1.6: Reserve IMS Connection Point and configure remote resources Request

| Address Information | Control information | Bearer information |
| --- | --- | --- |
| Local Descriptor { Port = ? IP Address = ? } Remote Descriptor { Port IP Address } | Transaction ID Termination ID = ? If Context Requested: Context ID = ? If Context Provided: Context ID = c1 If Resources for multiple Codecs shall be reserved: Reserve_Value If detection of hanging termination is requested: (NOTE 1) NotificationRequested (Event ID = x, “termination heartbeat”) If indication on Bearer Released requested: NotificationRequested (Event ID = x, "BNC Release (Cause)") – as defined in ITU-T Recommendation Q.1950 | Local Descriptor { Codec List RTP Payloads RtcpbwRS RtcpbwRR } Remote Descriptor { Codec List RTP Payloads RtcpbwRS RtcpbwRR } |
| NOTE 1: It is highly recommended to request termination heartbeat notification to detect hanging context and termination in the MGW that may result e.g. from a loss of communication between the MSC-S and the MGW. |

When the processing of command (1) is complete, the IM-MGW initiates the following procedure.

2    Add.resp (Reserve IMS Connection Point and configure remote resources Ack)

Table 15.1.7: Reserve IMS Connection Point and configure remote resources Acknowledge

| Address Information | Control information | Bearer information |
| --- | --- | --- |
| Local Descriptor { Port IP Address } Remote Descriptor { Port IP Address } | Transaction ID Termination ID Context ID | Local Descriptor { Codec List RTP Payloads RtcpbwRS RtcpbwRR } Remote Descriptor { Codec List RTP Payloads RtcpbwRS RtcpbwRR } |

### 15.1.4	Release IMS Termination

When the procedure “Release IMS Termination” is required the following procedure is initiated:

The MGCF sends an Sub.req command with the following information.

1    Sub.req (Release IMS Termination)	MGCF to IM-MGW

Table 15.1.8: Release IMS Termination Request

| Address Information | Control information | Bearer information |
| --- | --- | --- |
|  | Transaction ID Termination ID = termination/ALL Context ID = context/ALL |  |

When the processing of command (1) is complete, the IM-MGW initiates the following procedure.

2    Sub.resp (Release IMS Termination) 	IM-MGW to MGCF

Table 15.1.9: Release IMS Termination Acknowledge

| Address Information | Control information | Bearer information |
| --- | --- | --- |
|  | Transaction ID Termination ID Context ID |  |

### 15.1.5	Termination heartbeat indication

When the procedure  "Termination heartbeat indication" is required the following procedure is initiated: the MGW sends a NOT.req command with the following information.

Table 15.1.5.1: NOT.req (Termination heartbeat)	MGW to MGC

| Address Information | Control information | Bearer information |
| --- | --- | --- |
|  | Transaction ID = z Context ID = c1 Termination ID = bearer1 Event_ID (Event ID = x, “termination heartbeat") |  |

When the processing of command  is complete, the MGC initiates the following procedure.

Table 15.1.5.2: NOT.resp (Termination heartbeat)	MGC to MGW

| Address Information | Control information | Bearer information |
| --- | --- | --- |
|  | Transaction ID = z Context ID = c1 Termination ID = bearer1 |  |

The heartbeat timer shall be configured to a value much greater than the mean call holding time.

The MSC-S is in charge of correcting any detected mismatch, by substracting hanging terminations or clearing hanging contexts.

## 15.2	IMS packages

None

# 16	Transactions towards ISUP

Table 16.1: Correspondence between ITU-T Recommendation Q.1950 [13] or 29.232 [5] call-related transactions and 3GPP TS 29.163 [4] procedures related to a termination towards an ISUP network

| Procedure defined in 3GPP TS 29.163 [4] | Transaction used in ITU-T Q.1950 [14] | Transaction used in TS 29.232 [5] | Support | Comment |
| --- | --- | --- | --- | --- |
| Reserve TDM Circuit | n. a. for reuse | n. a. for reuse, (NOTE2) | Optional (NOTE 4) | See Clause 13.2.2.1 |
| Change TDM Through-connection | Cut Through (CSM Controlled) | Change Through-connection | Optional (NOTE 4) | only the Explicit (MGC Controlled Cut-Through) procedure is supported |
| Activate TDM voice-processing function | Echo Canceller | n. a. for reuse | Optional (NOTE 4) |  |
| Send TDM Tone | Insert_Tone | n. a. for reuse | Optional (NOTE 4) | Only H.248 MOD command to an existing termination |
| Stop TDM Tone | Insert_Tone | n. a. for reuse | Optional (NOTE 4) | Only H.248 MOD command to an existing termination |
| Play TDM Announcement | Insert_Announcement | n. a. for reuse | Optional (NOTE 4) | Only H.248 MOD command to an existing termination |
| TDM Announcement Completed | Signal_Completion | n. a. for reuse | Optional (NOTE 4) | (NOTE 5) |
| Stop TDM Announcement | Insert Announcement | n. a. for reuse | Optional (NOTE 4) | Only H.248 MOD command to an existing termination |
| Continuity Check | Continuity Check Tone | n. a. for reuse | Optional (NOTE 4) | The addition to “Prepare BNC Notify” defined in Annex B.7.1.1 of Q.1950 [10] shall be applied instead to “Reserve TDM Circuit”, as defined in Clause 13.2.2.1 |
| Continuity Check Verify | Continuity Check Verify | n. a. for reuse | Optional (NOTE 4) |  |
| Continuity Check Response | Continuity Check Response | n. a. for reuse | Optional (NOTE 4) | The addition to “Prepare BNC Notify” defined in Annex B.7.1.2 of Q.1950 [10] shall be applied instead to “Reserve TDM Circuit”, as defined in Clause 13.2.2.1 |
| Release TDM Termination | n. a. for reuse | n. a. for reuse | Optional (NOTE 4) | See Clause 13.2.2.2 |
| Termination Out Of Service | BIWF_Service_Cancellation_Indication | n. a. for reuse | Optional (NOTE 4) |  |
| Termination heartbeat Event | Not defined | Termination heartbeat Indication | Optional |  |
| Not defined | Not defined | TFO Activation | Optional |  |
| Not defined | Not defined | Codec Modify | Optional |  |
| Not defined | Not defined | Optimal Codec and Distant List_Notify | Optional |  |
| Not defined | Not defined | Distant Codec List | Optional |  |
| Not defined | Not defined | TFO status Notify | Optional |  |
| Not defined | Not defined | TFO status | Optional |  |
| Bearer Released | BNC Release | Bearer Released | Optional (NOTE 4) | (NOTE 5) |
| NOTE 1: A procedure defined in table 13.2.2 can be combined with another procedure in the same table. This means that they can share the same contextID and termination ID(s) and that they can be combined in the same H.248 command. NOTE 2: The reserve circuit procedure of 29.232 is not to be used only a reduced set of the parameters is required for reserve TDM circuit. NOTE 3: Enhanced to include Camel Prepaid, otherwise same as Q.1950 NOTE 4: Necessary for optional terminations towards ISUP NOTE 5: Termination ID shall be provided in the response. |

## 16.1	Procedures related to a termination towards ISUP

### 16.1.1	Reserve TDM Circuit

When the procedure “Reserve TDM Circuit” is required the following procedure is initiated:

The MGCF sends an Add.req command with the following information.

Table 16.1.1.1: Add.req (Reserve TDM Circuit)	MGCF to IM-MGW

| Address Information | Control information | Bearer information |
| --- | --- | --- |
|  | Transaction ID Termination ID If Context Requested: Context ID = ? If Context Provided: Context ID = c1 If detection of hanging termination is requested: NotificationRequested (Event ID = x, “termination heartbeat”) If indication on Bearer Released requested: NotificationRequested (Event ID = x, "BNC Release (Cause)") – as defined in ITU-T Recommendation Q.1950 | Bearer Service Characteristics |

When the processing of command (1) is complete, the IM-MGW initiates the following procedure.

Table 16.1.1.2: Add.resp (Reserve TDM Circuit) 	IM-MGW to MGCF

| Address Information | Control information | Bearer information |
| --- | --- | --- |
|  | Transaction ID Termination ID Context ID |  |

### 16.1.2	Release TDM Termination

When the procedure “Release TDM Termination” is required the following procedure is initiated:

The MGCF sends an Sub.req command with the following information.

Table 16.1.2.1: Sub.req (Release TDM Termination)	MGCF to IM-MGW

| Address Information | Control information | Bearer information |
| --- | --- | --- |
|  | Transaction ID Termination ID Context ID |  |

When the processing of command (1) is complete, the IM-MGW initiates the following procedure.

Table 16.1.2.2: Sub.resp (Release TDM Termination)	IM-MGW to MGCF

| Address Information | Control information | Bearer information |
| --- | --- | --- |
|  | Transaction ID Termination ID Context ID |  |

### 16.1.3	Termination heartbeat indication

When the procedure  "Termination heartbeat indication" is required the following procedure is initiated: the MGW sends a NOT.req command with the following information.

Table 16.1.3.1: NOT.req (Termination heartbeat)	MGW to MGC

| Address Information | Control information | Bearer information |
| --- | --- | --- |
|  | Transaction ID = z Context ID = c1 Termination ID = bearer1 Event_ID (Event ID = x, “termination heartbeat") |  |

When the processing of command  is complete, the MGC initiates the following procedure.

Table 16.1.3.2: NOT.resp (Termination heartbeat)	MGC to MGW

| Address Information | Control information | Bearer information |
| --- | --- | --- |
|  | Transaction ID = z Context ID = c1 Termination ID = bearer1 |  |

The heartbeat timer shall be configured to a value much greater than the mean call holding time.

The MSC-S is in charge of correcting any detected mismatch, by substracting hanging terminations or clearing hanging contexts.

## 16.2	ISUP packages

None

# 17	Transactions towards BICC

## 17.1	Procedures related to a termination towards BICC

Table 17.1: Correspondence between ITU-T Recommendation Q.1950 [13] or 3GPP TS 29.232 [5] call-related transactions and 3GPP TS 29.163 [4] procedures related to a termination towards a BICC network

| Procedure defined in 3GPP TS 29.163 [4] | Transaction used in Q.1950 [14] | Transaction used in TS 29.232 [5] | Support | Comment |
| --- | --- | --- | --- | --- |
| Establish Bearer | Establish_BNC_Notify +(tunnel) | Establish Bearer (NOTE 1) | Optional (NOTE 5) |  |
| Prepare Bearer | Prepare_BNC_Notify +(tunnel) | Prepare Bearer (NOTE 1), (NOTE 2) | Optional (NOTE 5) |  |
| Change Through-Connection | Cut_Through | Change Through-Connection | Optional (NOTE 5) | only the Explicit (MGC Controlled Cut-Through) procedure is supported |
| Release Bearer | Cut_BNC (MOD H.248 Command). | Release Bearer | Optional (NOTE 5) | (NOTE 3) |
| Release Termination | Cut_BNC (SUB H.248 Command). | Release Termination | Optional (NOTE 5) | Statistics about “Ctmbits” are not applicable in Sub.resp |
| Bearer Established | BNC Established | Bearer Established | Optional (NOTE 5) | (NOTE 3) |
| Bearer Released | BNC Release | Bearer Released | Optional (NOTE 5) | (NOTE 3) |
| Send Tone | Insert_Tone | n. a. for reuse | Optional (NOTE 5) | Only H.248 MOD command to an existing termination |
| Stop Tone | Insert Tone | n. a. for reuse | Optional (NOTE 5) | Only H.248 MOD command to an existing termination |
| Play Announcement | Insert_Annoucement | n. a. for reuse | Optional (NOTE 5) | Only H.248 MOD command to an existing termination |
| Stop Announcement | Insert Announcement | n. a. for reuse | Optional (NOTE 5) | Only H.248 MOD command to an existing termination |
| Announcement Completed | Signal Completion | n. a. for reuse | Optional (NOTE 5) | (NOTE 3) |
| Bearer Modification Support | Not defined | Bearer Modification Support | Optional (NOTE 5) |  |
| Confirm Char | Confirm_Char | Confirm Bearer Characterictics (NOTE 1) | Optional (NOTE 6) |  |
| Modify Bearer Characteristics | Modify Char | Modify Bearer Characteristics (NOTE 1) | Optional (NOTE 6) |  |
| Reserve Char | Reserve_Char_Notify | Reserve Bearer Characteristics (NOTE 1) | Optional (NOTE 6) |  |
| Bearer Modified | BNC Modified | Bearer Modified | Optional (NOTE 6) |  |
| Activate Voice Processing Function | Echo Canceller | n. a. for reuse | Optional (NOTE 5) |  |
| Tunnel Information Down | Tunnel (MGC-MGW) | Tunnel Information Down | Optional (NOTE 7) | For IP Transport at BICC termination |
| Tunnel Information Up | Tunnel (MGW-MGC) | Tunnel Information Up | Optional (NOTE 7) | For IP Transport at BICC termination |
| Termination Out-of-Service | BIWF Service Cancellation Indication | n. a. for reuse | Optional (NOTE 5) |  |
| Termination heartbeat | Not defined | Termination heartbeat indication | Optional (NOTE 8) |  |
| Not defined | Not defined | TFO Activation | Optional |  |
| Not defined | Not defined | Codec Modify | Optional |  |
| Not defined | Not defined | Optimal Codec and Distant List_Notify | Optional |  |
| Not defined | Not defined | Distant Codec List | Optional |  |
| Not defined | Not defined | TFO status Notify | Optional |  |
| Not defined | Not defined | TFO status | Optional |  |
| NOTE 1: The procedure is only applicable if the Nb framing protocol is applied at the BICC termination. Only requesting of Observed events defined in the corresponding TS 29.232 and parameters defined in the “3GUP” package of TS 29.232 are applicable in addition the parameters of the corresponding Q.1950 procedure. Those parameters shall be applies as follows: UP mode = Supported mode; UP versions = 2; interface = CN; NOTE 2: Parameters and Observed events defined for Cellular Text telephone Modem Text Transport in the corresponding procedure of TS 29.232 are not applicable. NOTE 3: Termination ID shall be provided in the response. NOTE 4: Enhanced to include Camel Prepaid, otherwise same as Q.1950 NOTE 5: Necessary for optional terminations towards BICC NOTE 6: Optional for optional terminations towards BICC NOTE 7: Necessary for optional terminations towards BICC network with IP transport NOTE 8: It is highly recommended to support this procedure to allow detection of hanging contexts and terminations in the MGW that may result e.g. from a loss of communication between the MSC-S and the MGW. |

## 17.2	BICC packages

This Clause is only applicable for terminations towards BICC Networks. The support of terminations towards BICC networks is optional.

No new packages for terminations towards BICC Networks are defined in the present specification. See Clause 12.1.14 for reused packages from other specifications.

If the Nb framing protocol (see 3GPP TS 29.415 [21]) is applied at the termination towards the BICC network, the following package shall be applied:

3GUP package (see subclause 15.1.1 of 3GPP TS 29.232 [5]);To enable bearer modification at OoBTC capable networks on Nb interface  (see 3GPP TS 23.153 [22]) at the termination towards the BICC network, the following package shall be applied:

Modification of Link Characteristics Bearer Capability (see subclause 15.1.5 of 3GPP TS 29.232 [5]);

Annex A (Normative):
Profile Description

## A.1	Profile Identification

Table A.1: Profile version

| Profile name: | threegimscsiw |
| --- | --- |
| Version: | 2 |

## A.2 	Summary

This Profile describes the minimum mandatory settings and procedures required to fulfil the Media Gateway control requirements for a) the interworking scenario between 3GPP IMS and 3GPP CS or PSTN/ISDN and b) the interworking scenario between NGN and PSTN/ISDN (i.e ETSI IMS-PSTN/ISDN, ETSI PES-PSTN/ISDN).

## A.3 	Gateway Control Protocol Version

ITU Recommendation H.248.1 Version 2

### A.4	Connection Model

Table A.4: Connection Model

| Maximum number of contexts: | No restriction |
| --- | --- |
| Maximum number of terminations per context: | 2 (NOTE1) 32 (NOTE 2) |
| Allowed terminations type combinations in a Context | All (NOTE 3) |
| NOTE1: Support of 2 terminations per context is required for TISPAN. Support of more than two terminations per context (e.g. for monitoring) is optional. NOTE2: Support of 32 termination per context is required for 3GPP NOTE3: For TISPAN NGN R1 only the following is required: Context[a](RTP, TDM), Context[b](TDM, TDM), |

## A.5	Context Attributes

Table A.5: Context attributes

| Context Attribute | Supported | Values Supported |
| --- | --- | --- |
| Topology | Optional | All |
| Priority Indicator | Yes | 0-15 |
| Emergency Indicator | Yes | Not Applicable |
| NOTE: The “Topology” attribute is optional for example support of monitoring. If requested and not supported error code 444 shall be returned |

## A.6	Terminations

### A.6.1	Termination Names

The Termination ID structure is provisioned in the MGC and MG and is known by the MG and the MGC at or before start up.

#### A.6.1.1	ASN.1 Encoding

The following general structure of TerminationID shall be used:

4 octets shall be used for the termination ID. The following defines the general structure for the termination ID:

| Termination type | X |
| --- | --- |

Termination type:

Length 3 bits

Values:

000 Reserved

001 Ephemeral termination

010 TDM termination

011 - 110 Reserved

111 Reserved for ROOT termination Id (ROOT Termination Id = 0xFFFFFFFF)

X:

Length 29 bits.

Usage dependent on Termination type. TDM terminations specified below in subclause 5.2.2. Other usage un-specified.

#### A.6.1.2	ABNF coding:

TerminationID  = "ROOT" / pathName / "$" / "*"  ; according to ITU-T H.248.1 [9] Annex B.

##### A.6.1.2.1	Termination Naming Convention for TDM Terminations

A hierarchical naming structure is recommended for physical Terminations.

The PCMsystem is recommended to follow the following physical and digital signal hierarchy:

PCMsytem = <unit-type1>_<unit #>/<unit-type2>_<unit #>/...

The <unit-type> identifies the particular hierarchy level.

Some example values of <unit-type> are:

"s", "su", "stm4", "stm1", "oc3", "ds3", "e3", "ds2", "e2", "ds1", "e1" where "s" indicates a slot number and "su" indicates a sub-unit within a slot.

Leading zeroes MUST NOT be used in any of the numbers ("#") above.

The <unit #> is a decimal number which is used to reference a particular instance of a <unit-type> at that level of the hierarchy. Value ranges always starting with one.

The number of levels and naming of those levels is based on the physical hierarchy within the Media Gateway.

Here are some examples of the Termination structure:

1.	TDM Terminations at SDH STM-1 ports:
tdm/s_<Card ID>/stm1_<STM1 ID>/e1_<E1 ID>/<channel #>

e.g., tdm/s_2/stm1_3/e1_17/25

2.	TDM Terminations at PDH E1 ports (e.g., for "PCM system" only applications):
tdm/s_<Card ID>/e1_<E1 ID>/<channel #>

e.g., tdm/s_2/e1_17/25

NOTE 1:	This Termination naming convention may be used to align with ASN.1 TDM Termination names as defined in A.6.1.1. The alignment must take into account the numbering scheme of "<E1 ID>" with the"PCM system" field, and the upper level(s) are regarded as prefix ("tdm/s-<Card ID>" versus  "3-bit codepoint for 'TDM' ").

NOTE 2:	See also clause 3/H.248.33 concerning "PCM system" definition.

3.	TDM Terminations at SONET OC-3 ports:
tdm/s_<Card ID>/oc3_<OC3 ID>/ds1_<DS1 ID>/<channel #>

e.g., tdm/s_2/oc3_3/ds1_17/22

###### A.6.1.2.1.1	Syntactical Specification

The syntax specification may be used for the population of valid TDM TerminationID structures for ETSI ES 283 024.

ABNF (IETF RFC 4234) is used for the syntax specification.

pathName = TDMToken SLASH (PCMsystem / "*")

TDMToken = "tdm"

PCMsystem = 0*(HierarchyLevelHIGHToken SLASH) HierarchyLevelLOWToken

HierarchyLevelHIGHToken = (UnitTypeToken "_" UnitNumber)

HierarchyLevelLOWToken  = (UnitTypeToken "_" Wildcard) / Channel / Wildcard

UnitTypeToken = "ChassisToken" / "SDHToken" / "SONETToken" / "PDHToken"

ChassisToken  = "s" / "su" 		; slot, sub-unit within slot

SDHToken      = "stm4" / "stm1" 	; relevant is capacity, but not
 									  electrical or optical interface type

SONETToken    = "oc12" / "oc3"

PDHToken      = "ds3" / "e3" / "ds2" / "e2" /"ds1" / "e1" 	; ANSI & ETSI

UnitNumber = 1*DIGIT

Channel    = %d0-31 / %d0-23	; value range E1/T1 system

Wildcard   = "*"

###### A.6.1.2.1.1	Wildcarding

Wildcarding (CHOOSE, ALL) is allowed for number fields ("<unit #>").

Examples for wildcarding:

1.	TDM Terminations at SDH STM-1 ports:

e.g., wildcarding on top level: 	tdm/*

e.g., wildcarding on slot level: 	tdm/s_3/*

e.g., wildcarding on STM-1 level: 	tdm/s_3/stm1_4/*

e.g., wildcarding on E1 level: 	tdm/s_2/stm1_4/e1_49/*

2.	TDM Terminations at PDH E1 ports:

e.g., wildcarding on E1 level: 	tdm/s_1/e1_2/*

###### A.6.1.2.1.2	Heterogeneous TDM Port Configurations

An homogeneous TDM port configuration relates to a MGW with a single port type for physical Terminations. There is therefore a single TDM Termination name structure in use.

Heterogeneous TDM configurations means different port types, either by different signal hierarchies, like SDH/STM-1 and SDH/STM-4, and/or a mix of SDH and PDH interfaces. The number of port types in use is determining the number of TDM Termination name structures. With heterogeneous configurations the TDM Termination name structure may be aligned, for instance, by using the "highest common digital signal hierarchy" as highest Termination name hierarchical level. There is consequently a single TDM Termination name structure with a "flattened" hierarchy.

Example:

MGW with SDH/STM-1 and PDH/E1 ports. Common denominator is "e1", a selected TDM Termination name might be therefore a common two-level structure with "tdm/e1_<E1 ID>/<channel #>". The unit types "s", "su" or "stm1" are not used here.

NOTE: This concept is followed in A.6.1.1,  ASN.1 for TDM Terminations.

##### A.6.1.2.2	Termination Naming Convention for IMS/NGN Terminations

ephemeral/<string of alphanumeric characters or "/">

e.g., Ephemeral/1/0/40000

###### A.6.1.2.2.1	Syntactical Specification

The syntax rules may be used for the population of valid ephemeral TerminationID structures for TISPAN TGW (ETSI ES 283 024 [yz]).

ABNF (IETF RFC 4234) is used for the syntax specification.

ABNF coding:

pathName = EphToken SLASH EPHsystem

EphToken = "Ephemeral" ; so called prefix

; The maximum length of 'pathname' is defined in Annex B.2/H.248.1.

EPHsystem = 0*(HierarchyLevelHIGHToken SLASH) HierarchyLevelLOWToken

HierarchyLevelHIGHToken = 1*alphanum

HierarchyLevelLOWToken  = Individual / Wildcard

alphanum   = ALPHA / DIGIT

Individual = 1*DIGIT

Wildcard   = "$" / "*"

### A.6.2	Multiplexed terminations

Table A.6.2: Multiplexed terminations

| MultiplexTerminations Supported | No |
| --- | --- |

## A.7	Descriptors

### A.7.1	Stream Descriptor

Table A.7.1: Stream descriptors

| Maximum number of streams per termination type | 1 |
| --- | --- |

#### A.7.1.1	Local Control Descriptor

Table A.7.1.1/1: Local Control Descriptor

|  | Termination Type | Stream Type |
| --- | --- | --- |
| Reserve group used: | No |  |  |
| Reserve value used: | Yes (NOTE1) | Terminations Toward IMS | Not Applicable |
| NOTE1: The “Reserve value” parameter is, inter alia, required for negotiation of multiple payload types, ie ITU-T Rec. G.711, comfort noise (according ITU-T Rec. G.711 Appendix II), DTMF tone relay (see RFC2833 [18]). |

Table A.7.1.1/2: Allowed Stream Modes

| Termination Type | Stream Type | Allowed StreamMode Values |
| --- | --- | --- |
| TDM | Not Applicable | SendOnly, RecvOnly, SendRecv, Inactive |
| IMS | Not Applicable | SendOnly, RecvOnly, SendRecv, Inactive |
| BICC IP | Not Applicable | SendOnly, RecvOnly, SendRecv, Inactive |
| BICC ATM | Not Applicable | SendOnly, RecvOnly, SendRecv, Inactive |

### A.7.2	Events Descriptor

Table A.7.2/1: Events Descriptor

| Events settable on termination types and stream types: | Yes |
| --- | --- |
|  | Event ID | Termination Type | Stream Type |
|  | Detect_Digit(Digit) (d0 to dd, inclusive) | ALL | Not Applicable |
|  | BNC Established | Terminations towards BICC network | Not Applicable |
|  | BNC Modification Failed | Terminations towards BICC network | Not Applicable |
|  | BNC Modified | Terminations towards BICC network | Not Applicable |
|  | BNC Release | Terminations towards BICC network | Not Applicable |
|  | Tunnel | Terminations towards BICC network with IP transport | Not Applicable |
|  | g/cause | ALL except ROOT | Not Applicable |
|  | g/sc | ALL except ROOT | Not Applicable |
|  | ct/cmp | TDM | Not Applicable |
|  | chp/mgcon | ROOT | Not Applicable |
|  | Hangterm/thb | ALL | Not Applicable |
|  | ocp/mg_overload | ROOT | Not Applicable |
|  | it/ito | ROOT | Not Applicable |
| NOTE: Events for Terminations towards BICC network dependent on option to support such interworking, e.g. not required for TISPAN NGN R1 TMGW. |

Table A.7.2/2: Event Buffer Control

| Event Buffer Control used: | No |
| --- | --- |

Table A.7.2/3: Keep active

| Keepactive used on events: | Yes |
| --- | --- |
| NOTE: Not required by TISPAN NGN R1 TMGW. |

Table A.7.2/4: Embedded events

| Embedded events in an event descriptor: | No |
| --- | --- |

Table A.7.2/5: Embedded signals

| Embedded signals in an event descriptor: | No |
| --- | --- |

### A.7.3	EventBuffer Descriptor

Table A.7.3: Event Buffer Descriptor

| Event Buffer descriptor used: | No |
| --- | --- |

### A.7.4	Signals Descriptor

Table A.7.4/1: Signals Descriptor

| Signals settable dependant on termination or streams types: | Yes NOTE: “Yes” means any signal not listed below may be played on any termination or stream, except Signals on ROOT termination shall not be supported. |
| --- | --- |
| If yes | Signal ID | Termination Type | Stream Type / ID |
|  | ct/* | TDM | Not Applicable |
|  | gb/* | BICC | Not Applicable |
|  | bt/* | BICC IP | Not Applicable |
|  | cg/rt cg/bt cg/ct | TDM | Not Applicable |
|  | an/apf | ALL except ROOT | Not Applicable |

Editors Note: Further contributions may be required to add tones from other packages.

Table A.7.4/2: Signal Lists

| Signals Lists supported: | Yes |
| --- | --- |
| If yes | Termination Type Supporting Lists: | ALL |
|  | Stream Type Supporting lists: | ALL |
|  | Maximum number of signals to a signal list: | FFS<integer> |
|  | Intersignal delay parameter supported: | FFS<Yes/No> |
| NOTE: Not required for TISPAN NGN R1 TMGW. |

Table A.7.4/3: Overriding Signal type and duration

| Signal type and duration supported: | Optional |
| --- | --- |
| NOTE: Not required for TISPAN NGN R1 TMGW. |

Table A.7.4/4: Notify completion

| Notify completion supported: | Yes |
| --- | --- |
| If yes | SignalID | Type of completion supported |
|  | an/apf | TO, EV, SD and NC |
| RequestID Parameter Supported: | NO |
| NOTE: Not required for TISPAN NGN R1 TMGW. |

Table A.7.4/5: Signals played simultaneously

| Signals played simultaneously: | No |
| --- | --- |

Table A.7.6/6: Keep active

| Keepactive used on signals: | Yes |
| --- | --- |
| NOTE: Not required for TISPAN NGN R1 TMGW. |

### A.7.5	DigitMap Descriptor

Table A.7.5: DigitMap Descriptor

| Digit Maps supported: | No |
| --- | --- |

### A.7.6	Statistics Descriptor

Table A.7.6: Statistics Descriptor

| Statistics reported on subtract: | No (for TDM Terminations) |
| --- | --- |
|  | Optional For Ephemeral Terminations (NOTE) |
| NOTE: This is required for TISPAN NGN R1 TMGW |

### A.7.7	ObservedEvents Descriptor

Table A.7.7: Observed Events Descriptor

| Event detection time supported: | No |
| --- | --- |

### A.7.8	Topology Descriptor

Table A.7.8: Topology Descriptor

| Allowed triples: | Optional (ALL) (NOTE) |
| --- | --- |
| NOTE: If not supported then error code 444 shall be returned. |

### A.7.9	Error Descriptor

Table A.7.9/1: Error Codes Sent by MGCF

| Supported H.248.8 Error Codes: | FFS < list of individual numbers> |
| --- | --- |
| Supported Error Codes defined in packages: | All error codes defined in supported packages shall be supported. |

Table A.7.9/2: Error Codes Sent by MGW:

| Supported H.248.8 Error Codes: | FFS< list of individual numbers> |
| --- | --- |
| Supported Error Codes defined in packages: | All error codes defined in supported packages shall be supported. |

## A.8	Command API

### A.8.1	Add

Table A.8.1/1: Descriptors used by Command Add Request

| Descriptors used by Add Request: | Events, Signals, Media (LocalControl, Local And Remote), Error, Audit, Topology |
| --- | --- |

Table A.8.1/2: Descriptors used by Command Add Reply

| Descriptors used by Add Reply: | Events, Signals, Media (LocalControl, Local And Remote), Error, Audit, Topology When command request excludes an Audit Descriptor, the MGW response shall only include descriptors which contained underspecified or overspecified properties in the command request, with the exception of the Error Descriptor. Furthermore, only those properties that were underspecified or overspecified in the request shall be sent in the reply. |
| --- | --- |

### A.8.2	Modify

Table A.8.2/1: Descriptors used by Command Modify Request

| Descriptors used by Modify Request: | Events, Signals, Media (LocalControl, Local And Remote), Error, Audit, Topology |
| --- | --- |

Table A.8.2/2: Descriptors used by Command Modify Reply

| Descriptors used by Modify Reply: | Events, Signals, Media (LocalControl, Local And Remote), Error, Audit, Topology When command request excludes an Audit Descriptor, the MGW response shall only include descriptors which contained underspecified or overspecified properties in the command request, with the exception of the Error Descriptor. Furthermore, only those properties that were underspecified or overspecified in the request shall be sent in the reply. |
| --- | --- |

### A.8.3	Subtract

Table A.8.3/1: Descriptor used by Command Subtract Request

| Descriptors used by Subtract Request: | AUDIT (empty) or NONE |
| --- | --- |

Table A.8.3/2: Descriptor used by Command Subtract Reply

| Descriptors used by Subtract Reply: | None or Statistics When command request contains "Audit(empty)", then no statistics are returned. Otherwise, connection statistics are returned in the Subtract reply dependent on the supported packages (see clause A.14). |
| --- | --- |

### A.8.4	Move

Table A.8.4/1: Command Move

| Move command used: | Optional(NOTE) |
| --- | --- |
| NOTE: If not supported then error code 443 shall be returned. |

Table A.8.4/2: Descriptors used by Move Request

| Descriptors used by Move Request: | Events, Signals, Media (LocalControl, Local And Remote), Error, Audit, Topology |
| --- | --- |

Table A.8.4/3: Descriptors used by Move Reply

| Descriptors used by Move Reply | Events, Signals, Media (LocalControl, Local And Remote), Error, Audit, Topology |
| --- | --- |

### A.8.5	Auditvalue

Table A.8.5: Auditvalue

| Audited Properties: | Property Name and Identity | Descriptor |
| --- | --- | --- |
| Termination ID | TerminationState: - TDM: ALL (indicating 1 TDM group) - ATM/IP: individual termination The ServiceState property within the TerminationState descriptor shall not take the value "Test". | TerminationState Descriptor |
| Termination ID | For Packages: - Root - TDM/ATM/IP: individual terminaition (NOTE1) | Packages Descriptor |
| Audited Statistics: | None |
| Audited Signals: | None |
| Audited Events: | None |
| Packages Audit Possible | Yes |
| NOTE1: The purpose to audit an individual Termination is to retrieve MGC Information if supported. |

### A.8.6	Auditcapabilities

Table A.8.6: Auditcapabilities

| Audited Properties: | Property Name and Identity | Descriptor |
| --- | --- | --- |
|  | FFS | FFS |
| Audited Statistics: | None |
| Audited Signals: | None |
| Audited Events: | None |
| NOTE: AuditCapabilities command is not supported by the ETSI TISPAN profile. |

### A.8.7	Notify

Table A.8.7: Descriptors Used Notify

| Descriptors used by Notify Request or Reply: | ObservedEvents, Error |
| --- | --- |

### A.8.8	Service Change

Table A.8.8/1: Service Change Methods and Reasons Sent By MGCF

| ServiceChange Methods supported: | ServiceChange Reasons supported: |
| --- | --- |
| Graceful, Forced, Restart, Handoff(not involving more than 1 MGCF – see NOTE1) When a Service Change command on the Root termination with a method other than Graceful is sent, the command shall always be sent as the only command in a message. The sending node shall always wait for the reply to a Service Change command on the Root termination with a method other than Graceful before sending further command requests. A Service Change command on the Root termination with method Graceful may be combined with other commands in a single message. | 900-910, 913-917 |
| NOTE 1: No support of handoff relates to a network deployment scenario with “primary H.248 systems only”, which translates to no geographic redundancy of the MGCF. |

Table A.8.8/2: Service Change Methods and Reasons Sent By MGW

| ServiceChange Methods supported: | ServiceChange Reasons supported: |
| --- | --- |
| Graceful, Forced, Restart, Disconnected, Handoff(not involving more than 1 MGW – see NOTE1), Failover (except for ‘MG impending failure’) When a Service Change command on the Root termination with a method other than Graceful is sent, the command shall always be sent as the only command in a message. The sending node shall always wait for the reply to a Service Change command on the Root termination with a method other than Graceful before sending further command requests. A Service Change command on the Root termination with method Graceful may be combined with other commands in a single message. | 900-910, 913-917 |
| NOTE: No support of handoff relates to a network deployment scenario with “primary H.248 systems only”, which translates to no geographic redundancy of the MGCF. |

Table A.8.8/3: Service Change Address

| ServiceChangeAddress used: | No |
| --- | --- |

Table A.8.8/4: Service Change Delay

| ServiceChangeDelay used: | No |
| --- | --- |

Table A.8.8/5: Service Change Incomplete Flag

| ServiceChange Incomplete Flag used: | No |
| --- | --- |

Table A.8.8/6: Service Change Version

| Version used in ServiceChangeVersion: | 2 |
| --- | --- |

Table A.8.8/7: Profile negotiation

| Profile negotiation as per H.248.18: | No |
| --- | --- |

### A.8.9	Manipulating and auditing context attributes

Table A.8.8: Manipulating and auditing context attributes

| Context Attributes Manipulated: | Topology (Optional) |
| --- | --- |
| Context Attributes Audited: | None |

## A.9	Generic command syntax and encoding

Table A.9: Encodings

| Supported Encodings: | Binary (optional) Text (optional) (NOTE) : The receiver shall support: Short Token Notation Long Token Notation |
| --- | --- |
| NOTE: Text encoding is required by TISPAN NGN R1 TMGW. |

## A.10	Transactions

Table A.10/1: Transactions per Message

| Maximum number of TransactionRequests / TransactionReplies / TransResponseAcks / Segment Replies per message: | 2 |
| --- | --- |

Table A.10/2: Commands per Transaction Requests

| Maximum number of commands per Transaction request: | 2(NOTE1) TBD(NOTE2) |
| --- | --- |
| NOTE1: Maximum required by TISPAN NGN R1 NOTE2: Maximum required by 3GPP |

Table A.10/3: Commands per Transaction Reply

| Maximum number of commands per Transaction reply: | 2 (NOTE1) TBD (NOTE2) |
| --- | --- |
| NOTE1: Maximum required by TISPAN NGN R1 NOTE2: Maximum required by 3GPP |

Table A.10/4: Optional Commands

| Commands able to be marked "Optional": | AuditValue |
| --- | --- |

Table A.10/5: Transaction Timers

| Transaction Timer: | Value |
| --- | --- |
| normalMGExecutionTime | Provisioned |
| normalMGCExecutionTime | Provisioned |
| MGOriginatedPendingLimit | Provisioned |
| MGCOriginatedPendingLimit | Provisioned |
| MGProvisionalResponseTimerValue | Provisioned |
| MGCProvisionalResponseTimerValue | Provisioned |

## A.11	Messages

It is recommended that MGC and MG names are in the form of fully qualified domain names.  For example the domain name of the MGC may be of the form mgc1.whatever.net and the name of the MG may be of the form mg1.whatever.net.

The fully qualified domain name will be used by the MGC and MG as part of the "Message Identifier" in the H.248 messages which identifies the originator of the message.

## A.12	Transport

Table A.12/1: Transport

| Supported Transports: | SCTP(recommended) (NOTE1). SCTP/M3UA(optional) optional – as defined in IETF RFC 3332 [6] with options detailed in 3GPP TS 29.202 [7] (NOTE2). UDP(optional). |
| --- | --- |
| NOTE 1 ( H.248 is “SCTP user” in this case of H.248/SCTP/IP based transport according ITU-T Rec. H.248.4. The number of used SCTP Streams for traffic of the H.248 Control Association must be defined, see § 8/H.248.4. A single SCTP Stream is the default assumption (“Single-Stream Mode”) in this Profile. NOTE 2 ( This is slightly different with regards to SCTP encapsulation. H.248 is “M3UA user” in this case of H.248/M3UA/SCTP/IP based transport. H.248 Messages are corresponding to M3UA user protocol data units. “SCTP multistreaming” may be also applied (see § 1.4.7/RFC 3332). If not then the complete M3UA traffic is mapped on a single SCTP Stream, i.e., the Single-Stream Mode. |

Table A.12/2: Segmentation

| Segmentation Supported: | No |
| --- | --- |

Table A.12/3: Support of Control Association Monitoring

| Control Association Monitoring Supported: | Monitoring mechanism is dependent on used H.248 transport (see Table A.12/1): SCTP: inherent capability of SCTP (NOTE) SCTP/M3UA: inherent capability of SCTP UDP: H.248.14 (MGW-driven monitoring) Empty AuditValue on ROOT (MGC-driven monitoring) |
| --- | --- |
| NOTE: Use of H.248.14 for this is FFS |

## A.13	Security

Table A.13: Security

| Supported Security: | None |
| --- | --- |

## A.14	 Packages

Table A.14/1: Mandatory packages

| Package Name | Package ID | Version |
| --- | --- | --- |
| Generic (see ITU-T Recommendation H.248.1 [9] Annex E.1); | g, (0x0001) | v1 |
| Base Root Package (see ITU-T Recommendation H.248.1 [9] Annex E.2); | root, (0x0002) | v2 |
| Tone Detection Package (see ITU-T Recommendation H.248.1 [9] Annex E.4); | tonegen, (0x0002) This package is “extension only”. It must be supported if extended but shall not be published over the protocol. It is here for information only. | v1 |
| Basic DTMF Generator Package (see ITU-T Recommendation H.248.1 [9] Annex E.5); Only the DTMF Signal Ids shall be used, not the Tone Ids within the PlayTone Signal Id. NOTE1 | dg, (0x0005) | v1 |
| DTMF Detection Package (see ITU-T Recommendation H.248.1 [9] Annex E.6); NOTE1 | dd, (0x0006) | v1 |
| TDM Circuit Package (see ITU-T Recommendation H.248.1 [9] Annex E.13); | tdmc, (0x000d) | v1 |
| Media Gateway Resource Congestion Handling Package (see ITU-T Recommendation H.248.10 [12]). | chp, (0x0051) | v1 |
| Basic Continuity Package (see ITU-T Recommendation H.248.1 [9] Annex E.10); | ct, (0x000a) Only required for TDM side terminations. | v1 |
| NOTE1: This package may not be required for TISPAN NGN R1TMGW. |

Table A.14/2: Optional packages

| Package Name | Package ID | Version | Support dependent on: |
| --- | --- | --- | --- |
| Generic Announcement Package (see ITU-T Recommendation H.248.7 [28]). Only Fixed Part is required. | an(0x001d) | v1 | 3GPP applications |
| Bearer Characteristics Package (see ITU-T Recommendation Q.1950 [23] annex A..3). | bcp (0x001e | V2 | Terminations Towards BICC |
| Generic Bearer Connection Package (see ITU-T Recommendation Q.1950 [23] annex A.6). | Gb, (0x0021) | v1 | Interworking with BICC |
| Tone Generator Package (see ITU-T Recommendation H.248.1 [9] Annex E.3); | tongen, (0x0003) | v1 | This package is “extension only”. It must be supported if extended but shall not be published over the protocol. It is here for information only. |
| Call Progress Tones Generator Package (see ITU-T Recommendation H.248.1 [10] annex E.7). | Cg, (0x0007) | v1 |  |
| Basic Call Progress Tones Generator with Directionality, (see ITU-T Recommendation Q.1950 [23] annex A.8). | bcg, (0x0023) | v1 | Services provided by network |
| Expanded Call Progress tones Generator Package (see ITU-T Recommendation Q.1950 [23] annex A.9). | xcg, (0x0024 | v1 | Services provided by network |
| Basic Services Tones Generation Package, (see ITU-T Recommendation Q.1950 [23] annex A.10). | srvtn, (0x0025) | v1 | Services provided by network |
| Bearer Control Tunnelling Package (see ITU-T Recommendation Q.1950 [23] annex A.7). | Bt, (0x0022) | v1 | Interworking with BICC and IP transport |
| Expanded Services Tones Generation Package (see ITU-T Recommendation Q.1950 [23] annex A.11). | xsrvtn, (0x0026) | v1 | Services provided by network |
| Intrusion Tones Generation Package (see ITU-T Recommendation Q.1950 [23] annex A.12). | Int, (0x0027) | v1 | Services provided by network |
| 3GUP package (see subclause 15.1.1 of 3GPP TS 29.232 [5]) | threegup, (0x002f) | v1 | Interworking with BICN PLMN |
| Modification of Link Characteristics Bearer Capability (see subclause 15.1.5 of 3GPP TS 29.232 [5]) | threegmlc, (0x0046) | v1 | Interworking with BICN PLMN with Codec Modification |
| Inactivity (see ITU-T Recommendation. H248.14 [xy]) | it | v1 | Only applicable for UDP transport. |
| Hanging Termination Detection package (see ITU-T Recommendation H.248.36 [27]). | hangterm (0x0098) | v1 |  |
| TFO package (see subclause 15.2.2 of 3GPP TS 29.232 [5]) |  | v2 |  |
| Media Gateway Overload Control Package (see ITU-T Recommendation H.248.11 [xx]). | ocp | v1 | NOTE2 |
| MGC Information (see ETSI TS 183 022 [xz]) | mgcinfo | v1 | This package may be supported as an operator option. For this Profile the information string shall be limited to 32 octets in length. NOTE2 |
| RTP (ITU-T Recommendation H248.1 [9] Annex E.12) (NOTE1) | rtp | V1 | Used for connection statistics NOTE2 |
| NOTE1: support of RTP Package does not require support of Network Package for the ETSI TISPAN TGW Profile. NOTE2: Only valid for ETSI TISPAN TGW Profile |

Table A.14/3: Package Provisioning Information

| Package Name | Property, Parameter, Signal, Event ID | Provisioned Value: |
| --- | --- | --- |
| Generic Announcement (H.248.7) | Fixed Announcement Play, AV | Provisioned |
| NOTE: This may not be required by TISPAN NGN R1 TMGW. |

### A.14.1 Generic Package

Table A.14.1: Package Usage Information For Generic Package

| Properties | Mandatory/ Optional | Used in command: | Supported Values: | Provisioned Value: |
| --- | --- | --- | --- | --- |
| None | - | - | - | - |
| Signals | Mandatory/ Optional | Used in command: | Duration Provisioned Value: |
| None | - | - | - |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
|  | - | - | - | - |
| Events | Mandatory/ Optional | Used in command: |
| Cause (g/cause. 0x0001/0x0001) | M | NOTIFY |
|  | Event Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | None | - | - | - |
|  | ObservedEvent Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | Generalcause | M | "NR" Normal Release (0x0001) "UR" Unavailable Resources (0x0002) "FT" Failure, Temporary (0x0003) "FP" Failure, Permanent (0x0004) "IW" Interworking Error (0x0005) "UN" Unsupported (0x0006) | Not Applicable |
| Events | Mandatory/ Optional | Used in command: |
| Signal Completion. (g/sc, 0x0001/0x0002) | M | NOTIFY |
|  | Event Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | None | - | - | - |
|  | ObservedEvent Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | Signal Identity | ? | “packagename ?” | - |
|  | Termination Method | ? | "TO" (0x0001) Signal timed out or otherwise completed on its own "EV" (0x0002) Interrupted by event "SD" (0x0003) Halted by new Signals descriptor "NC" (0x0004) Not completed, other cause | - |
|  | Signal List Id | ? | Integer | - |
| Statistics | Mandatory/ Optional | Used in command: | Supported Values: |
| None | - | - | - |
| Error Codes | Mandatory/ Optional |
| - | - |

### A.14.2 Base Root Package

Table A.14.2: Package Usage Information For Base Root Package

| Properties | Mandatory/ Optional | Used in command: | Supported Values: | Provisioned Value: |
| --- | --- | --- | --- | --- |
| root/maxNumberOfContexts | O | AuditValue | 1 and up | Not Applicable |
| root/maxTerminationPerContext | O | AuditValue | See A.4 | Not Applicable |
| root/normalMGExecutionTime | O | MOD | Integer | Operator Defined |
| root/normalMGCExecutionTime | O | MOD | Integer | Operator Defined |
| root/MGProvisionalResponseTimerValue | O | MOD | Integer(NormalMGExecutionTime + networkdelay) | Operator Defined |
| root/MGCProvisionalResponseTimerValue | O | MOD | Integer( NormalMGCExecutionTime + networkdelay) | Operator Defined |
| root/MGCOriginatedPendingLimit | O | MOD | Integer | Operator Defined |
| root/MGOriginatedPendingLimit | O | MOD | Integer | Operator Defined |
| Signals | Mandatory/ Optional | Used in command: | Duration Provisioned Value: |
| None | - | - | - |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
|  | - | - | - | - |
| Events | Mandatory/ Optional | Used in command: |
| None | - | - |
|  | Event Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | - | - | - | - |
|  | ObservedEvent Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | - | - | - | - |
| Statistics | Mandatory/ Optional | Used in command: | Supported Values: |
| None | - | - | - |
| Error Codes | Mandatory/ Optional |
| None | - |

### A.14.3 Basic DTMF Generator Package

Table A.14.3: Package Usage Information For Basic DTMF Generator Package

| Properties | Mandatory/ Optional | Used in command: | Supported Values: | Provisioned Value: |
| --- | --- | --- | --- | --- |
| None | - | - | - | - |
| Signals | Mandatory/ Optional | Used in command: | Duration Provisioned Value: |
| DTMF character 0 ,d0 DTMF character 1 d1 DTMF character 2 d2 DTMF character 3 d3 DTMF character 4 d4 DTMF character 5 d5 DTMF character 6 d6 DTMF character 7 d7 DTMF character 8 d8 DTMF character 9 d9 DTMF character * ds DTMF character # do DTMF character A da DTMF character B db DTMF character C dc DTMF character D dd | M | ADD, MOD, MOVE |  |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
|  | None | - | - | - |
| Events | Mandatory/ Optional | Used in command: |
| None | - | - |
|  | Event Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | - | - | - | - |
|  | ObservedEvent Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | - | - | - | - |
| Statistics | Mandatory/ Optional | Used in command: | Supported Values: |
| None | - | - | - |
| Error Codes | Mandatory/ Optional |
| None | - |

### A.14.4 Basic DTMF Detection Package

Table A.14.4: Package Usage Information For Basic DTMF Generator Package

| Properties | Mandatory/ Optional | Used in command: | Supported Values: | Provisioned Value: |
| --- | --- | --- | --- | --- |
| None | - | - | - | - |
| Signals | Mandatory/ Optional | Used in command: | Duration Provisioned Value: |
| None | - | - | - |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
|  | - | - | - | - |
| Events | Mandatory/ Optional | Used in command: |
| d0, "0" d1, "1" d2, "2" d3, "3" d4, "4" d5, "5" d6, "6" d7, "7" d8, "8" d9, "9" ds, "*" do, "#" da, "A" or "a" db, "B" or "b" dc, "C" or "c" dd, "D" or "d" | M | NOTIFY |
|  | Event Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | None | - | - | - |
|  | ObservedEvent Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | None | - | - | - |
| Statistics | Mandatory/ Optional | Used in command: | Supported Values: |
| None | - | - | - |
| Error Codes | Mandatory/ Optional |
| None | - |

### A.14.5 TDM Circuit Package

Table A.14.5: Package Usage Information For TDM Circuit Package

| Properties | Mandatory/ Optional | Used in command: | Supported Values: | Provisioned Value: |
| --- | --- | --- | --- | --- |
| Echo Cancellation, tdmc/ec | M | ADD, MOD, MOVE | ALL | Default=? |
| Gain Control, tdmc/gc | O | ADD, MOD, MOVE | Integer | Default=? |
| Signals | Mandatory/ Optional | Used in command: | Duration Provisioned Value: |
| None | - | - | - |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
|  | - | - | - | - |
| Events | Mandatory/ Optional | Used in command: |
| None | - | - |
|  | Event Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | - | - | - | - |
|  | ObservedEvent Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | - | - | - | - |
| Statistics | Mandatory/ Optional | Used in command: | Supported Values: |
| None | - | - | - |
| Error Codes | Mandatory/ Optional |
| None | - |

### A.14.6 MGW Congestion Package

Table A.14.6: Package Usage Information For Media Gateway Overload Control Package

| Properties | Mandatory/ Optional | Used in command: | Supported Values: | Provisioned Value: |
| --- | --- | --- | --- | --- |
| None | - | - | - | - |
| Signals | Mandatory/ Optional | Used in command: | Duration Provisioned Value: |
| None | - | - | - |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
|  | - | - | - | - |
| Events | Mandatory/ Optional | Used in command: |
| MG Congestion, chp/mgcon(0x0001) | M/ | MOD, NOTIFY |
|  | Event Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | None | - | - | - |
|  | ObservedEvent Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | Reduction (0x0001) | M | 0-100 | Not Applicable |
| Statistics | Mandatory/ Optional | Used in command: | Supported Values: |
| None | - | - | - |
| Error Codes | Mandatory/ Optional |
| None | - |

### A.14.7 Continuity Package

Table A.14.7: Package Usage Information For Basic Continuity Package

| Properties | Mandatory/ Optional | Used in command: | Supported Values: | Provisioned Value: |
| --- | --- | --- | --- | --- |
| None | - | - | - | - |
| Signals | Mandatory/ Optional | Used in command: | Duration Provisioned Value: |
| Continuity Test, ct/ct Respond, ct/rsp | M | ADD, MOD, MOVE | Default |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
|  | None | - | - | - |
| Events | Mandatory/ Optional | Used in command: |
| Completion, ct/cmp(0x0005) | M/ | NOTIFY |
|  | Event Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | None | - | - | - |
|  | ObservedEvent Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | result, res(0x0008) | M | success, failure | Not Applicable |
| Statistics | Mandatory/ Optional | Used in command: | Supported Values: |
| None | - | - | - |
| Error Codes | Mandatory/ Optional |
| None | - |

### A.14.8 Announcement Package

Table A.14.8: Package Usage Information For Announcement Package

| Properties | Mandatory/ Optional | Used in command: | Supported Values: | Provisioned Value: |
| --- | --- | --- | --- | --- |
| None | - | - | - | - |
| Signals | Mandatory/ Optional | Used in command: | Duration Provisioned Value: |
| Fixed Announcement Play, apf(0x0001) | M | ADD, MOD, MOVE | <Value / Not Applicable> |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
|  | Announcement name, an(0x0001) | M | enumeration | <Value / Not Applicable> |
|  | Number Of Cycles, noc(0x0002) | M | Any Integer | - |
|  | Announcement Variant, av(0x0003) | O | string | - |
|  | Announcement Direction, di(0x0004) | M | Internal, External | - |
| Events | Mandatory/ Optional | Used in command: |
| None | - | - |
|  | Event Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | - | - | - | - |
|  | ObservedEvent Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | - | - | - | - |
| Statistics | Mandatory/ Optional | Used in command: | Supported Values: |
| None | - | - | - |
| Error Codes | Mandatory/ Optional |
| None | - |

### A.14.9 Bearer Characteristics Package

Table A.14.9: Package Usage Information For Bearer Characteristics Package

| Properties | Mandatory/ Optional | Used in command: | Supported Values: | Provisioned Value: |
| --- | --- | --- | --- | --- |
| BNC Characteristics (BCP/BNCChar,0x001e/0x01) | M | ADD, MOD | AAL type 2 / IP/RTP | Not Applicable |
| Signals | Mandatory/ Optional | Used in command: | Duration Provisioned Value: |
| None | - | - | - |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
|  | - | - | - | - |
| Events | Mandatory/ Optional | Used in command: |
| None | - | - |
|  | Event Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | - | - | - | - |
|  | ObservedEvent Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | - | - | - | - |
| Statistics | Mandatory/ Optional | Used in command: | Supported Values: |
| None | - | - | - |
| Error Codes | Mandatory/ Optional |
| None | - |

### A.14.10 Generic Bearer Connection Package

Table A.14.10: Package Usage Information For Generic Bearer Connection Package

| Properties | Mandatory/ Optional | Used in command: | Supported Values: | Provisioned Value: |
| --- | --- | --- | --- | --- |
| None | - | - | - | - |
| Signals | Mandatory/ Optional | Used in command: | Duration Provisioned Value: |
| Establish BNC (GB/EstBNC,0x0021/0x01) | M | ADD, MOD | Not Applicable |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
|  | Not Applicable | - | - | Not Applicable |
| Modify BNC (GB/ModBNC,0x0021/0x02) | O | MOD | Not Applicable |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
|  | Not Applicable | - | - | Not Applicable |
| Release BNC (GB/RelBNC,0x0021/0x03) | O | MOD | Not Applicable |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
|  | General cause (Generalcause,0x01) | O | Normal Release/ Unavailable Resources/ Failure Temporary/ Failure Permanent/ Interworking Error/ Unsupported | Not Applicable |
|  | Failure Cause (Failurecause,0x02) | O | OCTET STRING | Not Applicable |
|  | Reset (Reset,0x03) | O | 0/ 1 | Not Applicable |
| Events | Mandatory/ Optional | Used in command: |
| BNC Change (GB/BNCChange,0x0021/0x01) | M | ADD, MOD,NOTIFY |
|  | Event Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | Type (Type ,0x01) | M | Bearer Established / Bearer Modified/ Bearer Mofification Failure | Not Applicable |
|  | ObservedEvent Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | Type (Type,0x01) | M/ | Bearer Established / Bearer Modified/ Bearer Mofification Failure | Not Applicable |
| Statistics | Mandatory/ Optional | Used in command: | Supported Values: |
| None |  |  |  |
| Error Codes | Mandatory/ Optional |
| None |  |

### A.14.11 Call Progress Tones Generator Package v1

Table A.14.11.1: Package Usage Information For Call Progress Tones Generator Package

| Properties | Mandatory/ Optional | Used in command: | Supported Values: | Provisioned Value: |
| --- | --- | --- | --- | --- |
| None | - | - | - | - |
| Signals | Mandatory/ Optional | Used in command: | Duration Provisioned Value: |
| Ringing Tone, cg/rt | M | MOD | Not Applicable |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
|  | - | - | - | - |
| Busy Tone, cg/bt | O | MOD | Not Applicable |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
|  | - | - | - | - |
| Congestion Tone, cg/ct | O | MOD | Not Applicable |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
|  | - | - | - | - |
|  | - | - | - | - |
| Events | Mandatory/ Optional | Used in command: |
| None | - | - |
|  | Event Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | - | - | - | - |
|  | ObservedEvent Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | - | - | - | - |
| Statistics | Mandatory/ Optional | Used in command: | Supported Values: |
| None | - | - | - |
| Error Codes | Mandatory/ Optional |
| None | - |

### A.14.12 Basic Call Progress Tones Generator with Directionality

Table A.14.12.1: Package Usage Information For Basic Call Progress Tones Generator with Directionality Package

| Properties | Mandatory/ Optional | Used in command: | Supported Values: | Provisioned Value: |
| --- | --- | --- | --- | --- |
| None | - |  |  |  |
| Signals | Mandatory/ Optional | Used in command: | Duration Provisioned Value: |
| Dial Tone (bcg/bdt, 0x0023/0x0040) Ringing Tone (bcg/brt,0x0023/0x0041) Busy Tone (bcg/bbt,0x0023/0x0042) Congestion Tone (bcg/bct,0x0023/0x0043) Special Information Tone (bcg/bsit,0x0023/0x0044) Warning Tone (bcg/bwt,0x0023/0x0045) Payphone Recognition Tone (bcg/bpt,0x0023/0x0046) Call Waiting Tone (bcg/bcw,0x0023/0x0047) Caller Waiting Tone (bcg/bcr, 0x0023/0x0048) Pay Tone (bcg/bpy, 0x0023/0x0049) | O | MOD | Value |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
|  | Tone Direction (btd, 0x0001) | M | Internal / External | Not Applicable |
| Events | Mandatory/ Optional | Used in command: |
| None | - | - |
|  | Event Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | - | - | - | - |
|  | ObservedEvent Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | - | - | - | - |
| Statistics | Mandatory/ Optional | Used in command: | Supported Values: |
| None | - | - | - |
| Error Codes | Mandatory/ Optional |
| None | - |

### A.14.13 Expanded Call Progress Tones Generator Package

Table A.14.13.1: Package Usage Information For Expanded Call Progress Tones Generator Package

| Properties | Mandatory/ Optional | Used in command: | Supported Values: | Provisioned Value: |
| --- | --- | --- | --- | --- |
| None | - | - | - | - |
| Signals | Mandatory/ Optional | Used in command: | Duration Provisioned Value: |
| Comfort Tone (xcg/cmft,0x0024/0x004a) Off-hook warning Tone (xcg/roh, 0x0024/0x004b) Negative Acknowledgement (xcg/nack,0x0024/0x004c) Vacant Number Tone (xcg/vac, 0x0024/0x004d) Special Conditions Dial Tone (xcg/spec,0x0024/0x004e) | O | MOD | Value |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
|  | Tone Direction (btd, 0x0001) | M | Internal / External | Not Applicable |
| Events | Mandatory/ Optional | Used in command: |
| None | - | - |
|  | Event Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | - | - | - | - |
|  | ObservedEvent Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | - | - | - | - |
| Statistics | Mandatory/ Optional | Used in command: | Supported Values: |
| None | - | - | - |
| Error Codes | Mandatory/ Optional |
| None | - |

### A.14.14 Basic Services Tones Generation Package

Table A.14.14.1: Package Usage Information For Basic Services Tones Generation Package

| Properties | Mandatory/ Optional | Used in command: | Supported Values: | Provisioned Value: |
| --- | --- | --- | --- | --- |
| None | - |  | - | - |
| Signals | Mandatory/ Optional | Used in command: | Duration Provisioned Value: |
| Recall Dial Tone (srvtn/rdt,0x0025/0x004f) Confirmation Tone (srvtn/conf,0x0025/0x0050) Held Tone (srvtn/ht,0x0025/0x0051) Message Waiting Tone (srvtn/mwt,0x0025/0x0052) | O | MOD | Value |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
|  | Tone Direction (btd, 0x0001) | M | Internal / External | Not Applicable |
| Events | Mandatory/ Optional | Used in command: |
| None | - | - |
|  | Event Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | - | - | - | - |
|  | ObservedEvent Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | - | - | - | - |
| Statistics | Mandatory/ Optional | Used in command: | Supported Values: |
| None | - | - | - |
| Error Codes | Mandatory/ Optional |
| None | - |

### A.14.15 Bearer Control Tunnelling Package

Table A.14.15.1: Package Usage Information For Bearer Control Tunnelling Package

| Properties | Mandatory/ Optional | Used in command: | Supported Values: | Provisioned Value: |
| --- | --- | --- | --- | --- |
| Tunneling Options (BT/TunOpt, 0x0022/0x01) | M | ADD, MOD | 1 /2 | Not Applicable |
| Signals | Mandatory/ Optional | Used in command: | Duration Provisioned Value: |
| Bearer Information Transport (BT/BIT, 0x0022/0x01) | M | ADD, MOD, MOVE, | Not Applicable |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
|  | Bearer Information Tunnel (BIT,0x01) | M | Octet String | Not Applicable |
| Events | Mandatory/ Optional | Used in command: |
| Tunnel Indication (BT/TIND. 0x0022/0x01) | M | ADD, MOD, MOVE, NOTIFY |
|  | Event Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | Not applicable | - | - | - |
|  | ObservedEvent Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | Bearer Information transport (BIT,0x01) | M | Octet String | Not Applicable |
| Statistics | Mandatory/ Optional | Used in command: | Supported Values: |
| None | - | - | - |
| Error Codes | Mandatory/ Optional |
| None | - |

### A.14.16 Expanded Services Tones Generation Package

Table A.14.16.1: Package Usage Information For Expanded Services Tones Generation Package

| Properties | Mandatory/ Optional | Used in command: | Supported Values: | Provisioned Value: |
| --- | --- | --- | --- | --- |
| None | - | - | - | - |
| Signals | Mandatory/ Optional | Used in command: | Duration Provisioned Value: |
| Call Transfer Dial Tone (xsrvtn/xferdt,0x0026/0x0053) Call Forward Tone (xsrvtn/cft,0x0026/0x0054) Credit Card service Tone (xsrvtn/ccst,0x0026/0x0055) Special Recall Dial Tone (xsrvtn/srdt,0x0026/0x0056) | O | MOD | Value |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
|  | Tone Direction (btd, 0x0001) | M | Internal / External | Not Applicable |
| Events | Mandatory/ Optional | Used in command: |
| None | - | - |
|  | Event Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | - | - | - | - |
|  | ObservedEvent Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | - | - | - | - |
| Statistics | Mandatory/ Optional | Used in command: | Supported Values: |
| None |  | - | - |
| Error Codes | Mandatory/ Optional |
| None | - |

### A.14.17 Intrusion Tones Generation Package

Table A.14.17.1: Package Usage Information For Intrusion Tones Generation Package

| Properties | Mandatory/ Optional | Used in command: | Supported Values: | Provisioned Value: |
| --- | --- | --- | --- | --- |
| None | - | - | - | - |
| Signals | Mandatory/ Optional | Used in command: | Duration Provisioned Value: |
| Intrusion Pending Tone (int/pend,0x0027/0x0057) Intrusion Tone (int/int,0x0027/0x0058) Intrusion Reminder Tone (int/rem,0x0027/0x0059) Toll Break-In Tone (int/tbi,0x0027/0x005a) Intrusion Queue Tone (int/intque,0x0027/0x005b) Busy Verification Tone (int/bv,0x0027/0x005c) | O | MOD | Value |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
|  | Tone Direction (btd, 0x0001) | M | Internal / External | Not Applicable |
| Events | Mandatory/ Optional | Used in command: |
| None | - | - |
|  | Event Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | - | - | - | - |
|  | ObservedEvent Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | - | - | - | - |
| Statistics | Mandatory/ Optional | Used in command: | Supported Values: |
| None | - | - | - |
| Error Codes | Mandatory/ Optional |
| None | - |

### A.14.18 3GUP Package

Table A.14.18.1: Package Usage Information For 3GUP Package

| Properties | Mandatory/ Optional | Used in command: | Supported Values: | Provisioned Value: |
| --- | --- | --- | --- | --- |
| UP Mode of operation (threegup/mode, 0x002f/0x0001) | M | ADD, MOD, MOVE | See 3GPP TS 29.232 | See 3GPP TS 29.232 |
| UP versions (threegup/ upversions, 0x002f/0x0002) | M | ADD, MOD, MOVE | See 3GPP TS 29.232 | See 3GPP TS 29.232 |
| Delivery of erroneous SDUs (threegup/ delerrsdu, 0x002f/0x0003) | M | ADD, MOD, MOVE | See 3GPP TS 29.232 | See 3GPP TS 29.232 |
| Interface (threegup/ interface, 0x002f/0x0004) | M | ADD, MOD, MOVE | See 3GPP TS 29.232 | See 3GPP TS 29.232 |
| Initialisation Direction (threegup/ initdir, 0x002f/0x0005) | M | ADD, MOD, MOVE | See 3GPP TS 29.232 | See 3GPP TS 29.232 |
| Signals | Mandatory/ Optional | Used in command: | Duration Provisioned Value: |
| None | - | - | - |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
|  | - | - | - | - |
| Events | Mandatory/ Optional | Used in command: |
| None | - | - |
|  | Event Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | - | - | - | - |
|  | ObservedEvent Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | - | - | - | - |
| Statistics | Mandatory/ Optional | Used in command: | Supported Values: |
| None | - | - | - |
| Error Codes | Mandatory/ Optional |
| None | - |

### A.14.19 Modification of Link Characteristics Bearer Capability

Table A.14.19.1: Package Usage Information For Modification of Link Characteristics Package

| Properties | Mandatory/ Optional | Used in command: | Supported Values: | Provisioned Value: |
| --- | --- | --- | --- | --- |
| None | - | - | - | - |
| Signals | Mandatory/ Optional | Used in command: | Duration Provisioned Value: |
| None | - | - | - |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
|  | - | - | - | - |
| Events | Mandatory/ Optional | Used in command: |
| Bearer Modification Support Event.( threegmlc/ mod_link_supp, 0x0046/0x0001) | M | ADD, MOD, NOTIFY |
|  | Event Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | None | - | - | - |
|  | ObservedEvent Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | None | - | - | - |
| Statistics | Mandatory/ Optional | Used in command: | Supported Values: |
| None | - | - | - |
| Error Codes | Mandatory/ Optional |
| None | - |

### A.14.20 Hanging Termination Detection Package

Table A.14.20.1: Package Usage Information For Hanging Termination Detection Package

| Properties | Mandatory/ Optional | Used in command: | Supported Values: | Provisioned Value: |
| --- | --- | --- | --- | --- |
| None |  |  |  |  |
| Signals | Mandatory/ Optional | Used in command: | Duration Provisioned Value: |
| None |  |  |  |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
| Events | Mandatory/ Optional | Used in command: |
| Termination Heartbeat | M | ADD, MOD, MOVE, AUDITVALUE |
|  | Event Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | Timer X | O | ALL | 0 (no heartbeat message) |
|  | ObservedEvent Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
| Statistics | Mandatory/ Optional | Used in command: | Supported Values: |
| None |  |  |  |
| Error Codes | Mandatory/ Optional |

### A.14.21 TFO package

Table A.14.19: Package Usage Information For TFO

| Properties | Mandatory/ Optional | Used in command: | Supported Values: | Provisioned Value: |
| --- | --- | --- | --- | --- |
| TFO Activity Control (threegtfoc /tfoenable, (0x0031/0x0001) | M | ADD, MOD, MOVE | See 3GPP TS 29.232 | See 3GPP TS 29.232 |
| TFO Codec List (threegtfoc / codeclist, (0x0031/0x0002) | O | ADD, MOD, MOVE | See 3GPP TS 29.232 | See 3GPP TS 29.232 |
| Signals | Mandatory/ Optional | Used in command: | Duration Provisioned Value: |
| None |  |  |  |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
| Events | Mandatory/ Optional | Used in command: |
| Optimal Codec Event (threegtfoc / codec_modify, (0x0031/0x0010) | O | NOTIFY |
|  | Event Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | None |  |  |  |
|  | ObservedEvent Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | Optimal Codec Type | M | See 3GPP TS 29.232 | See 3GPP TS 29.232 |
| Codec List Event (threegtfoc / distant codec_list, (0x0031/0x0012) | O | NOTIFY |
|  | Event Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | None |  |  |  |
|  | ObservedEvent Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | Distant Codec List | M | See 3GPP TS 29.232 | See 3GPP TS 29.232 |
| TFO Status Event (threegtfoc / TFO_status) (0x0031/0x0014) | O | NOTIFY |
|  | Event Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | None |  |  |  |
|  | ObservedEvent Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | TFO Status | M | See 3GPP TS 29.232 | See 3GPP TS 29.232 |
| Statistics | Mandatory/ Optional | Used in command: | Supported Values: |
| None |  |  |  |
| Error Codes | Mandatory/ Optional |

### A.14.22 Media Gateway Overload Control Package

Table A.14.xx: Media Gateway Overload Control Package

| Properties | Mandatory/ Optional | Used in command: | Supported Values: | Provisioned Value: |
| --- | --- | --- | --- | --- |
| None | ( | ( | ( | ( |
| Signals | Mandatory/ Optional | Used in command: | Duration Provisioned Value: |
| None | ( | ( | ( |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
|  | ( | ( | ( | ( |
| Events | Mandatory/ Optional | Used in command: |
| MG_Overload ocp/mg_overload | M | MOD, NOTIFY |
|  | Event Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | None | ( | ( | ( |
|  | ObservedEvent Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | None | ( | ( | ( |
| Statistics | Mandatory/ Optional | Used in command: | Supported Values: |
| None | ( | ( | ( |
| Error Codes | Mandatory/Optional |
| None | ( |

### A.14.23 Inactivity Timer Package

Table A.14.xy: Inactivity Timer Package

| Properties | Mandatory/ Optional | Used in command: | Supported Values: | Provisioned Value: |
| --- | --- | --- | --- | --- |
| None | - | - | - | - |
| Signals | Mandatory/ Optional | Used in command: | Duration Provisioned Value: |
| None | - | - | - |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
|  | - | - | - | - |
| Events | Mandatory/ Optional | Used in command: |
| Inactivity Timeout, it/ito | M | MOD, NOTIFY |
|  | Event Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | Maximum Inactivity Time, mit | M | Any integer | Unspecified |
|  | ObservedEvent Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | None | - | - | - |
| Statistics | Mandatory/ Optional | Used in command: | Supported Values: |
| None | - | - | - |
| Error Codes | Mandatory/ Optional |
| None | - |

### A.14.24 MGC Information Package

Table A.14.xz: MGC Information Package

| Properties | Mandatory/ Optional | Used in command: | Supported Values: | Provisioned Value: |
| --- | --- | --- | --- | --- |
| Data Block, MGCInfo/db | M | ADD, MOD, AUDITVALUE | A range of 0 to 32 octets | An empty string |
| Signals | Mandatory/ Optional | Used in command: | Duration Provisioned Value: |
| None | - | - | - |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
|  | - | - | - | - |
| Events | Mandatory/ Optional | Used in command: |
| None | - | - |
|  | Event Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | - | - | - | - |
|  | ObservedEvent Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | - | - | - | - |
| Statistics | Mandatory/ Optional | Used in command: | Supported Values: |
| None | - | - | - |
| Error Codes | Mandatory/ Optional |
| None | - |

### A.14.25 RTP Package

Table A.14.yz: RTP Package

| Properties | Mandatory/ Optional | Used in command: | Supported Values: | Provisioned Value: |
| --- | --- | --- | --- | --- |
| None | - | - | - | - |
| Signals | Mandatory/ Optional | Used in command: | Duration Provisioned Value: |
| None | - | - | - |
|  | Signal Parameters | Mandatory/ Optional | Supported Values: | Duration Provisioned Value: |
|  | - | - | - | - |
| Events | Mandatory/ Optional | Used in command: |
| Payload Transition, rtp/pltrans | - | NA |
|  | Event Parameters | Mandatory/Optional | Supported Values: | Provisioned Value: |
|  | None | - | - | - |
|  | ObservedEvent Parameters | Mandatory/ Optional | Supported Values: | Provisioned Value: |
|  | rtppayload, rtppltype | - | A valid encoding name | - |
| Statistics | Mandatory/ Optional | Used in command: | Supported Values: |
| Packets Sent, rtp/ps | M | SUBTRACT REPLY | ALL |
| Packets Received, rtp/pr | M | SUBTRACT REPLY | ALL |
| Packet Loss, rtp/pl | M | SUBTRACT REPLY | ALL |
| Jitter, rtp/jit | M | SUBTRACT REPLY | ALL |
| Delay, rtp/delay | M | SUBTRACT REPLY | ALL |
| Error Codes | Mandatory/ Optional |
| None | - |

## A.15	 Mandatory support of SDP and Annex C information elements

Table A.15: Supported Annex C and SDP information elements

| Information Element | Annex C Support | SDP Support |
| --- | --- | --- |
| v-line | "SDP_V " | The value must always be equal to zero: v=0. |
| m-line | "SDP_M " | <port> <transport> and <fmt-list> are required. Both static and dynamic payload types shall be supported. The MGC may underspecify the <fmt-list> subfield in place of a single dynamic payload type. In this case the mapping between the underspecified payload type and the <encoding name>/<clock rate> shall be provided in the rtpmap attribute. |
| c-line | "SDP_C " | <connection address> required The address type may be IPv4 or IPv6. The MGC will fully specify the IP version. The MGC may apply parameter underspecification to the <address type> subfield. (NOTE 2) |
| a-line | "SDP_A " | For a dynamic RTP payload type, for each codec information on the codec type shall be provided in a separate SDP "a=rtpmap "-line and possibly additional SDP "a=fmtp "-line(s). See Clause 10.2. |
| b-line | "SDP_B " | B:RS and b:RR bandwidth modifiers required Bandwidth information shall be supplied by the MGC if the required bandwidth cannot be immediately derived from the information contained in the m= line. If the MGC is using parameter underspecification, the MG shall assume a reasonable default bandwidth value for well-known codecs and shall provide this value in the response sent to the MGC. The Modifier field shall be set to “AS”. The Bandwidth Value field shall be set to the maximum bandwidth requirement of the media stream in kbit/s and shall take into account all headers down to the IP layer. The MGC may also supply additional RTCP bandwidth modifiers (i.e. RR and RS). If the RTCP modifiers are not supplied, the bandwidth value for the AS modifier shall take into account an extra 5% bandwidth for RTCP packets. |
| o-line | "SDP_O" | The origin line consists of 6 fields: o= <user name> <session ID> <version> <network type> <address type> <address>. The MGC is not required to supply this line but shall accept it. The MG should populate this line as follows or use the value received from the MGC: - <user name> should contain an hyphen - <session ID> and <version> should contain one or mode digits as described in RFC 2327 [x] - <network type> shall be set to IN - <address type> shall be set to IP4 or IP6 The Address Type shall be set to “IP4" or “IP6” depending on the addressing scheme used by the network to which the MG is connected. - <address> should contain the fully qualified domain name or IP address of the gateway. |
| s-line | "SDP_S" | The session name (s=) line contains a single field: s= <session-name>. The MGC is not required to supply a session name but shall accept one. This line may be used to convey correlation information for use in CDRs. The MG shall use an hyphen "-" as a session name or the value received from the MGC. |
| t-line | "SDP_T" | The time (t=) line consists of two fields: t= <start-time> <stop-time>. This line is ignored by both the MGC and the MG if received in local and remote descriptors. The MGC is not required to supply a time description but shall accept one. When supplied, this line shall be set to 0 0. |
| NOTE a: SDP or SDP_equivalents are only used for terminations towards the IM CN Subsystem. NOTE b: For BICC terminations, mandatory support of SDP and Annex C information elements shall be in accordance with the subclause "Mandatory Support of SDP and H.248.1 annex C information elements"(see clause 11). NOTE 1: b-line is optional in TISPAN NGN R1. NOTE 2: The address type may be IPv4 or IPv6. The default IP version (i.e. IPv4 or IPv6) may be provisioned in the H.248 MG. The MGC may apply H.248 parameter underspecification. If the MGC does require a different IP version than the provisioned default, then the MGC applies complete H.248 parameter specification. |

## A.16	 Optional support of SDP and Annex C information elements

Table A.16: Optional Supported Annex C and SDP information elements

| Information Element | Annex C Support | SDP Support |
| --- | --- | --- |

## A.17	Procedures

### A.17.1Call Independent Procedures

See clause 14.

### A.17.2 IMS Terminations Procedures

See clause 15.

### A.17.3 TDM Terminations Procedures

See clause 16.

### A.17.4 BICC Terminations Procedures

See clause 17.

Annex B (informative):
Change history

| Change history |
| --- |
| Date | TSG # | TSG Doc. | CR | Rev | Subject/Comment | Old | New |
| 2004-09 | CN#25 |  |  |  | Approved in CN#25 | 2.0.0 | 6.0.0 |
| 2005-03 | CN#27 | NP-050045 | 001 | 1 | Introduction Of Formal Profile | 6.0.0 | 6.1.0 |
|  |  |  | 002 | 1 | Corrections to Mn Specification |  |  |
| 2005-06 | CT#28 | CP-050208 | 0001 | 4 | Introduction Of Formal Profile | 6.1.0 | 6.2.0 |
|  |  | CP-050208 | 0005 |  | Inclusion of Insert Digit Procedure at IMS termination |  |  |
| 2005-09 | CT#29 | CP-050442 | 0007 | 3 | Alignment of Mn Profile with ITU template and Mc interface decisions | 6.2.0 | 6.3.0 |
|  |  | CP-050454 | 0008 | 3 | Alignment of Mn Profile with TISPAN TMGW | 6.3.0 | 7.0.0 |
| 2005-12 | CT#30 | CP-050630 | 0015 | 3 | Clean-up of hanging contexts and terminations | 7.0.0 | 7.1.0 |
|  |  | CP-050619 | 0017 | 1 | Addition of TFO procedure |  |  |
|  |  | CP-050630 | 0019 | 2 | Add virtual media gateway function |  |  |
|  |  | CP-050619 | 0022 |  | Alignment with TISPAN |  |  |
|  |  | CP-050619 | 0023 |  | Open Mn |  |  |
| 2006-03 | CT#31 | CP-060077 | 0024 | 1 | Add the UDPTL/TCPTL transport and mediatype for T.38 | 7.1.0 | 7.2.0 |
|  |  | CP-060077 | 0026 | 2 | Clarification the SDP used in the BICC termination |  |  |
|  |  | CP-060077 | 0028 |  | Remove the redundant symbols |  |  |
|  |  | CP-060066 | 0030 | 1 | Bearer Released Event to Reserve TDM Circuit procedure |  |  |
|  |  | CP-060066 | 0032 | 1 | BICC packages in Mn profile |  |  |
|  |  | CP-060066 | 0034 |  | Service Change Method “Disconnected” and “Failover” removal from Service Changes sent by MGCF |  |  |
| 2006-06 | CT#32 | CP-060314 | 0037 | 1 | Alignment with TISPAN TGW profile | 7.2.0 | 7.3.0 |
|  |  | CP-060306 | 0036 | 1 | Corrections to Mn Specification for Inter Vendor Operability |  |  |
|  |  |  | 0041 |  | Update of Mn profile with packages defined in 29.232 |  |  |
|  |  |  | 0044 | 1 | Adding of Bearer Released Event to Procedures related to a termination towards IM CN Subsystem |  |  |
|  |  |  | 0046 | 1 | Mode-change-period support on Mn interface |  |  |