INTERNATIONAL TELECOMMUNICATION UNION

| ITU-T | T.36 |
| --- | --- |
| TELECOMMUNICATION STANDARDIZATION SECTOR OF ITU | (07/97) |

SERIES T: TERMINALS FOR TELEMATIC SERVICES

Security capabilities for use with Group 3 facsimile terminals

ITU-T  Recommendation  T.36

(Previously  CCITT  Recommendation)

ITU-T  T-SERIES  RECOMMENDATIONS

TERMINALS FOR TELEMATIC SERVICES

For further details, please refer to ITU-T List of Recommendations.

ITU-T  RECOMMENDATION  T.36

SECURITY  CAPABILITIES  FOR  USE  WITH  GROUP  3  
FACSIMILE  TERMINALS

Summary

This Recommendation defines the two independent technical solutions which may be used in the context of secure facsimile transmission.  The two technical solutions are based upon the HKM/HFX40 algorithms and the RSA algorithm.

Annex A contains information regarding the HKM/HFX40 algorithms.

Annex B contains information regarding the RSA algorithm.

Annex C describes the use of the HKM system to provide secure key management capabilities for facsimile terminals.  The provision of the capabilities is described in terms of two main procedures:

–	the procedure for one way registration between entities X and Y (procREGxy); and

–	the procedure for the secure transmission of a secret key between entities X and Y (procSTKxy).

Annex D covers the procedures for the use of the HFX40 carrier cipher system to provide message confidentiality for facsimile terminals.

Annex E describes the HFX40-I hashing algorithm, in terms of its use, the necessary calculations and the information to be exchanged between the facsimile terminals to provide integrity for a transmitted facsimile message as either a selected or pre-programmed alternative to the encryption of the message.

Source

ITU-T Recommendation T.36 was prepared by ITU-T Study Group 8 (1997-2000) and was approved under the WTSC Resolution No. 1 procedure on the 2nd of July 1997.

FOREWORD

ITU (International Telecommunication Union) is the United Nations Specialized Agency in the field of telecommunications. The ITU Telecommunication Standardization Sector (ITU-T) is a permanent organ of the ITU. The ITU-T is responsible for studying technical, operating and tariff questions and issuing Recommendations on them with a view to standardizing telecommunications on a worldwide basis.

The World Telecommunication Standardization Conference (WTSC), which meets every four years, establishes the topics for study by the ITU-T Study Groups which, in their turn, produce Recommendations on these topics.

The approval of Recommendations by the Members of the ITU-T is covered by the procedure laid down in WTSC Resolution No. 1.

In some areas of information technology which fall within ITU-T's purview, the necessary standards are prepared on a collaborative basis with ISO and IEC.

NOTE

In this Recommendation, the expression "Administration" is used for conciseness to indicate both a telecommunication administration and a recognized operating agency.

INTELLECTUAL  PROPERTY  RIGHTS

The ITU draws attention to the possibility that the practice or implementation of this Recommendation may involve the use of a claimed Intellectual Property Right. The ITU takes no position concerning the evidence, validity or applicability of claimed Intellectual Property Rights, whether asserted by ITU members or others outside of the Recommendation development process.

As of the date of approval of this Recommendation, the ITU had/had not received notice of intellectual property, protected by patents, which may be required to implement this Recommendation. However, implementors are cautioned that this may not represent the latest information and are therefore strongly urged to consult the TSB patent database.

ã  ITU  1997

All rights reserved. No part of this publication may be reproduced or utilized in any form or by any means, electronic or mechanical, including photocopying and microfilm, without permission in writing from the ITU.

CONTENTS

Page

1	Scope		1

2	References		1

3	Abbreviations		1

Annex A – Procedures for secure Group 3 document facsimile transmission  using the HKM and HFX system		3

A.1	Introduction		3

A.2	Outline of the secure facsimile document procedure		3

Annex B – Security in facsimile G3 based on the RSA algorithm		4

B.1	Preamble		4

B.2	Introduction		4

B.3	References		4

B.4	Technical description		4

Annex C – Procedures for the use of the HKM key management system for secure document facsimile transmission		4

C.1	Scope		4

C.2	Conventions		5

C.2.1	General		5

C.2.2	Symbols		5

C.3	Description of the HKM algorithm for use with facsimile terminals		5

C.4	Registration mode		6

C.4.1	Procedure for the registration between entities X and Y (procREGxy)		6

C.4.2	Procedure for the registration between entities Y and X (procREGyx)		6

C.4.3	Procedure for registration in a single call		6

C.4.4	Authentication of registration		7

C.5	Secure mode  		8

C.5.1	Procedure for the secure transmission of SK from X to Y (procSTKxy)		8

C.5.2	Use of procSTKxy and procSTKyx in secure mode		8

C.5.3	Mutual authentication of X and Y		8

C.5.4	Secre session key establishment between X and Y		9

C.5.5	Confirmation of receipt		10

C.5.6	Confirmation or denial of integrity		10

C.6	The HKM algorithm 		11

C.6.1	Introduction		11

C.6.2	Stored information		11

C.6.3	Securely stored information		11

C.6.4	Registration mode		12

C.6.4.1	procREGxy using algebraic notation		12

C.6.4.2	Calculations at X to derive MPx		12

C.6.4.3	Calculations at X to derive TKx		13

C.6.4.4	Calculations at Y to recover MPx by decrypting TKx		14

C.6.4.5	Calculations at Y to derive RCNy		15

C.6.5	Secure mode		16

C.6.5.1	procSTKxy using algebraic notation		16

C.6.5.2	Calculations at X to re-create MPx		16

C.6.5.3	Calculations at X to form ESSKx using HKMD+1		17

C.6.5.4	Calculations at Y to recover SKx		18

C.6.6	The use of the HKM algorithm in secure mode		21

Page

Annex D – Procedures for the use of the HFX40 carrier cipher to provide message confidentiality for secure document facsimile transmission		21

D.1	Scope		21

D.2	Description of the HFX40 algorithm for use with facsimile terminals in secure mode		22

D.3	Example calculations for the HFX40 algorithm		22

D.3.1	Introduction		22

D.3.2	Stored information		23

D.3.3	Selection of the primes		23

D.3.4	Calculations using HFX40 to generate 3 PRSs		23

D.3.5	Use of the tables to encrypt the message and of the multiplexer to modify the tables.		24

Annex E – Procedures for the use of the HFX40-I hashing system to provide message integrity for secure document facsimile transmission		27

E.1	Scope		27

E.2	Use of the HFX40-I hashing system		27

E.3	The HFX40-I hashing system for use with facsimile terminals		28

E.3.1	Introduction		28

E.3.2	Stored information		28

E.3.3	Re-ordering of the system modulating prime numbers		28

E.3.4	Calculation of the primitives to be used with HFX40-I		29

E.3.5	Calculation of PH		30

E.3.6	First encryption (scrambling) of PH to form SH		30

E.3.7	Encryption of SH to form ESH		32

E.4	Use of the HKM Algorithm to produce a PseudoRandom Sequence		32

E.4.1	Introduction		32

E.4.1.1	Calculations using HKM to generate a PRS		34

Recommendation T.36

Recommendation T.36     (07/97)

SECURITY  CAPABILITIES  FOR  USE  WITH  GROUP  3  
FACSIMILE  TERMINALS

(Geneva, 1997)

1	Scope

This Recommendation defines the two independent technical solutions which may be used in the context of secure facsimile transmission:

·	a solution based on the HKM/HFX40 algorithms as described in Annex A and in Annex G/T.30;

·	a solution based on the RSA algorithm as described in Annex B and in Annex H/T.30.

2	References

The following ITU-T Recommendations and other references contain provisions which, through reference in this text, constitute provisions of this Recommendation. At the time of publication, the editions indicated were valid. All Recommendations and other references are subject to revision; all users of this Recommendation are therefore encouraged to investigate the possibility of applying the most recent edition of the Recommendations and other references listed below. A list of the currently valid ITU-T Recommendations is regularly published.

–	ITU-T Recommendation T.30 (1996), Procedures for document facsimile transmission in the general switched telephone network.

3	Abbreviations

This Recommendation uses the following abbreviations.

ASCII	American Standard Code for Information Interchange

B(n)	Base value (n)

ESH	Encrypted and Scrambled plain Hash (24 decimal digits)

ESIM	Encrypted Scrambled Integrity Message. A 12-decimal digit number

ESSK	Encrypted Scrambled Secret Key. A 12-decimal digit number

HKM	the HKM encryption algorithm

HKMD+1	double encryption using the HKM algorithm

IDx	Last six digits of the facsimile identification (facsimile telephone number) of X

IDy	Last six digits of the facsimile identification (facsimile telephone number) of Y

IM	Integrity Message used to confirm or deny integrity of the received message (12 decimal digits)

IMy	Integrity Message generated by Y to confirm or deny integrity of the received message. A 12-digit decimal number

ITU-T	International Telecommunication Union – Telecommunication Standardization Sector

mod n	modulo arithmetic using base n

MPx	Mutual Primitive of X. A 16-decimal digit number, only generatable by X. MPx is produced by X using the HKM algorithm with primitives formed from UINx, UCNx, IDx and IDy

MPy	Mutual Primitive of Y

OT	One-Time key. A 6- to 64-decimal digit number agreed by both users

OTx	One-Time key as first used by X in X's registration with Y

OTy	One-Time key as first used by Y, when Y initiates Y's registration with X to complete the mutual registration, whether it is different or identical to OTx

PH	Plain Hash of the message (24 decimal digits)

P(n)	Phase value (n)

Primitive	A 64-digit composite number formed from UIN and UCN

procREGxy	Procedure for registration between X and Y

procSTKxy	Procedure for the secure transmission of a secret key from X to Y

PRS	PseudoRandom Sequence

RCN	Registered Crypt Number. A 16-decimal digit number

RNCn	Non-secret random number associated with an SCn. A 4-decimal digit number

RNIM	Non-secret random number associated with an IM. A 4-decimal digit number

RNK	Non-secret random number used to provide variation of the primitives generated from MPx when encrypting an SK. A 4-decimal digit number

RNSRn	Non-secret random number associated with an SRn. A 4-decimal digit number

RNSSn	Non-secret random number associated with an SSn. A 4-decimal digit number

SCn	Secret Challenge key, number n. A 12-decimal digit number

SH	Scrambled plain Hash (24 decimal digits)

SK	A Secret Key which may be an SCn, SRn, SSn, etc. A 12-decimal digit number

SRn	Secret Response key, number n. A 12-decimal digit number

SS	Secret Session key used with the HFX40-I integrity algorithm (12 decimal digits)

SSK	Scrambled Secret Key. A 12-decimal digit number

SSn	Secret Session key, number n, to be used with the carrier cipher and/or hash. A 12-decimal digit number

SSx	Secret Session key generated by X to be used with the HFX40 cipher algorithm (12 decimal digits)

TKx	Transfer Key, an encryption of MPx generated by X. A 16-decimal digit number

UCN	Unique Crypt Number, e.g. UCNx, UCNy. A 16-decimal digit number known only to the system

UIN	Unique Identity Number, e.g. UINx, UINy. A 48-decimal digit number known only to the system

X	Name of one entity

x	Suffix identifying ownership or generation by X

XOR'd	Exclusively OR'd

Y	Name of a second entity

y	Suffix identifying ownership or generation by Y

Annex A

Procedures for secure Group 3 document facsimile transmission 
using the HKM and HFX system

A.1	Introduction

A.1.1	This Annex describes the procedures used by Group 3 document facsimile terminals to provide secure communications using the HKM and HFX systems.

A.1.2	Use of this Annex is optional.

A.1.3	The error correction defined in Annex A/T.30 or Annex C/T.30 (as appropriate) is mandatory.

A.2	Outline of the secure facsimile document procedure

A.2.1	The HKM and HFX systems provide the following capabilities for secure document communications between entities (terminals or terminal operators):

–	mutual entity authentication;

–	secret session key establishment;

–	document confidentiality;

–	confirmation of receipt;

–	confirmation or denial of document integrity.

A.2.2	Functions

Key management is provided using the HKM system defined in Annex C. Two procedures are defined: the first being registration and the second being the secure transmission of a secret key. Registration establishes mutual secrets and enables all subsequent transmissions to be provided securely. In subsequent transmissions, the HKM system provides mutual authentication, a secret session key for document confidentiality and integrity, confirmation of receipt and a confirmation or denial of document integrity.

Document confidentiality is provided using the carrier cipher defined in Annex D. The carrier cipher uses a 12-decimal digit key which is approximately equivalent to 40 bits.

Document integrity is provided using the system defined in Annex E. Annex E defines the hashing algorithm including the associated calculations and information exchange.

Annex B

Security in facsimile G3 based on the RSA algorithm

B.1	Preamble

(The preamble is left blank on purpose.)

B.2	Introduction

This Annex specifies the mechanisms to offer security features based on the RSA cryptographic mechanism.

B.3	References

–	ISO/IEC 9796:1991, Information technology – Security techniques – Digital signature scheme giving message recovery.

–	RIVEST (R.L.), SHAMIR (A.), ADLEMAN (L.): A method for obtaining digital signatures and public-key cryptosystems, Annex A: RSA, CACM (Communications of the ACM), Vol. 21, No. 2, pp.120-126, 1978.

–	2nd ISO/IEC CD 10118-3:1995, Information technology – Security techniques – Hash functions – Part 3: Dedicated hash-functions.

–	ISO/IEC JTC 1/SC 27 N1108:

·	SHA-1 (Secure Hash Algorithm), described in Secure Hash Standard, FIPS (Federal Information Processing Standard) PUB 180-1, April 1995, an algorithm which comes from the NIST (National Institute of Standardization) in USA.

·	MD-5 (RFC 1321).

–	ISO/IEC 9979:1991, Information technology – Security techniques – Procedures for the Registration of cryptographic algorithms.

B.4	Technical description

A full description of this solution is given in Annex H/T.30.

Annex C

Procedures for the use of the HKM key management system 
for secure document facsimile transmission

C.1	Scope

The purpose of this Annex is to define the HKM key management system to be used with facsimile terminals to enable the secure exchange of keys.

The HKM key management system is intended to be applicable for use with all types of dedicated facsimile terminals but is also equally applicable to computer-based facsimile systems.

This Annex describes the use of the HKM algorithm in two main procedures, procREGxy and procSTKxy to provide:

–	mutual authentication (described in C.5.3 and C.6.);

–	the use of a carrier cipher to provide message confidentiality (Annex D);

–	the use of a hash function to provide message integrity (Annex E);

–	the secure exchange of keys which may be challenge keys, response keys for authentication and session keys for message confidentiality or message integrity (described in C.5 and C.6).

An algebraic notation is developed to assist in the presentation of the key management protocols and procedures, see C.2.

The HKM system is based upon the use of 19 system prime numbers. These same 19 prime numbers are used also with the message cipher algorithm which is described in Annex D and the main message integrity hash algorithm which is described in Annex E. However, this Annex does not cover the message cipher algorithm nor the main message integrity hash algorithm.

Example calculations are given in C.6 and these can be used to verify the implementation of this Annex.

The HKM key management system is covered by intellectual property rights; however, the owner of those rights has agreed to follow the TSB code of practice. Further details can be obtained from the TSB.

C.2	Conventions

C.2.1	General

The algebraic notation detailed in C.2.2 is used to describe the key management protocols and procedures.

C.2.2	Symbols

[ ]	brackets the message
{ }	brackets the algorithm
( )	brackets the primitives
< >	brackets information to be stored
> <	brackets information to be retrieved from store
&	fusing or modifying, for example UCNx with IDx, without altering its length
RCNx>>>>>>	RCNx sent to Y
>>>>>> RCNx	receive RCNx from X
HKM+1	encryption using the HKM algorithm
HKM–1	decryption using the HKM algorithm
HKMD+1	double encryption using the HKM algorithm
HKMD–1	double decryption using the HKM algorithm

C.3	Description of the HKM algorithm for use with facsimile terminals

The HKM algorithm uses secret terminal-specific numbers and other user-specific variables to form primitives which, together with an encryption key, provide the input numbers for calculations using modular arithmetic. The secret numbers, UIN and UCN are stored securely in the facsimile terminal on manufacture or commissioning. There is no necessity to cross-reference them against any form of serial number.

The moduli for the modular arithmetic are provided from a set of 19 special prime numbers stored in the terminal.

The output of the modular arithmetical processes are long PRSs that are used to encrypt a message.

HKM is also used in an irreversible mode, that is, where an encryption process takes place, but where the inverse process cannot be performed.

The above features form the cryptographic basis for the two procedures, procREGxy and procSTKxy.

Details of the arithmetic and the special prime numbers are given in C.6.

C.4	Registration mode

C.4.1	Procedure for the registration between entities X and Y (procREGxy)

For X to register with Y, X generates an irreversible number by cryptographically combining UINx, and UCNx with IDx and IDy. The 16-digit number formed is MPx, which is used to encrypt and securely transfer keys as explained in the following subclauses.

In a secure environment outside the registration transmissions, the users agree an OT. The user at X selects registration mode and enters the facsimile identification (facsimile telephone number) of Y. IDx and IDy form the basis of the other primitives used by the algorithm. The user at X also enters OTx.

X uses OTx with HKM+1 to encrypt MPx to form TKx which is sent to Y. At Y, OTx is entered and is used with 
HKM–1 to decrypt TKx and to recover MPx.

Y does not store MPx but encrypts it immediately using HKM+1 with primitives formed from UINy and UCNy modified by IDx and IDy to form RCNy. Y sends RCNy to X to be stored. Y has no need to store RCNy, X will send it back openly to Y when X next initiates a secure transmission to Y.

The two terminals implicitly authenticate themselves since X is the only terminal that can create the MPx relating to Y, and Y is the only terminal that can recover the MPx from RCNy.

procREGxy can be shown using the algebraic notation:

| X | Y |
| --- | --- |
| > UINx, UCNx < | > UINy, UCNy < |
| MPx = (UINx, UCNx & IDx & IDy){HKM+1}[UCNx & IDx & IDy] TKx = (OTx){HKM+1}[MPx] TKx >>>>>> |
| >>>>>> TKx MPx = (OTx){HKM–1}[TKx] RCNy = (UINy, UCNy & IDx & IDy){HKM+1}[MPx] RCNy >>>>>> |
| >>>>>> RCNy <RCNy> |

A description and examples of all the calculations for procREGxy are given in C.6.4.

C.4.2	Procedure for the registration between entities Y and X (procREGyx)

To complete registration, Y carries out an identical procedure, procREGyx, with X which establishes MPy and RCNx. (OTy agreed by the users at Y, and X may be the same or different to OTx used during procREGxy.)

procREGyx can be represented using the algebraic notation:

| Y | X |
| --- | --- |
| >UINy, UCNy< | > UINx, UCNx < |
| MPy = (UINy, UCNy & IDy & IDx){HKM+1}[UCNy & IDy & IDx] TKy = (OTy){HKM+1}[MPy] TKy>>>>>> |
| >>>>>>TKy MPy = (OTy){HKM–1}[TKy] RCNx = (UINx, UCNx & IDy & IDx){HKM+1}[MPy] RCNx>>>>>> |
| >>>>>>RCNx <RCNx> |

C.4.3	Procedure for registration in a single call

The two separate registrations using procREGxy and procREGyx can be combined into a single call and is shown below using the algebraic notation. In this example, X initiates the call.

| X | Y |
| --- | --- |
| > UINx, UCNx < | >UINy, UCNy< |
| MPx = (UINx, UCNx & IDx & IDy) {HKM+1} [UCNx & IDx & IDy] TKx = (OTx) {HKM+1} [MPx] TKx >>>>>> |
| >>>>>> TKx MPx = (OTx) {HKM–1} [TKx] RCNy = (UINy, UCNy & IDx & IDy) {HKM+1} [MPx] |
|  | MPy = (UINy, UCNy & IDy & IDx){HKM+1}[UCNy & IDy & IDx] TKy = (OTy) {HKM+1} [Mpy] RCNy, TKy >>>>>> |
| >>>>>> RCNy, Tky < RCNy > MPy = (OTy) {HKM–1} [TKy] RCNx = (UINx, UCNx & IDy & IDx) {HKM+1} [MPy] RCNx >>>>>> |
| >>>>>> RCNx < RCNx > |

C.4.4	Authentication of registration

Authentication of registration is included in the procedures for the registrations between entities X and Y by providing challenge/response exchanges between X and Y. The challenge/responses use procSTKxy and procSTKyx as described in C.5.1. An example, within the procedure for two-way registration in a single call, is shown below using the algebraic notation.

| X | Y |
| --- | --- |
| >UINx, UCNx< MPx = (UINx, UCNx & IDx & IDy){HKM+1}[UCNx & IDx & IDy] TKx = (OTx){HKM+1}{MPx} | >UINy, UCNy< |
| <SC0x> by procSTKxy = ESSC0x TKx, RNC0x, ESSC0x>>>>>> |
| >>>>>TKx, RNC0x, ESSC0x |
|  | MPx = (OTx){HKM–1}[TKx] RCNy = (UINy, UCNy & IDx & IDy){HKM+1}[MPx] |
|  | MPy = (UINy, UCNy & IDy & IDx){HKM+1}[UCNy & IDy & IDx] TKy = (OTy){HKM+1}[MPy] |
|  | ESSC0x by procSTKxy = SC0x SC0x = SR0y SR0y by procSTKyx = ESSR0y |
|  | <SC0y> by procSTKyx = ESSC0y |
|  | RCNy, TKy, RNSR0y, ESSR0y, RNC0y, ESSC0y>>>>>> |
| >>>>>>RCNy, TKy, RNSR0y, ESSR0y, RNC0y, ESSC0y |
|  | <RCNy> |
|  | MPy = (OTy){HKM–1}[TKy] RCNx = (UINx, UCNx & IDy & IDx){HKM+1}[MPy] |
|  | ESSR0y by procSTKyx = SR0y Compare SR0y with <SC0y> |
|  | ESSC0y by STKyx = SC0y SC0y = SR0x SR0x by STKxy = ESSR0x |
|  | RCNx, RNSR0x, ESSR0x>>>>>> |

|  | >>>>>>RCNx, RNR0x, ESSR0x |
| --- | --- |
|  | <RCNx> |
|  | ESSR0x by procSTKxy = SR0x Compare SR0x with <SC0y> |

If challenge SC0x is equal to response SR0y and challenge SC0y is equal to response SR0x, mutual authentication of registration between X with Y is achieved.

C.5	Secure mode

Once registration of MPx and MPy has been established, the HKM algorithm is used to provide the means for secure communication of secret keys between X and Y. The secret keys may be SC, SR, or SS keys. The procedure, procSTKxy, used for this is described in the following subclauses.

C.5.1	Procedure for the secure transmission of SK from X to Y (procSTKxy)

SKx, a secret key to be securely communicated from X to Y is scrambled and encrypted using HKMD+1 to form ESSKx. The primitives used with HKMD+1 are generated from MPx and modified by RNKx. RNKx is sent openly to Y together with RCNy and ESSKx.

Y recovers MPx using RCNy and unscrambles and decrypts ESSKx using HKMD–1 to recover SKx. The primitives used with HKMD–1 are derived from MPx, modified by RNKx as at X.

procSTKxy can be represented using the algebraic notation:

| X | Y |
| --- | --- |
| > UINx, UCNx, RCNy < | > UINy, UCNy, RCNx < |
| MPx = (UINx, UCNx & IDx & IDy){HKM+1}[UCNx & IDx & IDy] ESSKx = (MPx & RNKx){HKMD+1}[SKx] RCNy, RNKx, ESSKx >>>>>> |
| >>>>>> RCNy, RNKx, ESSKx MPx = (UINy, UCNy & IDx & IDy){HKM–1}[RCNy] SKx = (MPx & RNKx){HKMD–1}[ESSKx] |

A description and examples of all the calculations for procSTKxy are given in C.6.5.

C.5.2	Use of procSTKxy and procSTKyx in secure mode

Once X and Y have completed registration all future transmissions can be made securely. The HKM algorithm is used in the secure mode to re-create MPx and MPy to enable the secure transfer of secret keys using procSTKxy and procSTKyx.

C.5.3	Mutual authentication of X and Y

In this context, X has initiated the call to send a secure message to Y.

At X

–	X enters the facsimile telephone number of Y;

–	X regenerates MPx, previously used in registration between X and Y;

–	X generates SC1x and RNC1x and stores SC1x;

–	X uses procSTKxy with MPx, RNC1x and SC1x to form ESSC1x;

–	X sends RCNy, RNC1x and ESSC1x to Y.

At Y

–	Y decrypts RCNy to form MPx;

–	Y uses procSTKxy with MPx, RNC1x and ESSC1x to recover SC1x;

–	Y regenerates MPy;

–	Y uses SC1x as the secret response key, SR1y, and generates RNSR1y;

–	Y uses procSTKyx with MPy, RNSR1y and SR1y to form ESSR1y;

–	Y generates SC1y and RNC1y and stores SC1y;

–	Y uses procSTKyx with MPy, RNC1y and SC1y to form ESSC1y;

–	Y sends RCNx, RNSR1y, ESSR1y, RNC1y and ESSC1y to X.

At X

–	X decrypts RCNx to form MPy;

–	X uses procSTKyx with MPy, RNSR1y and ESSR1y to form SR1y;

–	X compares SR1y with SC1x, if equal, then Y is authenticated to X;

–	X uses procSTKyx with MPy, RNC1y and ESSC1y to recover SC1y;

–	X uses SC1y as the secret response key, SR1x, and generates RNSR1x;

–	X uses procSTKxy with MPx, RNSR1x and SR1x to form ESSR1x;

–	X sends RNSR1x and ESSR1x to Y.

At Y

–	Y uses procSTKxy with MPx, RNSR1y and ESSR1x to recover SR1x;

–	Y compares SR1x with SC1y, if equal, then X is authenticated to Y.

At this point, X and Y have exchanged RCNx and RCNy and completed mutual/challenge-response exchanges. If SC1x is equal to SR1y and SC1y is equal to SR1x, mutual authentication is achieved.

The process of mutual authentication of X and Y can be represented using the algebraic notation:

| X | Y |
| --- | --- |
| > UINx, UCNx, RCNy < | > UINy, UCNy, RCNx < |
| < SC1x > by procSTKxy = ESSC1x RCNy, RNC1x, ESSC1x >>>>>> |
| >>>>>>RCNy, RNC1x, ESSC1x < RCNy > ESSC1x by procSTKxy = SC1x SC1x = SR1y SR1y by procSTKyx = ESSR1y < SC1y > by procSTKyx = ESSC1y RCNx, RNSR1y, ESSR1y, RNC1y, ESSC1y >>>>>> |
| >>>>>> RCNx, RNSR1y, ESSR1y, RNC1y, ESSC1y < RCNx > ESSR1y by procSTKyx = SR1y Compare SR1y with < SC1x > ESSC1y by procSTKyx = SC1y SC1y = SR1x SR1x by procSTKxy = ESSR1x RNSR1x, ESSR1x >>>>>> |
| >>>>>> RNSR1x, ESSR1x ESSR1x by procSTKxy = SR1x Compare SR1x with < SC1y > |

If challenge SC1x is equal to response SR1y and challenge SC1y is equal to response SR1x, mutual authentication is achieved.

C.5.4	Secret session key establishment between X and Y

In this context, X has initiated a call to send a secure message to Y and mutual authentication has been satisfactorily established as in C.5.3.

At X

–	X regenerates MPx previously used in registration between X and Y;

–	X generates SS1x and RNSS1x;

–	X uses procSTKxy with MPx, RNSS1x and SS1x to form ESSS1x;

–	X sends RCNy, RNSS1x and ESSS1x to Y.

At Y

–	Y decrypts RCNy to recover MPx;

–	Y uses procSTKxy with MPx, RNSS1x and ESSS1x to recover SS1x.

The process of secret session key establishment between X and Y can be shown using the algebraic notation:

| X | Y |
| --- | --- |
| < RCNy > | < RCNx > |
| SS1x by procSTKxy = ESSS1x RCNy, RNSS1x, ESSS1x >>>>>> |
| >>>>>> RCNy, RNSS1x, ESSS1x ESSS1x by procSTKxy = SS1x |

X and Y use SS1x with the carrier cipher, HFX40, to encrypt and decrypt the main message to provide confidentiality (Annex D) and/or with the hash algorithm, HFX40-I, to provide message integrity (Annex E) during transmission.

C.5.5	Confirmation of receipt

In this context, X initiated a call to send a secure message to Y, mutual authentication was established as in C.5.3, SS1x was securely exchanged as in C.5.4 and the message has been sent. At the end of the message, X sends SC2x to Y which Y uses as SR2y if the message was received intact.

At X

–	X regenerates MPx, previously used in registration between X and Y;

–	X generates SC2x and RNC2x and stores SC2x;

–	X uses procSTKxy with MPx, RNC2x and SC2x to form ESSC2x;

–	X sends RCNy, RNC2x and ESSC2x to Y.

At Y

–	Y decrypts RCNy to form MPx;

–	Y uses procSTKxy with MPx, RNC1x and ESSC2x to recover SC2x;

–	Y regenerates MPy;

–	Y uses SC2x as SR2y and generates RNSR2y;

–	Y uses procSTKyx with MPy, RNSR2y and SR2y to form ESSR2y;

–	Y sends RCNx, RNSR2y and ESSR2y to X.

At X

–	X decrypts RCNx to form MPy;

–	X uses procSTKyx with MPy, RNSR2y and ESSR2y to recover SR2y;

–	X compares SR2y with SC2x, if equal, then Y has confirmed receipt to X.

The process of confirmation of receipt can be represented using the algebraic notation:

| X | Y |
| --- | --- |
| > RCNy < | > RCNx < |
| < SC2x > by procSTKxy = ESSC2x RCNy, RNC2x, ESSC2x >>>>>> |
| >>>>>>RCNy, RNC2x, ESSC2x ESSC2x by procSTKxy = SC2x SC2x = SR2y SR2y by procSTKyx = ESSR2y RCNx, RNSR2y, ESSR2y >>>>>> |
| >>>>>> RCNx, RNSR2y, ESSR2y ESSR2y by procSTKyx = SR2y Compare SR2y with < SC2x > |

If SR2y, from Y equals SC2x stored by X, X accepts confirmation of receipt of the message by Y.

C.5.6	Confirmation or denial of integrity

In this context, X initiated a call to send a message to Y protected for integrity, mutual authentication has been satisfactorily established as in C.5.3, SSx has been securely exchanged as in C.5.4 and the message has either passed or failed Y's test for integrity (Annex E).

Y generates IMy to confirm or deny the integrity of the received message. IMy is a 12-digit random number selected from the digits 2 to 9. One digit is randomly selected to be replaced with a '1' to indicate confirmation of integrity or a '0' to indicate denial.

At Y

–	Y generates a 12-digit random number from the digits 2 to 9;

–	Y generates a random number between 1 and 12 to be the replacement pointer for the above random number;

–	Y changes the digit at the replacement point to either a '1' or a '0' to form IMy;

–	Y generates RNIMy;

–	Y uses procSTKyx with MPy, RNIMy and IMy to form ESIMy;

–	Y sends RCNx, RNIMy and ESIMy to X.

At X

–	X decrypts RCNx to form MPy;

–	X uses procSTKyx with MPy, RNIMy and ESIMy to recover IMy;

–	X checks if IMy contains a '1' or a '0' for confirmation or denial of integrity.

The process of confirmation of integrity can be represented using the algebraic notation:

| X | Y |
| --- | --- |
|  | > RCNx < |
|  | IMy by procSTKyx = ESIMy RCNx, RNIMy, ESIMy >>>>>> |
| >>>>>> RCNx, RNIMy, ESIMy ESIMy by procSTKyx = IMy Check IMy for a '1' or a '0' |

If the secret Integrity Message contains a '1', integrity is confirmed; if a '0', integrity is denied.

Example responses:

IMy = 257795199982	Integrity confirmed.

IMy = 317736845378	Integrity confirmed.

IMy = 738543680892	Integrity denied.

IMy = 457745204639	Integrity denied.

C.6	The HKM algorithm

C.6.1	Introduction

This subclause describes the HKM algorithm in terms of the numbers to be stored and the rules for the computations carried out using these numbers during the registration procedure, procREG, and the secure transmission of a key procedure, procSTK. The rules are best explained using numerical examples. The calculations using test values can be used to verify the implementation.

C.6.2	Stored information

All terminals are equipped with the same 19 system modulating prime numbers.

32603	32507	32183	32003	31847	31607	31583	31547	31259

31139	30803	30539	30467	30347	30323	30203	29879	29759	29663

The first nine numbers are used with the HKM algorithm for registration, authentication and other key management functions. All 19 numbers are used with the message confidentiality algorithm, Annex D, and with the message integrity algorithm, Annex E.

C.6.3	Securely stored information

Each terminal is equipped, by some suitable process, with two randomly generated decimal digit numbers, which are stored securely in the terminal. These are the 48-digit UIN and the 16-digit UCN. UIN and UCN are used with other identifying numbers to form the primitives for the HKM algorithm.

Test examples for X and Y are:

UINx	=	345092978336094172898029844342879120988727823781

UCNx	=	1333908734565521

UINy	=	973557693837783148353709167436722873449819767357

UCNy	=	7598247578649467

C.6.4	Registration mode

C.6.4.1	procREGxy using algebraic notation

| X | Y |
| --- | --- |
| >UINx, UCNx< | > UINy, UCNy < |
| MPx = (UINx, UCNx & IDx & IDy){HKM+1}[UCNx & IDx & IDy] TKx = (OTx){HKM+1}[MPx] TKx >>>>>> |
| >>>>>> TKx MPx = (OTx){HKM–1}[TKx] RCNy = (UINy, UCNy & IDx & IDy){HKM+1}[MPx] RCNy >>>>>> |
| >>>>>> RCNy <RCNy> |

The following subclauses use test values to show all the calculations used in procREGxy:

C.6.4.2	Calculations at X to derive MPx

MPx = (UINx, UCNx & IDx & IDy){HKM+1}[UCNx & IDx & IDy]

C.6.4.2.1	Preliminary calculations with the primitives (UINx, UCNx & IDx & IDy)

UINx	=	345092978336094172898029844342879120988727823781

UCNx	=	1333908734565521

IDx	=	642092

IDy	=	538249

A 64-digit Primitive is formed by concatenating UINx and UCNx.

Primitive = 3450929783360941728980298443428791209887278237811333908734565521

This primitive is split into two 32 digit numbers, 9 phase primitive values [P(0) to P(8)] are derived from the first number and 9 base primitive values [B(0) to B(8)] are derived from the second number. The phase values are derived by dividing the first number into 7 sets of 4 digits and 2 sets of 2 digits. The base values are derived in exactly the same way from the second number.

The phase primitive values are modified by adding incremental products of 101 and the base values are modified by adding incremental products of 79. The modification by 101 and 79 is used to ensure that modulation by the prime numbers starts as soon as possible.

Using the primitive = 3450929783360941728980298443428791209887278237811333908734565521, the phase and base primitive values are as shown below:

P(0)	3450 + (0 * 101) = 3450	B(0)	9120 + (0 * 79) = 9120

P(1)	9297 + (1 * 101) = 9398	B(1)	9887 + (1 * 79) = 9966

P(2)	8336 + (2 * 101) = 8538	B(2)	2782 + (2 * 79) = 2940

P(3)	  941 + (3 * 101) = 1244	B(3)	3781 + (3 * 79) = 4018

P(4)	7289 + (4 * 101) = 7693	B(4)	1333 + (4 * 79) = 1649

P(5)	8029 + (5 * 101) = 8534	B(5)	9087 + (5 * 79) = 9482

P(6)	8443 + (6 * 101) = 9049	B(6)	3456 + (6 * 79) = 3930

P(7)	    42 + (7 * 101) =   749	B(7)	    55 + (7 * 79) =   608

P(8)	    87 + (8 * 101) =   895	B(8)	    21 + (8 * 79) =   653

The six digit components of IDx, 642092, and IDy, 538249, are each split into two three digit groups (642, 092, 538 and 249) and are used to further modify P(0) to P(3) and B(0) to B(3):

P(0) = 3450 + 642 = 4092	B(0) = 9120 + 642 =   9762

P(1) = 9398 + 092 = 9490	B(1) = 9966 + 092 = 10058

P(2) = 8538 + 538 = 9076	B(2) = 2940 + 538 =   3478

P(3) = 1244 + 249 = 1493	B(3) = 4018 + 249 =   4267

C.6.4.2.2	Preliminary calculations with the message [UCNx & IDx & IDy]

IDx and IDy are concatenated to form a 12-digit number which is added (mod 10) to UCNx to form a modified UCNx.

IDx concatenated with IDy	=	642092538249

UCNx	=	1333908734565521

Modified UCNx	=	7753823016955521

C.6.4.2.3	Calculations using HKM+1

The HKM+1 algorithm uses the first 9 prime numbers from C.6.2 as moduli for performing modular arithmetic using the 9 phase primitives, P(0) to P(8) and the 9 base primitives, B(0) to B(8) derived in C.6.4.2.1 to generate a 16-entry (mod 10) PRS. The PRS is added (mod 10) to the modified UCNx to form MPx as explained below.

For example, using the first set of phase and base values, P(0), B(0) and the first prime number:

P(0) is multiplied by B(0)

4092 * 9762 = 39946104

39946104 (mod the first prime) = 39946104 (mod 32603) = 7429

7429 is then used as a new phase value, P, and is multiplied by the base value, B(0)

7429 * 9762 = 72521898

72521898 (mod the first prime) = 72521898 (mod 32603) = 12826

This process is carried out a total of 16 times (corresponding to the number of digits in the modified UCNx). It is also repeated for the remaining 8 sets of primes, phase and base values.

The results of the first calculation for each of the 9 prime, phase and base "sets" are added. The result (mod 10) is added (mod 10) to the first digit of the modified UCNx to form the first digit of MPx. The process is repeated for each digit of the modified UCNx.

The results of the above operations to produce the MPx, 4314920574868366, from the modified UCNx, 7753823016955521, are given in Table C.1.

Table C.1/T.36 – Calculations at X to derive MPx

| Prime B(n) P(n) | 32603 9762 4092 | 32507 10058 9490 | 32183 3478 9076 | 32003 4267 1493 | 31847 1649 7693 | 31607 9482 8534 | 31583 3930 9049 | 31547 608 749 | 31259 653 895 | Total | Last digit | Modified crypt number | Mutual Primitive |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 7429 | 9868 | 26988 | 2034 | 10651 | 5468 | 112 | 13734 | 21773 | 98057 | 7 | 7 | 4 |
|  | 12826 | 8473 | 18636 | 6265 | 15802 | 12096 | 29581 | 21864 | 26183 | 151726 | 6 | 7 | 3 |
|  | 11892 | 20587 | 31629 | 10250 | 6652 | 24076 | 27890 | 12025 | 30085 | 175086 | 6 | 5 | 1 |
|  | 23024 | 26963 | 4168 | 20652 | 13780 | 22878 | 14690 | 23843 | 14853 | 164851 | 1 | 3 | 4 |
|  | 27809 | 20460 | 13954 | 17825 | 16309 | 10355 | 29559 | 16471 | 8719 | 161461 | 1 | 8 | 9 |
|  | 18880 | 17370 | 48 | 20147 | 14673 | 14768 | 4596 | 13969 | 4369 | 108820 | 0 | 2 | 2 |
|  | 1801 | 14842 | 6029 | 7191 | 23904 | 11166 | 28387 | 7009 | 8388 | 108717 | 7 | 3 | 0 |
|  | 8345 | 8692 | 17729 | 25123 | 22957 | 24169 | 9754 | 2627 | 7039 | 126435 | 5 | 0 | 5 |
|  | 21596 | 12813 | 31017 | 21794 | 21857 | 19708 | 23041 | 19866 | 1394 | 173086 | 6 | 1 | 7 |
|  | 9154 | 15406 | 31893 | 28283 | 23236 | 10672 | 2669 | 27574 | 3771 | 150658 | 8 | 6 | 4 |
|  | 29128 | 25186 | 21236 | 11049 | 4223 | 17897 | 3614 | 13535 | 24261 | 150129 | 9 | 9 | 8 |
|  | 16773 | 26244 | 31006 | 5664 | 21081 | 1371 | 22253 | 27060 | 25379 | 176831 | 1 | 5 | 6 |
|  | 5760 | 5312 | 25818 | 6023 | 17492 | 9345 | 963 | 16493 | 5217 | 92423 | 3 | 5 | 8 |
|  | 21548 | 19095 | 4434 | 1732 | 22773 | 14869 | 26213 | 27345 | 30729 | 168738 | 8 | 5 | 3 |
|  | 29623 | 6154 | 5795 | 29754 | 5064 | 20638 | 24927 | 491 | 29018 | 151464 | 4 | 2 | 6 |
|  | 23719 | 3604 | 8452 | 4417 | 6622 | 10579 | 24227 | 14605 | 5800 | 102025 | 5 | 1 | 6 |
| MPx = (UINx, UCNx & IDx & IDy){HKM+1}[UCNx & IDx & IDy] = 4314920574868366 |

C.6.4.3	Calculations at X to derive TKx

TKx = (OTx){HKM+1}[MPx]

MPx, is encrypted using the HKM+1 algorithm to form the TKx, using OTx.

OTx = 71628582063812097215

OTx is expanded by concatenation to form a 64-digit primitive for the HKM algorithm. The 9 phase and 9 base primitive values are formed from the primitive in a similar way to that shown in C.6.4.2.1. There is however no further modification of P(0) to P(3) and B(0) to B(3).

The results of the calculations with the test values to form P(0) to P(8) and B(0) to B(8) using OTx are shown below:

Primitive = 71628582063812097215 71628582063812097215 71628582063812097215 7162

P(0)	7162 + 0 * 101 = 7162	B(0)	1209 + 0 * 79 = 1209

P(1)	8582 + 1 * 101 = 8683	B(1)	7215 + 1 * 79 = 7294

P(2)	  638 + 2 * 101 =   840	B(2)	7162 + 2 * 79 = 7320

P(3)	1209 + 3 * 101 = 1512	B(3)	8582 + 3 * 79 = 8819

P(4)	7215 + 4 * 101 = 7619	B(4)	  638 + 4 * 79 =   954

P(5)	7162 + 5 * 101 = 7667	B(5)	1209 + 5 * 79 = 1604

P(6)	8582 + 6 * 101 = 9188	B(6)	7215 + 6 * 79 = 7689

P(7)	      6 + 7 * 101 =   713	B(7)	    71 + 7 * 79 =   624

P(8)	    38 + 8 * 101 =   846	B(8)	    62 + 8 * 79 =   694

The phase values, P(0) to P(8), the base values, B(0) to B(8) and the 9 primes are used in the same way as in C.6.4.2.3. MPx forms the message and is added (mod 10) to the PRS and is thus encrypted by the HKM+1 algorithm to form TKx. The results of these operations to produce TKx, 5371333066610533, from MPx, 4314920574868366, are given in Table C.2.

Table C.2/T.36 – Calculations at X to derive TKx

| Prime B(n) P(n) | 32603 1209 7162 | 32507 7294 8683 | 32183 7320 840 | 32003 8819 1512 | 31847 954 7619 | 31607 1604 7667 | 31583 7689 9188 | 31547 624 713 | 31259 694 846 | Total | Last digit | Mutual Primitive | Transfer Key |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 19063 | 10166 | 1847 | 21080 | 7410 | 2745 | 26944 | 3254 | 24462 | 116971 | 1 | 4 | 5 |
|  | 29449 | 2337 | 3180 | 31096 | 30953 | 9607 | 19519 | 11488 | 2991 | 140620 | 0 | 3 | 3 |
|  | 1365 | 12410 | 9291 | 1917 | 6993 | 17019 | 30758 | 7343 | 12660 | 99756 | 6 | 1 | 7 |
|  | 20135 | 19052 | 7441 | 8439 | 15299 | 21635 | 4758 | 7717 | 2261 | 106737 | 7 | 4 | 1 |
|  | 21377 | 30370 | 14484 | 16566 | 9320 | 29661 | 11148 | 20264 | 6184 | 159374 | 4 | 9 | 3 |
|  | 23217 | 16082 | 12078 | 1859 | 5967 | 7709 | 710 | 25936 | 9213 | 102771 | 1 | 2 | 3 |
|  | 30773 | 16852 | 4259 | 8985 | 23752 | 6899 | 26914 | 453 | 16986 | 135873 | 3 | 0 | 3 |
|  | 4534 | 9521 | 22736 | 31290 | 16191 | 3546 | 9930 | 30296 | 3641 | 131685 | 5 | 5 | 0 |
|  | 4302 | 11222 | 9227 | 16644 | 419 | 30131 | 15659 | 8051 | 26134 | 121789 | 9 | 7 | 6 |
|  | 17241 | 642 | 21706 | 17678 | 17562 | 3021 | 7655 | 7851 | 6776 | 100132 | 2 | 4 | 6 |
|  | 11052 | 1740 | 449 | 15669 | 2626 | 9813 | 20166 | 9239 | 13694 | 84448 | 8 | 8 | 6 |
|  | 27241 | 13830 | 4014 | 27960 | 21138 | 31373 | 15427 | 23582 | 900 | 165465 | 5 | 6 | 1 |
|  | 5339 | 6799 | 31584 | 28128 | 6501 | 3948 | 24038 | 14266 | 30679 | 151282 | 2 | 8 | 0 |
|  | 32060 | 18731 | 24391 | 5579 | 23636 | 11192 | 4466 | 5730 | 3847 | 129632 | 2 | 3 | 5 |
|  | 28176 | 29500 | 23019 | 12590 | 1068 | 30799 | 8353 | 10709 | 12803 | 157017 | 7 | 6 | 3 |
|  | 27252 | 9167 | 21075 | 12803 | 31615 | 31462 | 17978 | 25999 | 7726 | 185077 | 7 | 6 | 3 |
| TKx = (OTx){HKM+1}[MPx] = 5371333066610533 |

C.6.4.4	Calculations at Y to recover MPx by decrypting TKx

MPx	=	(OTx){HKM–1}[TKx]

OTx	=	  71628582063812097215

The same processes as those used to derive TKx in C.6.4.3 are carried out using OTx. The same PRS(mod 10) is generated, however for HKM–1 this is subtracted (mod 10) from TKx which forms the 'message'. This subtraction process decrypts the TKx to recover MPx.

The results of the calculations with the test values to form P(0) to P(8) and B(0) to B(8) using the above OTx are shown below:

Primitive = 71628582063812097215 71628582063812097215 71628582063812097215 7162

P(0)	7162 + (0 * 101) = 7162	B(0)	1209 + (0 * 79) = 1209

P(1)	8582 + (1 * 101) = 8683	B(1)	7215 + (1 * 79) = 7294

P(2)	  638 + (2 * 101) =   840	B(2)	7162 + (2 * 79) = 7320

P(3)	1209 + (3 * 101) = 1512	B(3)	8582 + (3 * 79) = 8819

P(4)	7215 + (4 * 101) = 7619	B(4)	  638 + (4 * 79) =   954

P(5)	7162 + (5 * 101) = 7667	B(5)	1209 + (5 * 79) = 1604

P(6)	8582 + (6 * 101) = 9188	B(6)	7215 + (6 * 79) = 7689

P(7)	      6 + (7 * 101) =   713	B(7)	    71 + (7 * 79) =   624

P(8)	    38 + (8 * 101) =   846	B(8)	    62 + (8 * 79) =   694

The phase values, P(0) to P(8), the base values, B(0) to B(8) and the 9 primes are used in the same way as in C.6.4.3. The identical PRS is generated and subtracted (mod 10) from TKx to recover MPx.

The results of the above operations to recover MPx, 4314920574868366, from TKx, 5371333066610533, are given in Table C.3.

Table C.3/T.36 – Calculations at Y to recover MPx by decrypting TKx

| Prime B(n) P(n) | 32603 1209 7162 | 32507 7294 8683 | 32183 7320 840 | 32003 8819 1512 | 31847 954 7619 | 31607 1604 7667 | 31583 7689 9188 | 31547 624 713 | 31259 694 846 | Total | Last digit | Transfer Key | Mutual Primitive |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 19063 | 10166 | 1847 | 21080 | 7410 | 2745 | 26944 | 3254 | 24462 | 116971 | 1 | 5 | 4 |
|  | 29449 | 2337 | 3180 | 31096 | 30953 | 9607 | 19519 | 11488 | 2991 | 140620 | 0 | 3 | 3 |
|  | 1365 | 12410 | 9291 | 1917 | 6993 | 17019 | 30758 | 7343 | 12660 | 99756 | 6 | 7 | 1 |
|  | 20135 | 19052 | 7441 | 8439 | 15299 | 21635 | 4758 | 7717 | 2261 | 106737 | 7 | 1 | 4 |
|  | 21377 | 30370 | 14484 | 16566 | 9320 | 29661 | 11148 | 20264 | 6184 | 159374 | 4 | 3 | 9 |
|  | 23217 | 16082 | 12078 | 1859 | 5967 | 7709 | 710 | 25936 | 9213 | 102771 | 1 | 3 | 2 |
|  | 30773 | 16852 | 4259 | 8985 | 23752 | 6899 | 26914 | 453 | 16986 | 135873 | 3 | 3 | 0 |
|  | 4534 | 9521 | 22736 | 31290 | 16191 | 3546 | 9930 | 30296 | 3641 | 131685 | 5 | 0 | 5 |
|  | 4302 | 11222 | 9227 | 16644 | 419 | 30131 | 15659 | 8051 | 26134 | 121789 | 9 | 6 | 7 |
|  | 17241 | 642 | 21706 | 17678 | 17562 | 3021 | 7655 | 7851 | 6776 | 100132 | 2 | 6 | 4 |
|  | 11052 | 1740 | 449 | 15669 | 2626 | 9813 | 20166 | 9239 | 13694 | 84448 | 8 | 6 | 8 |
|  | 27241 | 13830 | 4014 | 27960 | 21138 | 31373 | 15427 | 23582 | 900 | 165465 | 5 | 1 | 6 |
|  | 5339 | 6799 | 31584 | 28128 | 6501 | 3948 | 24038 | 14266 | 30679 | 151282 | 2 | 0 | 8 |
|  | 32060 | 18731 | 24391 | 5579 | 23636 | 11192 | 4466 | 5730 | 3847 | 129632 | 2 | 5 | 3 |
|  | 28176 | 29500 | 23019 | 12590 | 1068 | 30799 | 8353 | 10709 | 12803 | 157017 | 7 | 3 | 6 |
|  | 27252 | 9167 | 21075 | 12803 | 31615 | 31462 | 17978 | 25999 | 7726 | 185077 | 7 | 3 | 6 |
| Mutual primitive = (OTx){HKM–1}[TKx] = 4314920574868366 |

C.6.4.5	Calculations at Y to derive RCNy

RCNy = (UINy, UCNy & IDx & IDy){HKM+1}[MPx]

Y follows the same preliminary calculations for (UINy, UCNy & IDx & IDy) as used by X to calculate MPx in C.6.4.2 but using UINy and UCNy to form the phase and base values. IDx and IDy are used to modify P(0) to P(3) and B(0) to B(3) as before. The phase and base values are used with the first 9 system modulating prime numbers according to the HKM+1 algorithm to develop a (mod 10) PRS which, added to MPx, forms RCNy, which can be communicated openly.

The results of these calculations using the test values are shown below.

Unique Identity Number, UINy = 973557693837783148353709167436722873449819767357

Unique Crypt Number, UCNy   = 7598247578649467

Primitive = 9735576938377831483537091674367228734498197673577598247578649467

P(0)	9735 + (0 * 101) = 9735	B(0)	2873 + (0 * 79) = 2873

P(1)	5769 + (1 * 101) = 5870	B(1)	4498 + (1 * 79) = 4577

P(2)	3837 + (2 * 101) = 4039	B(2)	1976 + (2 * 79) = 2134

P(3)	7831 + (3 * 101) = 8134	B(3)	7357 + (3 * 79) = 7594

P(4)	4835 + (4 * 101) = 5239	B(4)	7598 + (4 * 79) = 7914

P(5)	3709 + (5 * 101) = 4214	B(5)	2475 + (5 * 79) = 2870

P(6)	1674 + (6 * 101) = 2280	B(6)	7864 + (6 * 79) = 8338

P(7)	    36 + (7 * 101) =   743	B(7)	    94 + (7 * 79) =   647

P(8)	    72 + (8 * 101) =   880	B(8)	    67 + (8 * 79) =   699

P(0) to P(3), and B(0) to B(3) are modified as before using IDx and IDy

IDx = 642092     IDy = 538249

P(0) = 9735 + 642 = 10377	B(0) = 2873 + 642 = 3515

P(1) = 5870 + 092 =   5962	B(1) = 4577 + 092 = 4669

P(2) = 4039 + 538 =   4577	B(2) = 2134 + 538 = 2672

P(3) = 8134 + 249 =   8383	B(3) = 7594 + 249 = 7843

The results of the above operations to produce RCNy, 9865418902725854 from MPx, 43149205748688366, are shown in Table C.4.

Table C.4/T.36 – Calculations at Y to derive RCNy

| Prime B(n) P(n) | 32603 3515 10377 | 32507 4669 5962 | 32183 2672 4577 | 32003 7843 8383 | 31847 7914 5239 | 31607 2870 4214 | 31583 8338 2280 | 31547 647 743 | 31259 699 880 | Total | Last digit | Mutual Primitive | Registered Crypt Number |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 25001 | 10586 | 204 | 13707 | 28499 | 20306 | 29257 | 7516 | 21199 | 156275 | 5 | 4 | 9 |
|  | 13430 | 15394 | 30160 | 5924 | 632 | 26519 | 29357 | 4614 | 1335 | 127365 | 5 | 3 | 8 |
|  | 29909 | 1609 | 1288 | 25579 | 1669 | 31481 | 10416 | 19840 | 26654 | 148445 | 5 | 1 | 6 |
|  | 18063 | 3304 | 30138 | 21293 | 23808 | 17664 | 26941 | 28398 | 782 | 170391 | 1 | 4 | 5 |
|  | 13404 | 18058 | 6870 | 9345 | 9660 | 29659 | 15762 | 13152 | 15215 | 131125 | 5 | 9 | 4 |
|  | 3725 | 22151 | 12330 | 5965 | 16440 | 3679 | 6693 | 23201 | 7225 | 101409 | 9 | 2 | 1 |
|  | 19572 | 18252 | 22551 | 27112 | 11165 | 1992 | 3 0656 | 26222 | 17576 | 175098 | 8 | 0 | 8 |
|  | 3250 | 17741 | 9696 | 11484 | 16232 | 27780 | 8509 | 24895 | 837 | 120424 | 4 | 5 | 9 |
|  | 12700 | 4893 | 397 | 12570 | 21097 | 15746 | 12624 | 18095 | 22401 | 120523 | 3 | 7 | 0 |
|  | 6993 | 25503 | 30928 | 17270 | 19684 | 24617 | 24356 | 3528 | 28799 | 181678 | 8 | 4 | 2 |
|  | 30336 | 366 | 25855 | 11914 | 15499 | 9145 | 1638 | 11232 | 30964 | 136949 | 9 | 8 | 7 |
|  | 19230 | 18490 | 19842 | 24745 | 16289 | 12340 | 13788 | 11294 | 12608 | 148626 | 6 | 6 | 2 |
|  | 7431 | 23725 | 12423 | 8843 | 26337 | 15960 | 2224 | 19861 | 29213 | 146017 | 7 | 8 | 5 |
|  | 4962 | 20676 | 13583 | 5148 | 24250 | 6657 | 4491 | 10438 | 7760 | 97965 | 5 | 3 | 8 |
|  | 31428 | 22961 | 23535 | 19981 | 4478 | 14962 | 20103 | 2328 | 16433 | 156209 | 9 | 6 | 5 |
|  | 10456 | 29330 | 32121 | 24295 | 25028 | 18634 | 7833 | 23507 | 14614 | 185818 | 8 | 6 | 4 |
| Registered Crypt Number, RCNy = (UINy, UCNy & IDx & IDy) {HKM+1} [MPx] = 9865418902725854 |

C.6.5	Secure mode

C.6.5.1	procSTKxy using algebraic notation

The following subclauses use test values to show all calculations used in procSTKxy using HKMD to transfer SKx, between X and Y. The secret key may be specifically an SCn, SRn, SSn, etc.

| X | Y |
| --- | --- |
| > UINx, UCNx, RCNy < | > UINy, UCNy < |
| (UINx, UCNx & IDx & IDy){HKM+1}[UCNx & IDx & IDy] = MPx (MPx & RNKx){HKMD+1}[SKx] = ESSKx RCNy, RNKx, ESSKx >>>>>> |
| >>>>>> RCNy, RNKx, ESSKx MPx = (UINy, UCNy & IDx & IDy){HKM–1}[RCNy] SKx = (MPx & RNKx){HKMD–1}[ESSKx] |

C.6.5.2	Calculations at X to re-create MPx

>  UINx, UCNx, RCNy  <

MPx = (UINx, UCNx & IDx & IDy){HKM+1}[UCNx & IDx & IDy]

The test values and calculations are identical to those shown in C.6.4.2 giving:

MPx = (UINx, UCNx & IDx & IDy){HKM+1}[UCNx & IDx & IDy] = 4314920574868366

C.6.5.3	Calculations at X to form ESSKx using HKMD+1

ESSKx = (MPx & RNKx){HKMD+1}[SKx]

SKx is doubly encrypted using HKMD+1, the first encryption being a scrambling process based on a 12-digit (mod 12) PRS generated using HKM to form SSKx, and the second encryption is the normal (mod 10) addition to the 'message', SSKx, of the (mod 10) PRS generated using HKM.

C.6.5.3.1	Calculations at X to form SSKx

MPx is repeated and concatenated to form the 64-digit Primitive which is used to derive the phase and base primitive values as shown below.

Primitive = 4314920574868366 4314920574868366 4314920574868366 4314920574868366

P(0)	4314 + (0 * 101) = 4314	B(0)	4314 + (0 * 79) = 4314

P(1)	9205 + (1 * 101) = 9306	B(1)	9205 + (1 * 79) = 9284

P(2)	7486 + (2 * 101) = 7688	B(2)	7486 + (2 * 79) = 7644

P(3)	8366 + (3 * 101) = 8669	B(3)	8366 + (3 * 79) = 8603

P(4)	4314 + (4 * 101) = 4718	B(4)	4314 + (4 * 79) = 4630

P(5)	9205 + (5 * 101) = 9710	B(5)	9205 + (5 * 79) = 9600

P(6)	7486 + (6 * 101) = 8092	B(6)	7486 + (6 * 79) = 7960

P(7)	    83 + (7 * 101) =   790	B(7)	    83 + (7 * 79) =   636

P(8)	    66 + (8 * 101) =   874	B(8)	    66 + (8 * 79) =   698

RNKx, associated with SKx, is divided into 2 pairs of 2 digits and the first pair is added to P(0) and the second pair to P(1) to give new values of P(0) and P(1); new values for B(0) and B(1) are created in an identical manner.

RNKx = 3958

P(0) = 4314 + 39 = 4353	B(0) = 4314 + 39 = 4353

P(1) = 9306 + 58 = 9364	B(1) = 9284 + 58 = 9342

The prime numbers and the phase and base values are then used with HKM to generate a 12-digit PRS, (mod 12) + 1, (that is, the "Total" column is modulated to the base 12 and 1 is added to produce the PRS). The results of the calculations are given in Table C.5.

Table C.5/T.36 – Calculations at X to form the (mod 12) + 1 scrambler/descrambler PRS

| Prime B(n) P(n) | 32603 4353 4353 | 32507 9342 9364 | 32183 7644 7688 | 32003 8603 8669 | 31847 4630 4718 | 31607 9600 9710 | 31583 7960 8092 | 31547 636 790 | 31259 698 874 | Total | (mod 12) + 1 PRS |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 6266 | 2151 | 914 | 12417 | 29145 | 6957 | 14583 | 29235 | 16131 | 117799 | 8 |
|  | 19790 | 5316 | 2905 | 29440 | 5611 | 1609 | 13155 | 12277 | 6198 | 96301 | 2 |
|  | 8744 | 23883 | 31733 | 578 | 23625 | 22184 | 16155 | 16063 | 12462 | 155427 | 4 |
|  | 14931 | 19445 | 3781 | 12069 | 21152 | 30041 | 19407 | 26387 | 8474 | 155687 | 12 |
|  | 16864 | 6074 | 1630 | 11875 | 4235 | 11332 | 7267 | 30675 | 6901 | 96853 | 2 |
|  | 19639 | 18593 | 4899 | 7049 | 22145 | 27513 | 16847 | 13254 | 3012 | 132951 | 4 |
|  | 3501 | 10905 | 19127 | 28865 | 15857 | 16708 | 702 | 6495 | 8023 | 110183 | 12 |
|  | 14252 | 30079 | 31602 | 14318 | 10575 | 22882 | 29312 | 29710 | 4693 | 187423 | 8 |
|  | 28050 | 7510 | 90 | 30210 | 13411 | 30157 | 19899 | 30454 | 24778 | 184559 | 12 |
|  | 3415 | 8314 | 12117 | 267 | 23127 | 18687 | 7295 | 30433 | 8817 | 112472 | 9 |
|  | 31130 | 10165 | 31857 | 24788 | 8396 | 25475 | 18646 | 17077 | 27502 | 195036 | 1 |
|  | 10822 | 8483 | 18330 | 15175 | 20140 | 16641 | 13643 | 8804 | 3370 | 115408 | 5 |

The resultant scrambler/descrambler PRS is then used as the scrambler to scramble the SKx. The first digit in the scrambler indicates which digit in SKx should be interchanged with the first digit in SKx. The second digit in the scrambler indicates the interchange for the second digit of the SKx and so on for the remaining digits. The results of this scrambling process to produce SSKx, 721647935700, from SKx, 309126704577, are shown below.

Scrambler PRS

8	309126704577  =	SKx
	2	009126734577
	4	009126734577
	12	001926734577
	2	001726734579
	4	021706734579
	12	021607734579
	8	021607934577
	12	021607934577
	9	021607937574
	1	021607935774
	5	721607935704
		721647935700  =	SSKx

C.6.5.3.2	Calculations at X to form ESSKx

The same calculations using HKM as in C.6.5.3.1 are used to generate a 12-digit (mod 10) PRS, which is added (mod 10) to SSKx, to produce ESSKx.

The results of the calculations to produce ESSKx, 638378264968, from SSKx, 721647935700, are given in Table C.6.

Table C.6/T.36 – Calculations at X to form ESSKx

| Prime B(n) P(n) | 32603 4353 4353 | 32507 9342 9364 | 32183 7644 7688 | 32003 8603 8669 | 31847 4630 4718 | 31607 9600 9710 | 31583 7960 8092 | 31547 636 790 | 31259 698 874 | Total | Last digit | Scrambled Secret Key | Encrypted Scrambled Secret Key |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 6266 | 2151 | 914 | 12417 | 29145 | 6957 | 14583 | 29235 | 16131 | 117799 | 9 | 7 | 6 |
|  | 19790 | 5316 | 2905 | 29440 | 5611 | 1609 | 13165 | 12277 | 6198 | 96301 | 1 | 2 | 3 |
|  | 8744 | 23883 | 31733 | 578 | 23625 | 22184 | 16155 | 16063 | 12462 | 155427 | 7 | 1 | 8 |
|  | 14931 | 19445 | 3781 | 12069 | 21152 | 30041 | 19407 | 26387 | 8474 | 155687 | 7 | 6 | 3 |
|  | 16864 | 6074 | 1630 | 11875 | 4235 | 11332 | 7267 | 30675 | 6901 | 96853 | 3 | 4 | 7 |
|  | 19639 | 18593 | 4899 | 7049 | 22145 | 27513 | 1 6847 | 13254 | 3012 | 132951 | 1 | 7 | 8 |
|  | 3501 | 10905 | 19127 | 28865 | 15857 | 16708 | 702 | 6495 | 8023 | 110183 | 3 | 9 | 2 |
|  | 14252 | 30079 | 31602 | 14318 | 10575 | 22882 | 29312 | 29710 | 4693 | 187423 | 3 | 3 | 6 |
|  | 28050 | 7510 | 90 | 30210 | 13411 | 30157 | 19899 | 30454 | 24778 | 184559 | 9 | 5 | 4 |
|  | 3415 | 8314 | 12117 | 267 | 23127 | 18687 | 7295 | 30433 | 8817 | 112472 | 2 | 7 | 9 |
|  | 31130 | 10165 | 31857 | 24788 | 8396 | 25475 | 18646 | 17077 | 27502 | 195036 | 6 | 0 | 6 |
|  | 10822 | 8483 | 18330 | 15175 | 20140 | 16641 | 13643 | 8804 | 3370 | 115408 | 8 | 0 | 8 |

SSKx = 638378264968

X sents RCNy, ESSKx and RNKx to Y.

C.6.5.4	Calculations at Y to recover SKx

| Y |
| --- |
|  | > UINy, UCNy < >>>>>> RCNy, RNKx, ESSKx MPx = (UINy, UCNy & IDx & IDy){HKM–1}[RCNy] SKx = (MPx & RNKx){HKMD–1}[ESSKx] |

C.6.5.4.1	Calculations at Y to recover MPx, from RCNy

MPx = (UINy, UCNy & IDx & IDy){HKM–1}[RCNy]

The test values and calculations are identical to those shown in C.6.4.5, except that the decryption process HKM–1 is used to recover MPx from RCNy by subtracting the 16-digit PRS digit-by-digit from RCNy.

The results of these calculations using the test values are shown below.

UINy	=	973557693837783148353709167436722873449819767357

UCNy	=	7598247578649467

Primitive = 9735576938377831483537091674367228734498197673577598247578649467

P(0)	9735 + 0 * 101 = 9735	B(0)	2873 + 0 * 79 = 2873

P(1)	5769 + 1 * 101 = 5870	B(1)	4498 + 1 * 79 = 4577

P(2)	3837 + 2 * 101 = 4039	B(2)	1976 + 2 * 79 = 2134

P(3)	7831 + 3 * 101 = 8134	B(3)	7357 + 3 * 79 = 7594

P(4)	4835 + 4 * 101 = 5239	B(4)	7598 + 4 * 79 = 7914

P(5)	3709 + 5 * 101 = 4214	B(5)	2475 + 5 * 79 = 2870

P(6)	1674 + 6 * 101 = 2280	B(6)	7864 + 6 * 79 = 8338

P(7)	    36 + 7 * 101 =   743	B(7)	    94 + 7 * 79 =   647

P(8)	    72 + 8 * 101 =   880	B(8)	    67 + 8 * 79 =   699

P(0) to P(3), and B(0) to B(3) are modified as before using IDx and IDy.

IDx = 642092     IDy = 538249

P(0) = 9735 + 642 =	10377	B(0) = 2873 + 642 = 3515

P(1) = 5870 + 092 =	5962	B(1) = 4577 + 092 = 4669

P(2) = 4039 + 538 =	4577	B(2) = 2134 + 538 = 2672

P(3) = 8134 + 249 =	8383	B(3) = 7594 + 249 = 7843

The results of using these phase and base primitive values with the 9 primes in the HKM–1 algorithm to produce MPx, 43149205748688366, from RCNy, 9865418902725854, are shown in Table C.7.

Table C.7/T.36 – Calculations at Y to recover MPx from RCNy

| Prime B(n) P(n) | 32603 3515 10377 | 32507 4669 5962 | 32183 2672 4577 | 32003 7843 8383 | 31847 7914 5239 | 31607 2870 4214 | 31583 8338 2280 | 31547 647 743 | 31259 699 880 | Total | Last digit | Registered Crypt Number | Mutual Primitive |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 25001 | 10586 | 204 | 13707 | 28499 | 20306 | 29257 | 7516 | 21199 | 156275 | 5 | 9 | 4 |
|  | 13430 | 15394 | 30160 | 5924 | 632 | 26519 | 29357 | 4614 | 1335 | 127365 | 5 | 8 | 3 |
|  | 29909 | 1609 | 1288 | 25579 | 1669 | 31481 | 10416 | 19840 | 26654 | 148445 | 5 | 6 | 1 |
|  | 18063 | 3304 | 30138 | 21293 | 23808 | 17664 | 26941 | 28398 | 782 | 170391 | 1 | 5 | 4 |
|  | 13404 | 18058 | 6870 | 9345 | 9660 | 29659 | 15762 | 13152 | 15215 | 131125 | 5 | 4 | 9 |
|  | 3725 | 22151 | 12330 | 5965 | 16440 | 3679 | 6693 | 23201 | 7225 | 101409 | 9 | 1 | 2 |
|  | 19572 | 18252 | 22551 | 27112 | 11165 | 1992 | 30656 | 26222 | 17576 | 175098 | 8 | 8 | 0 |
|  | 3250 | 17741 | 9696 | 11484 | 16232 | 27780 | 8509 | 24895 | 837 | 120424 | 4 | 9 | 5 |
|  | 12700 | 4893 | 397 | 12570 | 21097 | 15746 | 12624 | 18095 | 22401 | 120523 | 3 | 0 | 7 |
|  | 6993 | 25503 | 30928 | 17270 | 19684 | 24617 | 24356 | 3528 | 28799 | 181678 | 8 | 2 | 4 |
|  | 30336 | 366 | 25855 | 11914 | 15499 | 9145 | 1638 | 11232 | 30964 | 136949 | 9 | 7 | 8 |
|  | 19230 | 18490 | 19842 | 24745 | 16289 | 12340 | 13788 | 11294 | 12608 | 148626 | 6 | 2 | 6 |
|  | 7431 | 23725 | 12423 | 8843 | 26337 | 15960 | 2224 | 19861 | 29213 | 146017 | 7 | 5 | 8 |
|  | 4962 | 20676 | 13583 | 5148 | 24250 | 6657 | 4491 | 10438 | 7760 | 97965 | 5 | 8 | 3 |
|  | 31428 | 22961 | 23535 | 19981 | 4478 | 14962 | 20103 | 2328 | 16433 | 156209 | 9 | 5 | 6 |
|  | 10456 | 29330 | 32121 | 24295 | 25028 | 18634 | 7833 | 23507 | 14614 | 185818 | 8 | 4 | 6 |
| MPx = (UINy, UCNy & IDx & IDy){HKM–1}[RCNy] = 4314920574868366 |

C.6.5.4.2	Calculations at Y to recover SKx, from ESSKx, using HKMD–1

SKx = (MPx & RNKx){HKMD–1}[ESSKx]

ESSKx is doubly decrypted using HKMD–1 in the reverse order to the double encryption carried out at X. The first decryption is the (mod 10) subtraction from the 'message' (ESSKx) of the same (mod 10) PRS as used by X. The second decryption is a descrambling process based on the same 12-digit PRS (mod 10) + 1 as used by X.

C.6.5.4.2.1	Calculations at Y for the first decryption of ESSKx, to recover SSKx

The same calculations using HKM, as in C.6.5.3.2, are used to generate a 12-digit (mod 10) PRS, which is subtracted (mod 10) from ESSKx, to produce SSKx.

MPx, is repeated and concatenated to form the 64-digit Primitive which is used to derive phase and base primitive values as shown below.

Primitive = 4314920574868366 4314920574868366 4314920574868366 4314920574868366

P(0)	4314 + (0 * 101) = 4314	B(0)	4314 + (0 * 79) = 4314

P(1)	9205 + (1 * 101) = 9306	B(1)	9205 + (1 * 79) = 9284

P(2)	7486 + (2 * 101) = 7688	B(2)	7486 + (2 * 79) = 7644

P(3)	8366 + (3 * 101) = 8669	B(3)	8366 + (3 * 79) = 8603

P(4)	4314 + (4 * 101) = 4718	B(4)	4314 + (4 * 79) = 4630

P(5)	9205 + (5 * 101) = 9710	B(5)	9205 + (5 * 79) = 9600

P(6)	7486 + (6 * 101) = 8092	B(6)	7486 + (6 * 79) = 7960

P(7)	    83 + (7 * 101) =   790	B(7)	    83 + (7 * 79) =   636

P(8)	    66 + (8 * 101) =   874	B(8)	    66 + (8 * 79) =   698

RNKx, associated with ESSKx, is divided into 2 pairs of 2-digits and the first pair is added to P(0) and the second pair to P(1) to give new values of P(0) and P(1); new values for B(0) and B(1) are created in an identical manner.

RNKx = 3958

P(0) = 4314 + 39 = 4353	B(0) = 4314 + 39 = 4353

P(1) = 9306 + 58 = 9364	B(1) = 9284 + 58 = 9342

The results of the calculations to decrypt ESSKx, 638378264968, to form SSKx, 721647935700, are given in Table C.8.

Table C.8/T.36 – Calculations at Y to form SSKx from ESSKx

| Prime B(n) P(n) | 32603 4353 4353 | 32507 9342 9364 | 32183 7644 7688 | 32003 8603 8669 | 31847 4630 4718 | 31607 9600 9710 | 31583 7960 8092 | 31547 636 790 | 31259 698 874 | Total | Last digit | Encrypted Scrambled Secret Key | Scrambled Secret Key |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 6266 | 2151 | 914 | 12417 | 29145 | 6957 | 14583 | 29235 | 16131 | 117799 | 9 | 6 | 7 |
|  | 19790 | 5316 | 2905 | 29440 | 5611 | 1609 | 13165 | 12277 | 6198 | 96301 | 1 | 3 | 2 |
|  | 8744 | 23883 | 31733 | 578 | 23625 | 22184 | 16155 | 16063 | 12462 | 155427 | 7 | 8 | 1 |
|  | 14931 | 19445 | 3781 | 12069 | 21152 | 30041 | 19407 | 26387 | 8474 | 155687 | 7 | 3 | 6 |
|  | 16864 | 6074 | 1630 | 11875 | 4235 | 11332 | 7267 | 30675 | 6901 | 96853 | 3 | 7 | 4 |
|  | 19639 | 18593 | 4899 | 7049 | 22145 | 27513 | 16847 | 13254 | 3012 | 132951 | 1 | 8 | 7 |
|  | 3501 | 10905 | 19127 | 28865 | 15857 | 16708 | 702 | 6495 | 8023 | 110183 | 3 | 2 | 9 |
|  | 14252 | 30079 | 31602 | 14318 | 10575 | 22882 | 29312 | 29710 | 4693 | 187423 | 3 | 6 | 3 |
|  | 28050 | 7510 | 90 | 30210 | 13411 | 30157 | 19899 | 30454 | 24778 | 184559 | 9 | 4 | 5 |
|  | 3415 | 8314 | 12117 | 267 | 23127 | 18687 | 7295 | 30433 | 8817 | 112472 | 2 | 9 | 7 |
|  | 31130 | 10165 | 31857 | 24788 | 8396 | 25475 | 18646 | 17077 | 27502 | 195036 | 6 | 6 | 0 |
|  | 10822 | 8483 | 18330 | 15175 | 20140 | 16641 | 13643 | 8804 | 3370 | 115408 | 8 | 8 | 0 |
| SSKx = 721647935700 |

C.6.5.4.2.2	Calculations at Y to derive SKx from SSKx

The same calculations that were used at X to produce the (mod 12) + 1 PRS (see C.6.5.3.1) are used at Y to produce the same scrambler/descrambler PRS, 8 2 4 12 2 4 12 8 12 9 1 5. This scrambler/descrambler PRS is reversed and used as the descrambler PRS to descramble SSKx.

The descrambler PRS is 5 1 9 12 8 12 4 2 12 4 2 8.

The first digit in the descrambler PRS indicates which digit in SSKx should be interchanged with the twelfth digit of the SSKx. The second digit in the descrambler PRS indicates the interchange for the eleventh digit of the SSKx and so on for the remaining digits. The steps of this descrambling process to produce SKx, 309126704577, from the SSKx, 721647935700, are shown below.

Descrambler PRS

5	721647935700  =	SSKx
	1	721607935704
	9	021607935774
	12	021607937574
	8	021607934577
	12	021607934577
	4	021607734579
	2	021706734579
	12	001726734579
	4	001926734577
	2	009126734577
	8	009126734577

		309126704577  =	SKx

Both X and Y are now in possession of the same SKx.

C.6.6	The use of the HKM algorithm in secure mode

The HKM algorithm is used in the secure mode to re-create MPx and MPy at X and Y and using procSTKxy and procSTKyx to securely transfer secret keys to provide mutual authentication, secret session key establishment for message confidentiality and /or message integrity, confirmation of receipt and confirmation or denial of integrity.

The procedures to achieve these capabilities are described in C.5.

Annex D

Procedures for the use of the HFX40 carrier cipher to provide message 
confidentiality for secure document facsimile transmission

D.1	Scope

This Annex defines the HFX40 carrier cipher system to be used with facsimile terminals to provide message confidentiality. Example calculations using test values are given in D.3. The calculations can be used to verify the implementation of this Annex.

The HFX40 carrier cipher is intended to be applicable for use with all types of dedicated facsimile terminals but is also equally applicable to computer-based facsimile systems.

The HFX40 system is based upon the use of 19 system prime numbers. These same 19 prime numbers are used also with the HKM key management system which is defined in Annex C and the message integrity hash algorithm which is described in Annex E. However, this Annex does not cover the key management system, nor the main message integrity hash algorithm.

Example calculations are given in D.3 and these can be used to verify the implementation of this Annex.

The HFX40 system is covered by intellectual property rights; however, the owner of those rights has agreed to follow the TSB code of practice. Further details can be obtained from the TSB.

D.2	Description of the HFX40 algorithm for use with facsimile terminals in secure mode

The HFX40 algorithm is used to provide message confidentiality using encryption. The algorithm uses a secret key to provide the input numbers for modular arithmetical calculations. The moduli for the modular arithmetic are provided by a selection of 3 primes made from a set of 19 system modulating prime numbers stored in the facsimile terminal. This set of prime numbers is the same as that used by the HKM key management system (Annex C) and the HFX40-I message integrity system (Annex E).

The output of the modular arithmetical processes are long PRSs that are used to encrypt the compressed facsimile message. Only by possessing the secret encryption key is it possible to recreate the message.

The HFX40 algorithm uses a 12-decimal digit key, approximately equivalent to a key length of 40 bits.

The key management procedures are detailed in Annex C.

If mutual registration has been carried out between X and Y, the secure mode can be used to establish mutual authentication of X and Y, following which SSx can be generated at X and transferred securely to Y. If registration has not been carried out, the override mode (see Recommendation T.30) can be used to allow the users at X and Y to manually enter a pre-agreed secret session key to form SSx.

X uses SSx with the HFX40 algorithm to generate three (mod 2) PRSs which are stored as entries in 3 tables, referred to as tables P, Q and R. The number of entries in each table is different. Table P is generated with 1021 entries, table Q with 1019 entries and table R with 1013 entries.

The last 4 entries in each table are used to form a multiplexer to modify the table entries as the message is encrypted and the shortened tables are used to encrypt the message. Table P is now 1017 entries, table Q is 1015 entries and table R is 1009 entries

The first bit of the compressed facsimile message is added (mod 2) to the addition (mod 2) of the bits in the first entries of the tables P, Q and R to form the first bit of the encrypted message. After each message bit has been processed, the corresponding P, Q and R table entries are modified based upon the entries in the multiplexer. The modification in each table is an interchange of the table entry with an entry in the multiplexer which is determined by the entries in the other two tables.

The entry in table P interchanges with the multiplexer entry determined by tables Q and R.

The entry in table Q interchanges with the multiplexer entry determined by tables R and P.

The entry in table R interchanges with the multiplexer entry determined by tables P and Q.

Note, the order has significance.

The second bit of the main message is processed in a similar way with the bits in the second entries in the tables. The new multiplexer formed by the interchange of the first entries in the tables is then used to interchange with the second entries in the tables.

The above procedure is followed for each of the message bits. When in table R entry 1009 has been used, the first (modified) entry is the next to be used. The procedure then continues with the new entries. Similarly, tables P and Q "restart" after entries 1017 and 1015 respectively.

The encrypted message is then sent to Y. Y uses the same SSx with the HFX40 algorithm to generate the identical tables and modifying multiplexer; subtracting the (mod 2) addition of the entries in the tables from the encrypted message to recover the original compressed facsimile message. The SSx used by Y is either transferred securely from X in the secure mode or is formed from the pre-agreed session key entered manually by the user at Y in the override mode.

D.3	Example calculations for the HFX40 algorithm

D.3.1	Introduction

This subclause describes the HFX40 algorithm in terms of the numbers to be stored and the rules for the computations carried out using these numbers to generate the PRSs which are used to encrypt the compressed facsimile message. The calculations can be used to verify the implementation.

D.3.2	Stored information

All terminals are equipped with the same 19 system modulating prime numbers.

32603	32507	32183	32003	31847	31607	31583	31547	31259

31139	30803	30539	30467	30347	30323	30203	29879	29759	29663

D.3.3	Selection of the primes

For each facsimile call, a different SSx is used to select 3 primes from the 19 stored system modulating primes. SSx is split into four groups of 3 digits. The first 2 groups of three digits, g1 and g2, are XOR'd to form a third group g3. The second 2 groups of 3 digits, g4 and g5, are XOR'd to form a sixth group, g6. 1024 is added to groups g1 to g3 to form P(0) to P(2) and to groups g4 to g6 to form B(0) to B(2). This procedure is shown below using a numerical example.

SSx for this example is 149162536496.

g1 = 149	P(0) =	149	+ 1024 = 1173

g2 = 162	P(1) =	162	+ 1024 = 1186

g3 = g1 XOR g2 = 55 	P(2) =	55	+ 1024 = 1079

g4 = 536	B(0) =	536	+ 1024 = 1560

g5 = 496	B(1) =	496	+ 1024 = 1520

g6 = g4 XOR g5 = 1000	B(2) =	1000	+ 1024 = 2024

Three 8 digit numbers are then formed by concatenating the pairs P(0) and B(0), P(1) and B(1), and P(2) and B(2) together and modulating each number to the base 19.

P(0) and B(0)	gives	11731560 (mod 19) = 10

P(1) and B(1)	gives	11861520 (mod 19) = 10

P(2) and B(2)	gives	10792024 (mod 19) =   5

In the list of the 19 system modulating prime numbers given in D.3.2 above, the first prime, 32603, is designated prime (0) and the last prime, 29663, prime (18).

Using the first value, 10, obtained from P(0) and B(0), the first prime, i.e. prime (0), 32603 is interchanged with prime (10), 30803.

Using the second value, 10, obtained from P(1) and B(1), the second prime i.e. prime (1), 32507 is interchanged with prime (10), 32603.

Using the third value, 5, obtained from P(2) and B(2), the third prime i.e. prime (2), 32183 is exchanged with prime (5), 31607

This process is shown below:

Unmodified system	32603	32507	32183	32003	31847	31607	31583	31547	31259
modulating primes	31139	30803	30539	30467	30347	30323	30203	29879	29759	29663

10	30803	32507	32183	32003	31847	31607	31583	31547	31259
		31139	32603	30539	30467	30347	30323	30203	29879	29759	29663

10	30803	32603	32183	32003	31847	31607	31583	31547	31259
		31139	32507	30539	30467	30347	30323	30203	29879	29759	29663

5	30803	32603	31607	32003	31847	32183	31583	31547	31259
		31139	32507	30539	30467	30347	30323	30203	29879	29759	29663

D.3.4	Calculations using HFX40 to generate 3 PRSs

The first three primes in the final arrangement, 30803, 32603 and 31607, are used as the moduli for calculations carried out with the 3 phase and 3 base primitive values derived from SSx in D.3.3 to generate three (mod 2) PRSs to be stored in tables P, Q and R. Table P to have 1021 entries, table Q, 1019 entries and table R, 1013 entries.

Example calculations for the first "set", i.e. prime (0) = 30803, phase P(0) = 1173 and base B(0) = 1560:

P(0) is multiplied by B(0):

1173 * 1560 = 1829880

1829880 [mod prime (0)] = 1829880 (mod 30803) = 12503

12503 (mod 2) = 1

12503 is then used as the new phase value and is multiplied by B(0):

12503 * 1560 = 19504680

19504680 [mod prime (0)] = 19504680 (mod 30803) = 6381

6381 (mod 2) = 1

The process is repeated to generate 1021 values to fill the entries in table P.

Similar calculations are carried out with the second and third "sets" of phases, bases and primes to generate entries for tables Q and R. Table D.1 shows 16 further sets of calculations using HFX40.

Table D.1/T.36– Calculations using HFX40 to generate 3 PRSs

| Phase | B(0) | New phase (mod 30803) | Table P (mod 2) | Phase | B(0) | New phase (mod 32603) | Table Q (mod 2) | Phase | *B(0) | New phase (mod 31607) | Table R (mod 2) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1173 | 1560 | 12503 | 1 | 1186 | 1520 | 9555 | 1 | 1079 | 2024 | 3013 | 1 |
| 12503 | 1560 | 6381 | 1 | 9555 | 1520 | 15265 | 1 | 3013 | 2024 | 29768 | 0 |
| 6381 | 1560 | 4991 | 1 | 15265 | 1520 | 22067 | 1 | 29768 | 2024 | 7490 | 0 |
| 4991 | 1560 | 23604 | 0 | 22067 | 1520 | 25956 | 0 | 7490 | 2024 | 20007 | 1 |
| 23604 | 1560 | 12655 | 1 | 25956 | 1520 | 3490 | 0 | 20007 | 2024 | 5601 | 1 |
| 12655 | 1560 | 27780 | 0 | 3490 | 1520 | 23114 | 0 | 5601 | 2024 | 21118 | 0 |
| 27880 | 1560 | 29767 | 1 | 23114 | 1520 | 19849 | 1 | 21118 | 2024 | 10168 | 0 |
| 29767 | 1560 | 16399 | 1 | 19849 | 1520 | 12705 | 1 | 10168 | 2024 | 3875 | 1 |
| 16399 | 1560 | 15950 | 0 | 12705 | 1520 | 10624 | 0 | 3875 | 2024 | 4464 | 0 |
| 15950 | 1560 | 23979 | 1 | 10624 | 1520 | 9995 | 1 | 4464 | 2024 | 27141 | 1 |
| 23979 | 1560 | 12398 | 0 | 9995 | 1520 | 32005 | 1 | 27141 | 2024 | 418 | 0 |
| 12398 | 1560 | 27399 | 1 | 32005 | 1520 | 3924 | 0 | 418 | 2024 | 24250 | 0 |
| 27399 | 1560 | 18679 | 1 | 3924 | 1520 | 30734 | 0 | 24250 | 2024 | 27936 | 0 |
| 18679 | 1560 | 30405 | 1 | 30734 | 1520 | 28184 | 0 | 27936 | 2024 | 29148 | 0 |
| 30405 | 1560 | 25983 | 1 | 28184 | 1520 | 31941 | 1 | 29148 | 2024 | 16890 | 0 |
| 25983 | 1560 | 27535 | 1 | 31941 | 1520 | 4453 | 1 | 16890 | 2024 | 18193 | 1 |
| : | : | : | : | : | : | : | : | : | : | : |
|  | : | : | : | : | : | : | : | : | : | : | : |

Table D.2 shows the complete P, Q and R tables.

The last 4 entries of each table are used to form the initial entries in a multiplexer which is used with a "truth table" to modify the P, Q and R table entries as the message is encrypted.

Multiplexer	"Truth table"

P	Q	R
1	1	1	0	0
1	1	1	0	1
1	1	1	1	0
0	1	1	1	1

The shortened tables, table P is now 1017 entries, table Q is 1015 entries and table R is 1009 entries, are used to encrypt the message as explained below.

D.3.5	Use of the tables to encrypt the message and of the multiplexer to modify the tables

The first bit of the main message is added (mod 2) to the (mod 2) addition of the first entries in each of the shortened tables P, Q and R to form the first bit of the encrypted message. The second bit of the main message is processed in the same way with the second entries in the tables and so on. After each message bit has been processed, the corresponding P, Q and R table entries are modified based upon the entries in the multiplexer. The modification in each table is an interchange of the table entry with an entry in the multiplexer which is determined by the entries in the other two tables.

Table D.2/T.36 – The complete P, Q and R tables

Table P (1021 entries)

111010110101111100010100011100100101101100010100111111000000000010011011100001101100001110111111011011000001111000011110110101110101101001000100110110100101100010000001010000100101110101011100001001010010011000010011100010010111100010111100110000000110101111111111001111010001111111100011011001011111010100100110110111110000111101011101101111010001100000101101010001101001111100010111110100111110110001100111110100010101001000101001100110011001000110011001100111101100001011000111001110010001011110111011010000000100001010101010111011010010001000000011010011110100011000000000000100011001101110111010010000001101011100000001110100001001110010010110001110111110101010011111111001111110010000110001000111000001011111000110110110111001001111000111011111000010111001100100101110111001010111001001101011000100101101000011000110000000000110001010111010111101110100011100000000101000010101000000011100111111111110111011000101110001101010100100011010011110101010000000101011100001111001010101000010010111111111000000001101111 1110

Table Q (1019 entries)

1110001101100011101000001100111011000011100111111110000010101111000011111110001011111100001111110101111110010110111111111001110110110100111100010101100010100110110110000011010010011010101001111000010011111010111100100100011111011010111101001101110001001110110000001110110011011100011011101000101010110100110010011100001011110010000111110110110001000010011010111001000010110100000000000000101001111001000111001011111001000010111001011110011001111110011110110101000001010101111101110110011100110111101111010011001000110001101010001010110010001010001101111000000000010111100101101011010110001110111100111101100010110011001100011101101010101001011110100011000010010110100011101001011110010001111111000111000011111110010101111110011100011110001110010111000010010000101100111111111000010001010001011011000101000101010001000100111001110100100110010100000010011100101011001101001101010100101001110110100000010000100101000100101110111011011011000010000111000101011101111011001110110010011101110110000100011101100011101011100 1111

Table R (1013 entries)

1001100101000001101111100011010101110101000110100101001100110001101100011010111000001100001100011100011110100001010010011010011110000000010100110001101101001100000100100100001011110100110111010010101101001111101011110111000000001101011111111011111000101110000001100110101000010110101110000101110101100101101011101010100111101001110110111000001111101111010101000111100000111111101000110110110011101101111111100010000001110110100101000101001110010110011000111000000010111101100100101000001001110100001000001100100110010111010110110011001000111101000000010000111100010011101110101011000110001110110001100101100100110100010001001100010111001111011111001111011101110010111000110100000101110011001011100000000000100110101011011100111110111001001100001111101110011110001110001101110010101010001001011011000110001110011010100001000011110000011001011010100000001001100000001110111111011100011110111111000111010100010100100110001111011010011010011010100100110110110110001010110101111000001111000011010101110001000110100 1111

After a set of entries in the P, Q and R tables has been used to encrypt a bit of the message:

–	the table P entry is interchanged with the multiplexer entry determined by the entries in tables Q and R;

–	the table Q entry is interchanged with the multiplexer entry determined by the entries in tables R and P;

–	the table R entry is interchanged with the multiplexer entry determined by the entries in tables P and Q.

Note, the order has significance.

The following example using the first 7 entries from tables P, Q and R shows in detail how the procedure is carried out.

The first 7 entries in the initial P, Q and R tables are:

P	Q	R
	1	1	1
	1	1	0
	1	1	0
	0	0	1
	1	0	1
	0	0	0
	1	1	0

The multiplexer initial entries and the truth table are:

P	Q	R	  Truth table

1	1	1	0	0
	1	1	1	0	1
	1	1	1	1	0
	0	1	1	1	1

The first entries in tables P, Q and R are 1, 1 and 1 respectively. The first entry in table P is interchanged according to the first entries in tables Q and R, these are 1 and 1. From the "truth table", the first entry in table P is interchanged with the entry in the P column of the multiplexer which corresponds to (1, 1) in the "truth table", in this case a 0.

The first entry in Q is interchanged with the entry in the Q column of the multiplexer corresponding to (1, 1), in this case a 1.

Similarly the first entry in R is interchanged with the entry in the R column of the multiplexer corresponding to (1, 1), in this case a 1.

The result of this is that the first entries in tables P, Q and R, i.e. 1, 1, 1, become 0, 1, 1 respectively. These entries will be used the next time the first entry in a table is used.

The multiplexer entries after these interchanges are:

P	Q	R

1	1	1
	1	1	1
	1	1	1
	1	1	1

The new multiplexer entries are then used with the second entries from tables P, Q and R in exactly the same way. The result of this is that the second entries in tables P, Q and R, 1, 1, 0 become 1, 1, 1 and the multiplexer becomes:

P	Q	R

1	1	1
	1	1	1
	1	1	1
	1	1	0

Following the above procedure for the first 5 message bits using the first 5 entries in tables P, Q and R gives the following results:

Initial tables	Tables after encrypting 5 message bits

Entry	P	Q	R	P	Q	R

1	1	1	1	0	1	1

2	1	1	0	1	1	1

3	1	1	0	1	1	0

4	0	0	1	1	1	1

5	1	0	1	0	1	1

6	0	0	0	0	0	0

7	1	1	0	1	1	0

:	:	:	:	:	:	:

:	:	:	:	:	:	:

The multiplexer settings used to modify the tables after encrypting each of the first 5 message bits are:

After bit number:	1	2	3	4	5

(initial setting)

P	Q	R	P	Q	R	P	Q	R	P	Q	R	P	Q	R	P	Q	R

1	1	1	1	1	1	1	1	1	1	1	1	1	1	1	1	1	1

1	1	1	1	1	1	1	1	1	1	1	1	0	1	1	1	1	1

1	1	1	1	1	1	1	1	1	1	1	1	1	0	1	1	0	1

0	1	1	1	1	1	1	1	0	1	1	0	1	1	0	1	0	0

The above procedure is followed for each of the message bits. After table R uses entry number 1009, it returns to entry number 1 (the top of the table) and continues the procedure with the table's new entries. Similarly tables Q and P, after bit numbers 1015 and 1017 respectively, "restart" at their new first entries. The procedure is continued until the complete message has been encrypted.

The encrypted message is then sent to Y. Y uses the same SSx with the HFX40 algorithm to generate the identical tables and modifying multiplexer; subtracting the (mod 2) addition of the entries in the tables from the encrypted message to recover the original compressed facsimile message and modifying the tables using the multiplexer.

Annex E

Procedures for the use of the HFX40-I hashing system to provide message 
integrity for secure document facsimile transmission

E.1	Scope

This Annex describes the HFX40-I hashing algorithm, in terms of its use, the necessary calculations and the information to be exchanged between the facsimile terminals to provide integrity for a transmitted facsimile message as either a selected or pre-programmed alternative to the encryption of the message.

In order to provide message integrity, a hash function is used to map arbitrarily long messages into fixed length values. The hash function generated by the HFX40-I algorithm maps the compressed facsimile message to a sequence of decimal digits.

A hash function is cryptographically strong if it is difficult to find any message that maps to a given hash value or any pair of messages that map to the same hash value. To protect against the possibility of this being achieved by a third party, the HFX40-I algorithm uses primitives derived from a secret key. The resultant hash value of the message is also doubly encrypted to prevent the possibility of a third party reversing the hash function to discover the original primitives.

The HFX40-I hashing algorithm is based upon the use of 19 system prime numbers. These same 19 prime numbers are used also with the HKM key management system which is defined in Annex C and the message carrier cipher which is described in Annex E. However, this Annex does not cover the key management system nor the message carrier cipher.

The secure exchange of the secret key follows the procedures detailed in Annex C.

Example calculations are given in E.3 and E.4 and these can be used to verify the implementation of the algorithm.

The HFX40-I system is covered by intellectual property rights; however, the owner of those rights has agreed to follow the TSB code of practice. Further details can be obtained from the TSB.

E.2	Use of the HFX40-I hashing system

To send a message protected for integrity, the user at X establishes a call to Y with which mutual registration has been carried out (see Annex C). Following successful mutual authentication of X and Y (see Annex C), X generates SSx which is sent securely to Y, using the procedure for the secure transfer of a secret key (procSTKxy) defined in Annex C.

X also uses SSx, to form the primitives for the hash function, HFX40-I. The primitives are used by HFX40-I for modular arithmetical calculations to operate on the compressed facsimile message byte by byte. The moduli for the modular arithmetic are provided by a set of 19 system modulating prime numbers stored in the facsimile terminal. The order in which the 19 prime numbers are used is derived from SSx. This set of prime numbers is the same as that used by the HKM key management system (Annex C) and the HFX40 carrier cipher algorithm (Annex D).

The output of one sequence of modular calculations with one byte of the message is used as the input to the calculation for the next byte of the message, and so on until the complete message has been processed. The resulting PH is doubly encrypted by the session key. The first encryption is a one-way function which scrambles the 24 digits of PH to form

SH. The second encryption uses a one-way variant of the HKM cipher to form ESH. X sends the compressed facsimile message and ESH to Y.

Y recovers SSx using procSTKxy and using the HFX40-I algorithm calculates PH of the received compressed facsimile message. Y performs the same two encryptions of PH as X to form ESH. If ESH matches the value of ESH received from X, not only is the integrity of the message confirmed but the authentication of the sender is also assured. Any discrepancy between the calculated ESH and the received ESH is evidence of loss of integrity.

To provide confirmation or denial of integrity to X, Y generates IMy. IMy is a 12-digit random number selected from the digits 2 to 9 in which one digit is randomly selected to be replaced with a 1 to indicate confirmation of integrity or a 0 to indicate denial. Y sends IMy securely to X using SSx and procSTKyx.

Example responses:

IMy = 257795199982	Integrity confirmed.

IMy = 317736845378	Integrity confirmed.

IMy = 738543680892	Integrity denied.

IMy = 457745204639	Integrity denied.

E.3	The HFX40-I hashing system for use with facsimile terminals

E.3.1	Introduction

This subclause describes the HFX40-I hashing system in terms of the numbers to be stored and the rules for the computations carried out using these numbers to generate PH, SH and ESH. The rules are best explained using numerical examples. The numerical examples also use test values to allow verification of the implementation.

E.3.2	Stored information

All terminals are equipped with the same 19 system modulating prime numbers (also used in Annexes C and D).

32603	32507	32183	32003	31847	31607	31583	31547	31259

31139	30803	30539	30467	30347	30323	30203	29879	29759	29663

E.3.3	Re-ordering of the system modulating prime numbers

X uses SSx to derive three initial phase primitive values, P(0) to P(2) and three base primitive values, B(0) to B(2) to be used with the first three system modulating prime numbers, 32603, 32507 and 32183 to generate 19 entries in a (mod 19) PRS.

SSx is split into six overlapping groups of three digits. The first group being formed of the first 3 digits, the second from the second, third and fourth digits and so on. The first group of three digits are XOR'd with the second, the result of this is XOR'd with the third and so on. Two is added to each of the resulting groups to prevent occurrences of an all zero result. The resulting values then are used as the initial phase and base primitive values, P(0) to P(2) and B(0) to B(2). Table E.1 shows an example for SSx = 568702123345.

Table E.1/T.36 – Generation of P(0) to P(2) and B(0) to B(2) to re-order 
the system modulating prime numbers

| SSx = 568702123345 The six groups are: 568, 870, 021, 123, 334 and 345 |
| --- |
| Group |
|  | Result | Add 2 | Phase/Base value |
| 568 |
|  | 568 | 570 | P(0) |
| 870 | XOR | 568 | 350 | 352 | P(1) |
| 021 | XOR | 350 | 331 | 333 | P(2) |
| 123 | XOR | 331 | 304 | 306 | B(0) |
| 334 | XOR | 304 | 126 | 128 | B(1) |
| 345 | XOR | 126 | 295 | 297 | B(2) |

The phase and base primitive values are then used with the first 3 system modulating prime numbers, 32603, 32507 and 32183, in the HKM algorithm to generate the first 19 values in a (mod 19) PRS. An example of the use of HKM with these test values is given in E.4.

The (mod 19) PRS generated is:

10,  14,  0,  12,  2,  14,  9,  6,  10,  1,  2,  9,  17,  6,  14,  5,  3,  15,  5

The 19 system modulating prime numbers are transposed using the PRS to determine the order in which they are to be used in the HFX40-I hash algorithm. The first value in the PRS determines which "numbered" prime is interchanged with the prime in the first position, the second value, which "numbered" prime is interchanged with the prime in the second position, and so on. Table E.2 shows the 19 stages of transpositions against the PRS.

Table E.2/T.36 – Transposing system modulating prime numbers, "numbers" 0 to 18, 
using the (mod 19) PRS

| Step PRS | Prime "number " (0 to 18) |
| --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 |
| 1 | 10 | 10 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 0 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 |
| 2 | 14 | 10 | 14 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 0 | 11 | 12 | 13 | 1 | 15 | 16 | 17 | 18 |
| 3 | 0 | 2 | 14 | 10 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 0 | 11 | 12 | 13 | 1 | 15 | 16 | 17 | 18 |
| 4 | 12 | 2 | 14 | 10 | 12 | 4 | 5 | 6 | 7 | 8 | 9 | 0 | 11 | 3 | 13 | 1 | 15 | 16 | 17 | 18 |
| 5 | 2 | 2 | 14 | 4 | 12 | 10 | 5 | 6 | 7 | 8 | 9 | 0 | 11 | 3 | 13 | 1 | 15 | 16 | 17 | 18 |
| 6 | 14 | 2 | 14 | 4 | 12 | 10 | 1 | 6 | 7 | 8 | 9 | 0 | 11 | 3 | 13 | 5 | 15 | 16 | 17 | 18 |
| 7 | 9 | 2 | 14 | 4 | 12 | 10 | 1 | 9 | 7 | 8 | 6 | 0 | 11 | 3 | 13 | 5 | 15 | 16 | 17 | 18 |
| 8 | 6 | 2 | 14 | 4 | 12 | 10 | 1 | 7 | 9 | 8 | 6 | 0 | 11 | 3 | 13 | 5 | 15 | 16 | 17 | 18 |
| 9 | 10 | 2 | 14 | 4 | 12 | 10 | 1 | 7 | 9 | 0 | 6 | 8 | 11 | 3 | 13 | 5 | 15 | 16 | 17 | 18 |
| 10 | 1 | 2 | 6 | 4 | 12 | 10 | 1 | 7 | 9 | 0 | 14 | 8 | 11 | 3 | 13 | 5 | 15 | 16 | 17 | 18 |
| 11 | 2 | 2 | 6 | 8 | 12 | 10 | 1 | 7 | 9 | 0 | 14 | 4 | 11 | 3 | 13 | 5 | 15 | 16 | 17 | 18 |
| 12 | 9 | 2 | 6 | 8 | 12 | 10 | 1 | 7 | 9 | 0 | 11 | 4 | 14 | 3 | 13 | 5 | 15 | 16 | 17 | 18 |
| 13 | 17 | 2 | 6 | 8 | 12 | 10 | 1 | 7 | 9 | 0 | 11 | 4 | 14 | 17 | 13 | 5 | 15 | 16 | 3 | 18 |
| 14 | 6 | 2 | 6 | 8 | 12 | 10 | 1 | 13 | 9 | 0 | 11 | 4 | 14 | 17 | 7 | 5 | 15 | 16 | 3 | 18 |
| 15 | 14 | 2 | 6 | 8 | 12 | 10 | 1 | 13 | 9 | 0 | 11 | 4 | 14 | 17 | 7 | 5 | 15 | 16 | 3 | 18 |
| 16 | 5 | 2 | 6 | 8 | 12 | 10 | 15 | 13 | 9 | 0 | 11 | 4 | 14 | 17 | 7 | 5 | 1 | 16 | 3 | 18 |
| 17 | 3 | 2 | 6 | 8 | 16 | 10 | 15 | 13 | 9 | 0 | 11 | 4 | 14 | 17 | 7 | 5 | 1 | 12 | 3 | 18 |
| 18 | 15 | 2 | 6 | 8 | 16 | 10 | 15 | 13 | 9 | 0 | 11 | 4 | 14 | 17 | 7 | 5 | 3 | 12 | 1 | 18 |
| 19 | 5 | 2 | 6 | 8 | 16 | 10 | 18 | 13 | 9 | 0 | 11 | 4 | 14 | 17 | 7 | 5 | 3 | 12 | 1 | 15 |

In the above process, the first step interchanged the first prime with prime "number" 10. The second step interchanged the second prime with prime "number" 14. The final step interchanged the nineteenth prime with prime "number" 5.

The final order of the system modulating prime "numbers" is:

2,  6,  8,  16,  10,  18,  13,  9,  0,  11,  4,  14,  17,  7,  5,  3,  12,  1,  15

giving the final order of the system modulating prime numbers:

32183, 31583, 31259, 29879, 30803, 29663, 30347, 31139, 32603

30539, 31847, 30323, 29759, 31547, 31607, 32003, 30467, 32507, 30203

The first three are used with the HFX40-I algorithm to generate PH and in the two encryptions SH and ESH.

E.3.4	Calculation of the primitives to be used with HFX40-I

Eight phase primitives P(0) to P(7) are derived from SSx as follows.

SSx, 568702123345, is split into eight overlapping groups of four digits. The first group being formed from the first 4 digits, the second from the third to sixth digits and so on. The first group of four digits are XOR'd with the second, the result of this is XOR'd with the third and so on. Two is added to each of the resulting values to prevent occurrences of an all zero result and the resulting values are used as the initial values for P(0) to P(7).

An example with SSx = 568702123345 is shown in Table E.3.

Table E.3/T.36 – Calculation of the primitives to be used with HFX40-I

| SSx = 568702123345 The eight groups are: 5687, 8702, 7021, 0212, 2123, 1233, 2334 and 3345 |
| --- |
| Group |
|  | Result | Add 2 | Phase/Base value |
| 5687 |
| 5689 | P(0) |
| 8702 | XOR | 5687 | 14281 | 14283 | P(1) |
| 7021 | XOR | 14281 | 11428 | 11430 | P(2) |
| 212 | XOR | 11428 | 11376 | 11378 | P(3) |
| 2123 | XOR | 11376 | 9275 | 9277 | P(4) |
| 1233 | XOR | 9275 | 8426 | 8428 | P(5) |
| 2334 | XOR | 8426 | 10740 | 10742 | P(6) |
| 3345 | XOR | 10740 | 9445 | 9447 | P(7) |

E.3.5	Calculation of PH

The phase values, P(0) to P(7) are used in rotation starting with P(1). When the initial value for P(1) has been used in the calculations with the first byte of the compressed message, it is replaced with a new value generated by the calculations detailed in the following paragraphs. This new value of P(1) is used the next time P(1) is used in the calculations. This same procedure is continued with P(2), P(3), etc. The whole procedure is continued until the end of the message and is explained in more detail below.

Let the current phase value being used be P(n). P(n) is modified to form P¢(n) by adding to P(n) the decimal ASCII value of the current message byte, b, and the Q (mod M) value, q, obtained from the previous byte. For the first byte, q = 0.

P¢(n) = P(n) + b + q

Q is derived from P¢(n) by multiplying by (b + 1).

Q = P¢(n) * (b + 1)

Q is modulated by one of the 19 re-ordered system modulating prime numbers used in rotation starting from Prime (1) to form the new P(n) and q values. For example, for the first byte of the message, Q (mod M) forms the q value for the second byte and P(n) for the ninth byte. The order of the system modulating prime numbers is as determined in E.3.3. For the first byte of the message, Prime (1) is used, for the second byte Prime (2) and so on.

Table E.4 shows the calculations to produce the hash for a 29 byte compressed facsimile message.

PH, is formed by concatenating the 3 least significant digits of the final eight phase values taken in the order P(0), P(1), P(2), etc. to P(7) to produce a 24-digit number. In this example, from Table E.4:

PH = 171 666 427 631 042 698 579 505

E.3.6	First encryption (scrambling) of PH to form SH

SSx is used to derive three phase primitives, P(0) to P(2) and three base primitives, B(0) to B(2). SSx is split into six overlapping groups of three. The first digits 1-3 form P(0), digits 3-5 form P(1), digits 4-6 form P(2), digits 7-9 form B(0), digits 9-11 form B(1) and digits 10-12 form B(2).

The first group of three digits are XOR'd with the second, the result of this is XOR'd with the third and so on. Two is added to each of the resulting groups of three to prevent occurrences of an all zero result. The new values are combined with the first 6 groups of three digits from PH to give the new values of P(0) to P(2) and B(0) to B(2).

Table E.5 shows a sample calculation using the same example values as previously.

Table E.4/T.36 – Hash calculations for a 29 byte compressed facsimile message

| b | y | P(n) | q | P¢(n) | Q | M | Q(mod M) | Hash result |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 103 | 1 | 14283 | 0 | 14386 | 1496144 | 31583 | 11743 |
| 121 | 2 | 11430 | 11743 | 23294 | 2841868 | 31259 | 28558 |
| 2 | 3 | 11378 | 28558 | 39938 | 119814 | 29879 | 298 |
| 0 | 4 | 9277 | 298 | 9575 | 9575 | 30803 | 9575 |
| 34 | 5 | 8428 | 9575 | 18037 | 631295 | 29663 | 8372 |
| 79 | 6 | 10742 | 8372 | 19193 | 1535440 | 30347 | 18090 |
| 92 | 7 | 9447 | 18090 | 27629 | 2569497 | 31139 | 16099 |
| 92 | 0 | 5689 | 16099 | 21880 | 2034840 | 32603 | 13454 |
| 33 | 1 | 11743 | 13454 | 25230 | 857820 | 30539 | 2728 |
| 33 | 2 | 28558 | 2728 | 31319 | 1064846 | 31847 | 13895 |
| 33 | 3 | 298 | 13895 | 14226 | 483684 | 30323 | 28839 |
| 10 | 4 | 9575 | 28839 | 38424 | 422664 | 29759 | 6038 |
| 4 | 5 | 8372 | 6038 | 14414 | 72070 | 31547 | 8976 |
| 238 | 6 | 18090 | 8976 | 27304 | 6525656 | 31607 | 14614 |
| 161 | 7 | 16099 | 14614 | 30874 | 5001588 | 32003 | 9120 |
| 141 | 0 | 13454 | 9120 | 22715 | 3225530 | 30467 | 26495 |
| 24 | 1 | 2728 | 26495 | 29247 | 731175 | 32507 | 16021 |
| 2 | 2 | 13895 | 16021 | 29918 | 89754 | 30203 | 29348 |
| 3 | 3 | 28839 | 29348 | 58190 | 232760 | 32183 | 7479 |
| 62 | 4 | 6038 | 7479 | 13579 | 855477 | 31583 | 2736 |
| 149 | 5 | 8976 | 2736 | 11861 | 1779150 | 31259 | 28646 |
| 66 | 6 | 14614 | 28646 | 43326 | 2902842 | 29879 | 4579 | 579 | [value for P(6)] |
| 11 | 7 | 9120 | 4579 | 13710 | 164520 | 30803 | 10505 | 505 | [value for P(7)] |
| 93 | 0 | 26495 | 10505 | 37093 | 3486742 | 29663 | 16171 | 171 | [value for P(0)] |
| 39 | 1 | 16021 | 16171 | 32231 | 1289240 | 30347 | 14666 | 666 | [value for P(1)] |
| 133 | 2 | 29348 | 14666 | 44147 | 5915698 | 31139 | 30427 | 427 | [value for P(2)] |
| 19 | 3 | 7479 | 30427 | 37925 | 758500 | 32603 | 8631 | 631 | [value for P(3)] |
| 124 | 4 | 2736 | 8631 | 11491 | 1436375 | 30539 | 1042 | 042 | [value for P(4)] |
| 92 | 5 | 28646 | 1042 | 29780 | 2769540 | 31847 | 30698 | 698 | [value for P(5)] |

Table E.5/T.36 – Calculation of P(0) to P(2) and B(0) to B(2) for the first encryption of PH

| Session Key = 568702123345 |
| --- |
| Initial P and B values |
| Add 2 |
| PH groups |
| New P and B values |
|  | 568 |
| 568 | 570 | + | 171 | = | 741 | P(0) |
| 870 XOR 568 | = | 350 | 352 | + | 666 | = | 1018 | P(1) |
| 021 XOR 350 | = | 331 | 333 | + | 427 | = | 760 | P(2) |
| 123 XOR 331 | = | 304 | 306 | + | 631 | = | 937 | B(0) |
| 334 XOR 304 | = | 126 | 128 | + | 042 | = | 170 | B(1) |
| 345 XOR 126 | = | 295 | 297 | + | 698 | = | 995 | B(2) |

The phase and base primitive values, P(0) to P(2) and B(0) to B(2) above, with the first three system modulating prime numbers, 32183, 31583 and 31259 from the re-ordered sequence derived in E.3.3, are used in the HKM algorithm in a similar way to that shown in E.4, to form the following 24-entry (mod 24) PRS:

4, 5, 4, 16, 2, 6, 16, 12, 24, 21, 6, 5, 11, 4, 8, 21, 22, 5, 24, 9, 3, 16, 19, 8

This PRS is used to transpose all 24 digits of PH to form SH. The first value in the PRS determines the position of the digit in PH which is interchanged with the first digit in PH, the second value determines the position of the digit which is interchanged with the second digit and so on. For the above PRS, the first step interchanges position 1 with position 4, the second step interchanges positions 2 and 5 and so on. This process continues until the final step in which position 24 is exchanged with position 8. Table E.6 shows the 24 stages of transpositions against the PRS.

Table E.6/T.36 –Transposition of PH to create SH

| Step/position | PRS | PH 171 666 427 631 042 698 579 505 |
| --- | --- | --- |
| 1 | 4 | 671 166 427 631 042 698 579 505 |
| 2 | 5 | 661 176 427 631 042 698 579 505 |
| 3 | 4 | 661 176 427 631 042 698 579 505 |
| 4 | 16 | 661 676 427 631 042 198 579 505 |
| 5 | 2 | 671 666 427 631 042 198 579 505 |
| 6 | 6 | 671 666 427 631 042 198 579 505 |
| 7 | 16 | 671 666 127 631 042 498 579 505 |
| 8 | 12 | 671 666 117 632 042 498 579 505 |
| 9 | 24 | 671 666 115 632 042 498 579 507 |
| 10 | 21 | 671 666 115 932 042 498 576 507 |
| 11 | 6 | 671 663 115 962 042 498 576 507 |
| 12 | 5 | 671 623 115 966 042 498 576 507 |
| 13 | 11 | 671 623 115 906 642 498 576 507 |
| 14 | 4 | 671 423 115 906 662 498 576 507 |
| 15 | 8 | 671 423 125 906 661 498 576 507 |
| 16 | 21 | 671 423 125 906 661 698 574 507 |
| 17 | 22 | 671 423 125 906 661 658 574 907 |
| 18 | 5 | 671 483 125 906 661 652 574 907 |
| 19 | 24 | 671 483 125 906 661 652 774 905 |
| 20 | 9 | 671 483 127 906 661 652 754 905 |
| 21 | 3 | 674 483 127 906 661 652 751 905 |
| 22 | 16 | 674 483 127 906 661 952 751 605 |
| 23 | 19 | 674 483 127 906 661 952 051 675 |
| 24 | 8 | 674 483 157 906 661 952 051 672 |
| SH = 674 483 157 906 661 952 051 672 |

E.3.7	Encryption of SH to form ESH

Three phase primitives, P(0) to P(2), and three base primitives B(0) to B(2) are derived from SSx in a similar process to that in E.3.6, except that the values resulting from the XOR and addition of 2 calculations are combined with the first six groups of three digits in SH to give the new values which are used as the initial values of P(0) to P(2) and B(0) to B(2).

Table E.7 shows the results for the calculations using the SH value obtained in E.3.6.

Table E.7/T.36 – Calculation of the primitives for the Encryption of EH to form ESH

| SH = 674 483 157 906 661 952 051 672 |
| --- |
| Initial P and B values |
| Add 2 |
| SH Groups |
| New P and B values |
|  | 568 |
| 568 | 570 | + | 674 | = | 1244 | P(0) |
| 870 XOR 568 | = | 350 | 352 | + | 483 | = | 835 | P(1) |
| 021 XOR 350 | = | 331 | 333 | + | 157 | = | 490 | P(2) |
| 123 XOR 331 | = | 304 | 306 | + | 906 | = | 1212 | B(0) |
| 334 XOR 304 | = | 126 | 128 | + | 661 | = | 789 | B(1) |
| 345 XOR 126 | = | 295 | 297 | + | 952 | = | 1249 | B(2) |

The phase and base primitive values, P(0) to P(2) and B(0) to B(2) above, together with the first three system modulating prime numbers 32183, 31583 and 31259, from the re-ordered sequence derived in E.3.3, are used in the HKM algorithm in a similar way to the example in E.4, to generate 24 entries in a (mod 10) PRS which are added (mod 10) to SH to form ESH.

SH:	674 483 157 906 661 952 051 672

(mod 10) PRS:	402 025 183 343 270 975 304 836

ESH:	076 408 230 249 831 827 355 408

E.4	Use of the HKM Algorithm to produce a PseudoRandom Sequence

E.4.1	Introduction

This subclause provides an example using test values to verify the implementation of the operation of the HKM algorithm using modular arithmetic to generate a PseudoRandom Sequence, PRS.

The modular arithmetic uses phase and base primitive values derived in a number of ways from a secret number, such as a session key, or a combination of a secret number and other identifying information, together with moduli taken from the universal set of system modulating prime numbers to generate a PRS which may be further modulated to form a specific PRS.

E.4.1.1	Calculations using HKM to generate a PRS

The test values used in this example are those used in E.3.3 to form the 19-entry (mod 19) PRS to re-order the system modulating prime numbers.

The 3 phase primitives, P(0) to P(2) and the 3 base primitives B(0) to B(2) are:

P(0) = 570	B(0) = 306

P(1) = 352	B(1) = 128

P(2) = 333	B(2) = 297

The 3 system modulating primes are:	32603, 32507 and 32183

Using the first "set" of phase, base and prime values, P(0), B(0) and 32603:

P(0) is multiplied by B(0)

570 * 306= 174420

174420 (mod the first prime) = 174420 (mod 32603) = 11405

11405 is then used as a new phase value and is multiplied by the base value, B(0)

11405 * 306 = 3489930

3489930 (mod the first prime) = 3489930 (mod 32603) = 1409

This process is carried out a total of 19 times (corresponding to the number of primes to be re-ordered). The complete process is also repeated for the remaining 2 "sets" of phase, base and prime values to generate similar sequences.

The results of the first calculation from each of the 3 phase, base and prime "sets" are added to form the first value in the total column. The results from each of the other calculations are added to form the other entries in the total column. The resulting sequence in this example is modulated by 19 to generate a (mod 19) PRS. Other suitable numbers can be used to modulate the sequence to generate other specific PRSs.

The full set of calculations is shown in Table E.8.

Table E.8/T.36 – Calculations using HKM to generate a 19-entry (mod 19) PRS

| Modulating Prime B(n) P(n) | 32603 306 570 | 32507 128 352 | 32183 297 333 | Total | (mod 19) PRS |
| --- | --- | --- | --- | --- | --- |
|  | 11405 | 12549 | 2352 | 26306 | 10 |
|  | 1409 | 13429 | 22701 | 37539 | 14 |
|  | 7315 | 28548 | 15950 | 51813 | 0 |
|  | 21386 | 13360 | 6249 | 40995 | 12 |
|  | 23516 | 19716 | 21522 | 64754 | 2 |
|  | 23236 | 20609 | 19800 | 63645 | 14 |
|  | 2762 | 4885 | 23294 | 30941 | 9 |
|  | 30097 | 7647 | 31156 | 68900 | 6 |
|  | 15636 | 3606 | 16811 | 36053 | 10 |
|  | 24578 | 6470 | 4502 | 35550 | 1 |
|  | 22178 | 15485 | 17591 | 55254 | 2 |
|  | 5044 | 31660 | 10881 | 47585 | 9 |
|  | 11123 | 21612 | 13357 | 46092 | 17 |
|  | 12926 | 3241 | 8520 | 24687 | 6 |
|  | 10393 | 24764 | 20166 | 55323 | 14 |
|  | 17767 | 16613 | 3264 | 37644 | 5 |
|  | 24604 | 13509 | 3918 | 42031 | 3 |
|  | 30134 | 6281 | 5058 | 41473 | 15 |
|  | 26958 | 23800 | 21808 | 72566 | 5 |

| ITU-T RECOMMENDATIONS SERIES |
| --- |
| Series A | Organization of the work of the ITU-T |
| Series B | Means of expression: definitions, symbols, classification |
| Series C | General telecommunication statistics |
| Series D | General tariff principles |
| Series E | Overall network operation, telephone service, service operation and human factors |
| Series F | Non-telephone telecommunication services |
| Series G | Transmission systems and media, digital systems and networks |
| Series H | Audiovisual and multimedia systems |
| Series I | Integrated services digital network |
| Series J | Transmission of television, sound programme and other multimedia signals |
| Series K | Protection against interference |
| Series L | Construction, installation and protection of cables and other elements of outside plant |
| Series M | Maintenance: international transmission systems, telephone circuits, telegraphy, facsimile and leased circuits |
| Series N | Maintenance: international sound programme and television transmission circuits |
| Series O | Specifications of measuring equipment |
| Series P | Telephone transmission quality, telephone installations, local line networks |
| Series Q | Switching and signalling |
| Series R | Telegraph transmission |
| Series S | Telegraph services terminal equipment |
| Series T | Terminals for telematic services |
| Series U | Telegraph switching |
| Series V | Data communication over the telephone network |
| Series X | Data networks and open system communication |
| Series Z | Programming languages |

# Comments

Page: 1
A: ASCII	American Standard Code for Information Interchange

Page: 1
A: ESH	Encrypted and Scrambled plain Hash

Page: 1
A: ESIM		Encrypted Scrambled Integrity Message

Page: 1
A: ESSK	Encrypted Scrambled Secret Key

Page: 1
A: HKM	 	HKM encryption algorithm

Page: 1
A: HKMD+1	double encryption using the HKM algorithm

Page: 1
A: IDx	Last six digits of the facsimile identification (facsimile telephone number) of X

Page: 1
A: IDy	Last six digits of the facsimile identification (facsimile telephone number) of Y

Page: 1
A: IM	Integrity Message

Page: 1
A: IMy	Integrity Message generated by Y to confirm or deny integrity of the received message

Page: 1
A: ITU-T	International Telecommunication Union – Telecommunication Standardization Sector

Page: 1
A: mod n	modulo arithmetic using base n

Page: 2
A: MPx		Mutual Primitive of X

Page: 2
A: MPy		Mutual Primitive of Y

Page: 2
A: OT	One-Time key

Page: 2
A: OTx		One-Time key as first used by X in X's registration with Y

Page: 2
A: OTy		One-Time key as first used by Y

Page: 2
A: PH	Plain Hash

Page: 2
A: P(n)	Phase value (n)

Page: 2
A: procREGxy		Procedure for registration between X and Y

Page: 2
A: procSTKxy		Procedure for the secure transmission of a secret key from X to Y

Page: 2
A: PRS	PseudoRandom Sequence

Page: 2
A: RCN	Registered Crypt Number

Page: 2
A: RNCn	Non-secret random number associated with an SCn

Page: 2
A: RNIM	Non-secret random number associated with an IM

Page: 2
A: RNK	Non-secret random number used to provide variation of the primitives generated from MPx when encrypting an SK

Page: 2
A: RNSRn	Non-secret random number associated with an SRn

Page: 2
A: RNSSn	Non-secret random number associated with an SSn

Page: 2
A: SCn	Secret Challenge key, number n

Page: 2
A: SH	Scrambled plain Hash

Page: 2
A: SK	Secret Key

Page: 2
A: SRn	Secret Response key, number n

Page: 2
A: SS	Secret Session key

Page: 2
A: SSK	Scrambled Secret Key

Page: 2
A: SSn	Secret Session key, number n

Page: 2
A: SSx	Secret Session key generated by X

Page: 2
A: TKx	Transfer Key, an encryption of MPx generated by X

Page: 2
A: UCN	Unique Crypt Number

Page: 3
A: UIN	Unique Identity Number

Page: 3
A: XOR’d	Exclusively OR’d