|  | INTERNATIONAL TELECOMMUNICATION UNION |
| --- | --- |

| ITU-T | T.563 |
| --- | --- |
| TELECOMMUNICATION STANDARDIZATION SECTOR OF ITU | Amendment 3 (04/99) |

SERIES T: TERMINALS FOR TELEMATIC SERVICES

Terminal characteristics for Group 4 facsimile apparatus

Amendment 3

ITU-T  Recommendation  T.563  –  Amendment 3

(Previously  CCITT  Recommendation)

ITU-T  T-SERIES  RECOMMENDATIONS

TERMINALS FOR TELEMATIC SERVICES

For further details, please refer to ITU-T List of Recommendations.

ITU-T  RECOMMENDATION  T.563

TERMINAL  CHARACTERISTICS  FOR  GROUP  4  FACSIMILE  APPARATUS

AMENDMENT  3

Summary

Amendment 3 introduces higher resolutions of 600 dpi and 1200 dpi to Recommendation T.563.

Source

Amendment 3 to ITU-T Recommendation T.563 was prepared by ITU-T Study Group 8 (1997-2000) and was approved under the WTSC Resolution No. 1 procedure on the 1st of April 1999.

FOREWORD

ITU (International Telecommunication Union) is the United Nations Specialized Agency in the field of telecommunications. The ITU Telecommunication Standardization Sector (ITU-T) is a permanent organ of the ITU. The ITU-T is responsible for studying technical, operating and tariff questions and issuing Recommendations on them with a view to standardizing telecommunications on a worldwide basis.

The World Telecommunication Standardization Conference (WTSC), which meets every four years, establishes the topics for study by the ITU-T Study Groups which, in their turn, produce Recommendations on these topics.

The approval of Recommendations by the Members of the ITU-T is covered by the procedure laid down in WTSC Resolution No. 1.

In some areas of information technology which fall within ITU-T’s purview, the necessary standards are prepared on a collaborative basis with ISO and IEC.

NOTE

In this Recommendation the term recognized operating agency (ROA) includes any individual, company, corporation or governmental organization that operates a public correspondence service. The terms Administration, ROA and public correspondence are defined in the Constitution of the ITU (Geneva, 1992).

INTELLECTUAL  PROPERTY  RIGHTS

The ITU draws attention to the possibility that the practice or implementation of this Recommendation may involve the use of a claimed Intellectual Property Right. The ITU takes no position concerning the evidence, validity or applicability of claimed Intellectual Property Rights, whether asserted by ITU members or others outside of the Recommendation development process.

As of the date of approval of this Recommendation, the ITU had not received notice of intellectual property, protected by patents, which may be required to implement this Recommendation. However, implementors are cautioned that this may not represent the latest information and are therefore strongly urged to consult the TSB patent database.

  ITU  1999

All rights reserved. No part of this publication may be reproduced or utilized in any form or by any means, electronic or mechanical, including photocopying and microfilm, without permission in writing from the ITU.

CONTENTS

Page

1)	Table 1	1

2)	Table 2a	1

3)	Table 2b	2

4)	Table 3	2

5)	Subclause B.6.2	3

6)	Subclause I.2.2	3

Introduction and background

To keep consistency between G3 facsimile service and G4 facsimile service, it is important to apply higher resolutions to G4 facsimile.

This Amendment 3 introduces the higher resolutions of 600 dpi and 1200 dpi.

Recommendation T.563

Recommendation T.563/Amd.3     (04/99)

TERMINAL  CHARACTERISTICS  FOR  GROUP  4  FACSIMILE  APPARATUS

AMENDMENT  3

(Geneva, 1999)

# 1)	Table 1

Amend Table 1/T.563 to read as follows:

Table 1/T.563

| Resolution (pels/25.4 mm) | Horizontal and vertical tolerance (%) |
| --- | --- |
| 200  200 240  240 300  300 400  400 600  600 1200  1200 |  1  1  1  1  1  1 |

# 2)	Table 2a

Amend Table 2a/T.563 to read as follows:

Table 2a/T.563 – Number of pels and scan line length for different paper sizes

|  |  | ISO A4 | North American Letter | ISO B4 | ISO A3 | Japanese Legal | Japanese Letter | North American Legal | North American Ledger |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Number of | Resolution (pels/ 25.4 mm) |  |  |  |  |  |  |  |  |
| picture elements along a scan line | 200 240 300 400 600 1200 | 1728 2074 2592 3456 5184 10368 | 1728 2074 2592 3456 5184 10368 | 2048 2458 3072 4096 6144 12288 | 2432 2918 3648 4864 7296 14592 | 2048 2458 3072 4096 6144 12288 | 1728 2074 2592 3456 5184 10368 | 1728 2074 2592 3456 5184 10368 | 2432 2918 3648 4864 7296 14592 |
| Scan line length (mm) (P) | 219.46 | 219.46 | 260.10 | 308.86 | 260.10 | 219.46 | 219.46 | 308.86 |
| Paper width (mm) (Q) | 210 | 215.9 | 250 | 297 | 257 | 182 | 215.9 | 279.4 |
| P – Q | 9.46 | 3.56 | 10.10 | 11.86 | 3.10 | 37.46 | 3.56 | 29.46 |

# 3)	Table 2b

Amend Table 2b/T.563 to read as follows:

Table 2b/T.563 – Nominal number of scan lines for different paper sizes

|  |  | ISO A4 | North American Letter | ISO B4 | ISO A3 | Japanese Legal | Japanese Letter | North American Legal | North American Ledger |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Nominal number | Resolution (pels/ 25.4 mm) |  |  |  |  |  |  |  |  |
| of scan lines per page for each pel-transmission density | 200 240 300 400 600 1200 | 2339 2806 3508 4677 7016 14031 | 2200 2640 3300 4400 6600 13200 | 2780 3335 4169 5559 8339 16677 | 3307 3969 4961 6614 9921 19843 | 2866 3439 4299 5732 8598 17197 | 2024 2428 3035 4047 6071 12142 | 2800 3360 4200 5600 8400 16800 | 3400 4080 5100 6800 10200 20400 |
| Nominal paper length (mm) | 297 | 279.4 | 353 | 420 | 364 | 257 | 355.6 | 431.8 |

# 4)	Table 3

Amend Table 3/T.563 to read as follows:

Table 3/T.563 – Blanking and address reference point for different paper sizes

| Paper size | Resolution (pels/25.4 mm) | Pels per line | Pels per each paper size line | Blanking margin (pels) | Reference point | Total line length (mm) |
| --- | --- | --- | --- | --- | --- | --- |
| ISO A4 | 200 ( 200 240 ( 240 300 ( 300 400 ( 400 600 ( 600 1200 ( 1200 | 1728 2074 2592 3456 5184 10368 | 1654 1984 2480 3308 4960 9922 | (B) 37 45 56 74 112 224 | (38.1) (46.1) (57.1) (75.1) (113.1) (225.1) | 219.46 219.46 219.46 219.46 219.46 219.46 |
| North American Letter | 200 ( 200 240 ( 240 300 ( 300 400 ( 400 600 ( 600 1200 ( 1200 | 1728 2074 2592 3456 5184 10368 | 1700 2040 2550 3400 5100 10200 | (A) 14 17 21 28 42 84 | (15.1) (18.1) (22.1) (29.1) (43.1) (85.1) | 219.46 219.46 219.46 219.46 219.46 219.46 |
| ISO B4 | 200 ( 200 240 ( 240 300 ( 300 400 ( 400 600 ( 600 1200 ( 1200 | 2048 2458 3072 4096 6144 12288 | 1968 2362 2952 3936 5904 11808 | 40 48 60 80 120 240 | (41.1) (49.1) (61.1) (81.1) (121.1) (241.1) | 260.10 260.10 260.10 260.10 260.10 260.10 |
| ISO A3 | 200 ( 200 240 ( 240 300 ( 300 400 ( 400 600 ( 600 1200 ( 1200 | 2432 2918 3648 4864 7296 14592 | 2338 2806 3508 4676 7016 14032 | 47 56 70 94 140 280 | (48.1) (57.1) (71.1) (95.1) (141.1) (281.1) | 308.86 308.86 308.86 308.86 308.86 308.86 |

Table 3/T.563 – Blanking and address reference point for different paper sizes (concluded)

| Paper size | Resolution (pels/25.4 mm) | Pels per line | Pels per each paper size line | Blanking margin (pels) | Reference point | Total line length (mm) |
| --- | --- | --- | --- | --- | --- | --- |
| Japanese Legal | 200 ( 200 240 ( 240 300 ( 300 400 ( 400 600 ( 600 1200 ( 1200 | 2048 2458 3072 4096 6144 12288 | 2024 2428 3036 4048 6072 12144 | 12 15 18 24 36 72 | (13.1) (16.1) (19.1) (25.1) (37.1) (73.1) | 260.10 260.10 260.10 260.10 260.10 260.10 |
| Japanese Letter | 200 ( 200 240 ( 240 300 ( 300 400 ( 400 600 ( 600 1200 ( 1200 | 1728 2074 2592 3456 5184 10368 | 1434 1720 2150 2868 4300 8600 | 147 177 221 294 442 884 | (148.1) (178.1) (222.1) (295.1) (443.1) (885.1) | 219.46 219.46 219.46 219.46 219.46 219.46 |
| North American Legal | 200 ( 200 240 ( 240 300 ( 300 400 ( 400 600 ( 600 1200 ( 1200 | 1728 2074 2592 3456 5184 10368 | 1700 2040 2550 3400 5100 10200 | 14 17 21 28 42 84 | (15.1) (18.1) (22.1) (29.1) (43.1) (85.1) | 219.46 219.46 219.46 219.46 219.46 219.46 |
| North American Ledger | 200 ( 200 240 ( 240 300 ( 300 400 ( 400 600 ( 600 1200 ( 1200 | 2432 2918 3648 4864 7296 14592 | 2200 2640 3300 4400 6600 13200 | 116 139 174 232 348 696 | (117.1) (140.1) (175.1) (233.1) (349.1) (697.1) | 308.86 308.86 308.86 308.86 308.86 308.86 |
| NOTE – The pels as defined in the blanking margin section (blanking margin A and B are shown in Figure 1) are equivalent to the discarded pels defined in Recommendation T.503. |

# 5)	Subclause B.6.2

Amend "Pel-Transmission-Density" in B.6.2 to read as follows:

Pel-Transmission-Density			:: = INTEGER {											--  see 8.2/T.417

p6 (1),  --  6 BMU (200 pels/25.4 mm)

p5 (2),  --  5 BMU (240 pels/25.4 mm)

p4 (3),  --  4 BMU (300 pels/25.4 mm)

p3 (4),  --  3 BMU (400 pels/25.4 mm)

p2 (5),  --  2 BMU (600 pels/25.4 mm)

p1 (6),  --  1 BMU (1200 pels/25.4 mm)  -- }

# 6)	Subclause I.2.2

Amend "Pel-Transmission-Density" in I.2.2 to read as follows:

Pel-Transmission-Density			:: = INTEGER {							--  see 8.2/T.417

p6 (1),  --  6 BMU (200 pels/25.4 mm)

p5 (2),  --  5 BMU (240 pels/25.4 mm)

p4 (3),  --  4 BMU (300 pels/25.4 mm)

p3 (4),  --  3 BMU (400 pels/25.4 mm)

p2 (5),  --  2 BMU (600 pels/25.4 mm)

p1 (6),  --  1 BMU (1200 pels/25.4 mm)  -- }

| ITU-T RECOMMENDATIONS SERIES |
| --- |
| Series A | Organization of the work of the ITU-T |
| Series B | Means of expression: definitions, symbols, classification |
| Series C | General telecommunication statistics |
| Series D | General tariff principles |
| Series E | Overall network operation, telephone service, service operation and human factors |
| Series F | Non-telephone telecommunication services |
| Series G | Transmission systems and media, digital systems and networks |
| Series H | Audiovisual and multimedia systems |
| Series I | Integrated services digital network |
| Series J | Transmission of television, sound programme and other multimedia signals |
| Series K | Protection against interference |
| Series L | Construction, installation and protection of cables and other elements of outside plant |
| Series M | TMN and network maintenance: international transmission systems, telephone circuits, telegraphy, facsimile and leased circuits |
| Series N | Maintenance: international sound programme and television transmission circuits |
| Series O | Specifications of measuring equipment |
| Series P | Telephone transmission quality, telephone installations, local line networks |
| Series Q | Switching and signalling |
| Series R | Telegraph transmission |
| Series S | Telegraph services terminal equipment |
| Series T | Terminals for telematic services |
| Series U | Telegraph switching |
| Series V | Data communication over the telephone network |
| Series X | Data networks and open system communications |
| Series Y | Global information infrastructure |
| Series Z | Languages and general software aspects for telecommunication systems |